Source	Marketwire
Date	01/29/2016
Time	11:10:54 PM

Company	 DISCOVERY VENTURES INC.
Title	Discovery Ventures Inc. Announces Receipt of an Amended Preliminary 
Economic Assessment (PEA) Technical Report





    CDNX Symbol: DVN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Discovery Ventures Inc.

TSX VENTURE SYMBOL: DVN
FRANKFURT SYMBOL: 0DV
OTCQX SYMBOL: DTVMF

January 30, 2016

Discovery Ventures Inc. Announces Receipt of an Amended Preliminary Economic 
Assessment (PEA) Technical Report


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Jan. 29, 2016) - Discovery Ventures 
Inc. ("Discovery" or the "Company") (TSX 
VENTURE:DVN)(FRANKFURT:0DV)(OTCQX:DTVMF) is pleased to announce that it has 
received a technical report entitled Amended Preliminary Economic Assessment 
Technical Report on the Willa Property. The report is an amendment of the 
Technical Report entitled "Preliminary Economic Assessment & Technical Report, 
Willa Max Project" dated May 26, 2014, which supported the original disclosure 
in a May 28, 2014 News Release entitled "WillaMAX PEA Highlights Low CAPEX and 
Robust Economics".

The amended report presents an updated Mineral Resource based on surface and 
underground drilling data collected between 1980 and 2004. The amended report 
also presents the results of a Preliminary Economic Assessment based on a mine 
plan focused on the Measured and Indicated Mineral Resources only of the west 
zone at Willa and processing the material at the MAX facility.

Mineral Resource Estimates

Updated Mineral Resources to form the basis of the PEA were estimated by Mr. 
Michael Waldegger, P.Geo., of MFW Geoscience Inc. Key assumptions and 
parameters considered during the preparation of the Mineral Resource estimate 
are described below.

Gold, copper, and silver grades from drillhole samples collected between 1980 
and 2004 formed the basis of the Mineral Resource estimate. All drillholes were 
completed by historic operators and holes completed prior to 1980 were not 
considered for this estimate. All samples were of half diamond drill core at 2 
m sample lengths and some at 1 m lengths. All missing intervals or blanks were 
replaced with half detection limits.

The estimate was prepared with commercial mining software packages employing 3D 
block modelling techniques.

A recoverable metal value per tonne ("RMV") was used to model the mineralized 
zones, which were used to constrain the grade estimate. The mineralized zones 
were modelled using geological modelling software Leapfrog Geo version 2.2.1 
(Leapfrog) supplied by Aranz Geo. The RMV assumed metal prices guided by the 
three-year average metal prices ($US) of $1400/oz Au, $3.15/lb Cu and $20/oz Ag 
and milling recoveries based on metallurgical test work of 82% for Au, 90% for 
Cu, and 82% for Ag. The mineralized zones are represented by a RMV grade shell 
at a cut-off of $US 100/t.

A geology model based on lithological logs was completed using Leapfrog and was 
used to guide and validate the mineralized zone model.

Block model grade estimation was completed using mining software Geovia Gems 
version 6.7.1 supplied by Dassault Systems. Capped assays were composited to 2 
m lengths and interrupted at the mineralized zone boundaries and the composites 
were used to estimate block grade by Ordinary Kriging within and outside of the 
mineralized zones. Blocks were sized to 4 m cubes and retained a percent rock 
type model. Assays were capped at 50 g/t for gold, 7% for copper, and at 100 
g/t for silver.

Based on estimated block grades for gold copper and silver, a gold equivalent 
grade was computed by block based on the one-year average metal prices ($US) of 
$1200/oz Au, $2.75/lb Cu and $16.50/oz Ag and milling recoveries of 82% for Au, 
90% for Cu, and 82% for Ag. The gold equivalent grade was used as the basis of 
the cut-off to report the Mineral Resources.

A trend of increasing density with increasing sample grade was observed within 
the mineralized zone and therefore a variable density model linked to grade was 
coded within the RMV shell. Outside of the mineralized zone the block model was 
coded with the mean density from samples grouped by the geological model rock 
type.

Mineral Resources were classified in accordance with CIM Definition Standards 
for Mineral Resources and Mineral Reserves (2014). Spacing of drillhole 
intersections was sufficient to reasonably assume continuity of mineralization 
and assign Indicated to most blocks within the RMV shell. Generally the 
Inferred category was assigned to the outer fringe of the RMV shell and where 
underground development intersected the RMV shell in the West Zone blocks were 
upgraded to Measured if they were within 10 m of an underground drillhole 
collar.

The updated Mineral Resources are estimated above a 3 g/t Au Equivalent cut-off 
to be:

/T/

--  198,000 t of Measured Resources at an average grade of 5.36 g/t Au,
0.83% Cu and 8.3 g/t Ag,

--  627,000 t of Indicated Resources at an average grade of 4.97 g/t Au,
0.86% Cu and 9.5 g/t Ag, and

--  151,000 t of Inferred Resources at an average grade of 4.21 g/t Au,
0.71% Cu and 9.8 g/t Ag.

/T/

Mineral Resources that are not Mineral Reserves do not have demonstrated 
economic viability.

Comparison of 2016 Mineral Resource Estimates to Previous Disclosed 2014 
Estimate

The original PEA was based on Mineral Resources disclosed in a 2012 Technical 
Report and estimated above a 3.5 g/t Au cut off to be:

/T/

--  495,784 t of Measured Resources at an average grade of 7.18 g /t Au,
0.94% Cu and 12.16 g/t Ag,

--  262,415 t of Indicated Resources at an average grade of 5.71 g/t Au,
0.67% Cu, and 13.26 g/t Ag, and

--  73,591 t of Inferred Resources at an average grade of 3.39 g/t Au, 0.29%
Cu, and 5.42 g/t Ag.

/T/

The only material technical information, pertinent to the mineral resource 
estimate, collected since the 2012 estimate was 96 samples of mineralized drill 
core tested for dry bulk density. The estimate presented in the Amended 
Technical Report has 21% more volume at a 3% lower density for 17% more tonnes. 
The reported tonnage is 23% lower in Au and Ag grades and 4% higher in Cu grade 
than the 2012 estimate. The updated resource contains 10% fewer ounces of gold, 
21% more pounds of copper, and 8% fewer ounces of silver.

A detailed review of the previous model was not completed; however, the factors 
contributing to the largest changes are likely due to the following changes in 
methodology:

/T/

--  The updated estimate used estimation constraints based on a grade shell
model and applied hard boundaries during grade estimation. The previous
estimate did not use estimation constraints other than the search radius
extent.

--  The updated estimate of grade used the Ordinary Kriging estimator. The
previous estimate used Inverse Distance to the 3rd power.

--  The updated estimate was reported above a 3 g/t gold equivalent cut-off
grade, which considered recoverable contributions from gold, copper and
silver. The previous resource was reported above a 3.5 g/t gold only
cut-off grade.

--  The updated estimate introduced a variable density model based on tests
on samples of drill core and taking into account the observation of an
increase in density with an increase in sample grade. The previous
estimate applied a constant density of 2.9 t/m3.

--  The current estimate applying different capping levels to raw assays.

--  The current estimate was classified differently, with far less tonnage
reporting to the measured category.

/T/

PEA Mine Plan

A mine plan was developed by Wayne Ash, P.Eng., based on the update Mineral 
Resources of the West Zone only. Eight stopes were planned and range in 
Measured and Indicated tonnage from 2,500 to over 180,000 tonnes. The total 
diluted and recoverable tonnage in the eight stopes is estimated at 617,460 
tonnes grading 4.51 g Au/t, 0.81% Cu, and 8.39 g Ag/t. The above recoverable 
Mineral Resource assumes 5% over-break dilution and 95% stope recovery.

Mineral Resources that are not Mineral Reserves do not have demonstrated 
economic viability. The Preliminary Economic Assessment is preliminary in 
nature, and although it does not include Inferred Mineral Resources, there is 
no certainty that the Preliminary Economic Assessment will be realized.

Capital Cost Estimate

The capital cost for the Willa mine is estimated at $C 14 million.

The capital cost for the MAX operation is estimated at $C 7.3 million.

Total capital cost of $C 21.3 million.

Operating Cost Estimate

The estimated operating costs for the project are $C 97.77/t.

Economic Analysis

The tonnage and grade used for the cash flow analysis is the average of all 
eight projected stopes.

Metal prices ($US) of 1200/oz for Au, 2.75/lb for Cu, and 16.60/oz for Ag and 
are based on one-year average prices. Milling recoveries were assumed at 83.9% 
for gold, 90% for copper and 82% for Ag.

The cash flow analysis assumes a daily mine and mill production rate of 400 
tonnes per day (146,000 tonnes per year).

The revenue is estimated at $C 140.3 million, the operating costs at $C 62.5 
million, cumulative cash flow at $C 56.1 million, the after-tax Net Present 
Value (based on a 10% discount rate) at $C 38.7 million, and the after-tax 
Internal Rate of Return at 83%. The mine has an estimated lifespan of 4.25 
years. Due to the accumulated tax pools of about $C 47 million at the MAX 
operation there will be no tax over the life of the Willa mine.

The PEA is preliminary in nature and there is no certainty that it will be 
realized.

Comparison of 2016 Amended PEA to Previous Disclosed 2014 PEA

/T/

----------------------------------------------------------------------------
Amended PEA
Item                                        2016      PEA 2014         units
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Stope Recoverable Tonnage West
Zone                                    617,460       748,826        tonnes
----------------------------------------------------------------------------
Stope Recoverable Gold Grade West
Zone                                       4.51          5.70        Au g/t
----------------------------------------------------------------------------
Stope Recoverable Copper Grade
West Zone                                  0.81          0.87          Cu %
----------------------------------------------------------------------------
Stope Recoverable Silver Grade
West Zone                                  8.39         13.12        Ag g/t
----------------------------------------------------------------------------
World Gold Price Used in Cash Flow
Analysis                                1,200.0       1,200.0   $US/oz troy
----------------------------------------------------------------------------
World Copper Price Used in Cash
Flow Analysis                              2.75          3.00     $US /% Cu
----------------------------------------------------------------------------
World Silver Price Used in Cash
Flow Analysis                             16.50         20.00   $US/oz troy
----------------------------------------------------------------------------
US dollar in Canadian Funds                 1.30          1.10    $C per $US
----------------------------------------------------------------------------
Gold Recovery in Mill                       83.9          82.0             %
----------------------------------------------------------------------------
Copper Recovery in Mill                     90.0          90.0             %
----------------------------------------------------------------------------
Silver Recovery in Mill                     82.0          82.0             %
----------------------------------------------------------------------------
Total Revenue                              140.3         164.8    $C million
----------------------------------------------------------------------------
Capital Cost                                21.7          12.8    $C million
----------------------------------------------------------------------------
Development Unit Cost                      2,000         3,000    $C / metre
----------------------------------------------------------------------------
Stope Mining, Mineral Transport,
Milling Unit Cost                         97.77        102.16         $C /t
----------------------------------------------------------------------------
Total Operating Expense                     62.5          82.8    $C million
----------------------------------------------------------------------------
Smelting Unit Cost                         200.0         220.0    $US/t conc
----------------------------------------------------------------------------
Copper Refining                             0.20          0.22   $US/ lb Cu.
----------------------------------------------------------------------------
Cumulative Cash Flow at End of
West Zone Resource                         56.1          69.1    $C million
----------------------------------------------------------------------------
NPV after tax (10% discount rate)           38.7          55.0    $C million
----------------------------------------------------------------------------
IRR (after tax)                               83           412             %
----------------------------------------------------------------------------
----------------------------------------------------------------------------

/T/

In the amended report, the Capital Costs have increased by 70%. For the Willa 
projected mine life, this increase in capital cost results in a lower Net 
Present Value and a much lower Internal Rate of Return.

Wayne M. Ash, P. Eng., a Qualified Person under NI 43-101 who has an arm's 
length relationship with the Discovery, has read and approved the scientific 
and technical disclosure in this news release that pertains to the Preliminary 
Economic Assessment, and consents to the public filing of this news release. 
Michael Waldegger, PGeo, a Qualified Person under NI 43-101 who has an arm's 
length relationship with Discovery, has read and approved the scientific and 
technical disclosure in the news release that pertains to the Mineral Resource 
Estimate, and consents to the public filling of this news release. The amended 
PEA is available on the Company's SEDAR profile, which is available at 
www.sedar.com.

About Discovery

Discovery Ventures Inc. is a gold, copper and silver mining company focused on 
the exploration and development of its WillaMAX project that is located in the 
Kootenay region of British Columbia. The company holds a 100% interest in four 
mineral properties in B.C., and is currently active in the development
of its Willa Property. Discovery's newly acquired Max Mine and Milling facility 
is located 142 km north of the Willa Project site.

On behalf of the Board of Directors,

Dan Omeniuk, Chief Executive Officer and Director

Neither the TSX Venture Exchange Inc. nor its Regulation Service Provider (as 
that term is defined in the policies of the TSX Venture Exchange Inc.) accepts 
responsibility for the adequacy or accuracy of this press release.

This press release contains forward-looking information that involve various 
risks and uncertainties regarding future events. Such forward-looking 
information can include without limitation statements based on current 
expectations involving a number of risks and uncertainties and are not 
guarantees of future performance of the Company, such as statements regarding 
estimated mineral resources, estimated net present values, internal rates of 
return, daily and annual production, costs, metal prices, and statements 
regarding the Company's development plan. The assumptions made in developing 
the forward-looking statements include: the accuracy of current resource 
estimates and the interpretation of drill, metallurgical testing and other 
exploration results; the timely receipt of required permits; the continuing 
support for mining by local governments; the availability of equipment and 
qualified personnel to advance the projects; execution of the Company's 
existing plans and further exploration and development programs, which may 
change due to changes in the views of the Company or if new information arises 
which makes it prudent to change such plans or programs; efficiency of the 
markets in factoring developments at the projects into its common share price 
and the assumptions and estimates disclosed in the Amended PEA. There are 
numerous risks and uncertainties that could cause actual results and 
Discovery's plans and objectives to differ materially from those expressed in 
the forward- looking information, including: risks of the mineral exploration 
industry which may affect the advancement of the Willa and MAX projects, 
including possible variations in mineral resources, grade, metal prices, 
capital and operating costs, and the application of taxes; availability of 
sufficient financing to fund planned or further required work in a timely 
manner and on acceptable terms; timely receipt of required permits, 
availability of equipment and qualified personnel, failure of equipment or 
processes to operate as anticipated, changes in project parameters as plans 
continue to be refined; failure of equipment or processes to operate as 
anticipated; regulatory, environmental and other risks inherent in the mining 
industry. These and all subsequent written and oral forward-looking information 
are based on estimates and opinions of management on the dates they are made 
and are expressly qualified in their entirety by this notice. Except as 
required by law, the Company does not intend to update these forward-looking 
statements.

- 30 -

CONTACT INFO:

Discovery Ventures Inc.
Dan Omeniuk
Chief Executive Officer and Director
204-697-7740

or

Discovery Ventures Inc.
Ron Birch
250-545-0383
info@discoveryventuresinc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: STK - STOCK/OTHER MARKET NEWS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=556142205