Source	MARKET NEWS
Date	02/10/2016
Time	05:33:48 AM

Company	 ATAC Resources Ltd.
Title	2016 
Exploration Program At The Rackla Gold Proj





    CDNX Symbol: ATC











Press Release





ATAC RESOURCES LTD ("ATC-V;ATADF-0")
- 2016 Exploration Program At The Rackla Gold Project, Yukon

ATAC Resources Ltd. ("ATAC" or the "Company") announces plans for
its fully-funded Phase I exploration and drilling program at its 100%
owned Rackla Gold Project in east-central Yukon. ATAC is well-funded
with approximately $16 million in its treasury.

The proposed 2016 exploration program at the Rackla Gold Project will
consist of Rotary Air Blast ("RAB") drilling at the newly discovered Orion
target and systematic follow up of the new 10 km2 Airstrip gold anomaly and
nearby high priority Rau Trend gold targets identified in 2015. Preparation
for permitting a tote road to the Rau Trend and optimization studies on the
Tiger Gold Deposit are underway.

2016 Phase I Exploration Objectives:

//st

RAB drilling will follow up on the 2015 discovery hole at the Orion
target which returned 3.79 g/t gold over 47.24 m. This hole bottomed in
gold mineralization with the last interval grading 2.56 g/t gold over 1.52
m;

Permitting of a 69 km tote road to the Rau Trend and Tiger Gold Deposit
will commence in spring 2016;

Soil sample coverage around the open-ended, 10 km2 Airstrip gold
anomaly will be significantly expanded and all high priority gold anomalies
will receive detailed prospecting, trenching and mapping; and,

Results and time permitting, RAB drilling will be carried out at the
Airstrip anomaly.

//et

"Both the Orion target and the Airstrip gold anomaly were discovered late
in 2015 and have not received any follow up work. We are excited to get
back into the field in the coming months to begin expansion drilling at the
Orion target and to assess the extensive 10 km2 Airstrip gold anomaly,"
states Graham Downs, President and CEO of ATAC. "Another major initiative
for 2016 will be the permitting of a 69 km tote road to the Rau Trend to
support future pre-feasibility level work at the Tiger Gold Deposit and
advanced exploration at over 20 gold targets and numerous gold-copper-skarn
and silver-lead-zinc targets. Obtaining a tote road permit to the Tiger
Gold Deposit would be a major milestone in advancing the Rackla Gold
Project. "
Orion Target

The Orion target was discovered late in 2015 and is located in the Anubis
cluster of gold targets within the 30 km long Nadaleen Trend.
Mineralization at Orion occurs in both a debris flow-bearing fossiliferous
limestone and a variably calcareous pyritic siltstone. The 2015 discovery
hole (ARB-15-026) was the only hole that was oriented north to exclusively
test the pyritic siltstone; which was previously thought to be an
unfavourable host rock for gold. This hole returned 47.24 m of 3.79 g/t
gold from 15.24 m to 62.48 m, bottoming in 1.52 m of 2.56 g/t gold.

The 2016, Phase I drill program at Orion will consist of approximately
2,000 m of RAB drilling and will continue to test the regionally extensive
pyritic siltstone unit along strike and to the north. A figure showing the
area of proposed 2016 RAB drilling at the Orion target is available on
ATAC's website.

Airstrip Gold Anomaly

The 10 km2 Airstrip gold anomaly was discovered in 2015 and is the largest
gold anomaly in the Rau Trend. The Airstrip anomaly is open in all
directions and is located approximately 4 km south of the Tiger Gold
Deposit. Gold is believed to be sourcing from a favourable package of
variably calcareous sedimentary rocks similar to that seen in a trench at
the Bengal Showing located at the western end of the Airstrip anomaly.
Channel sampling at the Bengal Showing yielded numerous elevated gold
results including 3.19 g/t gold over 1 m. The Bengal Showing has never been
drilled.

Eleven priority targets have been identified within the Airstrip anomaly
for immediate follow up based on the clustering of strongly anomalous
gold-in-soil values. Work in 2016 will include targeted geologic mapping,
test pitting, trenching, soil grid extension and prospecting, with follow
up RAB drilling if warranted. An updated Airstrip anomaly figure is
available on ATAC's website.

Tiger Tote Road

The proposed tote road to the Rau Trend and Tiger Gold Deposit would
branch off the Hanson Lake Road west of Keno City and is envisioned as a
gated, single-lane and radio-controlled road suitable for vehicles that
support advanced exploration. The total length of the tote road would be
approximately 69 km and would consist of 52 km of new road and upgrading of
17 km of pre-existing winter road.

ATAC has been very active in preparing for permitting the tote road to the
Rau Trend and Tiger Gold Deposit. Key studies have been completed along the
proposed tote road route, including heritage, wildlife, hydrological and
water quality surveys and preliminary engineering design. These studies
will be used to support the permitting process that is scheduled to begin
in April 2016.

The technical information in this news release has been approved by Julia
Lane, P.Geo., VP Exploration for ATAC and a qualified person for the
purposes of National Instrument 43-101.

About ATAC

ATAC is a Yukon-based exploration company focused on developing Canada's
only Carlin-type gold district at its 100% owned Rackla Gold Project.
Recent work on the 1,700 km2 project has resulted in a positive Preliminary
Economic Assessment for the Tiger Gold Deposit, drilling of multiple
high-grade Carlin-type gold zones and the identification of numerous
early-stage gold exploration targets. The Rackla Gold Project has no
underlying royalties or third-party interests. ATAC is well financed with
approximately $16 million in its treasury.

On behalf of Management and the Board of Directors
of ATAC Resources Ltd.
Graham Downs, President and CEOA

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.A

Vanessa Pickering
Manager, Corporate CommunicationsA
ATAC Resources Ltd.A
T: 604-687-2522 ext. 260A
info@atacresources.com
______________________________________
_______________________________________________
TSX Venture closing price for ATC-V
Date: 2016/02/09
Closing Price: 0.45
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1604000004TS11604000629-05325320160210