Source	MARKET NEWS
Date	02/10/2016
Time	06:31:57 AM

Company	 Merrex Gold Inc.
Title	Reports Initial 
Mineral Resource Estimate For Th





    CDNX Symbol: MXI











Press Release





MERREX GOLD INC ("MXI-V")
- Reports Initial Mineral Resource Estimate For The Diakha
- Deposit, Siribaya Gold Project, West Mali

Greg Isenor, President and CEO of Merrex Gold Inc., ("Merrex" or
the "Company") announces:

Initial Resource Estimate for Diakha Deposit

The Company announced the initial mineral resource estimate for
the Diakha deposit located on the Merrex-IAMGOLD 50/50 JV Siribaya gold
project in western Mali, West Africa.

The resource estimate, which includes previously reported
resources at Zone 1B and Taya Ko (part of Zone 1A) along the Siribaya
Trend as well as the new Diakha deposit, is comprised of Indicated
Resources totalling 2.1 million tonnes averaging 1.90 grams of gold per
tonne for 129,000 ounces and Inferred Resources comprised of 19.8
million tonnes averaging 1.71 grams of gold per tonne for 1.1 million
ounces. The bulk of the estimate is derived from the newly discovered
Diakha deposit which is open in all directions and at depth and has
significant potential for expansion.

The mineral resource estimate prepared in accordance with the
Canadian Institute of Mining, Metallurgy and Petroleum ("CIM")
Definition Standards incorporated by reference in National Instrument
43-101 is summarized in the following table at a cut-off grades ranging
from 0.45 to 0.60 grams of gold per tonne. The effective date of this
resource estimate is December 31, 2015.

//st
siribaya Project - Mineral Resource Estimate
December 31, 2015

Classification Zone Tonnage(000s) GoldGrade(g/tAu)Contained Ounces(Au)(000s)
Indicated   Zone 1B         2,102             1.90                       129
Total Indicated             2,102             1.90                       129
Inferred    Zone 1B         4,094             1.52                       200
Inferred    Taya Ko           882             1.02                        29
Inferred     Diakha        14,840             1.81                       863
Total Inferred             19,816             1.71                     1,092
//et

Notes:

* -- CIM definitions were followed for classification of Mineral
Resources.

* -- Cut-off grades range from 0.45 to 0.60 g/t Au and vary by
weathering material type.

* -- Mineral Resources are estimated using a gold price of
US$1,500 per ounce.

* -- Bulk density varies from 1.55 g/cm 3 to 2.63 g/cm 3 based on
deposit and weathering code.

* -- The resources are constrained by a Whittle optimized pit
shell.

* -- Numbers may not add due to rounding.

* -- Assays are capped prior to compositing. Capping levels
reduced the resource estimate gold grade for Diakha by approximately
12%, and for Zone 1B and Taya Ko by approximately 4%.

Commentary

"This Diakha resource estimate, combined with resources at 1B and
Taya Ko, now shows independently verified resources in excess of
1,000,000 ounces (1,092,000 ounces Inferred, 129,000 ounces Indicated).
This is a significant milestone and a major accomplishment for a junior
gold explorer" commented Merrex President Greg Isenor. "As stated
above, the Diakha deposit remains open in all directions and at depth,
and I believe that there is significant potential to expand the current
resource with infill and expansion drilling. Diakha was advanced from a
grass roots discovery in May 2014 to an initial resource in December
2015, a period of only 20 months, which is a remarkable achievement,
and on behalf of the management and the shareholders of Merrex I extend
our congratulations to our JV exploration team."

About the Resource Estimate

The mineral resource for the Diakha deposit incorporates assay
results from 216 diamond and reverse circulation drill holes totalling
25,696 metres, and for Zone 1B and Taya Ko zones, incorporates results
from 129 drill holes totalling 3,903 metres. The estimate was prepared
using a block model constrained with 3D wireframes of the principal
mineralized domains. Values for gold were interpolated into blocks
using inverse distance squared (ID 2 ). A preliminary open pit
optimization algorithm was run on the estimated grade block model to
constrain the resource and to support the Canadian Institute of Mining,
Metallurgy and Petroleum ("CIM") requirement that Mineral Resources
have 'reasonable prospects for eventual economic extraction'. The
resource estimate assumes a long-term gold price of US$1,500/ounce.
Only mineralization contained within the preliminary pit shell has been
included in the resource estimate.

In support of the mineral resource estimate SGS Minerals Services
in Lakefield, Ontario, completed preliminary metallurgical testing on
three composite samples prepared from Diakha diamond drill core which
indicated that the gold mineralization is not refractory and that a
gold recovery of approximately 92% can be expected from a conventional
leach / carbon in pulp (CIP) circuit.

For additional details about the resource estimate readers are
referred to the supporting NI 43-101 Technical Report which will be
posted on SEDAR at www.sedar.com no later than 45 days after the date
of this release.

About Merrex's Siribaya Gold Project

The Siribaya Gold Project is a 50/50 joint Merrex-IAMGOLD
advanced-stage gold exploration project in West Mali which consists of
11 contiguous exploration permits which cover a total area of 876.5
square kilometres and is located in the Kedougou-Kenieba inlier of the
West African Craton region of western Mali along the borders with
Senegal and Guinea. The Diakha, Siribaya 1B, and Taya Ko deposits are
hosted within highly prospective, Birimian-aged metasedimentary,
volcanic and intrusive rocks proximal to the Senegal-Mali Shear Zone.
At Diakha, gold mineralization occurs within an albitized sandstone
similar to IAMGOLD's Boto gold deposit located approximately 10
kilometres to the north along strike. Zone 1B and Taya Ko occur within
the north-northeast trending Siribaya structural trend, which extends
over 10 kilometres along strike, and gold mineralization occurs within
breccia-hosted stockworks or fault related silicified zones.

During 2014 and 2015 activity at the project was focussed
primarily on the Diakha deposit area which is located along the
Fekola-Boto trend in the western-most portion of land package
approximately 10 kilometres south along strike of IAMGOLD's Boto gold
deposit (evaluation studies in progress) and approximately 20
kilometres south along strike from B2Gold's Fekola deposit (mine
construction commenced).

Next Steps

The mineralization at Diakha remains open along strike and at
depth where further drilling is warranted. In 2016, additional drilling
is planned to increase confidence in the current resources and continue
to expand the mineralization along strike and at depth.

Jubilee Zinc Exploration License

The Province of Nova Scotia Department of Natural Resources has
granted to the Company an exploration license over certain property
contiguous to the Company's Jubilee lead-zinc prospect near Little
Narrows, Nova Scotia. The grant is subject to various conditions
including completion of formal documentation which is in progress.
Further details will be announced once all paperwork has been
completed.

Qualified Persons

The mineral resource estimate, including verification of the data
disclosed, has been completed by RPA Inc. ("RPA") and reported in
accordance with National Instrument 43-101 (NI43-101) requirements and
CIM Estimation Best Practice Guidelines. The resource estimate was
prepared by RPA Principal Geologist Luke Evans, P.Eng. The supporting
NI 43-101 Technical Report will be posted on SEDAR at www.sedar.com no
later than 45 days after the date of this release.

Mr. Evans, who is an independent qualified person under NI 43-101,
has reviewed and approved the contents of this release. Greg Isenor,
P.Geo., President of Merrex Gold and a Qualified Person as defined by
NI 43-101, has also reviewed and approved the contents of this release.


Merrex is primarily a West African focused gold exploration
company with experienced management, a solid exploration team, a
prominent gold-producer as a JV partner and an expanding gold resource.


For further details about the Company's exploration activities
visit Merrex's website at www.merrexgold.com . To be added to Merrex's
email contact list please email your request to info@merrexgold.com .

On Behalf of the Board
Gregory Isenor
Gregory Isenor, P.Geo.
President & CEO

Cautionary Note to U.S. Investors

The United States Securities and Exchange Commission limits
disclosure for U.S. reporting purposes to mineral deposits that a
company can economically and legally extract or produce. IAMGOLD uses
certain terms in this presentation, such as "measured," "indicated," or
"inferred," which may not be consistent with the reserve definitions
established by the SEC. U.S. investors are urged to consider closely
the disclosure in the IAMGOLD Annual Reports on Forms 40-F. You can
review and obtain copies of these filings from the SEC's website at
http://www.sec.gov/edgar.shtml or by contacting the Investor Relations
department.

Forward Looking Statement

This news release contains forward-looking statements. All
statements, other than of historical fact, that address activities,
events or developments that the Company believes, expects or
anticipates will or may occur in the future (including, without
limitation, statements regarding expected, estimated or planned gold
and niobium production, cash costs, margin expansion, capital
expenditures and exploration expenditures and statements regarding the
estimation of mineral resources, exploration results, potential
mineralization, potential mineral resources and mineral reserves) are
forward-looking statements. Forward-looking statements are generally
identifiable by use of the words "may", "will", "should", "continue",
"expect", "anticipate", "outlook", "guidance", "estimate", "believe",
"intend", "plan" or "project" or the negative of these words or other
variations on these words or comparable terminology. Forward-looking
statements are subject to a number of risks and uncertainties, many of
which are beyond the Company's ability to control or predict, that may
cause the actual results of the Company to differ materially from those
discussed in the forward-looking statements. Factors that could cause
actual results or events to differ materially from current expectations
include, among other things, without limitation: changes in the global
prices for gold, niobium, copper, silver or certain other commodities
(such as diesel, aluminum and electricity); changes in U.S. dollar and
other currency exchange rates, interest rates or gold lease rates;
risks arising from holding derivative instruments; the level of
liquidity and capital resources; access to capital markets, financing
and interest rates; mining tax regimes; ability to successfully
integrate acquired assets; legislative, political or economic
developments in the jurisdictions in which the Company carries on
business; operating or technical difficulties in connection with mining
or development activities; laws and regulations governing the
protection of the environment; employee relations; availability and
increasing costs associated with mining inputs and labour; the
speculative nature of exploration and development; contests over title
to properties, particularly title to undeveloped properties; and the
risks involved in the exploration, development and mining business.
Risks and unknowns inherent in all projects include the inaccuracy of
estimated reserves and resources, metallurgical recoveries, capital and
operating costs of such projects, and the future prices for the
relevant minerals. Development projects have no operating history upon
which to base estimates of future cash flows. The capital expenditures
and time required to develop new mines or other projects are
considerable, and changes in costs or construction schedules can affect
project economics. Actual costs and economic returns may differ
materially from estimates and the Company could fail to obtain the
governmental approvals necessary for the operation of a project; in
either case, the project may not proceed, either on its original timing
or at all.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for MXI-V
Date: 2016/02/09
Closing Price: 0.19

TEL:  (902) 832-5555  MERREX GOLD
FAX:  (902) 832-2223
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1604000010TS11604000856-06300820160210