Source	Marketwire
Date	02/22/2016
Time	08:47:43 AM

Company	 AURION RESOURCES LTD.
Title	Aurion Samples 30.7 and 22.3 g/t Au at Two New High-Grade Gold Prospects 
in Northern Finland





    CDNX Symbol: AU











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Aurion Resources Ltd.

TSX VENTURE SYMBOL: AU

February 22, 2016

Aurion Samples 30.7 and 22.3 g/t Au at Two New High-Grade Gold Prospects in 
Northern Finland


ST. JOHN'S, NEWFOUNDLAND AND LABRADOR--(Marketwired - Feb. 22, 2016) - Aurion 
Resources Ltd. ("Aurion") (TSX VENTURE:AU) is pleased to report that it's 2015 
field program generated several new, wholly-owned, high grade gold prospects in 
the Central Lapland Greenstone Belt of Northern Finland. These prospects have 
highly anomalous gold in rock and till, with the best sample from Ruoppa 
assaying 30.7g/t Au and the best sample from Risti assaying 22.3g/t Au. The 
prospects are all of significant size, with up to 17 km of strike potential and 
excellent access. (See attached map. The highlights of the 2015 program are 
summarized below:

Ruoppa

The Ruoppa target comprises an open-ended 1.9 km long zone of anomalous gold 
samples, within an overall target greater than 7km long, which is contiguous 
with Agnico Eagle's Kuotko deposit (1.8 million tonnes grading 2.9 g/t Au; see 
Agnico Eagle Annual Report).

In the fall of 2015, Aurion outlined extensive gold mineralization over a 
horizontal distance of 1.9km. A total of 81 rock chip samples were collected 
from outcrop, sub outcrop and angular boulders assaying from nil to 30.7 g/t Au 
including 21 samples which assayed greater than 1.0 g/t Au. The mineralization 
comprises narrow mm to less than 1m wide quartz-carbonate veins with minor 
sulphides, free gold and bismuth. Mineralization is hosted by felsic dykes, 
occurring along the margin of an intrusive body. The association of 
quartz-carbonate veins with free gold and bismuth with felsic dykes is very 
similar to that reported at Agnico Eagle's Kuotko gold deposit.

Agnico is currently exploring Kuotko as a potential satellite open pit. Agnico 
reported completing approximately 7,300m of drilling in 2015, identifying new 
mineralized zones outside of the known mineral resource areas. Agnico 
established a Mining Lease in early 2015 and studies are being carried out to 
assess the viability of mining the deposit (Agnico Eagle Press Release dated 
Feb 10, 2016). Historical drill intercepts of 17.5 g/t Au over 5.0m and 23.5 
g/t Au over 3.0m have been reported.

Risti

The Risti target is located approximately 13km east of the Company's Kutuvuoma 
property, which is under joint venture to B2Gold. The property hosts the 
Kaarestunturi prospect, which was discovered by the Geological Survey of 
Finland who completed various studies including 5 shallow diamond drill holes 
within a small area returning up to 5.2 g/t Au over 5.0m.

In 2015, Aurion outlined a new zone of gold mineralization approximately 750m 
northwest of the Kaarestunturi prospect. This new zone hosts gold 
mineralization within quartz-iron oxide veins and breccias cutting altered 
meta-sediments. A total of 30 rock samples from outcrop, sub outcrop and 
angular boulders, within an area of 250m by 250m, assayed up to 22.3 g/t Au 
including 10 samples which assayed greater than 1 g/t Au.

Sila (formerly Silasselka)

The Sila target covers approximately 11km along the northern strike extension 
of the Hanhimaa Shear Zone (HSZ), within sheared meta-volcanics and 
meta-sediments sandwiched between two large intrusive bodies. The HSZ south of 
Sila hosts several gold occurrences, which have reported drill intersections of 
4.5 g/t Au over 11.7m and 5.9 g/t Au over 7.5m (Agnico Eagle Annual report).

Aurion has identified extensive mineralization in quartz veins and silicified 
meta-volcanic and meta-sedimentary rocks. Assays from 56 rock samples collected 
over a distance of 6.5km ranged from nil to 219 g/t Au and nil to 5410 ppm As. 
Numerous till samples assayed up to 0.7 g/t Au within this trend and up to 1.12 
g/t Au elsewhere on the property. The gold-arsenic association at Sila, is 
similar to the Kittila deposit.

Rova

Rova comprises a 17km long less than 1km wide zone of sheared meta-volcanic and 
meta-sedimentary sandwiched between two large intrusive bodies. Historical work 
by the state mining company Outukumpu in the late 1980's highlights an 
approximately 6km long section with anomalous gold (and copper) in till with 
individual till samples assaying up to 4.0 g/t Au. The mineralization comprises 
quartz-carbonate vein sets in sulphide-rich metasedimentary rock, in the 
contact zone between meta-volcanic rocks and intrusives. Five shallow 
drillholes were completed in 1987, within a small area, with a best result of 
2.1 g/t Au over 1.2m.

Summary

These projects have classic "Granite-Greenstone" orogenic gold deposit 
characteristics, similar to those seen in the prolific gold-rich geological 
terranes of Canada, Western Australia and West Africa. Unlike those 
jurisdictions, these projects, and the Central Lapland Greenstone Belt of 
Northern Finland in general, have seen significantly less exploration work.

Since its first acquisition in Finland in mid-2014, Aurion has acquired a large 
database and land position north and south of Kittila, Europe's largest gold 
mine (7.7 Moz gold; Agnico Annual Report). The limited amount of fieldwork 
completed to date has already generated several exciting gold projects, clearly 
demonstrating the prospectivity of Aurion's holdings. It has also been 
successful in attracting B2Gold Corp., one of the most well-respected 
exploration and mining companies in Canada, to jointly explore the Kutuvuoma 
and Ahvenjarvi projects. Aurion is seeking creative partnerships to advance 
these exciting new opportunities.

Quality Assurance and Quality Control

All samples were delivered to Labtium Oy's facility in Sodankyla, Finland. The 
samples were analysed for gold using procedures 704P (Detection Limit - 0.01 
gold; Upper Limit - 100.00 g/t gold) - 25g fire assay with AAS finish or using 
procedures 705P (Detection Limit - 0.005 gold; Upper Limit - 100.00 g/t gold) - 
50g fire assay with AAS finish. Multi-element analysis was completed using 
procedure 511. This procedure detected 31 elements by aqua regia acid 
digestion, HCl leach followed by ICP-OES and ICP-MS analysis. Labtium is a 
Finnish, accredited, certified laboratory group. They are monitored by an 
internal QAQC program and include the inclusion of blank material, duplicates 
and certified reference material.

Mike Basha, P.Eng., P.Geo., President and CEO of Aurion, a Qualified Person as 
defined by National Instrument 43-101, is responsible for the preparation of 
this release. For more information on these projects please visit our website 
at www.aurionresources.com.

Forward-Looking Statement

Certain statements contained in this release constitute forward-looking 
information. These statements relate to future events or future performance. 
The use of any of the words "could", "intend", "expect", "believe", "will", 
"projected", "estimated" and similar expressions and statements relating to 
matters that are not historical facts are intended to identify forward-looking 
information and are based on the Companies' current belief or assumptions as to 
the outcome and timing of such future events. Actual future results may differ 
materially. The forward-looking information contained in this release is made 
as of the date hereof and Aurion is not obligated to update or revise any 
forward-looking information, whether as a result of new information, future 
events or otherwise, except as required by applicable securities laws. Because 
of the risks, uncertainties and assumptions contained herein, investors should 
not place undue reliance on forward-looking information. The foregoing 
statements expressly qualify any forward-looking information contained herein.

On behalf of the Board,

Mike Basha, President & CEO

For further information on these projects please visit our website at 
www.aurionresources.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

To view the map accompanying this press release please click on the following 
link: http://media3.marketwire.com/docs/AU0222.pdf

- 30 -

CONTACT INFO:

Aurion Resources Ltd.
Mike Basha
(709) 699-8300 or (709) 722-2141
mbasha@aurionresources.ca
www.aurionresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=558509738