Source	CANADA NEWSWIRE
Date	02/25/2016
Time	06:02:21 AM

Company	 Eureka Resources, Inc.
Title	Eureka Discovers Conductive Zones at Gemini Lithium Project





    CDNX Symbol: EUK











Press Release




" BC-EurekaConductiveZones   02-25 1345
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Eureka Discovers Conductive Zones at Gemini Lithium Project@

VANCOUVER, Feb. 25, 2016 /CNW/ - Eureka Resources Inc. ("Eureka" or the
"Company") (TSXV: EUK) and its joint venture partner, Nevada Sunrise Gold
Corporation (TSXV: NEV) are pleased to announce that the companies have
received the preliminary results from a time-domain electromagnetic survey
("TDEM") carried out on the Gemini Lithium Project ("Gemini") in Lida Valley,
Nevada. A reconnaissance moving-loop TDEM survey over Gemini West and Gemini
East has detected conductive zones within the sub-basins defined by recent
gravity surveys. The results gained from the TDEM survey are interpreted to be
conductive brines at depth located well below the non-conductive alluvium
(sediments) at surface.
A conductive layer 150-250 metres deep appears to cover most of Gemini
West and Gemini East, and several isolated strong conductive zones were
interpreted at depths from 400 to 600 metres. The conductive layers and zones
are indicative of brine solutions in porous aquifers and traps within each
sub-basin.
Michael Sweatman, President of Eureka stated "we are pleased that the
ground survey has detected conductive layers coincident to the gravity lows
that were previously located. Gemini appears to be a hidden gem and the next
step is to drill into the conductive zones to determine the extent and lithium
content of the interpreted brines".
Gemini is currently the subject of an interim agreement with Nevada
Sunrise Gold Corporation ("Nevada Sunrise") whereby Eureka can earn a 50%
working interest in a joint venture at Gemini with Nevada Sunrise (see Eureka
news release dated January 21, 2016). Nevada Sunrise acts as operator of
Gemini.
A diagram of the TDEM section pertaining to this release is available on
the Company's website: www.eurekaresourcesinc.com
About Gemini and the Lida Valley
Gemini is located approximately 6 miles (10 kilometres) east of the town
of Lida, Nevada, and currently consists of 247 placer claims totaling 4,940
acres (2,000 hectares). Gemini flanks the Gold Point Solar Energy Zone, a BLM
land reserve for solar power generation. The Lida Valley is a flat, desert
basin with a similar geological setting to the established Clayton Valley
basin, which hosts North America's only producing lithium mine at Silver Peak,
located 40 kilometres (26 miles) to the northwest.
The exploration strategy at Gemini is to target desert basins, or playas,
that exhibit similar geological and geophysical characteristics to the Clayton
Valley basin where lithium brines are known to accumulate in faulted
sub-basins, or "traps". Such sub-basins can be delineated by gravity surveys
that detect strong gravity lows.
A detailed gravity survey carried out in 2012 and 2013, indicated strong
gravity lows within two, faulted sub-basins approximately 7 kilometres (4.5
miles) apart, each interpreted to be hundreds of metres deep. Nevada Sunrise
made the decision to acquire claims covering the available land after
reviewing the geophysical results in conjunction with favourable local
geology, namely late Miocene felsic volcanic tuffs adjacent to Gemini. These
rocks provide the source of lithium for trapped, lithium-rich saline
ground-waters (brine) within the sub-basins. On completion of more detailed
TDEM surveys, drilling into the conductive zones within the sub-basin for
lithium-bearing brines is recommended. There are no known drill holes at
Gemini.
John R. Kerr, P. Eng., is the Company's designated Qualified Person for
this news release within the meaning of National Instrument 43-101 and has
reviewed and approved the technical information contained in this news
release.
About Eureka
Since its incorporation in 1981, Vancouver-based Eureka Resources Inc.
has focused on the exploration and evaluation of mineral properties. Its
flagship project, the Frasergold Project ("FG Project,") was the subject of a
National Instrument 43-101 compliant technical report entitled "NI 43-101
Technical Report Frasergold Exploration Project", dated July 20, 2015 and
amended July 27, 2015, authored by K. V. Campbell, Ph.D, P.Geo, and G. H.
Giroux, MA.Sc, P.Eng., and filed on SEDAR. The FG Project is located 100
kilometres east of Williams Lake, B.C. with good access by provincial highways
and secondary roads.
Eureka recently entered into an interim agreement which gives the Company
the right to acquire a 50% participating interest in the Gemini Lithium
Project located in the Lida Valley, Nevada.
FORWARD LOOKING STATEMENTS
All statements in this release, other than statements of historical fact,
are "forward-looking information" with respect to Eureka Resources Inc.
("Eureka") within the meaning of applicable Canadian securities laws,
including statements that address future mineral production, reserve
potential, exploration drilling, the future price of lithium, potential
quantity and/or grade of minerals, potential size of a mineralized zone,
potential expansion of mineralization, the timing and results of future
resource estimates, or other study, proposed exploration and development of
our exploration properties and the estimation of mineral resources.
Forward-looking information is often, but not always, identified by the use of
words such as "seek", "anticipate", "plan", "continue", "estimate", "expect",
"project", "predict", "potential", "targeting", "intends", "believe",
"potential", and similar expressions, or describes a "goal", or variation of
such words and phrases or state that certain actions, events or results "may",
"should", "could", "would", "might" or "will" be taken, occur or be achieved.
These statements involve known and unknown risks, uncertainties and other
factors which may cause the actual results, performance or achievement of
Eureka to differ materially from those anticipated in such forward-looking
information.
Such factors include, among others, risks related to the interpretation
and actual results of historical exploration at the Gemini property, reliance
on technical information provided by third parties on any of our exploration
properties, including access to historical information on the Gemini property,
current exploration and development activities; changes in project parameters
as plans continue to be refined; current economic conditions; future prices of
commodities; possible variations in grade or recovery rates; failure of
equipment or processes to operate as anticipated; the failure of contracted
parties to perform; labor disputes and other risks of the mining industry;
delays in obtaining governmental approvals, financing or in the completion of
exploration, as well as those factors discussed in the section entitled "Risk
Factors" in the Company's Management Discussion and Analysis for the Year
Ended October 31, 2015, which is available under Company's SEDAR profile at
www.sedar.com.
Although Eureka has attempted to identify important factors that could
cause actual actions, events or results to differ materially from those
described in forward-looking information, there may be other factors that
cause actions, events or results not to be as anticipated, estimated or
intended. There can be no assurance that such information will prove to be
accurate as actual results and future events could differ materially from
those anticipated in such statements. Eureka disclaims any intention or
obligation to update or revise any forward-looking information, whether as a
result of new information, future events or otherwise. Accordingly, readers
should not place undue reliance on forward-looking information.
Forward-looking statements are made as of the date hereof and accordingly
are subject to change after such date. Except as otherwise indicated by
Eureka, these statements do not reflect the potential impact of any
non-recurring or other special items or of any dispositions, monetizations,
mergers, acquisitions, other business combinations or other transactions that
may be announced or that may occur after the date hereof. Forward-looking
statements are provided for the purpose of providing information about
management's current expectations and plans and allowing investors and others
to get a better understanding of our operating environment. Eureka Resources
Inc. does not undertake to update any forward-looking statements that are
included in this document, except as required by applicable securities laws.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of TSX Venture Exchange) accepts
responsibility for the adequacy of accuracy of this release. The Securities of
Eureka Resources Inc. have not been registered under the United States
Securities Act of 1933, as amended, and may not be offered or sold within the
United States or to the account or benefit of any U.S. person.
SOURCE Eureka Resources, Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/February2016/25/c1842.html

Image with caption: "Eureka Resources, Inc. (CNW Group/Eureka Resources,
Inc.)".  Image available at:
http://photos.newswire.ca/images/20160225_C1842_PHOTO_EN_629024.jpg

-0-                           02/25/2016
/For further information: Further information about Eureka can be found
on the Company's website at www.eurekaresourcesinc.com and at www.sedar.com,
or by contacting Michael Sweatman, President and CEO or Bob Ferguson by email
at info(at)eurekaresourcesinc.com or by telephone at (604) 449-2273./
/Web Site: www.eurekaresourcesinc.com /
(EUK.)

CO:  Eureka Resources, Inc.
ST:  British Columbia
IN:  MNG
SU:  JVN

-30-