Source	Filing Services Canada
Date	02/26/2016
Time	05:30:11 AM

Company	 GOLDON RESOURCES LTD.
Title	GoldON Provides Drilling Update on Neville-Potier Property





    CDNX Symbol: GLD











Press Release




SOURCE: Filing Services Canada
Date: 02/26/2016
Time: 08:30:00

Company: GOLDON RESOURCES LTD.
Title:GoldON Provides Drilling Update on Neville-Potier Property (GLD - TSXV) 
TSXV SYMBOL: GLD


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: GoldON Resources Ltd.
TSXV SYMBOL: GLD
Friday, February 26, 2016 - 8:30 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/goldon-provides-drilling-update-neville-potie
r-property

GoldON Provides Drilling Update on Neville-Potier Property

The Property Adjoins IAMGOLDs multi-million ounce C[[118]]t[[107]] Gold Project


Victoria, British Columbia (FSCwire) - GoldON Resources Ltd. (GoldON or the 
Company) (TSX-V: GLD) today announced analytical results for the drill hole 
completed on the Neville-Potier property last fall.



As reported January 14, 2016 
(http://goldonresources.com/wp-content/pdfdoc/News%20Releases/2016/GoldON-PR_Jan
142016_NPClaims-Exploration-Update.pdf), a single 210 meter (m) hole (NEV15-11) 
was drilled to test an in-phase VLF cross-over response that lies immediately 
north (150m) of a sub-angular altered felsic volcanic float boulder that 
returned 2.19 g/t Au in previous sampling.



A total of 136 samples were sent for Au FA-AA finish with some for ICP 
analysis. The gold values encountered were only weakly anomalous (10-63 ppb Au) 
despite some strong mineralized argillite/carbonaceous/graphitic units 
alternating with mafic and intermediate volcanic flows. The zone of highest 
pyrrhotite mineralization is interpreted to be the conductive material 
identified by the VLF survey. ICP results did not show any significant 
elemental enrichments associated with only low Zn anomaly associated to one of 
the carbonaceous zones (0.16% Zn over 5.5m from 115.5m depth).



The property, which remains under explored, covers a 15 kilometer swath along 
the Ridout Deformation Zone that has been defined as the extension of the 
Larder Lake-Cadillac Break. All of the major and a host of the secondary gold 
mines, past and present, in the southern Abitibi Belt are near the Larder 
Lake-Cadillac Break or its northern equivalent, the Porcupine-Destor Break. 
Access and infrastructure are excellent, with the propertys southern boundary 
located approximately 3km north of the C[[118]]t[[107]] Gold Project 
(http://www.iamgold.com/English/operations/development-projects/cote-gold-projec
t-ontario/default.aspx).



Andrew Nevin, Ph.D, P.Eng., and Qualified Person as defined by National 
Instrument 43-101, has reviewed and approved the information contained in this 
news release on behalf of the Company.



About GoldON Resources Ltd.



GoldON is an exploration company geographically focused on two of the prolific 
gold mining belts of Ontario, Canada. All of its properties are in good 
standing and include the Slate Falls gold-silver property in northwestern 
Ontario and the Swayze gold property adjoining the multi-million ounce 
C[[118]]t[[107]] Gold Project owned by Trelawney Mining and Exploration, a 
subsidiary of IAMGOLD Corporation. For more information, visit 
www.goldonresources.com (http://www.goldonresources.com).



ON BEHALF OF THE BOARD



Signed Michael Romanik 

Michael Romanik, President

Direct line: (204) 724-0613

Email: info@goldonresources.com (mailto:info@goldonresources.com)



###



Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.


To view this press release as a PDF file, click onto the following link:
http://fscwire.com/sites/default/files/news_release_pdf/GoldOn02262016.pdf
Source: GoldON Resources Ltd. (TSX Venture:GLD) http://goldonresources.com/



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2016 Filing Services Canada Inc.