Source	MARKET NEWS
Date	02/23/2016
Time	07:53:49 AM

Company	 Nikos Explorations Ltd.
Title	Update





    CDNX Symbol: NIK











Press Release





NIKOS EXPLORATION LTD ("NIK-V")
- Update

Nikos Explorations Ltd. ("Nikos" or the "Company") is pleased to
announce its plans for exploration during 2016 to follow up on the
successful exploration at the Borden Lake Extension Project during
2015.
Till samples taken in the vicinity of a weakly anomalous sample
assaying 54ppb gold have been submitted to Actlabs Laboratories in
Ancaster Ontario for analysis. The follow up sampling was undertaken at
a detailed spacing of approximately 50 metres in the vicinity of this
anomaly.
In addition, nineteen samples (10 to 20 pounds) of the till taken
during 2015 have been submitted to Overburden Drilling Management (ODM)
in Ottawa for investigation of the gold content. Samples will be
screened to 2mm, concentrated on a shaking table and the number of gold
grain present will be counted.
Finally a heavy mineral concentrate will be produced for gold
analysis.
Future work planned for 2016 will follow up on the positive
results of the geophysical and geochemical surveys undertaken in 2015
which included an infill program of VLF-EM carried out between lines
3+00W and 6+50E and a soil sampling program over the same area.
Results of the VLF survey show four multi-line VLF anomalies that
correlate with anomalies observed in a 2014 survey and extend them a
further 200m to the northwest. Weak gold anomalies resulting from
mobile metal ion analyses of soil samples extend over 200 metres
sub-parallel to the VLF anomalies. (See map at
http://nikosexplorations.com/projects/borden_lake/ )
Follow up work currently being planned includes line cutting and
an induced polarization survey in the area of the anomalies close to
the boundary with Goldcorp's Borden Lake property. An Exploration Plan
has been submitted to the Ministry of Northern Development and Mines in
order to carry out this work. Results of the induced polarization
survey will be used to generate drill targets.
About Borden Lake Extension:
The Borden Lake Extension Project covers an area of 36 square
kilometres and lies approximately 5 km southeast of Goldcorp's Borden
Lake high grade gold zone where exploration has defined underground
constrained indicated resources of 1.6 MMoz grading 5.39g/t Au and
inferred resources of 0.4 MMoz grading 4.37 g/tAu at a 2.5g/t Au
cut-off grade. This zone remains open along strike to the southeast. In
addition, a lower grade pit constrained indicated resource of 2.3 MMoz
grading 1.03g/t gold has been defined.
Exploration carried out by Nikos is the first known work on the
property, which is located in the Kapuskasing Structural Zone. Nikos
holds an option to earn a 100% interest in the property.
About Nikos Explorations:
Nikos Explorations is a Canadian based mineral exploration company
focused on the acquisition and exploration of prospective gold projects
in the Americas. The company has 13,895,074 shares issued and
outstanding and trades on the TSX Venture Exchange under the symbol
NIK.
The scientific and technical content of this news release was
prepared by Roger Moss, Ph.D., P.Geo a qualified person as defined by
National Instrument 43-101.

The TSX Venture Exchange has not reviewed and does not accept
responsibility for the adequacy or accuracy of this release.























TSX Venture closing price for NIK-V
Date: 2016/02/22
Closing Price: 0.04

TEL: 416-704-8291
Internet: www.nikosexplorations.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1605300025TS11605301498-07525620160223