Source	MARKET NEWS
Date	02/01/2017
Time	10:52:19 AM

Company	 Unigold Inc.
Title	Extends Near 
Surface Oxide Mineralization At Can





    CDNX Symbol: UGD











Press Release





UNIGOLD INC ("UGD-V;UGDIF-0")
- Extends Near Surface Oxide Mineralization At Candelones
- Connector Deposit Intersecting 0.7 G/t Au Over 14.0 Metres And
- 0.8 G/t Au Over 8.6 Metres

Unigold Inc. ("Unigold" or the "Company") is pleased to announce
results from exploration drilling at the Candelones Connector deposit,
within the Company's 100% owned Neita Concession in the Dominican
Republic.

The Company has received results from eight holes evaluating the
potential to expand the footprint of near surface oxide mineralization
discovered at the Candelones Connector deposit in 2013. (Ref. Figure
1.0). The Company's initial mineral resource estimate (UGD PR#
2013-22); summarized in Table 1.0; included an inferred oxide resource
of:

3.5 M tonnes averaging 1.0 g/t Au containing 110,000 Au ounces
at a 1.3:1.0 strip ratio.

Metallurgical testing (SGS Lakefield, 2007), indicates that the
oxide mineralization is amenable to direct cyanidation, with gold
recoveries in excess of 96% reported.

The latest drilling was designed to evaluate the depth and extent
of sub-cropping oxide mineralization. Two fences of vertical holes,
spaced 50 metres apart, tested a 150 metre long by 100 metre wide gap
between the Candelones Main and Candelones Connector deposits where
previous drilling identified the oxide resource.

Significant results from the eight hole program include DCZ16-49:
17.0 metres averaging 0.5 g/t Au, 1.8 g/t Ag; DCZ16-50: 14.0 metres
averaging 0.7 g/t Au, 1.1 g/t Ag and DCZ16-52: 8.6m averaging 0.8 g/t
Au, 6.8 g/t Ag.Table 2.0 summarizes the results of all eight holes
testing the Candelones Connector deposit.

Joseph Del Campo, Interim President and CEO of Unigold notes: "We
are very pleased to have had an opportunity to drill the near surface
oxide mineralization at the Candelones Connector during this
exploration drill campaign. Our drilling at the Candelones Extension,
which successfully expanded the high grade mineralization identified
earlier in 2016, was completed ahead of schedule, providing us with an
opportunity to test the near surface resource potential of the oxide
mineralization identified in 2013. We believe that the robust
metallurgical recoveries and sub-cropping oxide mineralization present
an opportunity for low cost, low strip starter pit(s) that could
improve the overall economics of the Candelones Project. The first step
to capture this upside potential was wide spaced drilling to confirm
the oxide mineralization extended beyond the current resource
footprint, a fact these latest results successfully demonstrate. The
results suggest that the oxide mineralization is relatively flat lying
and is open along strike to the east and west where historical drill
information is sparse. We look forward to further increasing the oxide
resource footprint with targeted exploration as part of our 2017
program. Active drilling at the Candelones Project was suspended in
December and we are currently collecting and evaluating the results and
designing follow up programs to further advance the project."

Table 1.0 - November 2013 Mineral Resource Estimate - Micon
International

//st
--------------------------------------------------------------------
Source            Classification    Mineralization    Deposit
Type
--------------------------------------------------------------------
Open Pit          INFERRED          Oxide             Extension
Main
Connector
--------------------------------------------------------------------
Subtotal
--------------------------------
Sulphide          Extension
Main
Connector
--------------------------------
Subtotal
--------------------------------------------------------------------
Subtotal
--------------------------------------------------------------------
Underground       INFERRED          Sulphide          Extension
Main
Connector
--------------------------------------------------------------------
Subtotal
--------------------------------------------------------------------
TOTAL
--------------------------------------------------------------------

--------------------------------------------------------------------
Source                    Tonnes          Au      Au ozs       Strip
(x 1,000)       (g/t)   (x 1,000)       Ratio
--------------------------------------------------------------------
Open Pit                       -           -
2,448        0.92          72         1.3
1,108        1.12          40         1.3
--------------------------------------------------------------------
3,556        0.98         112         1.3
--------------------------------------------------
24,223        1.59       1,241         7.6
5,003        1.16         186         1.3
980        1.08          34         1.3
--------------------------------------------------
30,206        1.50       1,461         6.4
--------------------------------------------------------------------
Subtotal                  33,762        1.45       1,573         5.8
--------------------------------------------------------------------
Underground                4,977        2.42         387
704        2.21          50
50        2.49           4
--------------------------------------------------------------------
Subtotal                   5,731        2.39         441
--------------------------------------------------------------------
TOTAL                     39,493        1.59       2,014
--------------------------------------------------------------------

NOTES
1. The mineral resource estimate in the Table above has been prepared
under the supervision of Mr. Alan J. San Martin, MAusIMM(CP) and Mr.
William J. Lewis (P.Geo.) of Micon International Limited., both of
whom
are "qualified persons" as per the CIM Standards and independent of
Unigold Inc. The Effective date of the mineral resource estimate is
November 4, 2013.
2. The mineral resource estimate in the Table above is classified as an
Inferred Mineral Resource. The CIM Standards define a Mineral Resource
as "a concentration of material in or on the Earth's crust in such
form
and quantity and of such grade or quality that it has reasonable
prospects for economic extraction." The CIM Standards further define
an
Inferred Mineral Resource as "that part of a Mineral Resource for
which
quantity and grade or quality can be estimated on the basis of
geological evidence and limited sampling and reasonable assumed but
not
verified, geological and grade continuity." The CIM Standards state;
"Due to the uncertainty that may be attached to Inferred Mineral
Resources, it cannot be assumed that all or part of an Inferred
Mineral
Resource will be upgraded to an Indicated or Measured Mineral Resource
as a result of continued exploration.
3. Detailed disclosure on ALL procedures, methodology and assumptions
pertaining to this mineral resource estimate are fully documented and
disclosed in the Technical Report titled: "NI 43-101 Technical Report
Mineral Resource Estimate For The Candelones Project, Neita
Concession,
Dominican Republic" with an effective date of November 4, 2013. Said
report is available for downloading on the Company's website and
SEDAR.

The drill results suggest two, sub-parallel, E-W trending, flat lying zones
of oxide mineralization extend from the Candelones Main deposit through the
Candelones Connector deposit. Oxide mineralization has been intersected
along a 200 metres strike length in the northern zone and remains open to
the east. The southern zone, discovered in 2013, is open to the east and
west (Ref. Figure 1.0).

Mineralization starts at surface and extends to depths of 30 metres.
Oxidation intensity decreases with depth, transitioning to sulphide
mineralization at depths of 12.0 to 18.0 metres from surface. All eight
holes testing the Candelones Connector were vertical holes and as such, the
down hole interval should approximate the true thickness of the
mineralization (Ref. Figure 2.0).

Table 2.0 - Significant Results Candelones Connector



---------------------------------------------------------------------------
-
Hole        Type          From     To   Interval      Au      Ag    Cu
Zn
(m)    (m)     (m)(1)   (g/t)   (g/t)   (%)
(%)
---------------------------------------------------------------------------
-
DCZ 16-46   Sulphide      16.7   40.4       23.7     0.8     3.9   0.1
0.6
including   Sulphide      17.8   29.8       12.0     1.3     5.4   0.1
1.1
---------------------------------------------------------------------------
-
DCZ 16-47   Sulphide      23.0   43.5       20.5     0.3     1.4   0.0
0.2
---------------------------------------------------------------------------
-
DCZ 16-48   Sulphide      52.8   81.3       28.5     0.2     0.6   0.1
0.0
---------------------------------------------------------------------------
-
DCZ 16-49   Oxide          0.0   17.0       17.0     0.5     1.8   0.0
0.0
and         Sulphide      69.5   81.4       11.9     0.3     1.2   0.1
0.0
---------------------------------------------------------------------------
-
DCZ 16-50   Oxide          0.0   14.0       14.0     0.7     1.1   0.0
0.0
including   Oxide          3.0   11.0        8.0     1.2     1.2   0.0
0.0
---------------------------------------------------------------------------
-
DCZ 16-51   Oxide          0.0   24.1       24.1     0.2     0.2   0.0
0.0
---------------------------------------------------------------------------
-
DCZ 16-52   Oxide          6.0   14.6        8.6     0.8     6.8   0.0
0.0
DCZ 16-52   Sulphide      14.6   38.5       23.9     0.6     1.7   0.2
0.1
---------------------------------------------------------------------------
-
DCZ 16-53   Oxide          0.0   14.0       14.0     0.1     2.3   0.0
0.0
---------------------------------------------------------------------------
-
(1) Interval Width is measured down hole and is not True Width. There is
insufficient data to estimate True Width at this time.
---------------------------------------------------------------------------
-
//et

To view FIGURE 1.0 - CANDELONES CONNECTOR OXIDE RESOURCE AREA DRILL
PLAN, please visit the following link:
http://media3.marketwire.com/docs/unigold_feb1_figure1.0.pdf

To view FIGURE 2.0 - CANDELONES CONNECTOR OXIDE RESOURCE SECTION
A-A' LOOKING NORTH, please visit the following link:
http://media3.marketwire.com/docs/unigold_feb1_figure2.0.pdf

Premier Mining Destination - Dominican Republic

The Dominican Republic is host to world-class gold and base metal
mines and deposits. The government supports development and exploration
in the mining sector. In addition, the country has well established
Mining Laws and Environmental Laws. Unigold's wholly owned flagship
property, Neita is compliant with all mineral and environmental
requirements and work is conducted to internationally accepted
environmental and social standards. The Neita concession exploration
license is in good standing.

QA/QC

Diamond drilling at the Candelones Project utilizes both HQ and NQ
diameter tooling. Holes are established using HQ diameter tooling
before reducing to NQ tooling to complete the hole. The core is
received at the on-site logging facility where it is, photographed,
logged for geotechnical and geological data and subjected to other
physical tests including magnetic susceptibility and specific gravity
analysis. Samples are identified, recorded, split by wet diamond saw,
and half the core is sent for assay with the remaining half stored on
site. A minimum sample length of 0.3 metres and a maximum sample length
of 1.5 metres are employed with most samples averaging 1.0 metres in
length except where geological contacts dictate. Certified standards
and blanks are randomly inserted into the sample stream and constitute
approximately 5-10% of the sample stream. Samples are shipped to a
sample preparation facility in the Dominican Republic operated by
Bureau Veritas. Assaying is performed at Bureau Veritas Commodities
Canada Ltd.'s laboratory in Vancouver, B.C. Canada. All samples are
analyzed for gold using a 50 gram lead collection fire assay fusion
with an atomic adsorption finish. In addition, most samples are also
assayed using a 36 element multi-acid ICP-ES analysis method.

Wes Hanson P.Geo., Chief Operating Officer and Technical Director
of Unigold, who is a qualified person under the definitions established
by National Instrument 43-101, has reviewed and approved the contents
of this press release.
About Unigold Inc. - Discovering Gold in the Caribbean

Unigold is a Canadian based mineral exploration company traded on
the TSX Venture Exchange under the symbol UGD, focused primarily on
exploring and developing its gold assets in the Dominican Republic.

For Further Information please visit www.unigoldinc.com.

Forward-looking Statements

Certain statements contained in this document, including
statements regarding events and financial trends that may affect our
future operating results, financial position and cash flows, may
constitute forward-looking statements within the meaning of the federal
securities laws. These statements are based on our assumptions and
estimates and are subject to risk and uncertainties. You can identify
these forward-looking statements by the use of words like "strategy",
"expects", "plans", "believes", "will", "estimates", "intends",
"projects", "goals", "targets", and other words of similar meaning. You
can also identify them by the fact that they do not relate strictly to
historical or current facts. We wish to caution you that such
statements contained are just predictions or opinions and that actual
events or results may differ materially. The forward-looking statements
contained in this document are made as of the date hereof and we assumeno 
obligation to update the forward-looking statements, or to update
the reasons why actual results could differ materially from those
projected in the forward-looking statements. Where applicable, we claim
the protection of the safe harbour for forward-looking statements
provided by the (United States) Private Securities Litigation Reform
Act of 1995.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Mr. Joseph Del Campo
Interim President & CEO
416.866.8157
jdelcampo@unigoldinc.com
www.unigoldinc.com
______________________________________
_______________________________________________
TSX Venture closing price for UGD-V
Date: 2017/01/31
Closing Price: 0.25
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1703100043TS11703101759-10513320170201