Source	MARKET NEWS
Date	02/07/2017
Time	07:41:19 AM

Company	 Stakeholder Gold Corp.
Title	Ballarat 
2016 Exploration Summary and Plans for





    CDNX Symbol: SRC











Press Release





STAKEHOLDER GOLD CORP ("SRC-V")
- Ballarat 2016 Exploration Summary and Plans for 2017

During 2016, Stakeholder Gold Corp. completed a comprehensive
exploration program on the Ballarat project; this work included:
collection of 1,723 grid and reconnaissance soil samples; 425 GT Probe
bedrock interface samples over 5 lines on the Northwest Zone; 11.76
line-km of high-resolution DC IP-Resistivity surveys over 28 lines on
the Northwest and Eastern Zones; a 38.75 sq. km drone-derived, aerial
photographic and DEM data capture survey of the property; geologic
mapping and prospecting; and 1,728.15 m of RAB Drilling in 18 holes on
the Eastern Zone.

Although the 18 RAB holes drilled on the Eastern Zone (of a
planned 30 hole program curtailed due to weather) yielded only narrow
intervals of anomalous gold, the northeastern extension of the zone as
well as the newly-discovered Skye Zone, located 1,500 m to the
southwest, were not tested by drilling. Also, certain targets on the
Northwest Zone have not yet been drilled.

Eastern Zone

Interpretations made by Groundtruth Exploration Inc., who managed
the program, indicate there were two mineralizing events.
One, with an Au-Ag-Hg-Te signature, has similarities to known
occurrences on the White Gold showing and the deep zone in the Golden
Saddle deposit. These can be high grade in the right structural
setting, and the best continuity is found where the
mineralization/alteration is formed at a deeper setting with an Au-Mo
+/-Pb signature (Golden Saddle and QV)

The other event has an Ag-As-Bi-Cu-Pb-Sb-Zn signature. This is
likely later and intrusive-related, most likely dikes following the
same structures that host the earlier gold-rich event. This later event
may have overprinted the earlier one--possibly diluting the gold
content.

Skye Zone

This zone is very much the same as the Eastern Zone but with
better exposure. It contains more quartz veins and the significant
Au-Mo +/-Pb geochemical signature (similar to Golden Saddle). The
orientation of the mineralization is unknown, and this zone needs to be
tested with geophysics and drilling.

Northwest Zone

Mineralization at the Northwest Zone is interpreted to be
associated with E-NE oriented splay(s) from the NE-trending Ballarat
fault, but direct observations of mineralization are few due to cover.
Float of discrete, often sulfide bearing quartz veins and quartz vein
breccias occur; however, pieces of strongly quartz-sericite altered
felsic gneiss with stockwork quartz veining were noted, indicating that
more robust zones of alteration and mineralization exist. Overall,
three primary factors appear to be associated with localizing
mineralization in the NW Zone:

1.) Host rock,

2.) pre-mineral ductile deformation, and

3.) brittle, likely syn-mineral, faulting.

While mineralization can occur over the trend in any of the host
rocks, the primary focus of exploration should be along interpreted
brittle structures within the felsic gneiss and/or contact with the
amphibolite. The Ballarat property has strong potential to host
significant gold mineralization. It sources, and is adjacent to, four
placer bearing creeks: Ballarat, Kirkman, Thistle & Barker. The
property is cut by regional scale structures and has evidence of
multiple ductile-brittle deformation events. It is underlain by
chemically reactive and/or brittle host rocks with robust geochemical
anomalies.

While the results of 2016 exploration activities weren't
significant (in a market sense), they were positive. At the Northwest
Zone, results indicate the potential for km-scale mineralized
structures that are untested (despite historic diamond drilling in the
area) and warrant follow-up drilling. At the East Zone, RAB drilling
intersected significant zones of alteration, albeit at low grades,
adjacent to a regional scale fault, and there are indications of at
least two hydrothermal events. This is important because it
demonstrates that there were active gold-bearing, hydrothermal
system(s) in the area. The Skye zone is a new discovery at surface that
was missed during historic exploration efforts on the property. It is
open for expansion along strike and warrants drill testing. There are
also new anomalies identified from reconnaissance soils that warrant
follow-up grid sampling and prospecting.

A further 146 mineral claims were staked by the Company south of,
and contiguous with, the existing claims; the property now consists of
346 claims covering approximately 69 sq. km (6,900 ha). Little
information is available from this area. The access road planned for
Goldcorp's Coffee deposit will pass through the eastern half of these
claims (Link 1 below).

Specific recommendations for continued exploration on the Ballarat
property include: additional grid and reconnaissance soil samples,
additional IP-Resistivity surveys, additional geologic mapping and
prospecting and initial RAB drilling on the Northwest and Skye Zones.

"During 2016, GroundTruth Exploration Inc. management were able to
identify several targets of merit for gold exploration on Ballarat, and
to increase the size of the Stakeholder land position by more than 42%.
The White Gold District remains one of the world's premiere locations
for gold exploration. Stakeholder is positioned in proximity to much
larger companies (Link 2 below) that have already identified the
significant economic potential of the district, manifesting their
interest by way of acquisitions and joint venture agreements. Ballarat
Creek has been a prolific and rewarding placer gold producer, yielding
in excess of 104,000 oz. of historical gold production, and we are
looking forward to the 2017 exploration season." -- Christopher Berlet,
President and CEO.

Links to recently updated maps on Stakeholder website:

Link 1Ballarat Property Including New Claims & Proposed Coffee
RoadJan, 2017
http://stakeholdergold.com/wp-content/uploads/2016/04/CLAIM-LOCATIONS-BALLA
RAT-copy.jpg

Link 2Major Claim Holders & Deposits of the White Gold District, Yukon
TerritoryJan, 2017
http://stakeholdergold.com/wp-content/uploads/2016/04/WHITE-GOLD-DISTRICT-C
LAIMS-JANUARY-2017.png

John Nebocat, P.Eng is a Qualified Person under NI 43-101 and has
reviewed and approved the technical portions of this news release.

About Stakeholder Gold Corporation

Stakeholder Gold Corp. is a Canadian mineral exploration company
headquartered in Toronto, Canada. The primary focus of Stakeholder is
to explore and develop the Ballarat Gold Property in the White Gold
District of the Yukon Territory.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

For more Stakeholder Gold Corp. information, please contact
Christopher J. Berlet, CFA
President & CEO
416 525-6869
cberlet@stakeholdergold.com

Forward-Looking Statements: This news release contains
forward-looking statements that include risks and uncertainties. When
used in this news release, the words "estimate", "project",
"anticipate", "expect", "intend", "believe", "hope", "may" and similar
expressions, as well as "will", "shall" and other indications of future
tense, are intended to identify forward-looking statements. The
forward-looking statements are based on current expectations and apply
only as of the date on which they were made. The factors that could
cause actual results to differ materially from those indicated in such
forward-looking statements include changes in the prevailing price of
gold, the prevailing price of natural gas, the Canadian-United States
exchange rate, amount of gas produced that could affect revenues and
production costs. Other factors such as uncertainties regarding
government regulations could also affect the results. Other risks may
be set out in the Company's annual financial statements and MD&A.
______________________________________
_______________________________________________
TSX Venture closing price for SRC-V
Date: 2017/02/06
Closing Price: 0.23
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1703700028TS11703701256-07390420170207