Source	Marketwire
Date	02/15/2017
Time	07:22:11 AM

Company	 RIVERSIDE RESOURCES INC.
Title	Riverside Announces Exploration Results from $400,000 Partner-Funded 
Program at the Glor Gold Project





    CDNX Symbol: RRI











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Riverside Resources Inc.

TSX VENTURE SYMBOL: RRI
OTC PINK SYMBOL: RVSDF
FRANKFURT SYMBOL: R99

February 15, 2017

Riverside Announces Exploration Results from $400,000 Partner-Funded Program at 
the Glor Gold Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Feb. 15, 2017) - Riverside 
Resources Inc. ("Riverside" or the "Company") (TSX VENTURE:RRI)(OTC 
PINK:RVSDF)(FRANKFURT:R99), is pleased to report on the progress of the 
partner-funded exploration program being conducted with Centerra Gold Inc. 
("Centerra") at the Glor Gold Project (the "Project"), located approximately 8 
km west of Alamos Gold's El Chanate Mine in Sonora, Mexico. Between August 2016 
and the end of last year, a number of programs of geophysical and geochemical 
surveying were completed along with geological mapping. Expenditures on these 
exploration programs amounted to approximately US$400,000 and were entirely 
funded by Centerra as part of its earn-in requirements (see Riverside press 
release dated July 28, 2016). The results of the 2016 soil and rock sampling 
programs are very encouraging, having defined multiple gold targets in the 
north-eastern, central and western parts of the Glor property.

The 2016 exploration programs included geological mapping at a 1:5,000 scale, a 
37.7 line- kilometre induced polarization survey and a 136 line-kilometre 
ground magnetics survey. In addition, 926 soil samples, 341 rock chip samples 
and 1,468 saw-cut channel samples were collected and analysed. Shallow trenches 
with a combined length of more than 1,200 metres were excavated with a small 
backhoe machine as part of the rock sampling program (34 of 430 channel-cut 
samples (8%) collected from shallow trenches returned gold assays greater than 
0.150 g/t Au, with the highest value being 2.241 g/t Au). The geochemical 
anomalies for gold, arsenic and to lesser extent silver, lead and zinc that 
were outlined in the north-eastern sector of the property are particularly 
significant because they are broadly coincident with zones of anomalous 
geophysical responses detected by the induced polarization survey and with 
bedrock exposures of hydrothermally altered and sheared Mesozoic sedimentary 
rocks (see Riverside press release dated November 14, 2016). Geochemical 
results for gold are shown on the map figure at the bottom of this press 
release.

Highlighted Exploration Results:

/T/

--  2200 metre by 900 metre Au-As soil anomaly defined in northeastern
sector of the property where mapping has identified extensive area of
strongly altered and foliated metasedimentary rocks
--  Induced polarization chargeability anomalies that are broadly coincident
with Au-As soil anomalies identified in northeastern and central sectors
of the property.
--  52 of 341 rock chip samples (16%) show anomalous concentrations of gold,
ranging from 0.152 up to 21.0 g/t Au; mineralized rocks typically
display quartz-sericite-Fe oxide alteration
--  Semi-continuous series of channel-cut samples gave unweighted average
gold content of 0.606 g/t Au across 42 metres (individual 3 metre long
samples returned assays ranging from a low of 0.09 g/t to a high of
2.442 g/t Au)
--  Trench sampling results included of 9 metres @ 0.421 g/t Au; 27 metres @
0.368 g/t Au; 12 metres @ 0.506 g/t Au

/T/

Riverside's President and CEO, John-Mark Staude, stated: "We continue to be 
encouraged by the results of the geochemical and geophysical surveys completed 
to date at the Glor Project, which show positive indications of an orogenic 
gold system. The quartz-sericite alteration, veining and deformation styles are 
similar to such features commonly seen at Sonoran orogenic gold deposits, 
including the nearby Chanate Gold Mine. We now look forward to further results 
from the current trenching and structural mapping program, with plans in place 
to drill in 2017."

To view the map associated with this release, please visit the following link: 
http://media3.marketwire.com/docs/215rri_map.jpg

Figure Above: IP Chargeability Anomalies, Soils & Gold Geochemistry

Additional Exploration Work Now Underway:

Exploration has resumed at Glor and is focusing on the gold targets that were 
defined by the above-described work programs. Centerra will also be funding 
this year's field programs which will involve additional mechanical trenching, 
channel rock sampling and detailed geological mapping of rock alteration, 
structural features and lithologies deemed to be the preferred hosts of the 
gold mineralization found on the property. A heavy-duty excavator (Hyundai 220) 
is currently digging trenches to further test the Pitaya Target. A number of 
other zones of gold mineralization that were identified in 2016 will also be 
trenched and sampled this quarter. Trenches will generally be 50 to 100 metres 
in length and will be dug up to 3 metres into bedrock. Presently, the planned 
exploration program and budget for 2017 calls for two months of trenching and 
channel sampling. The goal of this work will be to clearly define 
high-potential gold targets for drilling which is expected to take place in the 
second half of the year. A drilling program will be planned after the results 
of the ongoing trenching have been received and evaluated.

Additional information about the Glor Project can be found at the Glor Project 
Page on Riverside's website.

Qualified Person and QA/QC:

The scientific and technical data contained in this news release pertaining to 
the Glor Project was reviewed and prepared under the supervision of Locke 
Goldsmith, P. Eng., P. Geo., a non-independent qualified person to Riverside 
Resources who is responsible for ensuring that the geologic information 
provided in this news release is accurate and acts as a "qualified person" 
under National Instrument 43-101 Standards of Disclosure for Mineral Projects.

Soil and rock samples are being taken to the Bureau Veritas Laboratories in 
Hermosillo, Mexico for fire assaying for gold and ICP analysis for 45 common 
and trace elements. A QA/QC program has been implemented as part of the rock 
sampling program at Glor, with 199 blank and standard samples being analysed 
along with the 1,809 rock samples that were collected from the field.

About Riverside Resources Inc.:

Riverside is a well-funded prospect generation team of focused, proactive gold 
discoverers. The Company currently has approximately $3,300,000 in the treasury 
and approximately 37,550,000 shares outstanding. The Company's model of growth 
through partnerships and exploration uses the prospect generation business 
approach to own resources, while partners share in de-risking projects on route 
to discovery. Riverside has additional properties available for option with 
more information available on the Company's website at www.rivres.com.

ON BEHALF OF RIVERSIDE RESOURCES INC.

Dr. John-Mark Staude, President & CEO

Certain statements in this press release may be considered forward-looking 
information. These statements can be identified by the use of forward-looking 
terminology (e.g., "expect"," estimates", "intends", "anticipates", "believes", 
"plans"). Such information involves known and unknown risks -- including the 
availability of funds, the results of financing and exploration activities, the 
interpretation of exploration results and other geological data, or 
unanticipated costs and expenses and other risks identified by Riverside in its 
public securities filings that may cause actual events to differ materially 
from current expectations. Readers are cautioned not to place undue reliance on 
these forward-looking statements, which speak only as of the date of this press 
release.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

John-Mark Staude
President & CEO
Riverside Resources Inc.
(778) 327-6671
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

or

Joness Lang
VP, Corporate Development
Riverside Resources Inc.
(778) 327-6671 or TF: (877) RIV-RES1
Fax: (778) 327-6675
jlang@rivres.com
www.rivres.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=587915334