Source	MARKET NEWS
Date	02/15/2017
Time	08:14:05 AM

Company	 Alba Minerals Ltd.
Title	Drill 
Results Deliver Highest Lithium Values to





    CDNX Symbol: AA.H











Press Release




[200/News Release]AA.HVALBA MINERALS LTDFEB 15 2017  08:11 AMDrill 
Results Deliver Highest Lithium Values to Date from Noram andAlba's Clayton 
Valley Project --->@NEWS RELEASE
NORAM VENTURES INC. ("NRM-V")
ALBA MINERALS LTD. ("ALBA") ("AA.H-V")
- Drill Results Deliver Highest Lithium Values to Date
- from Noram and Alba's Clayton Valley Project

Results from initial 10 holes return lithium values ranging from
600 ppm to a high of 2,320 ppm over 1.22m intervals with an
interval-weighted average value of 1,087.1 ppm lithium

Noram Ventures Inc. ("Noram" or the "Company") and Alba Minerals
Ltd. ("Alba") are pleased to announce the initial sample results from
the first 10 holes of the 46-hole Phase I core drilling program that
focused on the Zeus portion of its Clayton Valley Lithium Project in
Nevada (see Figure 1). The Zeus claims are located within two
kilometers (1.25 miles) of Albemarle's Silver Peak Lithium Mine that
has been in production since 1966 and is the only lithium-brine
production operation in North America.

The 10 holes consisted of 139.3 meters (457 feet) of core drilling
with an average hole depth of 13.9 meters (45.7 feet) and core sampling
done primarily on 1.22 meter (4-foot) intervals. Bradley C. Peek, MSc
and Certified Professional Geologist supervised the collection of the
cores and samples; and sample analysis was performed by ALS Labs (Reno,
NV) on 116 samples from the 10 holes using a 4-acid digestion and
MS-ICP methods for 48 elements.

Table 1 lists each drill hole's location (NAD 83, Zone 11S),
elevation and depth " all in meters. All holes were vertical. All core
size was BQ.
//st
Table 1 - Drill Hole Location Information

Hole ID  UTM Easting  UTM Northing  Approx. Elev.  Depth   Dip
CVZ-01    455519.5     4180579.7       1369.6       15.1   -90
CVZ-02    455574.9     4180542.2       1353.7       14.6   -90
CVZ-03    455583.5     4180419.2       1357.4       14.5   -90
CVZ-04    455652.1     4180441.4       1357.9       14.0   -90
CVZ-05    455624.4     4180375.4       1360.8       13.4   -90
CVZ-06    455840.1     4180350.4       1362.5       11.0   -90
CVZ-07    455608.8     4180596.2       1356.3       14.6   -90
CVZ-08    455684.3     4180599.5       1357.0       14.5   -90
CVZ-09    456084.3     4180778.6       1369.3       15.2   -90
CVZ-12    456147.2     4180742.4       1371.4       12.2   -90
//et
Drill holes CVZ-01 through CVZ-08 are located in an area measuring
approximately 366 meters (1,200 feet) by 213 meters (700 feet ). The
other two holes, CVZ-09 and CVZ-12 are located approximately 366 meters
(1,200 feet) northeast of the main drill-hole grouping (see Figure 2).
Lithium values were found to be very consistent across both groupings.

Table 2 lists the samples, their intervals, their weights and
their lithium analytical results. The core holes were vertical and the
sedimentary units that were tested are horizontal or dipping at less
than 5, so the intervals sampled are true widths.

//st

Hole      Sample   Sample wt.      From       To     From     To       Li
ID            ID         (kg)      (ft)     (ft)      (m)    (m)    (ppm)

CVZ-01    289501         0.76         0        4     0.00   1.22    1,010
CVZ-01    289502          0.4         4        8     1.22   2.44    1,010
CVZ-01    289503         0.58         8       12     2.44   3.66    1,050
CVZ-01    289504          0.8        12       16     3.66   4.88    1,120
CVZ-01    289505          0.7        16       20     4.88   6.10      840
CVZ-01    289506         0.82        20       24     6.10   7.32      940
CVZ-01    289507         0.66        24       28     7.32   8.53      790
CVZ-01    289508         0.72        28       32     8.53   9.75      750
CVZ-01    289509          0.7        32       36     9.75  10.97      760
CVZ-01    289510         0.72        36       40    10.97  12.19    1,010
CVZ-01    289511         0.76        40       44    12.19  13.41      710
CVZ-01    289512         0.76        44       48    13.41  14.63      910
CVZ-01    289514         0.36        48     49.5    14.63  15.09      990
CVZ-02    289515         0.42         0        4     0.00   1.22      940
CVZ-02    289516         0.96         4        8     1.22   2.44    1,410
CVZ-02    289517         0.76         8       12     2.44   3.66    1,000
CVZ-02    289518         0.86        12       16     3.66   4.88    1,060
CVZ-02    289519          0.9        16       20     4.88   6.10      770
CVZ-02    289520         0.72        20       24     6.10   7.32      920
CVZ-02    289521         0.56        24       28     7.32   8.53    1,140
CVZ-02    289522          0.4        28       32     8.53   9.75    1,090
CVZ-02    289523         0.62        32       36     9.75  10.97      850
CVZ-02    289525         0.72        36       40    10.97  12.19      920
CVZ-02    289526          0.8        40       44    12.19  13.41      780
CVZ-02    289527         0.62        44       48    13.41  14.63      720
CVZ-03    289551         0.34         0        4     0.00   1.22    1,630
CVZ-03    289552          0.9         4        8     1.22   2.44    1,190
CVZ-03    289553         0.86         8       12     2.44   3.66    1,100
CVZ-03    289554         0.92        12       16     3.66   4.88    1,330
CVZ-03    289555          0.8        16       20     4.88   6.10      810
CVZ-03    289556         0.82        20       24     6.10   7.32      910
CVZ-03    289557         0.86        24       28     7.32   8.53    1,300
CVZ-03    289558         0.48        28       32     8.53   9.75    1,220
CVZ-03    289559          0.7        32       36     9.75  10.97    1,200
CVZ-03    289560         0.86        36       40    10.97  12.19    1,280
CVZ-03    289561         0.92        40       44    12.19  13.41      950
CVZ-03    289562         0.64        44     47.5    13.41  14.48    1,050
CVZ-04    289563         0.94         0        4     0.00   1.22    1,850
CVZ-04    289564          0.6         4        8     1.22   2.44    1,200
CVZ-04    289565         0.84         8       12     2.44   3.66    1,050
CVZ-04    289566         0.72        12       16     3.66   4.88    1,160
CVZ-04    289567         0.72        16       20     4.88   6.10      880
CVZ-04    289568         0.66        20       24     6.10   7.32    1,090
CVZ-04    289569         0.68        24       28     7.32   8.53    1,290
CVZ-04    289570         0.86        28       32     8.53   9.75      670
CVZ-04    289571         0.94        32       36     9.75  10.97      920
CVZ-04    289572         0.76        36       40    10.97  12.19      860
CVZ-04    289573         0.84        40       44    12.19  13.41    1,010
CVZ-04    289574         0.26        44       46    13.41  14.02    1,100
CVZ-05    289576          0.3         0        4     0.00   1.22    1,530
CVZ-05    289577          0.8         4        8     1.22   2.44    1,610
CVZ-05    289578         0.72         8       12     2.44   3.66    1,500
CVZ-05    289579          0.7        12       16     3.66   4.88    1,630
CVZ-05    289580         0.76        16       20     4.88   6.10    1,110
CVZ-05    289581         0.88        20       24     6.10   7.32    1,000
CVZ-05    289582         0.74        24       28     7.32   8.53      900
CVZ-05    289583         0.38        28       32     8.53   9.75      930
CVZ-05    289584         0.74        32       36     9.75  10.97    1,240
CVZ-05    289585          0.8        36       40    10.97  12.19      880
CVZ-05    289586         0.84        40       44    12.19  13.41      860
CVZ-06    289543         0.72         0        4     0.00   1.22    1,400
CVZ-06    289544          0.9         4        8     1.22   2.44      990
CVZ-06    289545         0.72         8       12     2.44   3.66      980
CVZ-06    289546         1.02        12       16     3.66   4.88    1,400
CVZ-06    289547         0.76        16       20     4.88   6.10    2,320
CVZ-06    289548         0.94        20       24     6.10   7.32    1,290
CVZ-06    289549          1.3        24       28     7.32   8.53      940
CVZ-06    289550         1.74        28       32     8.53   9.75    1,040
CVZ-06    289601         1.22        32    36.25     9.75  11.05      940
CVZ-07    289631         0.54         0        4     0.00   1.22    1,050
CVZ-07    289632         0.76         4        8     1.22   2.44    1,130
CVZ-07    289633          0.9         8       12     2.44   3.66    1,280
CVZ-07    289634         0.82        12       16     3.66   4.88      970
CVZ-07    289635         0.94        16       20     4.88   6.10      970
CVZ-07    289636         0.92        20       24     6.10   7.32      750
CVZ-07    289637         0.84        24       28     7.32   8.53    1,010
CVZ-07    289638         1.12        28       32     8.53   9.75      990
CVZ-07    289639         0.58        32       36     9.75  10.97      900
CVZ-07    289640         0.84        36       40    10.97  12.19      940
CVZ-07    289641         0.42        40       44    12.19  13.41      810
CVZ-07    289642         0.74        44       48    13.41  14.63      690
CVZ-08    289588         0.42         0        4     0.00   1.22    1,020
CVZ-08    289589         0.68         4        8     1.22   2.44    1,080
CVZ-08    289590         0.56         8       12     2.44   3.66    1,010
CVZ-08    289591         0.48        12       16     3.66   4.88    1,130
CVZ-08    289592         0.56        16       20     4.88   6.10    1,340
CVZ-08    289593         0.94        20       24     6.10   7.32    1,150
CVZ-08    289594         0.92        24       28     7.32   8.53      980
CVZ-08    289595         0.88        28       32     8.53   9.75      870
CVZ-08    289596          0.5        32       36     9.75  10.97      600
CVZ-08    289597          0.8        36       40    10.97  12.19      890
CVZ-08    289598            1        40       44    12.19  13.41    1,070
CVZ-08    289599          0.8        44       48    13.41  14.63      850
CVZ-09    289603         0.52         0        4     0.00   1.22    1,020
CVZ-09    289604         0.74         4        8     1.22   2.44      980
CVZ-09    289605         0.72         8       12     2.44   3.66    1,180
CVZ-09    289606          0.8        12       16     3.66   4.88    1,260
CVZ-09    289607         0.66        16       20     4.88   6.10    1,630
CVZ-09    289608         0.54        20       24     6.10   7.32      930
CVZ-09    289609         0.54        24       28     7.32   8.53    1,220
CVZ-09    289610         0.72        28       32     8.53   9.75    1,460
CVZ-09    289611          0.7        32       36     9.75  10.97    1,800
CVZ-09    289612         0.76        36       40    10.97  12.19    1,590
CVZ-09    289613          0.3        40       44    12.19  13.41    1,320
CVZ-09    289614         0.36        44       48    13.41  14.63    1,210
CVZ-09    289615         0.38        48       50    14.63  15.24    1,050
CVZ-12    289617         0.66         0        4     0.00   1.22    1,060
CVZ-12    289618         0.52         4        8     1.22   2.44    1,110
CVZ-12    289619         0.24         8       12     2.44   3.66    1,010
CVZ-12    289620         0.22        12       16     3.66   4.88      920
CVZ-12    289621         0.92        16       20     4.88   6.10      980
CVZ-12    289622         1.28        20       24     6.10   7.32    1,780
CVZ-12    289623         0.98        24       28     7.32   8.53    1,050
CVZ-12    289624         1.04        28       32     8.53   9.75      860
CVZ-12    289625         1.12        32       36     9.75  10.97    1,070
CVZ-12    289626         1.08        36       40    10.97  12.19    1,030




//et
Samples intervals were split by geologists at the drilling program
staging area. Half of the core was retained in the core boxes for
future review and/or sampling. The other half was securely sent to ALS
Laboratories in Reno, Nevada, USA for testing. Core recovery for these
first 10 core holes averaged 79.5%.

The lithium content of the 116 samples had an interval-weighted
average of 1,087.1 ppm with a minimum value of 600 ppm and a maximum
value of 2,320 ppm, both over 1.22m (4 ft) intersections. The samples
had a median value of 1020 ppm Li. These results are well above those
seen in the 73 surface samples collected from the drilling area and
analyzed during exploration work in 2016 and indicate that some
leaching of the lithium has occurred at surface.

Laboratory standards with two different lithium ranges (1,237 ppm
and 783 ppm) were inserted into the sample stream, along with lithium
blanks and duplicate samples (8 QA/QC samples, in all, with this sample
batch). The standards and blanks were obtained from MEG Labs of Reno,
Nevada, USA. Duplicate samples were obtained by splitting the remaining
half of the split core (1/4 of the original core). All analyses of the
standards, blanks and duplicates were well within acceptable ranges.

"These initial results are better than expected and it is rare to
see drill core sample values that exceed the best of previously
reported surface-sampling results (Dec 8 2016). The amazing consistency
of the lithium values, both vertically and horizontally, across the
initial 10 holes is also very encouraging," said Mark Ireton President
and CEO.

Analytical results from the remaining 36 drill holes from the
Phase 1 drilling program are pending.
Noram is amassing one of the largest land packages in Nevada's
Clayton Valley. Its non-contiguous North and South Blocks now total 888
claims covering 17,738 acres and are positioned both north and south of
Albemarle's Silver Peak mine, North America's only lithium producer.

The technical information contained in this news release has been
reviewed and approved by Bradley C. Peek, MSc and Certified
Professional Geologist, who is a Qualified Person with respect to
Noram's Clayton Valley Lithium Project as defined under National
Instrument 43-101.

About Noram Ventures Inc.:

Noram Ventures Inc. (TSX-Venture: NRM / Frankfurt: N7R / OTCBB:
NRVTF) is a Canadian based junior exploration company, with a goal of
becoming a force in the Green Energy Revolution through the development
of lithium and graphite deposits and becoming a low-cost supplier for
the burgeoning lithium battery industry. The Company's primary business
focus since formation has been the exploration of mineral properties.
Current projects include lithium properties in the Clayton Valley of
Nevada and the Hector Lode in San Bernardino County, California; and
the Jumbo graphite property in southeastern British Columbia. Noram's
long term strategy is tobuild a multi-national lithium-graphite
dominant industrial minerals company to produce and sell lithium and
graphite into the markets of Europe, North America and Asia.

Please visit our web site for further information:
www.noramventures.com.

ON BEHALF OF THE BOARD OF DIRECTORS

/s/ "Mark R. Ireton" President & Director

This news release contains projections and forward-looking
information that involve various risks and uncertainties regarding
future events. Such forward-looking information can include without
limitation statements based on current expectations involving a number
of risks and uncertainties and are not guarantees of future performance
of the Company. The following are important factors that could cause
the Company's actual results to differ materially from those expressed
or implied by such forward looking statements; the uncertainty of
future profitability; and the uncertainty of access to additional
capital. These risks and uncertainties could cause actual results and
the Company's plans and objectives to differ materially from those
expressed in the forward-looking information. Actual results and future
events could differ materially from anticipated in such information.
These and all subsequent written and oral forward-looking information
are based on estimates and opinions of management on the dates they are
made and expressed qualified in their entirety by this notice. The
Company assumes no obligation to update forward-looking information
should circumstance or management's estimates or opinions change.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.




______________________________________
_______________________________________________
TSX Venture closing price for AA.H-V
Date: 2017/02/14
Closing Price: 0.21
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1704500024TS11704501342-08114420170215