Source	CANADA NEWSWIRE
Date	02/21/2017
Time	06:07:48 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Upgrades La Curva Project with New Gold-Silver Rock Chip Results
from Cerro Chato Drill Target, Santa Cruz Argentina





    CDNX Symbol: MRZ











Press Release




" BC-Mirasol-La-Curva-updt   02-21 1185
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Upgrades La Curva Project with New Gold-Silver Rock Chip Results
from Cerro Chato Drill Target, Santa Cruz Argentina@

VANCOUVER, Feb. 21, 2017 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
"Mirasol") Recent exploration at the 100%-owned La Curva gold project Santa
Cruz Argentina, has identified a 300 m-long zone of Au+Ag-bearing epithermal
veinlets which crosscut a well-developed barren silica cap at the Cerro Chato
prospect. The veinlets assay up to 10.76 g/t Au and 24 g/t Ag, and directly
overlie a portion of a 1.2 km-long IP geophysical resistivity anomaly centred
at shallow depths beneath the Au+Ag barren silica cap. Mirasol's geologists
interpret the veinlets as possible indications of "geochemical leakage" from a
concealed zone of Au+Ag mineralization beneath the silica cap evidenced by the
large IP resistivity anomaly at the Cerro Chato prospect.
La Curva is a 100% Mirasol-owned, 36,100 ha project at low attitude with
excellent infrastructure on the maritime side of Santa Cruz Province. The
Company has recently announced the signing of a letter of intent (LOI) for a
JV with gold and copper producer OceanaGold Corporation (OGC) to explore and
develop the project (see news release January 30, 2017). The LOI is subject to
due diligence currently being completed by OGC. Mirasol has granted OGC an
exclusivity period ending on March 31, 2017, to negotiate and enter into a
binding JV agreement with Mirasol.
Mirasol has previously reported on the La Curva Project where the
Company's exploration has led to the discovery of wide-spread, undrilled
precious metal mineralization (Figure 1; see news releases; January 23, 2014,
February 24, 2009 and April 11, 2008). Between 2008 and 2014, Mirasol
conducted several phases of exploration at the project which identified the
three drill-ready prospects at Cerro Chato, Loma Arthur and SouthWest; these
are aligned along the 6 km-La Castora gold trend. These prospects are
characterized by coincident large-scale outcropping alteration, IP geophysical
anomalies, and wide-spread anomalous rock chip assays ranging up to 66.8 g/t
Au. Additionally, a series of early-stage prospects have also been identified
in the Curva West area where rock chip anomalies ranging up to 20.73 g/t Au
and 153.6 g/t Ag are found in a prospective geological setting which warrants
further exploration to define drill targets.
During December 2016, Mirasol re-initiated exploration at La Curva,
initially focused on the Cerro Chato prospect where select veinlet rock chip
samples were collected along recently recognized veinlet trends that transect
a 500 m by 650 m silica cap (Figure 2). These veinlets are individually up to
20 cm wide, defining three parallel trends that together encompass a 300 m by
55 m wide veinlet zone. The 109 select rock-chip samples from the veinlets
returned; a maximum assay of 10.76 g/t Au, an average assay of 1.21 g/t Au,
and with 50 samples assaying greater than 0.5 g/t Au and 14 samples assaying
greater than 2 g/t Au (Table 1). The veinlets have textures typical of the
upper zones of high-grade, low-sulphidation epithermal precious vein and
stockwork deposits, suggesting the potential for improving Au+Ag grades at
depth beneath the silica cap.
These anomalous veinlet trends overlie a portion of a 1.2 km-long
northwest-trending IP geophysical resistivity anomaly that in plan view has a
northwest-trending, sigmoidal ("s") shape (Figure 2) and in cross section has
an upward flaring funnel shape, as in seen three dimensional models developed
by Mirasol from the IP resistivity sections (Figure 3). The northwest-trend,
plan view and cross sectional shape of the Cerro Chato IP resistivity anomaly
are characteristics of a number of important Au+Ag deposits in Santa Cruz
Province, where IP resistivity has been used to "map" the dimensions of Au+Ag
deposits developed in large extensional faults.
Table 1: Cerro Chato Veinlet Rock Chip Assay Summary, December 2016
Samples  % of         Au           Ag
Samples      g/t           g/t
---               -------      ---           ---

Min value                     < 0.01        < 2.0
---------                     ------        -----

Max value                            10.76         24.1
---------                            -----         ----

Average value                         1.21          1.7
-------------                         ----          ---

50 Samples                46% > 0.5         > 2.1
----------                ---  -----         -----

28 Samples                26% > 1.0         > 3.0
----------                ---  -----         -----

14 Samples                13%  > 2.0        > 5.1
----------                ---  -----         -----

7 Samples                  6%  > 5.0       > 13.0
---------                 ---  -----        ------

Cerro Chato hosts a number of features indicative of the presence of
concealed high grade vein and bulk mineable stockwork Au+Ag mineralization,
marking this prospect as a priority conceptual drill target. These include; a
large-area of alteration evidenced by the silica cap, the structural fabric of
Au+Ag veinlets, and a large-scale IP resistivity anomaly mapping out a
potentially concealed zone of stockwork and veining. Mirasol's exploration has
developed additional compelling drill targets at Loma Arthur and SouthWest
prospects at La Curva.
Mirasol is pleased to be partnering with OceanaGold at La Curva. Mirasol
has initiated drill permitting of the La Curva project to facilitate a rapid
first-pass drill test following the anticipated late March execution of the
JV. Further updates on additional La Curva prospects will be provided as we
progress toward the start of drilling at the project.
Stephen Nano, President and CEO of Mirasol, has approved the technical
content of this news release and is a Qualified Person under NI 43 -101.
Quality Assurance/Quality Control of the La Curva exploration program:
All previous exploration on the projects was supervised by Mirasol CEO
Stephen C. Nano, who is the Qualified Person under NI 43-101. The technical
interpretations presented here are those of Mirasol Resources Ltd.
Mirasol applies industry standard exploration methodologies and
techniques. All geochemical rock and drill samples are collected under the
supervision of the Company's geologists in accordance with industry practice.
Geochemical assays are obtained and reported under a quality assurance and
quality control (QA/QC) program. Samples are dispatched to an ISO 9001:2008
accredited laboratory in Argentina for analysis. Assay results from drill core
samples may be higher, lower or similar to results obtained from surface
samples due to surficial oxidation and enrichment processes or due to natural
geological grade variations in the primary mineralization.
Forward Looking Statements: The information in this news release contains
forward looking statements that are subject to a number of known and unknown
risks, uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward looking statements. Factors
that could cause such differences include: changes in world commodity markets,
equity markets, costs and supply of materials relevant to the mining industry,
change in government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding future
exploration programs, operation plans, geological interpretations, mineral
tenure issues and mineral recovery processes. Although we believe the
expectations reflected in our forward looking statements are reasonable,
results may vary, and we cannot guarantee future results, levels of activity,
performance or achievements. Mirasol disclaims any obligations to update or
revise any forward looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/February2017/21/c3443.html

-0-                           02/21/2017
/For further information: Stephen Nano, President and CEO, or John
Toporowski, Manager of Investor Relations, Tel: +1 (604) 602-9989: Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG PRM
SU:

-30-