Source	CANADA NEWSWIRE
Date	02/28/2017
Time	04:02:52 AM

Company	 Azarga Metals Corp.
Title	Azarga Metals samples five meters of 32.2g/t silver and 0.69% copper
among other samples in near-surface trenching results





    CDNX Symbol: AZR











Press Release




" BC-AzargaTrenchingResult   02-28 1017
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Azarga Metals samples five meters of 32.2g/t silver and 0.69% copper
among other samples in near-surface trenching results@

TSX-V: AZR
VANCOUVER, Feb. 28, 2017 /CNW/ - AZARGA METALS CORP. ("Azarga Metals" or
the "Company") (TSX-V:AZR) announces assay results from channel sampling of
trenches at its Unkur Copper-Silver Project in the Zabaikalsky administrative
region of eastern Russia. Samples are reported from two trenches that were
excavated at the project. Two additional trenches were excavated on the basis
of copper staining on surface but fell short of the target to intercept
mineralization identified by historic trenching. The onset of winter
conditions at camp precluded continuing undertaking additional trenching
during the first phase field program.
Azarga Metals' President and CEO Dorian (Dusty) Nicol said, "These trench
samples, together with drill hole and samples announced earlier now define an
area of silver-copper mineralization extending over 3,200 meters in strike
length and up to 600 meters in width, which is still open in all directions.
In addition, drilling results suggest the presence of multiple stacked zones
of mineralization. These results of the first phase exploration program add to
our confidence that with continued exploration, Unkur will develop into a
significant and high grade silver-copper deposit."
The Company has now received all assays for its first phase exploration
program. Interpretation of these results is ongoing. Azarga Metals has engaged
SRK Consulting (Russia) Ltd. to prepare a maiden NI 43-101 Resource estimate
at Unkur, which is expected to be completed late in Q1 or early in Q2 of 2017.
TRENCH CHANNEL SAMPLES OF OUTCROPPING MINERALIZATION
Channel samples are reported from each of two trenches located about 400
meters apart from each other and 200 to 400 meters up-dip to the south-west of
the drilling area. Trench K-615 assayed nine meters at 14.0g/t silver and
0.30% copper (ie, 46.0g/t silver equivalent or 0.43% copper equivalent)
including five meters at 20.2 g/t silver and 0.41% copper (ie. 64.0g/t silver
equivalent or 0.60% copper equivalent). Trench K-616 assayed 11 meters at
16.8g/t silver and 0.41% copper (ie, 60.6g/t silver equivalent or 0.57% copper
equivalent) including five meters at 32.2g/t silver and 0.69% copper (ie,
106.0g/t silver equivalent or 0.99% copper equivalent). These trenches add 200
to 400 meters to the identified width of the recognized mineralization at
Unkur.
Note: copper and silver equivalencies have been calculated using
US$17.89/oz silver price and US$2.79/lb copper price and assuming 100%
recoveries.
Note: channel assays are reported as sampled and may not be
representative of true widths. Channels have been sited to attempt to
intersect mineralization as close to perpendicular as possible, but there is
not sufficient information about geometry of the mineralization at this time
to estimate true widths. A Quality Assurance / Quality Control program is part
of the sampling program on the Unkur prospect. This program includes chain of
custody protocols as well as systematic submittals of standards, duplicates
and blank samples into the flow of samples produced by the sampling including
check assays of approximately 10% of the samples by another certified
laboratory. Samples were analyzed at SGS Vostok Limited in Chita, Russia.
Check assays will be analyzed at ALS Geochemistry in Chita, Russia.
FIRST PHASE EXPLORATION UPDATE
The company has now received all assays from drill holes, outcrop and
trench sampling conducted during its first phase exploration program at Unkur.
Significant results are shown on the above map.
UNKUR COPPER-SILVER PROJECT
Azarga Metals owns 60% of the Unkur Copper-Silver Project along with the
right to acquire the remaining 40% in the future.
Sediment-hosted copper and silver mineralization has been identified
across the 5,390 hectare project license area, in outcrops, trenches and by
historical diamond drilling. The prior exploration outlined a large area of
high-grade shallow stratiform sediment hosted copper-silver 20 to 50 meters
thick over an area four to six kilometers long.
Further details concerning Unkur Copper-Silver Project are contained in a
technical report filed by the Company as per its news release of 5 April 2016.
Qualified Person
The Company's President and Chief Executive Officer, Dorian L. (Dusty)
Nicol, B.Sc. Geo, MA Geo, a Qualified Person as defined by NI 43-101, has
reviewed and approved the exploration information disclosures contained in
this Press Release.
About Azarga Metals Corp.
Azarga Metals is a mineral exploration and development company that owns
60% of the Unkur Copper-Silver Project in the Zabaikalsky province in eastern
Russia.
AZARGA METALS CORP.
"Dusty Nicol"Dorian L. (Dusty) Nicol, President and CEO
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Statement:This news release contains forward-looking
statements that are based on the Corporation's current expectations and
estimates. Forward-looking statements are frequently characterized by words
such as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements that
certain events or conditions "may" or "will" occur. Such forward-looking
statements involve known and unknown risks, uncertainties and other factors
that could cause actual events or results to differ materially from estimated
or anticipated events or results implied or expressed in such forward-looking
statements. Such factors include, among others: the actual results of current
planned exploration activities; conclusions of economic evaluations; changes
in project parameters as plans to continue to be refined; possible variations
in ore grade or recovery rates; accidents, labour disputes and other risks of
the mining industry; delays in obtaining governmental approvals or financing;
and fluctuations in metal prices. There may be other factors that cause
actions, events or results not to be as anticipated, estimated or intended.
Any forward-looking statement speaks only as of the date on which it is made
and, except as may be required by applicable securities laws, the Corporation
disclaims any intent or obligation to update any forward-looking statement,
whether as a result of new information, future events or results or otherwise.
Forward-looking statements are not guarantees of future performance and
accordingly undue reliance should not be put on such statements due to the
inherent uncertainty therein.
SOURCE Azarga Metals Corp.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/February2017/28/c7954.html

-0-                           02/28/2017
/For further information: Doris Meyer, at +1 604 536-2711 ext 6, or visit
www.azargametals.com/
/Web Site: https://www.azargametals.com/ /
(AZR.)

CO:  Azarga Metals Corp.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-