Source	Marketwire
Date	01/07/2008
Time	11:21:32 AM

Company	 FIRST MAJESTIC SILVER CORP.
Title	First Majestic Silver Corp.: La Encantada Silver Mine Update and New NI 
43-101 Resource





    CDNX Symbol: FR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: First Majestic Silver Corp.

TSX VENTURE SYMBOL: FR
PINK SHEETS SYMBOL: FRMSF
FRANKFURT SYMBOL: FMV

January 7, 2008

First Majestic Silver Corp.: La Encantada Silver Mine Update and New NI 43-101 
Resource


VANCOUVER, BRITISH COLUMBIA--(Marketwire - Jan. 7, 2008) - First Majestic 
Silver Corp. (TSX VENTURE:FR)(PINK SHEETS:FRMSF)(FRANKFURT:FMV)(WKN:A0LHKJ) 
("First Majestic" or the "Company") is pleased to announce an update regarding 
its activities in Mexico at the La Encantada Silver Mine and a new NI 43-101 
Resource/Reserve update.

La Encantada Silver Mine is located in northern Mexico, in the northern part of 
the physiographic province of the Sierra Madre Oriental in the NW portion of 
the State of Coahuila. It is located in the municipality of Ocampo, at about 
120km to the N60 degrees W from the city of Muzquiz, and 120km to the N7 
degrees W from the city of Ocampo, Coahuila.

First Majestic owns mining rights that cover 2,826 hectares (6,982 acres) 
within 18 titled concessions and 2 claim applications. Also, surface land 
ownership of 1,343 hectares (3,319 acres) where mine, plant, housing, camp and 
associated facilities are installed was acquired from the Ejido Tenochtitlan, 
Municipality of Ocampo. The La Encantada mine consists of all supporting 
facilities, including; a flotation plant with an installed capacity of 800 
tonnes per day ("tpd"), laboratory, maintenance buildings, water wells and 
pipeline, airstrip, 180 houses, mine office, warehouses, club house, kitchen 
and restaurant facilities and guest houses. The mill is presently running at 
700 tpd or approximately 87% capacity. Feed for the mill was split almost 
evenly between ore coming from the mine and ore coming from the reprocessing of 
waste dumps through a pre-screening process implemented in early 2007. This 
mixing of ore from both sources has allowed time for the development within the 
mine to prepare for feeding the mill at a higher percentage rate of ore in 2008.

The aggressive development and exploration program implemented shortly after 
the La Encantada mine was purchased in late 2006 resulted in the release of a 
NI 43-101 Resource estimate in June 2007. This aggressive program has continued 
with exploration efforts carried out during the second half of 2007 being 
primarily focused in proving and developing additional Reserves and Resources 
within the mine. This ongoing program has resulted in a significant increment 
of both Resources and Reserves. Major efforts were undertaken in the areas of 
Breccia Milagros, Bonanza, San Francisco, Intrusivo Milagros, Azul y Oro, and 
Cuerpo de Zinc at mine level N-1535 and in the sampling of old dumps. 
Additional efforts were also carried out in drilling and metallurgical test 
work of the old tailings dams that have resulted in a positive outcome for 
reprocessing by Cyanide Leaching this material to recuperate the contained 
silver.

During the period of June to October, 2007 a total of about 5,000 meters of 
underground workings for exploration purposes were developed at the La 
Encantada mine, including about 4,000 meters of access ramps, drifts, and 
crosscuts, and about 1,000 meters of exploration preparation for underground 
drill sites access for the 2008 program. As can be seen by the tables below, 
significant increases in all categories have been achieved over the previously 
reported Reserves and Resources. Proven and Probable Reserves have increased by 
48% from 8,206,336 ounces Silver to 12,110,507 ounces Silver; the Measured and 
Indicated Resources increased by 212% from 12,548,168 ounces Silver to 
39,099,835 ounces Silver, and; Inferred Resources have increased by 30% from 
9,587,585 ounces Silver to 12,479,000 ounces Silver. The most significant 
increases in Reserves and Resources are within the Breccia Milagros, Bonanza, 
San Francisco areas of the mine and in the two old tailings dams.

The following summary tables were taken from the complete La Encantada Silver 
Mine NI 43-101 Technical Report prepared by Pincock Allen & Holt, Lakewood, 
Colorado (PAH). Shareholders and interested parties are encouraged to read this 
positive report which can be viewed on SEDAR (www.sedar.com) and the Company's 
web site at www.firstmajestic.com.

/T/

Total Proven + Probable Mineral Reserves (Mineable Reserves)(1,3,8)
--------------------------------------------------------------------------
Grade               Metal Contained(2)
----------------------- -----------------------
Silver
(oz.)
Silver  including
Silver    Lead  Zinc(4)        only       Lead
Category(3)        Tonnes  g/tonne       %       %           oz.    Credit
--------------------------------------------------------------------------
Proven Reserves   850,684      283    1.80    0.84    7,731,371  8,068,833
Probable Reserves 358,449      380    1.70    0.75    4,379,136  4,552,002
--------------------------------------------------------------------------
Total Proven +
Probable
Reserves       1,209,133      312    1.77    0.81   12,110,507 12,620,835
--------------------------------------------------------------------------

Total Measured + Indicated Resources(1,3,8)
--------------------------------------------------------------------------
Grade               Metal Contained(2)
----------------------- -----------------------
Silver
(oz.)
Silver  including
Silver    Lead  Zinc(4)        only       Lead
Category(3)        Tonnes  g/tonne       %       %           oz.    Credit
--------------------------------------------------------------------------
Measured
Resources        879,895      347    1.99    0.33    9,823,264 10,247,603
Indicated
Resources(5,6) 6,157,081      148    1.70    2.30   29,276,571 29,875,056
--------------------------------------------------------------------------
Total Measured
+ Indicated
Resources(5,6) 7,036,976      173    1.73    2.05   39,099,835 40,122,659
--------------------------------------------------------------------------

Total Inferred Resources(3,7,8)
--------------------------------------------------------------------------
Grade               Metal Contained(2)
----------------------- -----------------------
Silver
(oz.)
Silver  including
Silver    Lead  Zinc(4)        only       Lead
Category(3)        Tonnes  g/tonne       %       %           oz.    Credit
--------------------------------------------------------------------------
Total Inferred
Resources(7)   1,967,000      200    0.50    0.50   12,479,000 13,428,000
--------------------------------------------------------------------------

(1) Cut Off Grade (COG) estimated as 256 g/tonne Ag only; and 241 g/tonne
Ag eq net of Pb credit. Cut Off Grade for dumps is 98 g/tonne Ag only;
and 91 g/tonne Ag eq net of Pb credit (COG is based on actual sales).
(2) Silver equivalent includes Pb credit, at prices US$10.50/oz-Ag,
US$0.68/lb-Pb. Pb credit equals 15 g/tonne-Ag. For dumps Pb credit
equals 7 g/tonne Ag.
(3) Mining dilution is included at over 2.00m width. Estimates do not
include mining recovery.
(4) Zinc is not recovered.
(5) Tailings are considered as indicated resources. Bulk sampling testwork
in progress.
(6) La Morena sulfide deposit requires additional metallurgical testwork to
prove its economic recovery. La Encantada mill does not have an
operating zinc circuit at this time.
(7) Rounded figures
(8) Total Proven & Probable Reserves, Total Measured & Indicated Resources
and Total Inferred Resources are reported exclusive of each other and
thus are not combined.

/T/

First Majestic is continuing its aggressive program of exploration and 
development throughout 2008 which is believed to have a high probability of 
success given the geological conditions of the mineralization at the mine. In 
PAH's opinion the combination of direct exploration methods, drilling and 
underground development represents a good balance for exploration at La 
Encantada. The program is directed to access projected known areas of 
mineralization as well as to investigate other adjacent and new promising areas 
that may result in an increment of the Resource base and a higher level of 
Reserves for the mine.

The exploration and development program for the La Encantada Silver Mine for 
calendar year 2008 is planned to consist of a minimum of 8,200 meters of 
surface diamond drilling, 5,000 meters of diamond drilling from underground 
sites, and 2,340 meters of underground drifting. In addition to drilling and 
underground exploration and development, an extensive geophysical survey 
consisting of 50 line km's of Induced Polarization will be conducted to 
investigate the various identified anomalous areas, and to confirm other 
indicated potential zones. Some of the most outstanding targets for 
investigation are the La Escalera Breccia zone and the Anomalous areas "A", 
"B", "C" and "D". The La Escalera breccia zone appears to be a significant 
target for exploration and will also be a target in the upcoming drill program. 
Due to the current successes and number of targets at La Encantada, it is 
likely the 2008 exploration and development budget will be expanded further.

The Company's independent Qualified Persons under the policies of National 
Instrument 43-101 who have reviewed the contents of this news release and who 
authored the most recent qualifying report are Leonel Lopez, C.P.G., P.G., and 
Richard Addison P.E., Principal Process Engineer, of Pincock Allen & Holt, who 
are employees of PAH and are independent of the Company.

First Majestic is a producing silver company focused in Mexico and is 
aggressively pursuing its business plan to become a senior silver producer 
through the development of its existing assets and the pursuit through 
acquisition of additional assets that contribute to achieving its corporate 
growth objectives.

FIRST MAJESTIC SILVER CORP.

Keith Neumeyer, President & CEO

This press release includes certain "Forward-Looking Statements" within the 
meaning of section 21E of the United States Securities Exchange Act of 1934, as 
amended. All statements, other than statements of historical fact, included 
herein, including without limitation, statements regarding potential 
mineralization and reserves, exploration results and future plans and 
objectives of First Majestic Silver Corp. are forward-looking statements that 
involve various risks and uncertainties. There can be no assurance that such 
statements will prove to be accurate and actual results and future events could 
differ materially from those anticipated in such statements.

- 30 -

CONTACT INFO:

First Majestic Silver Corp.
Keith Neumeyer
President & CEO
(604) 688-3033 or Toll Free: 1-866-529-2807
Fax: (604) 639-8873
Email: info@firstmajestic.com
Website: www.firstmajestic.com

The TSX Venture Exchange does not accept responsibility for the adequacy or 
accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS