Source	Marketwire
Date	01/18/2012
Time	11:43:09 AM

Company	 PRO MINERALS INC.
Title	Pro Minerals Inc.: Lac Laura Gold-Copper Project Delivers Positive Sample 
Results





    CDNX Symbol: PRM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: Pro Minerals Inc.

TSX VENTURE SYMBOL: PRM

January 18, 2012

Pro Minerals Inc.: Lac Laura Gold-Copper Project Delivers Positive Sample 
Results


VANCOUVER, BRITISH COLUMBIA--(Marketwire - Jan. 18, 2012) - Pro Minerals Inc. 
(TSX VENTURE:PRM) and its Board of Directors are pleased to report that the 
Company has received positive assay results from the channel sampling portion 
of its recent stripping, channel sampling, and diamond drilling program carried 
out on its 100% owned Lac Laura Gold Project; situated near the mining town of 
Chapais, Quebec. Results from the channel sampling are discussed and detailed 
below and the results from the drilling portion of the program are yet to be 
received.

The mineralized showings, where the stripping and drilling programs were being 
carried out, are located approximately 800m north of the Chapais-Senneterre 
Highway. They were discovered in 2009 and had not been drilled previously. In 
2009, one of the grab samples collected by Dr. Christian Derosier, P.Geo., QP 
for the project, returned 128.5 g/t Au (4.1 oz Au), 113 g/t Ag and 2.61% Cu. 
The most recent stripping and sampling program covered and area of 
approximately half a hectare around that high-grade 2009 showing; which was 
discovered on the south face of a small cliff of a rounded hill. The recent 
stripping was made utilizing a hydraulic shovel and powerful high pressure 
washing equipment. The work uncovered favourable meta andesite units cut by 
faults and narrow shear zones.

Pro Mineral's channel sampling was made across a number of mineralized veins, 
mostly following a N-S direction, in order to intersect, at a good angle, the 
three sets of shear zones. The channel samples were each 1 m long, 5 cm in 
width and 7 cm deep. They were cut utilizing a gas powered diamond grit saw. 
Each sample was removed using a chisel and a hammer and placed in a plastic 
sample bag which was then tagged and sealed by the project QP. The sample bags 
were then sent to Techni-Lab S.G.B. Abitibi Inc., a member of the ACTLABS 
Group. Samples were assayed for base and precious metals by fire assay method 
(Au, Co, Pt, and Pd) with the AA and gravimetric finish (Au); and the base 
metals were assayed by the ICP method. A total of 62 channel samples were been 
taken and assayed.

Patrick D. O'Brien, ICD.D, Pro Mineral's Chairman and Chief Executive Officer, 
comments: "Pro's team was delighted to receive sample results of this nature in 
a gold-driven economic climate. Pro Minerals placed considerable faith in the 
merits of the Lac Laura Gold-Copper Project to provide results encouraging 
enough to justify an aggressive follow-up diamond drill program. The desired 
outcome has been achieved and Pro Minerals plans to move the Lac Laura 
Gold-Copper Project forward as expediently as possible."

It preparation for review of the following sampling results it should be noted 
that two major ENE-WSW trending vertical faults divide the stripping target 
area into three distinctive zones. For ease of reference they are referred to 
as he Northern, Central and Southern zones.

The Southern zone is represented by a unit of silicified meta-andesite having a 
schistosity oriented ENE and dissected by a network of NE-SW, E-W, WNW-ESE and 
NW-SE faults and joints. The meta-andesite shows elongated and highly foliated 
pillow lavas in the western part passing to a more massive and granular 
meta-andesite in the Eastern zone.

Some of the NE oriented faults have been filled by quartz- sulfide veins and 
veinlets, displaying a rusty alteration on surface. A WNW-ESE trending shear 
zone (SZ#1), varying in thickness from 10 cm to 2.2 m has been evaluated by two 
channels cut 16 metres apart. Results obtained are as follows:

East section:

/T/

---------------------------------------------------------------------------
Sample #           Length in m         Au g/t         Ag g/t           Cu %
---------------------------------------------------------------------------
43879                    0.75m       4.32 g/t      12.90 g/t          0.10%
---------------------------------------------------------------------------

/T/

West section:

/T/

---------------------------------------------------------------------------
Sample #           Length in m         Au g/t         Ag g/t           Cu %
---------------------------------------------------------------------------
43881                   0.80 m      11.30 g/t       5.50 g/t          0.07%
---------------------------------------------------------------------------
43882                   0.80 m       1.65 g/t       3.60 g/t          0.22%
---------------------------------------------------------------------------

/T/

Immediately North, of the ENE-WNW faults, the "Discovery" mineralized zone was 
found to correspond to a narrow NW oriented shear zone. Along this shear zone, 
the mineralization appears lenticular. Boudinage (geological term for 
often-favourable structures formed by extension, where a rigid tabular body 
such is stretched and deformed amidst less competent surroundings) is well 
visible along this shear zone. Because the Discovery showing was found on the 
south mirror of the fault, it was very difficult to cut a horizontal channel 
right on the gossan itself. A representative channel sample taken a few metres 
above the showing, on top of the cliff, gave the following results:

Discovery North:

/T/

---------------------------------------------------------------------------
Sample #           Length in m         Au g/t         Ag g/t           Cu %
---------------------------------------------------------------------------
43859                    1.15m       1.13 g/t          Trace          Trace
---------------------------------------------------------------------------

/T/

The Central zone of the "Discovery" area is divided into two sectors by a NW 
trending shear zone. The Western sector is covering a highly schistozed 
pillowed meta-andesite with considerable small elongated pillows. In this part, 
the schistosity is oriented NW and dipping vertically. Tops of the pillows have 
been interpreted to be trending towards west. East of the NW shear zone, the 
meta-andesite is aphanitic to porphyritic, highly schistozed and cut by 
considerable stringers and veinlets of quartz and numerous joints. In the 
center of this Central zone, a favourable WNW-ESE strongly sheared and faulted 
zone (SZ #2), about 8 m wide; accompanied by metric quartz-sulfide veins can be 
followed for more than 30 m and appears to be still open in both directions. 
The quartz-carbonate sulfide veins visible are boudinaged, and range in 
thickness, from 0.30 m to 2.50 m.

Shear Zone #2 - North (SZ #2), the North Shear: was sampled with four channel 
samples cut at approximately 5 m intervals. Starting from the east end, results 
are as follows:

/T/

---------------------------------------------------------------------------
Sample #  Area of Shear Zone      Length in m     Au g/t     Ag g/t    Cu %
---------------------------------------------------------------------------
43853     NSE                          0.70 m   1.41 g/t   1.60 g/t   Trace
---------------------------------------------------------------------------
43849     NSE2                         0.80 m   4.99 g/t   8.70 g/t   0.21%
---------------------------------------------------------------------------
43897     NSC                          1.00 m   2.11 g/t   7.20 g/t   0.52%
---------------------------------------------------------------------------
43838     NSC                          1.10 m   3.84 g/t   6.90 g/t   0.07%
---------------------------------------------------------------------------
43841     NSW                          1.00 m  21.86 g/t  10.80 g/t   0.21%
---------------------------------------------------------------------------
43840     NSW                          1.20 m   4.68 g/t   5.50 g/t   0.19%
---------------------------------------------------------------------------
43829     NSW2                         0.90 m   2.61 g/t   2.80 g/t   0.14%
---------------------------------------------------------------------------

/T/

Shear Zone #2 - South

/T/

---------------------------------------------------------------------------
Sample #  Area of Shear Zone      Length in m     Au g/t     Ag g/t    Cu %
---------------------------------------------------------------------------
43837     South Shear                  1.50 m   9.43 g/t   8.60 g/t   0.36%
---------------------------------------------------------------------------
43836     South Shear                  1.00 m  10.35 g/t   6.10 g/t   0.36%
---------------------------------------------------------------------------
43833     South Shear 2                0.50 m   3.74 g/t   0.90 g/t   Trace
---------------------------------------------------------------------------

/T/

The Northern Zone area has the same lithologies as the Central Zone area. 
Despite the presence of evident gossan and rusty zones, the NW trending shear 
zone separating the pillowed meta-andesite from the aphanitic and porphyric 
meta-andesite returned very low gold and silver grades, but showed anomalous 
copper values ranging from 243 ppm to 1863 ppm (0.18% Cu) over 1 m.

The channel sampling program confirmed the presence of very encouraging gold, 
silver and copper mineralization in the Northern part of the Lac Laura 
property. The results show that the precious metals are mostly associated to 
WNW-ESE and NW-SE shear zones which affect both the aphanitic and the pillowed 
meta-andesite. The vertical quartz- sulfides veins are boudinaged and seem to 
plunge to the SE.

While working on the stripping, Pro Mineral's technicians discovered a 
mineralized gossan on an outcrop. This meta-andesite outcrop forms the south 
bank of the Otter River and is located at about 125 m NW of the stripping. This 
gossan was channel sampled and the sample assayed as well. Results obtained are 
as follows:

/T/

---------------------------------------------------------------------------
Sample #  Sample Area             Length in m     Au g/t     Ag g/t    Cu %
---------------------------------------------------------------------------
43902     Otter River Copper Fault      1.0 m  51.26 g/t  38.80 g/t   1.07%
---------------------------------------------------------------------------

/T/

It has been noted that the Otter River follows the Chiboug Copper Fault which 
is known in the surrounding Chapais area for its potential to host economic 
"Cooke Mine type" gold-copper mineralized orebodies. This Chiboug Copper Fault 
crosses over and through the well-known "Cooke Mine" which was successfully 
operated from 1977 to 1989 by Inmet Mining Corporation. The Cooke Mine produced 
2 Mt grading 5.00 g/t Au, 10 g/t Ag and 0.66% Cu; from mesothermal 
quartz-sulfide veins, deeply embanked in narrow E-W to WNW-ESE oriented shear 
zones which cut the south part of the Blondeau Formation. All numbers re the 
Cooke Mine are for reference purposes only and are non NI 43-101 compliant.

Pro Mineral's Lac Laura diamond drill program which commenced on December 7, 
2011 was designed to test at depth the extensions of the main shear zones with 
their quartz-sulfide veins. Four holes were bored for a total length of 477 
metres (1,565 feet) and the drill samples have now been submitted for assaying, 
with the results pending. Pro Minerals will now analyze the data it has 
received to date in more detail, and will be utilizing its findings in planning 
its next phase of diamond drilling for the Lac Laura Gold Copper Project.

This press release has been reviewed by Dr. Christian Derosier, P.Geo., 
Consulting Geologist. Dr. Derosier is the Qualified Person (QP) for the Lac 
Laura Gold Project under the National Instrument 43-101. Additional information 
regarding the Lac Laura Gold Copper Project is contained on the Company's 
website at www.promineralsinc.com.

ON BEHALF OF THE BOARD OF DIRECTORS OF PRO MINERALS INC.

Patrick D. O'Brien, ICD.D, Director

- 30 -

CONTACT INFO:

Pro Minerals Inc.
Adrian Bakker
604-608-6168 or Toll Free: 1-800-663-8990
Fax: 604-683-8903
info@promineralsinc.com
www.promineralsinc.com

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=329417515