Source	Marketwire
Date	01/13/2014
Time	04:00:42 AM

Company	 MUNDORO CAPITAL INC.
Title	Mundoro's Trenching at Savinac License Continues to Yield Results





    CDNX Symbol: MUN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN
FRANKFURT SYMBOL: NGU:GR

January 13, 2014

Mundoro's Trenching at Savinac License Continues to Yield Results


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Jan. 13, 2014) - Mundoro Capital 
Inc. (TSX VENTURE:MUN)(FRANKFURT:NGU:GR) (www.mundoro.com) ("Mundoro" or the 
"Company") is pleased to provide an update on its exploration activities at its 
100% owned Savinac, Zeleznik and Sumrakovac properties along the Timok Magmatic 
Complex (TMC). Located in northeast Serbia, the TMC hosts significant 
gold-copper porphyry and related gold-copper epithermal deposits with the 
benefit of European infrastructure.

Teo Dechev, President and CEO commented, "We are very pleased to provide 
investors with an update to our exploration program. At Savinac, we continued 
trenching at Tilva Rosh, for which we previously reported high grade gold 
results near surface. The follow up trenches continued to extend the 
mineralization and the geochemical sampling around the area identified new 
parallel zones. Our next step at Tilva Rosh will be to drill test at depth. 
Work at our Zeleznik license, which sits along the same geological and 
structural setting as the Majdanpek Mine, highlighted two areas with 
significant Cu-Au-Mo anomalies which are slated for trenching and drilling in 
2014. Mundoro has quickly moved along from compiling an extensive property 
package in the TMC area to defining a number of near surface mineralized zones 
to now drill testing in 2014". "In parallel to our exploration activity, we 
continue to evaluate joint venture opportunities for our projects while at the 
same time evaluating developed assets closer to production."

Savinac

The soil geochemical campaign highlighted three major mineralized areas:

/T/

--  Tilva Rosh to the North,
--  Bukovo in the center, and
--  Markov Kamen to the South.

/T/

The high grade gold results previously obtained at Tilva Rosh are controlled by 
a north-west fault directly related to a gold-in-soil anomaly of 600 m by 170 
m. The north-west fault also intersects the north-east structure adding an 
additional 1200 m by 400 m gold-in-soil anomaly to be followed up in Q1 2014 
(Figure 1 - Savinac Gold-in-Soil Geochemical Anomalies, Figure 2 - Tilva Rosh 
Trench and Rock Results). Follow-up exploration work in 2014 will consist of 
mapping, trenching along the new parallel zones and drill testing the trenched 
gold prospect in mid-2014.

The soil sampling comprised 1,679 samples and was designed to cover Savinac's 
hydrothermal alteration system. The results confirmed the presence of a 
mineralized structural zone extending over a strike length of more than 7 km 
identified by soil samples containing greater than 20 parts per billion (ppb) 
gold associated with Ag, Cu, Mo, Pb, Zn, Sb and As anomalies (Figure 1). This 
structural zone, marked by intense argillic and advance argillic altered 
andesite volcanics, contains two major fault directions north-west and 
north-east.

The gold in-soil anomaly and the initial high grade trench results were 
followed up by step-out trenches and outcrop rock sampling. The trenches were 
dug down to bedrock (0.5 to 1.5 m depth), perpendicular to strike of the 
mineralised structure and the trend of the soil anomaly. Continuous channel 
samples of up to 2 m long were collected along the base of the trenches.

Selected results are summarized in Table 1. The location of trenches and rock 
outcrop results are shown on Figures 1 and 2. Table 1: Summary of significant 
trench results from Tilva Rosh prospect, Savinac license. (Trench results 4, 2 
and 1 were previously reported on September 3, 2013)

/T/

----------------------------------------------------------------------------
Interval
Trench ID        From (m)    To (m)       (m)  Au (g/t)  Ag (g/t) AuEq (g/t)
----------------------------------------------------------------------------
T4                      0        12        12     30.39    127.00      32.51
----------------------------------------------------------------------------
Including               8        12         4     59.34    277.41      63.96
----------------------------------------------------------------------------
Including              10        12         2     80.70    174.00      83.60
----------------------------------------------------------------------------
T2                    130       138         8      5.31     21.07       5.66
----------------------------------------------------------------------------
Including             130       132         2     24.50     17.60      24.79
----------------------------------------------------------------------------
T1                      0        18        18      2.21     29.00       2.69
----------------------------------------------------------------------------

----------------------------------------------------------------------------
T13                    20      30.8      10.8      1.40      7.58       1.53
----------------------------------------------------------------------------
Including              24        26         2      6.99     21.10       7.34
----------------------------------------------------------------------------
T6                     25        27         2      1.08     14.20       1.32
----------------------------------------------------------------------------
T7                     26        38        12      1.05     13.95       1.28
----------------------------------------------------------------------------
T14                  39.6      43.2       3.6      0.77      6.80       0.88
----------------------------------------------------------------------------
T5                     12        16         4      0.72      4.40       0.79
----------------------------------------------------------------------------
T11                    26        30         4      0.71      8.75       0.86
----------------------------------------------------------------------------
T8                      2         4         2      0.50      2.60       0.54
----------------------------------------------------------------------------
T12                     0        22        22      0.49      4.27       0.56
----------------------------------------------------------------------------
Including            17.4        20       3.6      0.65     12.15       0.85
----------------------------------------------------------------------------
Including              10        12         2      3.47      1.70       3.50
----------------------------------------------------------------------------
Including               6         8         2      0.67     21.70       1.03
----------------------------------------------------------------------------
-Weighted average calculated using uncut assays.
-Trench intercepts are sample lengths and further work is required to
determine true widths.

/T/

The results from the soil geochemistry between trenches T13 and T5 identifies a 
high grade bearing north-west structure. The structural mapping and the soil 
geochemistry suggests an intersection with the mineralized north-east structure 
for at least 1200 m. The mineralisation is associated with hydrothermal 
breccias, quartz veins and veinlets hosted in altered andesite volcanics. The 
results from all trenches demonstrate that the high grade gold intervals are 
contained within a wider halo of enhanced gold content.

Zeleznik

The Zeleznik license covers 6,026 hectares (60 sq.km.) and is located at the 
northern part of the Timok Magmatic Complex. The southern portion of this 
license is along strike and shares the same geological and structural setting 
as its neighbor, the Majdanpek Copper-Gold porphyry mine, which has a reported 
resource of 1000 mt @ 0.4-0.8% Cu, 0.25-1 g/t Au (Jelenkovic, 2007).

Mundoro recently completed the stream sediment sampling program on this license 
and identified five anomalous areas. The Company followed up the anomalies with 
prospecting, geological mapping, soil and rock geochemical sampling. There were 
708 soil samples collected with promising anomalies followed up in further 
detail. The results highlighted two areas with significant Cu-Au-Mo anomalies. 
They are located at the southern part of the license, defined by 20-189 ppb 
gold and 130-2260 parts per million (ppm) copper (Figure 3 - Zeleznik 
Copper-in-Soil Results, Figure 4 - Zeleznik Gold-in-Soil Results). Both 
anomalies are centered on andesite porphyry intrusions.

The best copper geochemistry of the western anomaly was obtained within a 
covered area. A small exposure of copper-bearing magnetite skarn and more 
widespread marbleized limestone characterize part of the eastern anomaly. The 
Copper-Gold-Molybdenum geochemical anomalies defined are typical of copper-gold 
porphyry systems and as such is a positive result to be follow up with further 
work to determine the source of the anomalies. Follow-up exploration work in 
2014 will consist of mapping, trenching, ground magnetic surveys and drill 
testing the anomalies in H2-2014.

Sumrakovac

The Sumrakovac License covers 103 sq.km in the southern portion of the Timok 
Magmatic Complex. The property contains a cluster of underexplored gold-copper 
porphyry style mineralization. The Company has completed stream sediment 
screening, a partial reconnaissance mapping as well as rock and soil 
geochemical sampling.

A ground magnetic survey is underway over the Skorusa porphyry and the adjacent 
area.

Reconnaissance mapping at the Skorusa porphyry revealed the existence of three 
dioritic intrusive phases: early, inter-mineral and late-mineral. The early and 
inter-mineral phases are both potassic altered, contain approx. 5 volume % of 
magnetite and are cut by chalcopyrite-bearing A-type quartz veinlets. Veinlet 
intensity and observed chalcopyrite contents are higher in the early mineral 
phase. Rock sampling of the quartz veining returned:

/T/

--  23m @ 0.72 g/t Au and 1670 ppm Cu (1.03 g/t AuEq); including single 2 m
samples with up to 1.64 g/t Au and 0.3% Cu (2.20 g/t AuEq).

/T/

Soil surveys confirmed a Copper-Gold-Molybdenum geochemical anomaly related to 
the outcropping porphyry mineralisation and delineated a 700 m by 400 m 
copper-gold anomalous area which needs to be followed up by trenching and 
drilling. The molybdenum anomaly covers an area of 1500 m by 600 m and is open 
to the north. The soil survey also highlighted additional anomalous centers to 
the east of Skorusa porphyry which will require further in-fill sampling and 
trenching (Figure 5 - Sumrakovac Copper-in-Soil Results, Figure 6 - Sumrakovac 
Gold-in-Soil Results, Figure 7 - Sumrakovac Molybdenum-in-Soil Results).

Sampling and Analysis

All trench intercepts were obtained from continuous channel sampling at 2 m 
intervals. All samples are assayed using 50 gram fire assay with atomic 
absorption finish by ALS Bor, Serbia. Quality Assurance and quality control 
procedures include the systematic insertion of standards and duplicates into 
the sample streams. Field duplicate samples are taken every 25 samples and 
standards and blanks are inserted after every 20th sample. All data collected 
in the field and assay results from the laboratories are routinely verified and 
entered in an Access data base.

Soil samples were collected from "B" horizon of the soil media by hand digging 
a hole from 0.1 to 0.5m. Material of approx. 500 grams was collected, sealed 
and send directly to the ALS laboratory in Bor. Samples were dried at less than 
60 degrees C/140F, sieve sample to -180 micron (80 mesh) and assayed using 30 
gram fire assay with atomic absorption finish.

Gold Equivalent ("AuEq.") is calculated using the formula AuEq = (g/t/Au) + 
(g/t/Ag) + ($/ozAu)/60. Metal prices used are: copper price of US$3.25/lb, gold 
price of US$1200/oz, silver price US$20/oz or 60 silver ounces per one gold 
ounce.

The technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., the Qualified Person as defined by 
National Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a well-funded, Canadian based, company focused on mineral 
acquisition, exploration, and development. Our primary focus is advancing our 
properties on the Tethyan Belt in Southeastern Europe. Mundoro has methodically 
acquired a district-scale land position on this prolific mineral belt which 
hosts significant Gold-Copper porphyry and related epithermal deposits. Our 
strong project pipeline, which also includes assets in Mexico and China, is 
positioned to drive long-term, sustainable growth in order to attain production 
and shareholder return.

Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into this News 
Release may contain forward-looking statements. All statements, other than 
statements of historical fact, included or incorporated by reference in this 
News Release are forward-looking statements, including, without limitation, 
statements regarding activities, events or developments that the Board expects 
or anticipates may occur in the future. These forward-looking statements can be 
identified by the use of forward-looking words such as "will", "expect", 
"intend", "plan", "estimate", "anticipate", "believe" or "continue" or similar 
words or the negative thereof. The material assumptions that were applied in 
making the forward looking statements in this News Release include expectations 
as to the Company's future strategy and business plan and execution of the 
Company's existing plans. There can be no assurance that the plans, intentions 
or expectations upon which these forward-looking statements are based will 
occur. We caution readers of this News Release not to place undue reliance on 
forward looking statements contained in this News Release, which are not a 
guarantee of performance and are subject to a number of uncertainties and other 
factors that could cause actual results to differ materially from those 
expressed or implied by such forward-looking statements. These factors include 
general economic and market conditions, changes in law, regulatory processes, 
the status of Mundoro's assets and financial condition, actions of competitors 
and the ability to implement business strategies and pursue business 
opportunities. The forward-looking statements contained in this News Release 
are expressly qualified in their entirety by this cautionary statement. The 
forward-looking statements included in this News Release are made as of the 
date of this News Release and the Board undertakes no obligation to publicly 
update such forward-looking statements to reflect new information, subsequent 
events or otherwise, except as required by law. Shareholders are cautioned that 
all forward-looking statements involve risks and uncertainties and for a more 
detailed discussion of such risks and other factors that could cause actual 
results to differ materially from those expressed or implied by such 
forward-looking statements, refer to the Company's filings with the Canadian 
securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO, President and Director
+1-604-669-8055

or

Roth Investor Relations
Michelle Roth
+1-732-792-2200
www.mundoro.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=462278115