Source	MARKET NEWS
Date	01/21/2014
Time	06:02:10 AM

Company	 Brazil Resources Inc.
Title	NI 43 101 
Resource Estimates for its Recently Ac





    CDNX Symbol: BRI











Press Release	





BRAZIL RESOURCES INC ("BRI-V;BRIZF-0")
- NI 43-101 Resource Estimates for its Recently Acquired
- Sao Jorge, Boa Vista and Surubim Gold Projects

Brazil Resources Inc. (the "Company" or "Brazil Resources") is
pleased to announce that it has received National Instrument 43-101
("NI 43-101") resource estimates for each of its Sao Jorge, Boa Vista
and Surubim Gold Projects located in Para State, Brazil. The projects
were acquired by Brazil Resources through its acquisition of Brazilian
Gold Corporation ("BGC") in November 2013. The resource estimates
confirm the historical estimates completed by BGC as disclosed by the
Company in its press release dated November 22, 2013.

Sao Jorge Gold Project

Brazil Resources engaged Coffey Mining Pty Ltd. ("Coffey") to
prepare an NI 43-101 resource estimate on the Sao Jorge Project (the
"Sao Jorge Estimate"). The Sao Jorge Estimate has an effective date of
November 22, 2013 and provides the following estimates for the project
(oxide and primary mineralization) at various cut-off grades (the oxide
resource comprises a small part (approximately 9%) of the overall
resource):

//st
Sao Jorge Gold Project
Mineral Resource Estimates Summary
Lower     Million   Average   Contained
Cutoff    Tonnes    Grade     Gold
Grade               (g/t Au)  (Kozs)
(g/t Au)
Indicated Mineral Resource   0.3     14.42       1.54      715
0.4     12.15       1.77      690
0.5     10.49       1.97      666
Inferred Mineral Resource    0.3     28.19       1.14    1,035
0.4     22.43       1.35      971
0.5     18.78       1.52      918
//et

The Sao Jorge Estimate was based on a block model of the deposit.
Coffey classified the resource estimate as an indicated or inferred
mineral resource based upon the confidence of the input data,
geological interpretation and grade estimation. Indicated and Inferred
Mineral Resources are reported at a cut-off grade of 0.3 g/t Au, which
is estimated by Coffey based upon economic estimates, process recovery,
government taxes, other expenses and a gold price of US$1,300/oz. The
Sao Jorge Estimate is based on 37,154 m (145 holes) of diamond drilling
completed by previous operators, including 14,708 m (37 holes) of
diamond drilling completed by BGC since late 2010. Gold assays (19,590)
were composited at 1 m lengths and interpolated into the block model
using multiple indicator kriging. A three-dimensional solid model of
the sulphide and oxide mineralization was constructed to constrain the
resource estimate. The block model is comprised of individual blocks
measuring 5 m by 5 m by 5 m and grade is interpolated into these blocks
using multiple indicator kriging. The above estimates may not reconcile
due to rounding. No additional material exploration work has been
completed on the project by the Company.

The Sao Jorge Estimate was prepared for Brazil Resources by
Porfirio Rodriquesz, B.Sc. (Min Eng.), MAIG and Leonardo de Moraes
Soares, B.Sc (Geo), MAIG of Coffey, who are qualified persons as
defined under NI 43-101, are independent of the Company and have
reviewed and approved the disclosure regarding the Sao Jorge Estimate
above.

Boa Vista Gold Project

The Company has received an NI 43-101 resource estimate respecting
the VG1 deposit (Boa Vista Gold Project), located in Para State in
northern Brazil (the "Boa Vista Estimate"), with an effective date of
July 3, 2012. The following tables set out the Boa Vista Estimate
(oxide and primary mineralization) at various cut-off grades (the oxide
resource comprises a small part (approximately 1.3%) of the overall
resource):

//st
Boa Vista Gold Project - VG1 Deposit
Inferred Mineral Resource Estimates Summary

Au Cut-off   Tonnes ) Cut-off  Grade ) Cut-off  Contained Metal
(g/t)        (tonnes)          Au (g/t)         Au (ozs)
0.50         8,470,000         1.23             336,000
0.60         6,980,000         1.38             310,000
0.70         5,930,000         1.51             288,000
0.80         5,090,000         1.64             268,000
0.90         4,580,000         1.73             254,000
1.00         4,150,000         1.81             241,000

//et



The Boa Vista Estimate was based on shallow ((150m depth) and
limited drilling  (15 holes in 3,007m) and 14 trenches (2,299 m)
containing 3,399 assays. The  drill holes intersected a west-northwest
striking, steeply dipping mineralized  zone that is up to 85 m in
thickness and extends at least 150 m below surface  based on existing
drilling. The mineralized zone consists of quartz-pyrite  stockwork and
silicified zone(s) that are hosted within a foliated, mixed mafic
volcanic and intrusive unit at or adjacent to granite rocks. Gold
assays were  composited at 5 m lengths and interpolated into the block
model using ordinary  kriging. A three-dimensional solid model of the
primary and oxide mineralization  was constructed to constrain the
resource estimate. 12 of the 15 diamond drill holes and 6 of the 14
trenches penetrated these solids over a strike length of  500 m and
were used in the resource estimate. The block model is comprised of
individual blocks measuring 20 m by 20 m by 5 m with the long
dimensions of the  block orientated east-west and down dip. At the time
of the Boa Vista Estimate  no economic studies have been completed on
the project and, as a result, an  economic cut-off is unknown. No
additional material exploration work has been  completed on the project
by the Company.
The Boa Vista Estimate was prepared for Brazil Resources by Jim
Cuttle, B.Sc., P. Geo, Gary Giroux, MAsc., P. Eng. and Michael
Schmulian, Bsc (Hons), Msc, FAusIMM, who are qualified persons as
defined under NI 43-101, are independent of the Company and have
reviewed and approved the disclosure regarding the Boa Vista Estimate
above.
Surubim Gold Project (previously called Rio Novo project)
Brazil Resources has received an NI 43-101 resource estimate (the
"Surubim Estimate") respecting the Surubim Gold Project, located in
Para State in northern Brazil, with an effective date of April 15,
2012. The following table sets out the Surubim Estimate at various
cut-off grades:

//st
Surubim Gold Project - Jau Prospect
Inferred Mineral Resource Estimates Summary

Au Cut-off   Tonnes ) Cut-off  Grade ) Cut-off  Contained Metal
(g/t)        (tonnes)          Au (g/t)         Au (ozs)

0.30         19,440,000        0.81             503,000
0.40         15,230,000        0.93             456,000
0.50         11,960,000        1.06             409,000
0.60          9,520,000        1.20             336,000
0.70          7,750,000        1.32             329,000
0.80          6,660,000        1.42             303,000
0.90          5,790,000        1.50             279,000
1.00          4,880,000        1.60             252,000
1.10          3,910,000        1.74             219,000
1.20          3,080,000        1.90             188,000
1.30          2,510,000        2.05             165,000

//et

The Surubim Estimate was based on a total of 20 drill holes
containing 2,978 gold assays. Gold assays were composited at 2.5 m
lengths and interpolated into the block model using ordinary kriging. A
three dimensional solid model of the mineralization was constructed to
constrain the resource estimate. The block model is comprised of
individual blocks measuring 20 m by 20 m by 5 m with the long
dimensions of the block orientated east-west and north-south. No
economic studies have been completed on this property and, as a result,
the economic cut-off is unknown. A gold cut-off of 0.3 g/t was
highlighted in the estimate as a possible open pit cut-off. No
additional material exploration work has been completed on the project
by the Company.

The Surubim Estimate was prepared for Brazil Resources by Jim
Cuttle, P. Geo and Gary Giroux, P. Eng., who are qualified persons as
defined under NI 43-101, are independent of the Company and have
reviewed and approved the disclosure regarding the Surubim Estimate
above.

Technical reports respecting each of the above resource estimates
will be filed under the Company's profile on SEDAR in due course.
There is no new material scientific or technical information respecting
each of the above projects since the effective date of their respective
resource estimates.

About Brazil Resources Inc.

Brazil Resources is a public mineral exploration company with a
focus on the acquisition and development of projects in emerging
producing gold districts in Brazil, Paraguay and other parts of South
America. Currently, Brazil Resources is advancing its Cachoeira and Sao
Jorge Gold Projects located in the State of Para, northeastern Brazil.

Paulo Pereira, Brazil Resources' Vice President of Exploration has
reviewed and approved the technical information contained in this news
release. Mr. Pereira holds a Bachelor degree in Geology from
Universidade do Amazonas in Brazil, is a qualified person as defined in
NI 43-101 and is a member of the Association of Professional
Geoscientists of Ontario.

Cautionary Note

Investors are cautioned not to assume that any part or all of
mineral deposits in the "indicated" and "Inferred" categories will ever
be converted into mineral reserves with demonstrated economic viability
or that inferred mineral resources will be converted to the measured
and/or indicated categories through further drilling. In addition, the
estimation of inferred resources involves far greater uncertainty as to
their existence and economic viability than the estimation of other
categories of resources. Under Canadian rules, estimates of Inferred
Mineral Resources may not form the basis of feasibility or other
economic studies.

Forward Looking Statements

This document contains certain forward-looking statements that
reflect the current views and/or expectations of Brazil Resources with
respect to its business and future events. Forward-looking statements
are based on the then-current expectations, beliefs, assumptions,
estimates and forecasts about the business and the markets in which
Brazil Resources operates. Investors are cautioned that all
forward-looking statements involve risks and uncertainties, including:
the inherent risks involved in the exploration and development of
mineral properties, the uncertainties involved in interpreting drill
results and other exploration data, the uncertainties respecting
historical resource estimates, the potential for delays in exploration
or development activities, the geology, grade and continuity of mineral
deposits, the possibility that future exploration, development or
mining results will not be consistent with Brazil Resources'
expectations, accidents, equipment breakdowns, title and permitting
matters, labour disputes or other unanticipated difficulties with or
interruptions in operations, fluctuating metal prices, unanticipated
costs and expenses, uncertainties relating to the availability and
costs of financing needed in the future, commodity price fluctuations,
regulatory restrictions, including environmental regulatory
restrictions, or any failure to integrate acquired companies and
projects into the Company's existing business as planned. These risks,
as well as others, including those set forth in Brazil Resources'
filings with Canadian securities regulators, could cause actual results
and events to vary significantly. Accordingly, readers should not place
undue reliance on forward-looking statements and information. There can
be no assurance that forward-looking information, or the material
factors or assumptions used to develop such forward looking
information, will prove to be accurate. Brazil Resources does not
undertake any obligations to release publicly any revisions for
updating any voluntary forward-looking statements, except as required
by applicable securities law.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

TSX Venture closing price for BRI-V
Date: 2014/01/20
Closing Price: 0.68

TEL:  (855) 630-1001   Brazil Resources Inc.
Stephen Swatton, Chief Executive Officer
Patrick Obara, Chief Financial Officer
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1402000009TS11402000903-06001820140121