Source	MARKET NEWS
Date	01/12/2015
Time	06:23:24 AM

Company	 Mundoro Capital Inc.
Title	Extends 
Copper Mineralization with Drill Program





    CDNX Symbol: MUN











Press Release	





MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Extends Copper Mineralization with Drill Program at
- Zeleznik Property, Serbia

Mundoro Capital Inc. (www.mundoro.com) ("Mundoro" or the
"Company") is pleased to announce the drilling results from its 100%
owned Zeleznik license, located at the northern portion of the Timok
Magmatic Complex in northeastern Serbia.

The Zeleznik license covers 60km2 and is located 1.8km directly
north of, and adjacent to, the Majdanpek open pit copper-gold mining
operation (see Zeleznik Location Map) and 45km northwest of the Bor
Mine Complex.

Teo Dechev, CEO and President of Mundoro commented, "The Zeleznik
drill program has demonstrated that the previously defined surface
mineralization remains open at depth and along strike at both the West
Zone and East Zone targets.  At the East Zone, drilling returned a
number of high grade intersections such as 2.8m @ 2.98% CuEq in massive
sulphides from hole ZELDD05 and bottomed with 4.9m @ 1.40% CuEq in hole
ZELDD06. These initial drill results are encouraging as they confirm
the presence of a mineralized porphyry and related epithermal systems
with higher copper-gold grades.  The West Zone's long intersections
were in porphyry style copper-gold mineralization in all three
drillholes.  They contained higher grade zones such as 25.8m @ 0.43%
CuEq from hole ZELDD01.  The results are very promising as they
demonstrate the potential for discovery of new near surface copper-gold
mineralization with open pit minable grades."

Interpretation of Drill Results

This first pass drilling of the Zeleznik property is follow up to
the mapping, trench sampling, geophysics and soil geochemical work
completed throughout the year in 2014 (see May 1, 2014 and January 13,
2014 press releases).  Six inclined diamond drill holes totaling 1000m
were drilled to test the vertical extent of the previously defined
encouraging surface copper-gold mineralization at the West Zone (see
Zeleznik West Zone Drill Hole Location Map) and East Zone (see Zeleznik
East Zone Drill Hole Location Map) targets. Three drill holes were
drilled at each zone in order to test the down dip mineralization to
approximately 150m as well as gain additional information about the
geological and structural controls.

//st

Table 1: Summary of significant results from drill holes ZELDD01 to ZELDD06.



Drill Hole From   To   Interval
ID          (m)   (m)    (m)    Cu (%) Au (g/t) CuEq (%) AuEq (g/t)

ZELDD_01    0.0  230.3  230.3    0.16   0.025     0.17      0.30
Including  29.2   55.0   25.8    0.39   0.076     0.43      0.74
ZELDD_02    0.0  164.7  164.7    0.14   0.017     0.15      0.26
ZELDD_03    0.0  176.0  176.0    0.18   0.029     0.20      0.34
Including   2.0   32.0   30.0    0.23   0.037     0.25      0.43
Including 161.5  166.7    5.2    0.26   0.045     0.29      0.49
ZELDD_04   12.0  133.1  117.0    0.11    0.17     0.21      0.36
Including  33.0   39.0    6.0    0.48    0.46     0.75      1.28
Including  90.0   91.0    1.0    0.52    1.09     1.16      1.98
Including 100.0  101.0    1.0    0.74    1.22     1.45      2.49
ZELDD_05   24.5  105.7   81.2    0.22    0.23     0.35      0.61
Including  26.6   29.4    2.8     2.1     1.5     2.98      5.10
ZELDD_06    4.0   12.0    8.0    0.11    0.40     0.34      0.59
Including  77.0   77.6    0.6    0.35    0.63     0.72      1.23
Including 90.0  142.3   52.3    0.18    0.22     0.31      0.53
115.0  116.0    1.0    0.61    0.67     1.00      1.72
137.4  142.3    4.9    0.82    1.00     1.40      2.41
//et

Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+[(%Cu) x (22.0462) x ($/lbCu)]  [(1/31.1035) x ($/ozAu)].
Copper equivalent (CuEq%) is calculated using the formula CuEq = (%Cu)
+ [(g/t/AuEq) x (1/31.1035) x ($/ozAu)]  [(22.0462) x ($/lbCu)].
Metal prices used are: gold price of US$1200/oz, copper price of
US$3/lb. All thicknesses from intersections from drill holes are
down-hole drilled thicknesses or outcrop sample length thickness.

At the West Zone, Mundoro's geological team believes the
mineralized porphyry dykes and chalcopyrite bearing veins are surface
expressions of a mineralization source which remains to be defined in
future drilling programs.  The West Zone target mineralization is
related to diorite porphyry dikes intruded into the basement gneiss
unit. Quartz-diorite porphyry was intersected in drillhole ZELDD01 from
30.6m to 35.5m striking north-northeast (see Individual Drill Hole
Sections for ZELDD01, ZELDD02, ZELDD03). Mineralization related to it
consists of A-type and B-type quartz-chalcopyrite-pyrite veins hosted
in the porphyry and in the surrounding wall rock. It is associated with
k-feldspar veins and has well defined copper-gold-moly geochemical
signatures. The intersected quartz-diorite porphyry outcrops at surface
and was sampled in trench ZELCH001.  The outcropping porphyry is a
small portion of the overall copper-moly-gold in-soil and rock anomaly
which remains open in all directions and is a target for further drill
testing.

At the East Zone (see Cross Section of ZELDD04, ZELDD05 and
ZELDD06), regional stratigraphy, preserved limestone capping and
epithermal geochemical signature suggest little erosion and a
potentially preserved copper-gold mineralised system which needs
further exploration/drilling along strike and at depth.  The East Zone
target mineralization is related to andesite-diorite porphyry intruded
into a basement gneiss and limestone cap on top. A sub-vertical to east
dipping north-northeast striking fault is a major controlling
structure. The East Zone target is characterized with skarn
mineralization at the limestone-andesite contacts and massive sulphide
veins of high-sulphidation affinity which our geological team believes
is probably overprinted on, or related to, the porphyry. The skarn and
massive sulphides are bearing high grade copper-gold mineralization up
to 2.65% Cu and 7.57 g/t Au.

At the East Zone target, drillhole ZELDD05 intersected 2.8m @
2.11% Cu; 1.50 g/t Au which we believe is related to magnetite skarn
mineralisation from 26.6m to 29.4m while drillhole ZELDD06 ended in
mineralization of 4.9m @ 0.8% Cu; 1.00 g/t Au at a depth of 142.3 m.
Locally intersected high grade zinc values and
carbonate-pyrite-chalcopyrite stockwork veining suggest proximal
location to a mineralised porphyry center with related skarn and
massive sulphide high sulphidation mineralization.  This is similar to
the Majdanpek orebody which is currently being mined approximately
2000m to the south of this hole. The Majdanpek operation is reported to
be mining ore grading 0.30% Cu and 0.26 g/t Au.

Drill Hole Description Highlights

West Zone

ZELDD 01 (AZ 266; -60) starts in propylitic altered gneiss with
quartz-iron oxide-magnetite veinlets and disseminated copper oxides
(copper wad) up to 26.7m. From 26.7m to 29.2m the hole is cutting
diorite dike with quartz-chalcopyrite veinlets (B-type) and
disseminated chalcopyrite. After 1.4m of brecciated gneiss,
quartz-chalcopyrite veins and massive chalcopyrite the drillhole cuts
potassic altered quartz-diorite porphyry dike from 30.6m to 35.5m
containing quartz-chalcopyrite B-veins and stockwork veining. Up to 55
m the chalcopyrite veining is relatively intensive with an average
sulphide content of 5-10%. By the end of the drillhole (230.3m) several
quartz diorite and diorite porphyry dikes are intersected. B-type
quartz-chalcopyrite-pyrite veining continues to the end of the
drillhole (230.3m) with appearance of A-type quartz veining from 187.1m
and a decrease of sulphide content to 3-5%. The length of the drillhole
is anomalous in copper, gold and molybdenum with the best intersection
reporting 25.8m @ 0.43% CuEq or 0.74 g/t AuEq related to quartz-diorite
porphyry.

ZELDD 02 (AZ 266; -60) was drilled 100m north of ZELDD01.  The
main objective was to test the continuity of Cu mineralisation
encountered in ZELTR1 and ZELTR14 (Figure 2). The drillhole intersected
propylitic altered gneiss from top to bottom (164.7m) cut by two thin
diorite dikes at 55.35m and 131.8m. Week potassic alteration started
from 131.8m to the end of the hole. Quartz-pyrite-chalcopyrite vein and
disseminated mineralization and magnetite veining was encountered
throughout the whole drillhole. Average sulphide content varied from 1%
to 3%.

ZELDD 03 (AZ 86; -60) was drilled 140m south of ZELDD01 and
inclined to the east in order to test the continuity of Cu
mineralisation encountered in ZELCH004. The drillhole intersected
diorite dikes from 45.8m to 47.7m and from 82.6m to 90.5m in overall
propylitic altered gneiss lithology. Although vein and disseminated
chalcopyrite is present from the top to the bottom of the drillhole,
structural analysis showed that the surface mineralisation changes dip
direction at depth and the drillhole cut under it.

East Zone

ZELDD 04 (AZ 112; -60) intersected brecciated and faulted diorite
stock intruded into limestone. The diorite is propylitic altered and
contains quartz-carbonate-pyrite-chalcopyrite veinlets throughout as
well as pyrite-chalcopyrite veins. The higher copper-gold grades are
related to massive pyrite-chalcopyrite veins with anomalous arsenic and
zinc controlled by faults. The drillhole is characterized by higher
average gold content as reported in Table 1.

ZELDD 05 (AZ 115; -60) cut through propylitic altered diorite from
top to bottom (0-131.7m). The diorite contains
quartz-carbonate-pyrite-chalcopyrite veinlets throughout as well as
pyrite-chalcopyrite veins. The higher copper-gold grades are related to
magnetite-chalcopyrite-pyrite endo-skarn mineralisation and massive
sulphides with high arsenic and elevated zinc contents.

ZELDD 06 (AZ 297; -60) is the last drillhole of this first pass
exploration drilling program in the East Zone.  It tests for the
continuation of the encouraging copper-gold results at depth and seeks
to confirm the strike and dip of the mineralised possible feeder
structure controlling it. The drillhole intersected brecciated and
faulted diorite, propylitic altered, and containing
quartz-carbonate-pyrite-chalcopyrite veinlets at upper levels with an
increase of massive sulphides and copper-gold grades at depth as
reported in Table 1. The drillhole ended in brecciated fault zone
bearing massive and disseminated pyrite-chalcopyrite mineralization of
4.9m @ 0.8% Cu; 1.00 g/t Au.

Sampling, Analysis and Qualified Person

Drillhole orientations were surveyed at approximately 50 meters
intervals. Drill core was collected from drill sites by the Company's
geologists and processed and sampled at the Company's core shed
according to industry best practice standard procedures. Samples were
collected as half PQ or HQ core at two meters length intervals. Where
necessary the sampling lengths were adjusted to reflect the geological
boundaries.

All samples are assayed using 50 gram fire assay with atomic
absorption finish and ME-ICP61 by ALS Romania. The entire sample was
crushed to 2mm, then split off a 1 kg sample and pulverized the split
to better than 85% passing 75 microns. Quality Assurance and Quality
Control procedures include the systematic insertion of standards and
duplicates into the sample streams. Duplicate core samples are taken
every 25 samples and standards and blanks are inserted after every 20th
sample. All data collected from detailed logging and assay results from
the laboratories are routinely verified and entered in an Access data
base.

Technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., Qualified Person as
defined by National Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based company with the mandate to generate
value for its shareholders through the acquisition, exploration,
development and investment of mineral projects.  Mundoro has
methodically acquired and is now exploring a district-scale land
position on the prolific Tethyan mineral belt which hosts significant
Gold-Copper deposits. Our strong project pipeline in Serbia and
Bulgaria, as well as our mineral interest in the Maoling Gold Project
in China, is positioned to drive long-term growth to attain production
related and shareholder return.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference
into this News Release may contain forward-looking statements. All
statements, other than statements of historical fact, included or
incorporated by reference in this News Release are forward-looking
statements, including, without limitation, statements regarding
activities, events or developments that the Board expects or
anticipates may occur in the future. These forward-looking statements
can be identified by the use of forward-looking words such as "will",
"expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material
assumptions that were applied in making the forward looking statements
in this News Release include expectations as to the Company's future
strategy and business plan and execution of the Company's existing
plans. There can be no assurance that the plans, intentions or
expectations upon which these forward-looking statements are based will
occur. We caution readers of this News Release not to place undue
reliance on forward looking statements contained in this News Release,
which are not a guarantee of performance and are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, changes in law, regulatory processes, the status of
Mundoro's assets and financial condition, actions of competitors and
the ability to implement business strategies and pursue business
opportunities. The forward-looking statements contained in this News
Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release
are made as of the date of this News Release and the Board undertakes
no obligation to publicly update such forward-looking statements to
reflect new information, subsequent events or otherwise, except as
required by law. Shareholders are cautioned that all forward-looking
statements involve risks and uncertainties and for a more detaileddiscussion of 
such risks and other factors that could cause actual
results to differ materially from those expressed or implied by such
forward-looking statements, refer to the Company's filings with the
Canadian securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.


TEL:  +1-604-669-8055    Teo Dechev, CEO, President and Director of
Mundoro Capital Inc.
TSX Venture closing price for MUN-V
Date: 2015/01/09
Closing Price: 0.16

TEL:  +1-732-792-2200    Michelle Roth, Roth Investor Relations
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1501100016TS11501100900-06213620150112