Source	CANADA NEWSWIRE
Date	01/12/2015
Time	06:07:30 AM

Company	 Mundoro Capital Inc.
Title	Mundoro extends copper mineralization with drill program at Zeleznik
property, Serbia





    CDNX Symbol: MUN











Press Release	




" BC-Mundoro-Serbia   01-12 2199
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Mundoro extends copper mineralization with drill program at Zeleznik
property, Serbia@

VANCOUVER, Jan. 12, 2015 /CNW/ - Mundoro Capital Inc. (TSXV: MUN,
www.mundoro.com) ("Mundoro" or the "Company") is pleased to announce the
drilling results from its 100% owned Zeleznik license, located at the northern
portion of the Timok Magmatic Complex in northeastern Serbia.
The Zeleznik license covers 60km² and is located 1.8km directly north of,
and adjacent to, the Majdanpek open pit copper-gold mining operation (see
Zeleznik Location Map) and 45km northwest of the Bor Mine Complex.
Teo Dechev, CEO and President of Mundoro commented, "The Zeleznik drill
program has demonstrated that the previously defined surface mineralization
remains open at depth and along strike at both the West Zone and East Zone
targets. At the East Zone, drilling returned a number of high grade
intersections such as 2.8m (at) 2.98% CuEq in massive sulphides from hole 
ZELDD05
and bottomed with 4.9m (at) 1.40% CuEq in hole ZELDD06. These initial drill
results are encouraging as they confirm the presence of a mineralized porphyry
and related epithermal systems with higher copper-gold grades. The West Zone's
long intersections were in porphyry style copper-gold mineralization in all
three drillholes. They contained higher grade zones such as 25.8m (at) 0.43% 
CuEq
from hole ZELDD01. The results are very promising as they demonstrate the
potential for discovery of new near surface copper-gold mineralization with
open pit minable grades."
Interpretation of Drill Results
This first pass drilling of the Zeleznik property is follow up to the
mapping, trench sampling, geophysics and soil geochemical work completed
throughout the year in 2014 (see May 1, 2014 and January 13, 2014 press
releases). Six inclined diamond drill holes totaling 1000m were drilled to
test the vertical extent of the previously defined encouraging surface
copper-gold mineralization at the West Zone (see Zeleznik West Zone Drill Hole
Location Map) and East Zone (see Zeleznik East Zone Drill Hole Location Map)
targets. Three drill holes were drilled at each zone in order to test the down
dip mineralization to approximately 150m as well as gain additional
information about the geological and structural controls.
Table 1: Summary of significant results from drill holes ZELDD01 to
ZELDD06.
Drill Hole       From        To       Interval       Cu (%)       Au 
(g/t)       CuEq (%)      AuEq (g/t)

ID                (m)       (m)          (m)
---               ---       ---          ---

ZELDD_01                0.0     230.3          230.3         0.16          
0.025          0.17            0.30

Including
---------

29.2       55.0      25.8           0.39        0.076           0.43          
0.74
----       ----      ----           ----        -----           ----          
----

ZELDD_02                0.0     164.7          164.7         0.14          
0.017          0.15            0.26
--------                ---     -----          -----         ----          
-----          ----            ----

ZELDD_03                0.0     176.0          176.0         0.18          
0.029          0.20            0.34

including

including
---------

2.0        32.0      30.0           0.23        0.037           0.25          
0.43
---        ----      ----           ----        -----           ----          
----

161.5      166.7       5.2           0.26        0.045           0.29          
0.49
-----      -----       ---           ----        -----           ----          
----

ZELDD_04               12.0     133.1          117.0         0.11           
0.17          0.21            0.36

Including

Including

Including
---------

33.0       39.0       6.0           0.48         0.46           0.75          
1.28
----       ----       ---           ----         ----           ----          
----

90.0       91.0       1.0           0.52         1.09           1.16          
1.98
----       ----       ---           ----         ----           ----          
----

100.0      101.0       1.0           0.74         1.22           1.45          
2.49
-----      -----       ---           ----         ----           ----          
----

ZELDD_05               24.5     105.7           81.2         0.22           
0.23          0.35            0.61

Including
---------

26.6       29.4       2.8            2.1          1.5           2.98          
5.10
----       ----       ---            ---          ---           ----          
----

ZELDD_06                4.0      12.0            8.0         0.11           
0.40          0.34            0.59







Including

Including
---------

77.0       77.6       0.6           0.35         0.63           0.72          
1.23
----       ----       ---           ----         ----           ----          
----

90.0      142.3      52.3           0.18         0.22           0.31          
0.53
----      -----      ----           ----         ----           ----          
----

115.0      116.0       1.0           0.61         0.67           1.00          
1.72
-----      -----       ---           ----         ----           ----          
----

137.4      142.3       4.9           0.82         1.00           1.40          
2.41
-----      -----       ---           ----         ----           ----          
----
Gold Equivalent ("AuEq.") is calculated using the formula AuEq (equal sign)
(g/t/Au)+[(%Cu) x (22.0462) x ($/lbCu)] ÷ [(1/31.1035) x ($/ozAu)]. Copper
equivalent (CuEq%) is calculated using the formula CuEq (equal sign) (%Cu) + 
[(g/t/AuEq)
x (1/31.1035) x ($/ozAu)] ÷ [(22.0462) x ($/lbCu)]. Metal prices used are:
gold price of US$1200/oz, copper price of US$3/lb. All thicknesses from
intersections from drill holes are down-hole drilled thicknesses or outcrop
sample length thickness.
At the West Zone, Mundoro's geological team believes the mineralized
porphyry dykes and chalcopyrite bearing veins are surface expressions of a
mineralization source which remains to be defined in future drilling programs.
The West Zone target mineralization is related to diorite porphyry dikes
intruded into the basement gneiss unit. Quartz-diorite porphyry was
intersected in drillhole ZELDD01 from 30.6m to 35.5m striking north-northeast
(see Individual Drill Hole Sections for ZELDD01, ZELDD02, ZELDD03).
Mineralization related to it consists of A-type and B-type
quartz-chalcopyrite-pyrite veins hosted in the porphyry and in the surrounding
wall rock. It is associated with k-feldspar veins and has well defined
copper-gold-moly geochemical signatures. The intersected quartz-diorite
porphyry outcrops at surface and was sampled in trench ZELCH001. The
outcropping porphyry is a small portion of the overall copper-moly-gold
in-soil and rock anomaly which remains open in all directions and is a target
for further drill testing.
At the East Zone (see Cross Section of ZELDD04, ZELDD05 and ZELDD06),
regional stratigraphy, preserved limestone capping and epithermal geochemical
signature suggest little erosion and a potentially preserved copper-gold
mineralised system which needs further exploration/drilling along strike and
at depth. The East Zone target mineralization is related to andesite-diorite
porphyry intruded into a basement gneiss and limestone cap on top. A
sub-vertical to east dipping north-northeast striking fault is a major
controlling structure. The East Zone target is characterized with skarn
mineralization at the limestone-andesite contacts and massive sulphide veins
of high-sulphidation affinity which our geological team believes is probably
overprinted on, or related to, the porphyry. The skarn and massive sulphides
are bearing high grade copper-gold mineralization up to 2.65% Cu and 7.57 g/t
Au.
At the East Zone target, drillhole ZELDD05 intersected 2.8m (at) 2.11% Cu;
1.50 g/t Au which we believe is related to magnetite skarn mineralisation from
26.6m to 29.4m while drillhole ZELDD06 ended in mineralization of 4.9m (at) 0.8%
Cu; 1.00 g/t Au at a depth of 142.3 m. Locally intersected high grade zinc
values and carbonate-pyrite-chalcopyrite stockwork veining suggest proximal
location to a mineralised porphyry center with related skarn and massive
sulphide high sulphidation mineralization. This is similar to the Majdanpek
orebody which is currently being mined approximately 2000m to the south of
this hole. The Majdanpek operation is reported to be mining ore grading 0.30%
Cu and 0.26 g/t Au.
Drill Hole Description Highlights
West Zone
ZELDD 01 (AZ 266°; -60) starts in propylitic altered gneiss with
quartz-iron oxide-magnetite veinlets and disseminated copper oxides (copper
wad) up to 26.7m. From 26.7m to 29.2m the hole is cutting diorite dike with
quartz-chalcopyrite veinlets (B-type) and disseminated chalcopyrite. After
1.4m of brecciated gneiss, quartz-chalcopyrite veins and massive chalcopyrite
the drillhole cuts potassic altered quartz-diorite porphyry dike from 30.6m to
35.5m containing quartz-chalcopyrite B-veins and stockwork veining. Up to 55 m
the chalcopyrite veining is relatively intensive with an average sulphide
content of 5-10%. By the end of the drillhole (230.3m) several quartz diorite
and diorite porphyry dikes are intersected. B-type quartz-chalcopyrite-pyrite
veining continues to the end of the drillhole (230.3m) with appearance of
A-type quartz veining from 187.1m and a decrease of sulphide content to 3-5%.
The length of the drillhole is anomalous in copper, gold and molybdenum with
the best intersection reporting 25.8m (at) 0.43% CuEq or 0.74 g/t AuEq related 
to
quartz-diorite porphyry.
ZELDD 02 (AZ 266°; -60) was drilled 100m north of ZELDD01. The main
objective was to test the continuity of Cu mineralisation encountered in
ZELTR1 and ZELTR14 (Figure 2). The drillhole intersected propylitic altered
gneiss from top to bottom (164.7m) cut by two thin diorite dikes at 55.35m and
131.8m. Week potassic alteration started from 131.8m to the end of the hole.
Quartz-pyrite-chalcopyrite vein and disseminated mineralization and magnetite
veining was encountered throughout the whole drillhole. Average sulphide
content varied from 1% to 3%.
ZELDD 03 (AZ 86°; -60) was drilled 140m south of ZELDD01 and inclined to
the east in order to test the continuity of Cu mineralisation encountered in
ZELCH004. The drillhole intersected diorite dikes from 45.8m to 47.7m and from
82.6m to 90.5m in overall propylitic altered gneiss lithology. Although vein
and disseminated chalcopyrite is present from the top to the bottom of the
drillhole, structural analysis showed that the surface mineralisation changes
dip direction at depth and the drillhole cut under it.
East Zone
ZELDD 04 (AZ 112°; -60) intersected brecciated and faulted diorite stock
intruded into limestone. The diorite is propylitic altered and contains
quartz-carbonate-pyrite-chalcopyrite veinlets throughout as well as
pyrite-chalcopyrite veins. The higher copper-gold grades are related to
massive pyrite-chalcopyrite veins with anomalous arsenic and zinc controlled
by faults. The drillhole is characterized by higher average gold content as
reported in Table 1.
ZELDD 05 (AZ 115°; -60) cut through propylitic altered diorite from top
to bottom (0-131.7m). The diorite contains
quartz-carbonate-pyrite-chalcopyrite veinlets throughout as well as
pyrite-chalcopyrite veins. The higher copper-gold grades are related to
magnetite-chalcopyrite-pyrite endo-skarn mineralisation and massive sulphides
with high arsenic and elevated zinc contents.
ZELDD 06 (AZ 297°; -60) is the last drillhole of this first pass
exploration drilling program in the East Zone. It tests for the continuation
of the encouraging copper-gold results at depth and seeks to confirm the
strike and dip of the mineralised possible feeder structure controlling it.
The drillhole intersected brecciated and faulted diorite, propylitic altered,
and containing quartz-carbonate-pyrite-chalcopyrite veinlets at upper levels
with an increase of massive sulphides and copper-gold grades at depth as
reported in Table 1. The drillhole ended in brecciated fault zone bearing
massive and disseminated pyrite-chalcopyrite mineralization of 4.9m (at) 0.8% 
Cu;
1.00 g/t Au.
Sampling, Analysis and Qualified Person
Drillhole orientations were surveyed at approximately 50 meters
intervals. Drill core was collected from drill sites by the Company's
geologists and processed and sampled at the Company's core shed according to
industry best practice standard procedures. Samples were collected as half PQ
or HQ core at two meters length intervals. Where necessary the sampling
lengths were adjusted to reflect the geological boundaries.
All samples are assayed using 50 gram fire assay with atomic absorption
finish and ME-ICP61 by ALS Romania. The entire sample was crushed to 2mm, then
split off a 1 kg sample and pulverized the split to better than 85% passing 75
microns. Quality Assurance and Quality Control procedures include the
systematic insertion of standards and duplicates into the sample streams.
Duplicate core samples are taken every 25 samples and standards and blanks are
inserted after every 20th sample. All data collected from detailed logging and
assay results from the laboratories are routinely verified and entered in an
Access data base.
Technical information contained in this Press Release has been reviewed
and approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by
National Instrument 43-101.
On behalf of the Company,
Teo Dechev, Chief Executive Officer, President and Director
About Mundoro Capital Inc.
Mundoro is a Canadian based company with the mandate to generate value
for its shareholders through the acquisition, exploration, development and
investment of mineral projects. Mundoro has methodically acquired and is now
exploring a district-scale land position on the prolific Tethyan mineral belt
which hosts significant Gold-Copper deposits. Our strong project pipeline in
Serbia and Bulgaria, as well as our mineral interest in the Maoling Gold
Project in China, is positioned to drive long-term growth to attain production
related and shareholder return.
Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into thisNews 
Release may contain forward-looking statements. All statements, other
than statements of historical fact, included or incorporated by reference in
this News Release are forward-looking statements, including, without
limitation, statements regarding activities, events or developments that the
Board expects or anticipates may occur in the future. These forward-looking
statements can be identified by the use of forward-looking words such as
"will", "expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material assumptions
that were applied in making the forward looking statements in this News
Release include expectations as to the Company's future strategy and business
plan and execution of the Company's existing plans. There can be no assurance
that the plans, intentions or expectations upon which these forward-looking
statements are based will occur. We caution readers of this News Release not
to place undue reliance on forward looking statements contained in this News
Release, which are not a guarantee of performance and are subject to a number
of uncertainties and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-

" BC-Mundoro-Serbia   01-12 2199
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Mundoro extends copper mineralization with drill program at Zeleznik
property, Serbia@

VANCOUVER, Jan. 12, 2015 /CNW/ - Mundoro Capital Inc. (TSXV: MUN,
www.mundoro.com) ("Mundoro" or the "Company") is pleased to announce the
drilling results from its 100% owned Zeleznik license, located at the northern
portion of the Timok Magmatic Complex in northeastern Serbia.
The Zeleznik license covers 60km² and is located 1.8km directly north of,
and adjacent to, the Majdanpek open pit copper-gold mining operation (see
Zeleznik Location Map) and 45km northwest of the Bor Mine Complex.
Teo Dechev, CEO and President of Mundoro commented, "The Zeleznik drill
program has demonstrated that the previously defined surface mineralization
remains open at depth and along strike at both the West Zone and East Zone
targets. At the East Zone, drilling returned a number of high grade
intersections such as 2.8m (at) 2.98% CuEq in massive sulphides from hole 
ZELDD05
and bottomed with 4.9m (at) 1.40% CuEq in hole ZELDD06. These initial drill
results are encouraging as they confirm the presence of a mineralized porphyry
and related epithermal systems with higher copper-gold grades. The West Zone's
long intersections were in porphyry style copper-gold mineralization in all
three drillholes. They contained higher grade zones such as 25.8m (at) 0.43% 
CuEq
from hole ZELDD01. The results are very promising as they demonstrate the
potential for discovery of new near surface copper-gold mineralization with
open pit minable grades."
Interpretation of Drill Results
This first pass drilling of the Zeleznik property is follow up to the
mapping, trench sampling, geophysics and soil geochemical work completed
throughout the year in 2014 (see May 1, 2014 and January 13, 2014 press
releases). Six inclined diamond drill holes totaling 1000m were drilled to
test the vertical extent of the previously defined encouraging surface
copper-gold mineralization at the West Zone (see Zeleznik West Zone Drill Hole
Location Map) and East Zone (see Zeleznik East Zone Drill Hole Location Map)
targets. Three drill holes were drilled at each zone in order to test the down
dip mineralization to approximately 150m as well as gain additional
information about the geological and structural controls.
Table 1: Summary of significant results from drill holes ZELDD01 to
ZELDD06.
Drill Hole       From        To       Interval       Cu (%)       Au 
(g/t)       CuEq (%)      AuEq (g/t)

ID                (m)       (m)          (m)
---               ---       ---          ---

ZELDD_01                0.0     230.3          230.3         0.16          
0.025          0.17            0.30

Including
---------

29.2       55.0      25.8           0.39        0.076           0.43          
0.74
----       ----      ----           ----        -----           ----          
----

ZELDD_02                0.0     164.7          164.7         0.14          
0.017          0.15            0.26
--------                ---     -----          -----         ----          
-----          ----            ----

ZELDD_03                0.0     176.0          176.0         0.18          
0.029          0.20            0.34

including

including
---------

2.0        32.0      30.0           0.23        0.037           0.25          
0.43
---        ----      ----           ----        -----           ----          
----

161.5      166.7       5.2           0.26        0.045           0.29          
0.49
-----      -----       ---           ----        -----           ----          
----

ZELDD_04               12.0     133.1          117.0         0.11           
0.17          0.21            0.36

Including

Including

Including
---------

33.0       39.0       6.0           0.48         0.46           0.75          
1.28
----       ----       ---           ----         ----           ----          
----

90.0       91.0       1.0           0.52         1.09           1.16          
1.98
----       ----       ---           ----         ----           ----          
----

100.0      101.0       1.0           0.74         1.22           1.45          
2.49
-----      -----       ---           ----         ----           ----          
----

ZELDD_05               24.5     105.7           81.2         0.22           
0.23          0.35            0.61

Including
---------

26.6       29.4       2.8            2.1          1.5           2.98          
5.10
----       ----       ---            ---          ---           ----          
----

ZELDD_06                4.0      12.0            8.0         0.11           
0.40          0.34            0.59







Including

Including
---------

77.0       77.6       0.6           0.35         0.63           0.72          
1.23
----       ----       ---           ----         ----           ----          
----

90.0      142.3      52.3           0.18         0.22           0.31          
0.53
----      -----      ----           ----         ----           ----          
----

115.0      116.0       1.0           0.61         0.67           1.00          
1.72
-----      -----       ---           ----         ----           ----          
----

137.4      142.3       4.9           0.82         1.00           1.40          
2.41
-----      -----       ---           ----         ----           ----          
----
Gold Equivalent ("AuEq.") is calculated using the formula AuEq (equal sign)
(g/t/Au)+[(%Cu) x (22.0462) x ($/lbCu)] ÷ [(1/31.1035) x ($/ozAu)]. Copper
equivalent (CuEq%) is calculated using the formula CuEq (equal sign) (%Cu) + 
[(g/t/AuEq)
x (1/31.1035) x ($/ozAu)] ÷ [(22.0462) x ($/lbCu)]. Metal prices used are:
gold price of US$1200/oz, copper price of US$3/lb. All thicknesses from
intersections from drill holes are down-hole drilled thicknesses or outcrop
sample length thickness.
At the West Zone, Mundoro's geological team believes the mineralized
porphyry dykes and chalcopyrite bearing veins are surface expressions of a
mineralization source which remains to be defined in future drilling programs.
The West Zone target mineralization is related to diorite porphyry dikes
intruded into the basement gneiss unit. Quartz-diorite porphyry was
intersected in drillhole ZELDD01 from 30.6m to 35.5m striking north-northeast
(see Individual Drill Hole Sections for ZELDD01, ZELDD02, ZELDD03).
Mineralization related to it consists of A-type and B-type
quartz-chalcopyrite-pyrite veins hosted in the porphyry and in the surrounding
wall rock. It is associated with k-feldspar veins and has well defined
copper-gold-moly geochemical signatures. The intersected quartz-diorite
porphyry outcrops at surface and was sampled in trench ZELCH001. The
outcropping porphyry is a small portion of the overall copper-moly-gold
in-soil and rock anomaly which remains open in all directions and is a target
for further drill testing.
At the East Zone (see Cross Section of ZELDD04, ZELDD05 and ZELDD06),
regional stratigraphy, preserved limestone capping and epithermal geochemical
signature suggest little erosion and a potentially preserved copper-gold
mineralised system which needs further exploration/drilling along strike and
at depth. The East Zone target mineralization is related to andesite-diorite
porphyry intruded into a basement gneiss and limestone cap on top. A
sub-vertical to east dipping north-northeast striking fault is a major
controlling structure. The East Zone target is characterized with skarn
mineralization at the limestone-andesite contacts and massive sulphide veins
of high-sulphidation affinity which our geological team believes is probably
overprinted on, or related to, the porphyry. The skarn and massive sulphides
are bearing high grade copper-gold mineralization up to 2.65% Cu and 7.57 g/t
Au.
At the East Zone target, drillhole ZELDD05 intersected 2.8m (at) 2.11% Cu;
1.50 g/t Au which we believe is related to magnetite skarn mineralisation from
26.6m to 29.4m while drillhole ZELDD06 ended in mineralization of 4.9m (at) 0.8%
Cu; 1.00 g/t Au at a depth of 142.3 m. Locally intersected high grade zinc
values and carbonate-pyrite-chalcopyrite stockwork veining suggest proximal
location to a mineralised porphyry center with related skarn and massive
sulphide high sulphidation mineralization. This is similar to the Majdanpek
orebody which is currently being mined approximately 2000m to the south of
this hole. The Majdanpek operation is reported to be mining ore grading 0.30%
Cu and 0.26 g/t Au.
Drill Hole Description Highlights
West Zone
ZELDD 01 (AZ 266°; -60) starts in propylitic altered gneiss with
quartz-iron oxide-magnetite veinlets and disseminated copper oxides (copper
wad) up to 26.7m. From 26.7m to 29.2m the hole is cutting diorite dike with
quartz-chalcopyrite veinlets (B-type) and disseminated chalcopyrite. After
1.4m of brecciated gneiss, quartz-chalcopyrite veins and massive chalcopyrite
the drillhole cuts potassic altered quartz-diorite porphyry dike from 30.6m to
35.5m containing quartz-chalcopyrite B-veins and stockwork veining. Up to 55 m
the chalcopyrite veining is relatively intensive with an average sulphide
content of 5-10%. By the end of the drillhole (230.3m) several quartz diorite
and diorite porphyry dikes are intersected. B-type quartz-chalcopyrite-pyrite
veining continues to the end of the drillhole (230.3m) with appearance of
A-type quartz veining from 187.1m and a decrease of sulphide content to 3-5%.
The length of the drillhole is anomalous in copper, gold and molybdenum with
the best intersection reporting 25.8m (at) 0.43% CuEq or 0.74 g/t AuEq related 
to
quartz-diorite porphyry.
ZELDD 02 (AZ 266°; -60) was drilled 100m north of ZELDD01. The main
objective was to test the continuity of Cu mineralisation encountered in
ZELTR1 and ZELTR14 (Figure 2). The drillhole intersected propylitic altered
gneiss from top to bottom (164.7m) cut by two thin diorite dikes at 55.35m and
131.8m. Week potassic alteration started from 131.8m to the end of the hole.
Quartz-pyrite-chalcopyrite vein and disseminated mineralization and magnetite
veining was encountered throughout the whole drillhole. Average sulphide
content varied from 1% to 3%.
ZELDD 03 (AZ 86°; -60) was drilled 140m south of ZELDD01 and inclined to
the east in order to test the continuity of Cu mineralisation encountered in
ZELCH004. The drillhole intersected diorite dikes from 45.8m to 47.7m and from
82.6m to 90.5m in overall propylitic altered gneiss lithology. Although vein
and disseminated chalcopyrite is present from the top to the bottom of the
drillhole, structural analysis showed that the surface mineralisation changes
dip direction at depth and the drillhole cut under it.
East Zone
ZELDD 04 (AZ 112°; -60) intersected brecciated and faulted diorite stock
intruded into limestone. The diorite is propylitic altered and contains
quartz-carbonate-pyrite-chalcopyrite veinlets throughout as well as
pyrite-chalcopyrite veins. The higher copper-gold grades are related to
massive pyrite-chalcopyrite veins with anomalous arsenic and zinc controlled
by faults. The drillhole is characterized by higher average gold content as
reported in Table 1.
ZELDD 05 (AZ 115°; -60) cut through propylitic altered diorite from top
to bottom (0-131.7m). The diorite contains
quartz-carbonate-pyrite-chalcopyrite veinlets throughout as well as
pyrite-chalcopyrite veins. The higher copper-gold grades are related to
magnetite-chalcopyrite-pyrite endo-skarn mineralisation and massive sulphides
with high arsenic and elevated zinc contents.
ZELDD 06 (AZ 297°; -60) is the last drillhole of this first pass
exploration drilling program in the East Zone. It tests for the continuation
of the encouraging copper-gold results at depth and seeks to confirm the
strike and dip of the mineralised possible feeder structure controlling it.
The drillhole intersected brecciated and faulted diorite, propylitic altered,
and containing quartz-carbonate-pyrite-chalcopyrite veinlets at upper levels
with an increase of massive sulphides and copper-gold grades at depth as
reported in Table 1. The drillhole ended in brecciated fault zone bearing
massive and disseminated pyrite-chalcopyrite mineralization of 4.9m (at) 0.8% 
Cu;
1.00 g/t Au.
Sampling, Analysis and Qualified Person
Drillhole orientations were surveyed at approximately 50 meters
intervals. Drill core was collected from drill sites by the Company's
geologists and processed and sampled at the Company's core shed according to
industry best practice standard procedures. Samples were collected as half PQ
or HQ core at two meters length intervals. Where necessary the sampling
lengths were adjusted to reflect the geological boundaries.
All samples are assayed using 50 gram fire assay with atomic absorption
finish and ME-ICP61 by ALS Romania. The entire sample was crushed to 2mm, then
split off a 1 kg sample and pulverized the split to better than 85% passing 75
microns. Quality Assurance and Quality Control procedures include the
systematic insertion of standards and duplicates into the sample streams.
Duplicate core samples are taken every 25 samples and standards and blanks are
inserted after every 20th sample. All data collected from detailed logging and
assay results from the laboratories are routinely verified and entered in an
Access data base.
Technical information contained in this Press Release has been reviewed
and approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by
National Instrument 43-101.
On behalf of the Company,
Teo Dechev, Chief Executive Officer, President and Director
About Mundoro Capital Inc.
Mundoro is a Canadian based company with the mandate to generate value
for its shareholders through the acquisition, exploration, development and
investment of mineral projects. Mundoro has methodically acquired and is now
exploring a district-scale land position on the prolific Tethyan mineral belt
which hosts significant Gold-Copper deposits. Our strong project pipeline in
Serbia and Bulgaria, as well as our mineral interest in the Maoling Gold
Project in China, is positioned to drive long-term growth to attain production
related and shareholder return.
Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into thisNews 
Release may contain forward-looking statements. All statements, other
than statements of historical fact, included or incorporated by reference in
this News Release are forward-looking statements, including, without
limitation, statements regarding activities, events or developments that the
Board expects or anticipates may occur in the future. These forward-looking
statements can be identified by the use of forward-looking words such as
"will", "expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material assumptions
that were applied in making the forward looking statements in this News
Release include expectations as to the Company's future strategy and business
plan and execution of the Company's existing plans. There can be no assurance
that the plans, intentions or expectations upon which these forward-looking
statements are based will occur. We caution readers of this News Release not
to place undue reliance on forward looking statements contained in this News
Release, which are not a guarantee of performance and are subject to a number
of uncertainties and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking statements.
These factors include general economic and market conditions, changes in law,
regulatory processes, the status of Mundoro's assets and financial condition,
actions of competitors and the ability to implement business strategies and
pursue business opportunities. The forward-looking statements contained in
this News Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release are
made as of the date of this News Release and the Board undertakes no
obligation to publicly update such forward-looking statements to reflect new
information, subsequent events or otherwise, except as required by law.
Shareholders are cautioned that all forward-looking statements involve risks
and uncertainties and for a more detailed discussion of such risks and other
factors that could cause actual results to differ materially from those
expressed or implied by such forward-looking statements, refer to the
Company's filings with the Canadian securities regulators available on
www.sedar.com.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mundoro Capital Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/January2015/12/c6842.html

-0-                           01/12/2015
/For further information: please contact Teo Dechev, CEO, President and
Director of Mundoro Capital Inc. at +1-604-669-8055 or Michelle Roth, Roth
Investor Relations at +1-732-792-2200/
/Web Site: http://www.mundoro.com /
(MUN.)

CO:  Mundoro Capital Inc.
ST:  British Columbia
IN:  MNG
SU:

-30-