Source	MARKET NEWS
Date	01/12/2015
Time	01:12:15 PM

Company	 Magnum Goldcorp Inc.
Title	2014 Drill 
Program Confirms Encouraging Gold Bea





    CDNX Symbol: MGI











Press Release	





INTERNATIONAL BETHLEHEM MINING CORP. ("IBC-V")
MAGNUM GOLDCORP INC. ("MGI-V)
- 2014 Drill Program Confirms Encouraging Gold-Bearing System at
- LH Property near Silverton, BC

International Bethlehem Mining Corp. (the "Company" or
"International Bethlehem") is pleased to announce that its
optionee/partner, Magnum Goldcorp Inc. has today reported its assay
results from Magnum's helicopter-supported drill program recently
completed by it on its optioned gold exploration property (the "LH
Property"). The LH Property consists of 19 contiguous crown granted
claims and six mineral claims, located approximately 7 km south of
Silverton, British Columbia, on the east side of Slocan Lake. Access to
the LH Property is via Highway 6 for 8 km south of Silverton and then
via Red Mountain Road for 2 km and a four-wheel drive road along
Fingland Creek for 5 km.

As part of its 2014 exploration program, Magnum reported that it
had completed 4 helicopter supported drill holes at 2 separate
locations for a total of 707 metres (see Magnum's News Releases dated
Aug. 26 and Sept. 12, 2014).  According to Magnum, the program
successfully tested magnetic anomalies identified from a ground
geophysical survey completed in June/July 2014.  Coincident
Self-Potential ("SP") and Induced Potential ("IP") anomalies are
associated with the magnetic trend.

A review of previous exploration results, particularly those from
the 2012 drill program completed by International Bethlehem, have been
interpreted by Magnum to suggest that moderately to strongly anomalous
gold values are associated with intervals having strong pyrrhotite
mineralization.  Pyrrhotite, being both magnetic and strongly
conductive, is interpreted to be a probable causative source for
coincident SP / IP / magnetic anomalies.  Therefore, the anomalies may
indicate elevated pyrrhotite content, with potentially elevated gold
values. As indicated by Magnum, the objective of the drill program was
to test for anomalous to elevated gold associated with the prominent
magnetic trend, at locations associated with anomalous SP and IP
responses.

Magnum reported that the first pad, from which drill holes LH14-26
and 27 were drilled, was located at the southern end of a linear trend
of magnetic anomalies, coincident with both SP and IP anomalies
identified previously (see Magnum's News Release dated Sept. 12, 2014).
The pad was located on the western margin of the magnetic trend, with
the two holes drilled to the east-southeast and east, respectively.
The second pad was located approximately 280 m southeast and 80 m
higher than pad 1, on the southeast margin of the magnetic trend.
Drill holes LH14-28 and 29 were drilled to the west and northwest,
respectively.



Magnum's analytical results for the 2014 drill holes are presented
in the following table:



//st

Hole Number   From(m)    To(m)  Width(m)    Gold (Au) (g/tonne)
LH-14-26       3.50      94.03     90.53        0.30
including      5.49      27.65     22.16        0.57
including     13.50      14.50      1.00        1.11
including     18.50      19.53      1.03        1.75
including     25.50      26.50      1.00        1.47
including     27.03      27.31      0.92        5.26
and           53.52      65.61     12.09        0.55
including     61.98      63.00      1.02        2.77
and          133.00     139.96      6.96        1.81
including    133.00     134.00      1.00       11.40
and          145.03     146.03      1.00        1.27
and          167.02     167.15      0.13        3.53
LH-14-27       4.00     117.00    113.00        0.28
including      9.31      18.50      9.19        0.980
including      9.31      10.00      0.69        1.19
including     12.50      13.53      1.03        1.31
including     13.53      14.53      1.00        3.94
and           29.56      30.54      0.98        1.98
and           67.92      71.00      3.08        1.91
including     67.92      69.00      1.08        1.23
including     69.00      70.00      1.00        3.79
LH-14-28      70.00      71.00      1.00        1.04
and           75.00      76.00      1.00        2.39
and          107.00     108.01      1.01        1.05
LH-14-29      43.00      66.00     23.00        0.19
and          161.00     209.36     48.36        0.18
including    186.00     189.00      3.00        0.41
and          192.00     195.13      3.13        0.36
and          204.00     208.00      4.00        0.39

//et
*True width not known at this time.



//st
Hole Number    Azimuth   Inclination      Depth (metres)
LH-14-26      106.5     -50             207
LH-14-27       95.5     -50             167
LH-14-28      271.5     -45             124
LH-14-29      344.5     -44             209

//et



Property Geology of the Area

The host rock underlying the property comprise volcanic -
volcaniclastic to sedimentary strata correlated to the Rossland and
Slocan Groups, respectively.  These strata are interpreted to represent
a roof pendant suspended within, and enclosed by, intrusive lithologies
corrected to the Nelson Batholith.

There is a history of exploration in the Property area, with
underground development of the former "LH mine".  Mineralization in the
workings has been described as a zone 6.1 to 13.7 metres wide, striking
nearly east-west and dipping north at about 55 degrees. According to
the BC MINFILE database, mineralization is hosted in quartz lenses and
veins 30 to 60 centimetres wide and consists of disseminated native
gold, arsenopyrite, pyrite and pyrrhotite with minor chalcopyrite and
native arsenic.

Previous exploration programs between 1986 - 1988 identified
surface geochemical anomalies and subsequent drilling documented
gold-bearing intercepts. A drill program completed by International
Bethlehem in 2012 comprised a single hole (LH-12-25), drilled to a
depth of 246 metres. Significant results are presented in the following
table:

//st

Hole Number      From (m)   To (m)   Width (m)  Gold (Au) (g/tonne)
LH-12-25         37.00      38.00    1.00       14.700
53.00      92.00   39.00        0.437
including        59.00      65.00    6.00        0.616
including        63.58      64.00    0.42        2.501
and              81.86      90.00    8.14        0.903
including        83.37      86.50    3.13        1.432
and              99.00     124.00   25.00        0.152
145.04     163.00   17.96        0.466
including       149.00     154.00    5.00        1.277
including       153.23     154.00    0.77        2.555

*True width not known at this time.

//et

Drill hole LH12-25 was drilled in the "Ridge Zone" at the southern
margin of the magnetic trend subsequently identified by the 2014 ground
geophysical survey.  The geology and associated alteration in the Ridge
Zone was mapped for a distance of at least 450 metres north of drill
hole LH12-25.  Alteration consists of strong silicification and
calc-silicate alteration of host rocks correlated to the Rossland
Group.  The zone of alteration, as mapped, trends due north, while the
magnetic anomaly trends obliquely to the northeast.  The magnetic
anomaly defined associated with the Ridge Zone is very strong,
decreasing to the north-northeast where drill holes LH14-26 to 29 were
drilled.

As reported by Magnum, the objective of the 2014 drill program was
to test the interpretation of an association between magnetic anomalies
and the presence of pyrrhotite and, more importantly, associated gold.
The program is considered by Magnum to have been successful, with
approximately 37.6% of the core returning gold values in excess of 0.1
gm/tonne and a further 5.5% returned gold values in excess of 0.5
gm/tonne.



According to Magnum, the results are interpreted to indicate a
strong gold-bearing system associated with widespread silicification
and calc-silicate alteration.  Furthermore, increased pyrrhotite
content, qualitatively based on visual estimates at this time, is
associated with increased gold content.

In addition, narrow intercepts of relatively high-grade gold
(greater than 1 gm/tonne) may be indicative of high grade veins similar
to those reported from the underground workings of the LH Mine.
Therefore, Magnum believes that there may be two gold-bearing targets
requiring further evaluation: (1) gold associated with pyrrhotite and
skarn-style alteration, and (2) gold-bearing quartz veins.

Magnum's successful 2014 program utilized the existing road system
to minimize reliance on helicopter-use and reduce the cost of the
program. Subsequent drilling to test the stronger, more prominent
magnetic anomaly associated with the Ridge Zone, will necessitate
helicopter-supported drilling above the existing road network.

Based on its drilling and analytical results to date, Magnum
believes the results continue to confirm a potentially significant
gold-bearing skarn target associated with the Ridge Zone.

As indicated by Magnum, drill core was split, with one half sent
to AGAT Laboratories in Burnaby, BC for initial preparation. The
remaining core was returned to the core box, with the core for the 2012
and 2014 programs stored in Crescent Valley, BC.  The samples for
analysis were crushed to 75% passing 2 mm and a 250 gram subsample was
riffle split then pulverized to 85% passing 75 microns. Each sample was
subjected to Aqua Regia digestion and analyzed by Inductively Coupled
Plasma - Optical Emission Spectrometry ("ICP-OES").  Samples returning
gold values in excess of 0.5 ppm were re-analyzed using Fire Assay on a
30 gram sample with an Atomic Absorption Spectrometry ("AAS") finish.
Samples returning gold values in excess of 10 ppm were further analyzed
using Fire Assay on a 30 gram sample with a Gravimetric Finish.

This news release has been reviewed and approved by Rick Walker,
P. Geo., who is acting as the Company's Qualified Person for the LH
Property project, in accordance with regulations under NI 43-101.

By option agreement dated September 6, 2012, the Company granted
an option to Magnum to acquire a 51% interest in the LH Property (the
"Option"). Under the Option, Magnum has agreed to incur expenditures on
the LH Property totaling $500,000 ($250,000 by November 2014 and an
additional $250,000 by November 2015), with approximately $300,000
having been incurred by Magnum to date. As well, Magnum has agreed to
issue 3,000,000 shares to International Bethlehem (1,000,000 shares by
November 2014 (issued); an additional 1,000,000 shares by November
2015; and an additional 1,000,000 shares upon the LH Property receiving
a bankable feasibility report on or before 10 years after the option
has been earned in). The LH Property is subject to certain net smelter
return royalties (see Magnum's News Release dated September 21, 2012
for additional details and information regarding the Option and the LH
Property).



"Douglas L. Mason"

Douglas L. Mason, President and CEO

International Bethlehem Mining Corporation
TSX Venture closing price for MGI-V
Date: 2015/01/08
Closing Price: 0.03

TEL:  604-922 2030 Mr. Clive Shallow, Shareholder Communications
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1501100030TS11501101937-13110820150112