Source	Marketwire
Date	01/13/2015
Time	04:00:27 AM

Company	 SAMA RESOURCES INC./RESSOURCES SAMA INC.
Title	Metallurgical Testing Yield's +99% Graphite Concentrate Purity at Sama's 
Lola Graphite Deposit in Guinea





    CDNX Symbol: SME











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Sama Resources Inc.

TSX VENTURE SYMBOL: SME

January 13, 2015

Metallurgical Testing Yield's +99% Graphite Concentrate Purity at Sama's Lola 
Graphite Deposit in Guinea


MONTREAL, QUEBEC--(Marketwired - Jan. 13, 2015) - Sama Resources 
Inc./Ressources Sama Inc. (TSX VENTURE:SME)  ("Sama" or the "Company") today 
announced that a second series of laboratory scale metallurgical tests once 
again corroborate the high potential of the Lola Graphite Project in Guinea, 
West Africa. Purification tests, using combined sulphuric and hydrofluoric 
("HF") acids, performed on graphite concentrate obtained through conventional 
flotation and gravity processing, increased the graphite content ("% Cg") of 
all flake categories to greater than 99%.

Highlights

/T/

--  Over 94% graphite recovery in the batch flotation tests
--  Over 99% purified concentrate grade across all flake categories
--  78% of the concentrate was in the jumbo and large flake categories
--  8.7 kilometer length of deposit

/T/

"We are very pleased with the results of these second metallurgical tests, 
which confirm the high value of the concentrate," stated Dr. Marc-Antoine 
Audet, P.Geo, President and Chief Executive Officer, Sama Resources. "These 
results speak to the enormous potential of the Lola Graphite Project, which 
covers an area of over 8.7 kilometers ("km") long by 300 meters ("m") wide at 
surface, potentially up to 1,000 mwide. Graphite flakes are free within the 
first 20 m or so of the deposit, it is well weathered or laterized, thereby 
allowing for easy grinding and optimal recovery of all large and jumbo flakes," 
added Dr. Audet.

As in the maiden metallurgical tests (reference Sama's press release dated July 
8, 2014), the graphite recovery was high with the second tests returning a 
global recovery of 94% of graphite, while producing a graphite concentrate 
comprising 78% of large and jumbo size flakes (reference: Table 1). 
Petrological investigations showed that muscovite and other silicate minerals 
remained attached to graphite flakes, hence affecting the purity of the 
flotation/gravity concentrate. Washing the graphite concentrate in a solution 
of sulphuric and hydrofluoric acids selectively leached and removed muscovite 
and silicate minerals returning jumbo, large, medium and small flake 
concentrates assaying 99.1% Cg, 99.2% Cg, 99.6% Cg and 100% Cg, respectively.

Furthermore, the concentrate in the maiden test was analyzed for a series of 
trace metals (reference Sama's press release dated July 8, 2014). As reported, 
it was found that the trace metal levels in the graphite concentrate were 
extremely low.

Table 1

All metallurgical tests were performed by the Thunder Bay laboratories of 
Activation Laboratories Ltd of Ancaster, Ontario, Canada on surface oxide 
material from the Lola graphite deposit. The second series of tests described 
here were performed on surface, graphite-rich oxide material, nominally 
representative of the first 20 m sub-surface of the deposit.

/T/

------------------------------------------------------------------
Maiden Test (July 2,2014)     Second Test (November 2014)
------------------------------------------------------------------
Head grade                11.5% Cg  Head grade            12.2% Cg
------------------------------------------------------------------
Recovery                       96%    Recovery                 94%
----------------------------------------------------------------------------
-4 Mesh Flash
Flotation,  Graphite
Grinding            100% - 35 Mesh    Grinding    -32 Mesh Regrind    purity
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Distribution,                   Distribution,
Flake Size                %   % Cg  Flake Size            %   % Cg      % Cg
----------------------------------------------------------------------------
+48 mesh                              +48 mesh
(jumbo)               29.2   92.9     (jumbo)         54.2   89.0      99.1
----------------------------------------------------------------------------
+80 mesh                              +80 mesh
(large)               30.8   90.0     (large)         23.8   83.0      99.2
----------------------------------------------------------------------------
+150 mesh              17.9   80.4   +150 mesh          7.7   78.7      99.6
----------------------------------------------------------------------------
-150 mesh              22.2   71.0   -150 mesh         14.3   67.9     100.0
----------------------------------------------------------------------------
Notes:
1. Tyler 4 mesh is 4.76 mm, 32 mesh is 0.5 mm and 35 mesh is 0.42 mm
2. Graphite purity is after acid washing

/T/

The samples for the two tests reflect the oxide layer of the Lola deposit. The 
sample for the maiden test, representing approximately 15% of the deposit, had 
a higher level of supergene silicate content. The sample for the second test, 
representing approximately 85% of the deposit, was a more friable material and 
was much lower in supergene silicate material.

The samples for the maiden and the second tests had similar head grades, 11.5% 
Cg and 12.2% Cg, respectively.

The Lola Graphite Project is 100% owned by Sama Resources Guinea SARL, a fully 
owned subsidiary of Sama Resources Inc. The Lola Graphite Project is located 
near the town of Lola in eastern Guinea and within 50 km of the border of Cote 
d'Ivoire.

Additional information regarding the Lola Graphite Project is available in 
Sama's updated presentation on the corporate website at www.samaresources.com 
or via the following link: 
http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

The technical information in this release has been reviewed and approved by Dr. 
Marc-Antoine Audet, P.Geo and President and CEO, Sama Resources and by Dr. 
Phillip Mackey, P.Eng., a metallurgical consultant, both acting as qualified 
persons as defined by NI 43-101 Standards of Disclosure for Mineral Projects.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements Certain of the statements made and information 
contained herein are "forward-looking statements" within the meaning of 
Canadian securities legislation or "forward-looking information" within the 
meaning of the Ontario Securities Act and the Securities Act (British 
Columbia).  This includes statements concerning the Company's plans at its 
mineral properties, which involve known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company, or industry results, to vary or be materially different from 
any future results, performance or achievements expressed or implied by such 
forward-looking statements or forward-looking information. Information 
regarding drilling results may also be deemed to be forward-looking statements 
or forward-looking information in that they reflect a prediction of what may be 
found to be present when and if a project is actually developed.

Forward-looking statements and forward-looking information are subject to a 
variety of risks and uncertainties which could cause actual events or results 
to differ from those reflected in the forward-looking statements or 
forward-looking information, including, without limitation, the availability of 
financing for activities, risks and uncertainties relating to the 
interpretation of drill results and the estimation of mineral resources and 
reserves, the geology, grade and continuity of mineral deposits, the 
possibility that future exploration, development or mining results will not be 
consistent with the Company's expectations, metal price fluctuations, 
environmental and regulatory requirements, availability of permits, escalating 
costs of remediation and mitigation, risk of title loss, the effects of 
accidents, equipment breakdowns, labour disputes or other unanticipated 
difficulties with or interruptions in exploration or development, the potential 
for delays in exploration or development activities, the inherent uncertainty 
of cost estimates and the potential for unexpected costs and expenses, 
commodity price fluctuations, currency fluctuations, expectations and beliefs 
of management and other risks and uncertainties.

In addition, forward-looking statements and forward-looking information are 
based on various assumptions. Should one or more of these risks and 
uncertainties materialize, or should underlying assumptions prove incorrect, 
actual results may vary materially from those described in forward-looking 
information or forward-looking statements. Accordingly, readers are advised not 
to place undue reliance on forward-looking statements or forward-looking 
information. Except as required under applicable securities legislation, the 
Company undertakes no obligation to publicly update or revise forward-looking 
statements or forward-looking information, whether as a result of new 
information, future events or otherwise.

- 30 -

CONTACT INFO:

Sama Resources Inc.
Dr. Marc-Antoine Audet
President and CEO
(514) 726-4158

or

Sama Resources Inc.
Mr. Matt Johnston
(604) 443-3835 or Toll Free: 1 (877) 792-6688, Ext. 4

INDUSTRY: Financial Services - Venture Capital, Manufacturing and Production - 
Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=513208141