Source	MARKET NEWS
Date	01/13/2015
Time	05:53:23 AM

Company	 Sama Resources Inc./Ressources Sama Inc.
Title	Metallurgical Testing Yield's +99% Graphite Conc





    CDNX Symbol: SME











Press Release	





Metallurgical Testing Yield's +99% Graphite Concentrate Purity AtSama's Lola 
Graphite Deposit In Guinea --->@NEWS RELEASE
SAMA RESOURCES INC ("SME-V;LNZCF-0")
- Metallurgical Testing Yield's +99% Graphite Concentrate
- Purity At Sama's Lola Graphite Deposit In Guinea

Sama Resources Inc./Ressources Sama Inc. ("Sama" or the "Company")
today announced that a second series of laboratory scale metallurgical
tests once again corroborate the high potential of the Lola Graphite
Project in Guinea, West Africa. Purification tests, using combined
sulphuric and hydrofluoric ("HF") acids, performed on graphite
concentrate obtained through conventional flotation and gravity
processing, increased the graphite content ("% Cg") of all flake
categories to greater than 99%.

Highlights

//st

Over 94% graphite recovery in the batch flotation tests

Over 99% purified concentrate grade across all flake categories

78% of the concentrate was in the jumbo and large flake categories

8.7 kilometer length of deposit

//et

"We are very pleased with the results of these second metallurgical
tests, which confirm the high value of the concentrate," stated Dr.
Marc-Antoine Audet, P.Geo, President and Chief Executive Officer, Sama
Resources. "These results speak to the enormous potential of the Lola
Graphite Project, which covers an area of over 8.7 kilometers ("km")
long by 300 meters ("m") wide at surface, potentially up to 1,000
mwide. Graphite flakes are free within the first 20 m or so of the
deposit, it is well weathered or laterized, thereby allowing for easy
grinding and optimal recovery of all large and jumbo flakes," added Dr.
Audet.

As in the maiden metallurgical tests (reference Sama's press
release dated July 8, 2014), the graphite recovery was high with the
second tests returning a global recovery of 94% of graphite, while
producing a graphite concentrate comprising 78% of large and jumbo size
flakes (reference: Table 1). Petrological investigations showed that
muscovite and other silicate minerals remained attached to graphite
flakes, hence affecting the purity of the flotation/gravity
concentrate. Washing the graphite concentrate in a solution of
sulphuric and hydrofluoric acids selectively leached and removed
muscovite and silicate minerals returning jumbo, large, medium and
small flake concentrates assaying 99.1% Cg, 99.2% Cg, 99.6% Cg and 100%
Cg, respectively.

Furthermore, the concentrate in the maiden test was analyzed for a
series of trace metals (reference Sama's press release dated July 8,
2014). As reported, it was found that the trace metal levels in the
graphite concentrate were extremely low.

Table 1

All metallurgical tests were performed by the Thunder Bay
laboratories of Activation Laboratories Ltd of Ancaster, Ontario,
Canada on surface oxide material from the Lola graphite deposit. The
second series of tests described here were performed on surface,
graphite-rich oxide material, nominally representative of the first 20
m sub-surface of the deposit.

//st
Maiden Test (July 2,2014)     Second Test (November 2014)
------------------------------------------------------------------
Head grade                11.5% Cg  Head grade            12.2% Cg
------------------------------------------------------------------
Recovery                       96%    Recovery                 94%
----------------------------------------------------------------------------
-4 Mesh Flash
Flotation, Graphite
Grinding            100% - 35 Mesh    Grinding    -32 Mesh Regrind   purity
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Distribution,                   Distribution,
Flake Size                %   % Cg  Flake Size            %   % Cg      % Cg
----------------------------------------------------------------------------
+48 mesh                              +48 mesh
(jumbo)               29.2   92.9     (jumbo)         54.2   89.0     99.1
----------------------------------------------------------------------------
+80 mesh                              +80 mesh
(large)               30.8   90.0     (large)         23.8   83.0     99.2
----------------------------------------------------------------------------
+150 mesh              17.9   80.4   +150 mesh          7.7   78.7     99.6
----------------------------------------------------------------------------
-150 mesh              22.2   71.0   -150 mesh         14.3   67.9    100.0
----------------------------------------------------------------------------
Notes:
1. Tyler 4 mesh is 4.76 mm, 32 mesh is 0.5 mm and 35 mesh is 0.42 mm
2. Graphite purity is after acid washing
//et

The samples for the two tests reflect the oxide layer of the Lola
deposit. The sample for the maiden test, representing approximately 15%
of the deposit, had a higher level of supergene silicate content. The
sample for the second test, representing approximately 85% of the
deposit, was a more friable material and was much lower in supergene
silicate material.

The samples for the maiden and the second tests had similar head
grades, 11.5% Cg and 12.2% Cg, respectively.

The Lola Graphite Project is 100% owned by Sama Resources Guinea
SARL, a fully owned subsidiary of Sama Resources Inc. The Lola Graphite
Project is located near the town of Lola in eastern Guinea and within
50 km of the border of Cote d'Ivoire.

Additional information regarding the Lola Graphite Project is
available in Sama's updated presentation on the corporate website at
www.samaresources.com or via the following link:
http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

The technical information in this release has been reviewed and
approved by Dr. Marc-Antoine Audet, P.Geo and President and CEO, Sama
Resources and by Dr. Phillip Mackey, P.Eng., a metallurgical
consultant, both acting as qualified persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-Looking Statements Certain of the statements made and
information contained herein are "forward-looking statements" within
the meaning of Canadian securities legislation or "forward-looking
information" within the meaning of the Ontario Securities Act and the
Securities Act (British Columbia).  This includes statements concerning
the Company's plans at its mineral properties, which involve known and
unknown risks, uncertainties and other factors which may cause the
actual results, performance or achievements of the Company, or industry
results, to vary or be materially different from any future results,
performance or achievements expressed or implied by such
forward-looking statements or forward-looking information. Information
regarding drilling results may also be deemed to be forward-looking
statements or forward-looking information in that they reflect a
prediction of what may be found to be present when and if a project is
actually developed.

Forward-looking statements and forward-looking information are
subject to a variety of risks and uncertainties which could cause
actual events or results to differ from those reflected in the
forward-looking statements or forward-looking information, including,
without limitation, the availability of financing for activities, risks
and uncertainties relating to the interpretation of drill results and
the estimation of mineral resources and reserves, the geology, grade
and continuity of mineral deposits, the possibility that future
exploration, development or mining results will not be consistent with
the Company's expectations, metal price fluctuations, environmental and
regulatory requirements, availability of permits, escalating costs of
remediation and mitigation, risk of title loss, the effects of
accidents, equipment breakdowns, labour disputes or other unanticipated
difficulties with or interruptions in exploration or development, the
potential for delays in exploration or development activities, the
inherent uncertainty of cost estimates and the potential for unexpected
costs and expenses, commodity price fluctuations, currency
fluctuations, expectations and beliefs of management and other risks
and uncertainties.

In addition, forward-looking statements and forward-looking
information are based on various assumptions. Should one or more of
these risks and uncertainties materialize, or should underlying
assumptions prove incorrect, actual results may vary materially from
those described in forward-looking information or forward-looking
statements. Accordingly, readers are advised not to place undue
reliance on forward-looking statements or forward-looking information.
Except as required under applicable securities legislation, the Company
undertakes no obligation to publicly update or revise forward-looking
statements or forward-looking information, whether as a result of new
information, future events or otherwise.



Sama Resources Inc.
Dr. Marc-Antoine Audet
President and CEO
TEL: (514) 726-4158

Sama Resources Inc.


















TSX Venture closing price for SME-V
Date: 2015/01/12
Closing Price: 0.26

TEL: (604) 443-3835
Toll Free: 1 (877) 792-6688, Ext. 4
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1501200011TS11501200739-05511220150113