Source	MARKET NEWS
Date	01/08/2015
Time	09:31:35 AM

Company	 Uragold Bay Resources Inc.
Title	Quebec Quartz Montpetit Quarry Assay Results, Va





    CDNX Symbol: UBR











Press Release	





Quebec Quartz Montpetit Quarry Assay Results, Validated as Suitablefor High 
Purity Ferrosilicon and High Purity Quartz Applications --->@NEWS RELEASE
URAGOLD BAY RESOURCES INC. ("UBR-V")
- Quebec Quartz Montpetit Quarry Assay Results, Validated
- as Suitable for High Purity Ferrosilicon  and High Purity
- Quartz Applications

Uragold Bay Resources Inc. ("Uragold") is pleased to announce
that it's wholly owned subsidiary, Quebec Quartz, has received assay
results for samples taken on the Montpetit Quarry quartz (silica)
property located in the Monteregie Region of Quebec, some 40 km south
of Montreal and 7 km south of Saint-Clotilde-de-Chateauguay

The corrected SiO2 average for 9 of the 10 samples assayed is
99.46 %, ranging from 99.16% to 99.67%. The corrected SiO2 average for
the 10 samples assayed is 99.13%, ranging from 96.21% to 99.67%. These
results validate the fact that a significant portion of the Quartz
material from the Montpetit Property would make suitable feedstock for
High Purity Ferrosilicon, and could be amenable to be beneficiated to
Silicon Metal purity requirement and even high purity quartz sands.

Patrick Levasseur, President and COO of Uragold stated, "We are
extremely happy with these results, just like our Roncevaux property,
it shows that the Montpetit Quarry has great potential." Mr. Levasseur
added, "2015 will be an exciting year as we continue to develop Quebec
Quartz's exciting high purity silica projects while developing two gold
mines in the Beauce region of Quebec."

IMPORTANCE OF QUARTZ (SILICA)

Quartz (SiO2) is one of the most abundant minerals. It occurs in
many different settings and in many different rock types. However, High
Purity Quartz deposits with low impurities are rare and only a few
deposits are suitable in volume, quality and amenability to be tailored
to refining methods for specialty high purity applications.

High Purity Quartz (HPQ), and Silicon Metal is used in large part
in the aluminum industry while Ultra High Purity Quartz (UHPQ) has
become one of today's key strategic minerals with applications in
high-tech industries that include semiconductors, LCD displays, fused
quartz tubing, microelectronics, solar silicon applications and
recently, Silicon Anode Lithium Batteries.

GO FORWARD PLAN:

The Corporation intends to advance the development of the
Montpetit project by completing the following steps during Q1 & Q2
2015:

1.Send material to specialized laboratories to find the best
beneficiation process to transform the Montpetit Quartz material into
Silicon Metal grade material and further test to see if the material
could be purified to the Ultra High Purity Quartz specifications needed
for advanced material and pharmaceutical applications.




High Purity Quartz beneficiated to 99.998% Si02 can command prices
up to
US$ 6,000/T (Source: Dorfner Anzaplan). The Corporation intends to
focus its interest on this segment of the market.

Run of mine quartz for usage as Ferrosilicon commands sale price
averages between US$ 50/T to US$100/T; while run of mine quartz for
Silicon Metal commands sale prices averaging between US$ 100/T to US$
250/T.

2.Evaluating the Property Potential.

The exact volume of the quartzite body found on the Montpetit
Property needs to be confirmed and measured. Furthermore, the grade
distribution needs to be better understood. Of significance will be
identifying, the controls that could explain the one-outlier result
found in the assay results.

PARTIAL TABLE OF RESULTS:

//st

-------------------------------------------------------------------
|Report         |       |       |        |       |       |        |
|Number:        |       |       |        |       |       |        |
|A14-09140      |       |       |        |       |       |        |
|-----------------------------------------------------------------|
|Analyte Symbol |SiO2   |Al2O3  |Fe2O3(T)|LOI    |Total  |SiO2    |
|-----------------------------------------------------------------|
|Unit Symbol    |%      |%      |%       |%      |%      |        |
|-----------------------------------------------------------------|
|Detection Limit|0.01   |0.01   |0.01    |       |0.01   |        |
|-----------------------------------------------------------------|
|Analysis Method|FUS-XRF|FUS-XRF|FUS-XRF |FUS-XRF|FUS-XRF|ADJUSTED|
|-----------------------------------------------------------------|
|41764          |99.75  |0.22   |0.05    |0.21   |100.40 |99.35%  |
|-----------------------------------------------------------------|
|41764-B        |98.96  |0.51   |0.03    |0.18   |99.80  |99.16%  |
|-----------------------------------------------------------------|
|41765          |98.21  |0.26   |0.04    |0.23   |98.86  |99.34%  |
|-----------------------------------------------------------------|
|41765-B        |99.40  |0.11   |0.03    |0.10   |99.71  |99.69%  |
|-----------------------------------------------------------------|
|41766          |96.51  |1.69   |0.32    |0.36   |100.30 |96.22%  |
|-----------------------------------------------------------------|
|41766-B        |98.44  |0.32   |0.03    |0.13   |99.02  |99.41%  |
|-----------------------------------------------------------------|
|41767          |100.01 |0.23   |0.03    |0.16   |100.50 |99.51%  |
|-----------------------------------------------------------------|
|41767-B        |99.39  |0.10   |0.02    |0.13   |99.71  |99.68%  |
|-----------------------------------------------------------------|
|41768          |99.81  |0.20   |0.03    |0.14   |100.30 |99.51%  |
|-----------------------------------------------------------------|
|41768-B        |100.06 |0.13   |0.04    |0.28   |100.60 |99.46%  |
|-----------------------------------------------------------------|
|Average        |99.05  |0.38   |0.06    |0.19   |99.92  |99.13%  |
-------------------------------------------------------------------

//et

The total exploration area of the Montpetit deposit is 2.42 Km2,
while the old quarry is 100 m long by 35 m large and is inside a
tabular quartzite. The deposit is composed of consolidated beach sand
that diagenesis has transformed into a quartzite. In order to have a
good sampling spread, 5 samples were taken at different zones of the
quartzite deposit. Each quartzite layer along the stratigraphy has been
sampled.

In 1956, 3,000 tons of quartzite averaging 99.27% SiO2 was mined
from the Montpetit Quarry and used to produce ferrosilicon @  (Source:
Resources Naturelles du Quebec, Sigeom 2014, Work Reports GM03695).

The material was first sent to the INRS (Institut National de la
Recherche Scientifique) laboratory in Quebec City to be prepared for
testing for Silica values. 10 prepared samples (an original and a
duplicate) were sent to the Activation Laboratories in Ancaster,
Ontario for whole rock and trace elements assay (FUS X-Ray Fluorescence
("XRF")).

The average losses in ignition ("LOI") (material and moisture
burned off during the assays) for the 10 samples is 0.19% (ranging
between 0.13% and 0.36%) this suggest that a certain percentage of the
alkali metals are present as a carbonate molecule, and with an average
laboratory total of 99.92% (ranging between 98.80 % and 100.6%), a
correction for the loss of carbonate is required in order to present
the actual SiO2 grade of the samples.

(img src='https://www.thenewswire.com/client_files/tnwKKfheR_.png'
/) @ https://www.thenewswire.com/client_files/tnwKKfheR.png
Click Image To View Full Size

Picture 1: Field sample from the Montpetit Property, Sample #
41767 tested 99.51% SIO2

(img src='https://www.thenewswire.com/client_files/tnwI73npI_.png'
/) @ https://www.thenewswire.com/client_files/tnwI73npI.png
Click Image To View Full Size

Picture 2: Quartzite outcrop at the Montpetit Property.

Mr. Vivian Stuart-Williams, SACNASPS, working under Special
Authorization #308 of the Quebec Order of Geologist, is an Independent
Qualified Person as defined by National Instrument 43-101 that
supervised the preparation of the information in this news release.

All the information on exploration potential herewithin presented
is historical in nature and while relevant, the information was
obtained before the implementation of National Instrument 43-101 and as
such does not meet National Instrument 43-101 reporting standards. The
historical estimate should not be relied upon until the Company can
confirm them.

About Quebec Quartz

Uragold 100 % wholly owned subsidiary, Quebec Quartz, by virtue of
being a first mover into this market, succeeded in becoming the largest
holder of distinct High Purity Quartz properties in Quebec. Quebec
Quartz strategic portfolio of High Purity Quartz (+99.+% SiO2) deposits
and closed silicon metal mines in Quebec represent a unique and
valuable asset. Quebec Quartz aims to become a leading supplier of
Ultra High Purity Quartz

About Uragold Bay Resources Inc.

Uragold Bay Resources is a TSX-V listed Gold and High Purity
Quartz exploration junior focused on generating free cash flow from
mining operations. Our business model is centered on developing mining
projects suited for smaller-scale start-up, (Capex ( C$10M), that will
generate high yield returns (IRR ) 50%). Uragold will reach these goals
by developing Quebec's first placer mine in 50 years, the Beauce Placer
Project developing and, in partnership with Golden Hope Mines, the
Bellechasse-Timmins Gold Deposit.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for UBR-V
Date: 2015/01/07
Closing Price: 0.05

TEL:  (514) 846-3271     Bernard J. Tourillon, Chairman and CEO
Patrick Levasseur, President and COO
Internet: www.uragold.com/Quebec-Quartz.php
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1500700019TS11500701372-09301420150108