Source	Marketwire
Date	01/08/2015
Time	10:13:06 AM

Company	 AMEX EXPLORATION INC.
Title	New Drill Hole Intercept Returns  4,55 g/t Au, 20,9 g/t Ag, 0,21% Cu and 
0,14% Zn Over 1,5 Meters at Amex's Perron Property, Abitibi





    CDNX Symbol: AMX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

January 8, 2015

New Drill Hole Intercept Returns  4,55 g/t Au, 20,9 g/t Ag, 0,21% Cu and 0,14% 
Zn Over 1,5 Meters at Amex's Perron Property, Abitibi


MONTREAL, QUEBEC--(Marketwired - Jan. 8, 2015) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex" or the "Corporation") is very pleased to announce that a 
new polymetallic gold-bearing structure has been identified during the second 
phase of drilling on Amex's Perron property executed in 2014 under the option 
agreement with Agnico Eagle Mines Ltd "Agnico Eagle" (TSX:AEM)(NYSE:AEM) (see 
press release of June 21, 2013 for details on the option agreement terms and 
conditions).

This new structure, that returned values of 4,55 g/t Au, 20,9 g/t Ag, 0,21% Cu 
and 0,14% Zn over 1,5 meters, is located at some 250 meters east and 100 meters 
deeper than Amex initial discovery hole PE-13-03 ( 3,84 g/t Au, 23.0 g/t Ag, 
0,10%Cu and 1,4% Zn over 15,2 m; see PR2013-03-04). Geologically speaking, it 
bears the same type of alteration and mineralization as recognized by Amex in 
its discovery hole PE-2013-03 that consists of semi massive sulfide stockwork 
hosted by a garnet bearing rhyolite volcanic unit. As for the mineralized 
structure in hole PE-2013-03, this new mineralization is interpreted as a 
synvolcanic feeder zone that is also oriented NE-SW, hence crosscutting at 
about a right angle to the general stratigraphic orientation of the volcanic 
sequences.

According to Amex's president and CEO Jacques Trottier, PhD, "The recognition 
of a second mineralized feeder zone, typically associated with gold-rich 
polymetallic VMS deposits, confirms that the Perron Property has the potential 
to become the host of more than one single deposit, but also a new mining 
district for this type of deposit. Obviously, we are still at a very early 
stage in the understanding of this district and a lot of additional exploration 
work, including an intensive drilling campaign, will be needed just to confirm 
the existence of a single mineralized body. But, in my opinion, all the good 
ingredients are already there!".

This information was contained in in the Agnico Eagle Report on the Perron 2014 
Exploration Program that was recently presented to Amex. During 2014, four 
holes totalling 2112 meters of drilling were completed on the property. The 
main objective of this relatively short drill campaign was to test the 
lithostratigraphic potential at the contact between two favourable horizons, 
namely the V1-V2 contact (for polymetallic VMS gold rich mineralization) and 
the 6a-7 Rhyolitic anomalous gold bearing horizon as described in PR2014-01-30. 
These four holes were drilled on a spacing of about 350 and 550 meters covering 
an east-west strike length of about 1, 2 km. Even though the distance between 
holes was significant, each hole did intersect gold mineralization with values 
up to 35,8 g/t Au, 9,1 g/t Ag and 0, 45% Zn over 0,7 meter (see Table 1 for 
more results).

Table 1: Results from 2014 drilling program.

/T/

----------------------------------------------------------------------------
Length       Au       Ag       Cu       Zn
Hole              From       to      (m)    (ppm)    (ppm)    (ppm)    (ppm)
----------------------------------------------------------------------------
163-14-004       603.5    609.0      5.5     0.51     0.73       11      282
----------------------------------------------------------------------------
incl.    603.5    604.0      0.5     2.26     4.00       28      167
----------------------------------------------------------------------------
and inlc.    608.0    609.0      1.0     1.25     0.50        7      126
----------------------------------------------------------------------------
660.6    662.1      1.5     4.55    20.93     2123     1444
----------------------------------------------------------------------------
incl.    660.6    661.1      0.5    11.35    58.20     5450      972
----------------------------------------------------------------------------
719.5    721.0      1.5     3.03   570.00        9       27
----------------------------------------------------------------------------
163-14-005       243.0    247.0      4.0     0.44     0.95      290       83
----------------------------------------------------------------------------
incl.    243.0    244.0      1.0     1.15     3.20      968      120
----------------------------------------------------------------------------
439.8    440.5      0.7    35.80     9.10       20     4470
----------------------------------------------------------------------------
163-14-006        31.0     41.0     10.0      0.3     0.25        5       38
----------------------------------------------------------------------------
93.7     96.7      3.0     0.41     0.10        9       16
----------------------------------------------------------------------------
163-14-007       143.5    152.5      9.0     0.12     0.10        2       10
----------------------------------------------------------------------------
202.0    203.3      1.3     1.38     0.50        7      189
----------------------------------------------------------------------------
284.5    291.5      7.0     0.12     0.26        7       55
----------------------------------------------------------------------------

/T/

Note: 4 drill holes totalling 2112 meters have been drilled in 2014. 
Geochemical analysis was executed by ALS Chemex Laboratories in Val d'Or under 
Agnico Eagle QA/QC program and supervision.

Besides this major highlight from this drilling campaign, it is also now 
interpreted that the high grade polymetallic gold-rich sulphide mineralization 
intersected by Amex in its discovery hole PE-2013-03 (see press release of 
March 4, 2013) is potentially located in close relationship with a synvolcanic 
fault that could be genetically related to the encountered alteration and 
mineralization. The identification of such an environment in hole PE-2013-03 is 
consistent with a typical gold-rich VMS (volcanogenic massive sulphide) deposit 
in the DBL (Dumagami-LaRonde-Bousquet) mining camp in the Quebec Abitibi 
greenstone Belt.

Jacques Trottier, PhD, President and CEO of Amex Exploration comments, "We are 
very pleased with Agnico Eagle's work done so far on our Perron Property. From 
their work and expertise, various gold target types have been identified and 
should be further tested in a follow-up exploration program still to be 
confirmed and announced. I look forward to seeing the exploration work resuming 
there as soon as possible in 2015."

Amex Exploration Inc. is a junior mining exploration company listed on the TSX 
Venture Exchange whose primary objective is to develop and bring into 
production viable gold and base metal deposits. Jacques Trottier, PhD Geol, 
Qualified Person as defined by Canadian N43-101 has approved the technical 
information reported in this news release.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Amex Exploration Inc.
Jacques Trottier
514-866-8209
Fax: 514-866-8096

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=512949058