Source	MARKET NEWS
Date	01/06/2016
Time	11:03:07 PM

Company	 Lomiko Metals Inc.
Title	Complete 
Drilling Program With Intercepts Of 28.





    CDNX Symbol: LMR











Press Release





CANADA STRATEGIC METALS INC ("CJC-V")
LOMIKO METALS INC ("LMR-V")
- Complete Drilling Program With Intercepts Of 28.50 M Of 16.53%,
- 30.95 M Of 8.18%, 46.25 M Of 5.43% And 47.15 M Of 4.42% Flake
- Graphite

Canada Strategic Metals Inc. ("Canada Strategic Metals" or "the
Company") and Lomiko Metals Inc. are very pleased to announce the
results for seven (7) exploration holes from the Refractory Zone at the
La Loutre Graphite Property. The recent drilling campaign on La Loutre
Graphite property has now been completed.

"High Grade material in a large, near surface mineralized system
such as La Loutre is a very positive indicator for the viability of a
future mining operation", stated A. Paul Gill, CEO Lomiko Metals Inc.

Results*

//st
Hole #   From (m)     To (m) Length* (m)   Gp %
LL-15-49  100.00     106.00        6.00    5.00
143.50     175.00       31.50    2.79
LL-15-50    2.20      48.45       46.25    5.43
including   5.80       9.75        3.95   17.95
including  42.70      46.95        4.25   15.56
LL-15-51    4.20      37.50       33.30   14.62
including   9.00      37.50       28.50   16.53
91.55     122.50       30.95    8.18
including  91.55      98.50        6.95   18.31
including 115.00     122.50        7.50    9.61
LL-15-52   64.65     111.80       47.15    4.42
including 109.00     111.80        2.80   17.28
LL-15-53     NSV
LL-15-54     NSV
LL-15-55    7.50      13.50        6.00    1.13
130.35     134.15        3.80    3.82
//et

* Length along the core. The Company doesn't have enough
information to estimates the true width of the mineralized zone
intersected in the drill holes
The La Loutre property consists of contiguous claim blocks
totalling approximately 2,867.29 hectares (28.67 km2) situated
approximately 53 km east of Imerys Carbon and Graphite, formerly known
as the Timcal Graphite Mine, North America's only operating graphite
mine, and 117 km northwest of Montreal. The property will now be
assessed for a resource. Viable near surface mineralization reduces the
amount of waste rock that needs to be moved, reducing overall cost of
the project and reducing environmental impact.

In addition, Lomiko hopes to define material )99.99% Graphite
Crystalline Flake to serve as the base material for testing graphite
for the ultrapure carbon market and for conversion to graphene and use
in 3D Printing and Supercapacitors.

A map of hole localisation and results is available on the web
site of the Company at: www.csmetals.ca and www.lomiko.com under the
Quicklinks tab.

The 2015 drilling program is managed by Consul-Teck Exploration of
Val-d'Or, Quebec, who designed the drilling campaign, supervised the
program and logged and sampled the core.

Consul-Teck Exploration implemented QA/QC procedures to ensure
best practices in sampling and analysis of the core samples. The drill
core was logged and then split, with one half sent for assay and the
other retained in the core box as a witness sample. Duplicates and
blanks were inserted regularly into the sample stream.

The samples in secure tagged bags were delivered directly to the
analytical facility for analysis. In this case, the analytical facility
was the ALS minerals in Val-d'Or, Quebec. The samples are weighed and
identified prior to sample preparation. The samples are crushed to 70%
minus 2 mm, then separated and pulverized to 85% passing 75 um. All
samples are analyzed for Carbon Graphite using C-IR18.

Jean-Sebastien Lavallee (OGQ #773), geologist, shareholder of both
companies, President and Chief Executive Officer of the Company and a
Qualified Person under NI 43-101, has reviewed and approved the
technical content of this release.

About Canada Strategic Metals

Canada Strategic Metals is an emerging company focused on the
exploration and development of a number of projects covering over
20,000 hectares in Quebec. With broad management experience in green
technology and junior resource exploration and development, Canada
Strategic Metals is well positioned to aggressively advance this
promising property portfolio for its shareholders.

For more information on the Company, please visit www.csmetals.ca.


Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 819-354-5146  Jean-Sebastien Lavallee, P. Geo
President and Chief Executive Officer
Canada Strategic Metals
TSX Venture closing price for LMR-V
Date: 2016/01/05
Closing Price: 0.04

TEL: 514-341-0408  Paradox Public Relations
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1600500020TS11600501307-08210420160106

[200/News Release]LMRVLOMIKO METALS INCJAN 06 2016  08:21 AMComplete 
Drilling Program With Intercepts Of 28.50 M Of 16.53%,30.95 M Of 8.18%, 46.25 
M Of 5.43% And 47.15 M Of 4.42% FlakeGraphite --->@NEWS RELEASE
CANADA STRATEGIC METALS INC ("CJC-V")
LOMIKO METALS INC ("LMR-V")
- Complete Drilling Program With Intercepts Of 28.50 M Of 16.53%,
- 30.95 M Of 8.18%, 46.25 M Of 5.43% And 47.15 M Of 4.42% Flake
- Graphite

Canada Strategic Metals Inc. ("Canada Strategic Metals" or "the
Company") and Lomiko Metals Inc. are very pleased to announce the
results for seven (7) exploration holes from the Refractory Zone at the
La Loutre Graphite Property. The recent drilling campaign on La Loutre
Graphite property has now been completed.

"High Grade material in a large, near surface mineralized system
such as La Loutre is a very positive indicator for the viability of a
future mining operation", stated A. Paul Gill, CEO Lomiko Metals Inc.

Results*

//st
Hole #   From (m)     To (m) Length* (m)   Gp %
LL-15-49  100.00     106.00        6.00    5.00
143.50     175.00       31.50    2.79
LL-15-50    2.20      48.45       46.25    5.43
including   5.80       9.75        3.95   17.95
including  42.70      46.95        4.25   15.56
LL-15-51    4.20      37.50       33.30   14.62
including   9.00      37.50       28.50   16.53
91.55     122.50       30.95    8.18
including  91.55      98.50        6.95   18.31
including 115.00     122.50        7.50    9.61
LL-15-52   64.65     111.80       47.15    4.42
including 109.00     111.80        2.80   17.28
LL-15-53     NSV
LL-15-54     NSV
LL-15-55    7.50      13.50        6.00    1.13
130.35     134.15        3.80    3.82
//et

* Length along the core. The Company doesn't have enough
information to estimates the true width of the mineralized zone
intersected in the drill holes
The La Loutre property consists of contiguous claim blocks
totalling approximately 2,867.29 hectares (28.67 km2) situated
approximately 53 km east of Imerys Carbon and Graphite, formerly known
as the Timcal Graphite Mine, North America's only operating graphite
mine, and 117 km northwest of Montreal. The property will now be
assessed for a resource. Viable near surface mineralization reduces the
amount of waste rock that needs to be moved, reducing overall cost of
the project and reducing environmental impact.

In addition, Lomiko hopes to define material )99.99% Graphite
Crystalline Flake to serve as the base material for testing graphite
for the ultrapure carbon market and for conversion to graphene and use
in 3D Printing and Supercapacitors.

A map of hole localisation and results is available on the web
site of the Company at: www.csmetals.ca and www.lomiko.com under the
Quicklinks tab.

The 2015 drilling program is managed by Consul-Teck Exploration of
Val-d'Or, Quebec, who designed the drilling campaign, supervised the
program and logged and sampled the core.

Consul-Teck Exploration implemented QA/QC procedures to ensure
best practices in sampling and analysis of the core samples. The drill
core was logged and then split, with one half sent for assay and the
other retained in the core box as a witness sample. Duplicates and
blanks were inserted regularly into the sample stream.

The samples in secure tagged bags were delivered directly to the
analytical facility for analysis. In this case, the analytical facility
was the ALS minerals in Val-d'Or, Quebec. The samples are weighed and
identified prior to sample preparation. The samples are crushed to 70%
minus 2 mm, then separated and pulverized to 85% passing 75 um. All
samples are analyzed for Carbon Graphite using C-IR18.

Jean-Sebastien Lavallee (OGQ #773), geologist, shareholder of both
companies, President and Chief Executive Officer of the Company and a
Qualified Person under NI 43-101, has reviewed and approved the
technical content of this release.

About Canada Strategic Metals

Canada Strategic Metals is an emerging company focused on the
exploration and development of a number of projects covering over
20,000 hectares in Quebec. With broad management experience in green
technology and junior resource exploration and development, Canada
Strategic Metals is well positioned to aggressively advance this
promising property portfolio for its shareholders.

For more information on the Company, please visit www.csmetals.ca.


Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TEL: 819-354-5146  Jean-Sebastien Lavallee, P. Geo
President and Chief Executive Officer
Canada Strategic Metals
TSX Venture closing price for LMR-V
Date: 2016/01/05
Closing Price: 0.04

TEL: 514-341-0408  Paradox Public Relations
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1600500020TS11600501307-08210420160106