Source	MARKET NEWS
Date	01/06/2016
Time	11:02:35 PM

Company	 Rye Patch Gold Corp.
Title	Hits at 
Gold Ridge





    CDNX Symbol: RPM











Press Release





RYE PATCH GOLD CORP ("RPM-V;RPMGF-0")
- Hits at Gold Ridge

Rye Patch Gold Corp (the "Company" or "Rye Patch") announces
completion of drilling and assay results for its 100% owned Gold Ridge
project located along the Oreana trend in Pershing County, Nevada.

The drill program focused along a 2.2 kilometre, north-south
oriented structural zone associated with a fold and thrust system.  The
style of mineralization appears similar to and along strike with the
Florida Canyon mine located 16 kilometres to the north.  The folded
sediments host gold and silver mineralization along the axial plane of
the anticline and within low-angle structural zones (thrust faults).

The drill program tested the limbs and axial zone of the anticline
with 18 of the 24 drillholes intersecting significant mineralization.
A total of 2,420 metres (7,940 feet) was completed in this drill
campaign. The mineralization is open to the north and south with a
follow-up drill program planned as part of the larger Plan of
Operations permit that is in progress.

Highlights:

//st

GR-027 tested the west side in the southern portion of the anticline and
cut 1.16 g/t AuEq. over 42.7m including 3.28 g/t AuEq over 7.6m;
GR-032 tested the west limb in the northern portion of the anticline and
intercepted 0.91 g/t AuEq over 18.3m with the drillhole ending in
mineralization;
75% of the drillholes encountered significant gold and silver
mineralization;
Two target areas are showing good potential and continuity along the
zone; and
Structural style, alteration, and precious metal content look similar to
the nearby Florida Canyon mine.
//et

Two target areas are showing good potential and continuity along
the zone.  The northern target has a strike length of 800 metres and is
characterized by outcrops of jasperoid breccia with fragments of quartz
vein and jasperoid in an iron rich matrix. The amount of quartz-vein
fragments has a relationship with higher gold and silver grades than
breccia with jasperoid fragments only.  Sedimentary rocks consisting of
limestone and black mudstone are inter-bedded and folded in to a large
anticline overlying a major thrust fault.  The west limb is over
steepened with the hinge zone exposed at the surface and providing the
structural preparation to host gold and silver.  At North target,
mapping shows a repetition of the mineralized zone.  Drillholes GR-045,
GR-046 and GR-047 targeted a jasperoid zone beneath the outcropping
mineralization. Multiple mineralized intervals were intercepted in two
drillholes and indicates upside potential for multiple, stacked zones
of gold and silver.

The South target area is approximately 1.5 kilometres south of the
North area and has a surface exposure of 500 metres, where four
drillholes intersected significant gold and silver mineralization.
Drillhole GR-027 cut 42.7 metres grading 1.16 g/t AuEq starting at
shallow depths.  Limited drilling has been completed on the South
target area; however, the zone is open to the south and north along the
axial plane of the anticline.

Geologically, the mineralized intervals encountered are within the
oxide zone.  However, no metallurgical test work has been completed
yet.

Table 1 summarizes the result of the Gold Ridge fall 2015 drill
program.

//st
Table 1: Gold Ridge Project - 2015 Drilling Results (cut off 0.2 g/t Au)

Drillhole  Remarks       Au    Ag    AuEq  Drill hole    From   To     TD
g/t   g/t   g/t   interval      (m)    (m)    (m)
(m)
GR-026     South Target  0.45  3.6   0.51  12.2          12.2   24.4   61.0
GR-027     South Target  0.92  14.6  1.16  42.7          9.1    51.8   61.0
Including                2.58  42.1  3.28  7.6           15.2   22.9
GR-028     South Target  0.38  8.8   0.53  42.7          25.9   68.6  106.7
GR-029     South Target  0.52  4.2   0.59  15.2          12.2   27.4   76.2
GR-030     North Target  0.29  1.7   0.32  3.0           21.3   24.4  128.0
GR-030     North Target  0.33  4.3   0.40  7.6           41.1   48.8
GR-031     North Target  0.21  3.4   0.27  10.7          9.1    19.8   91.4
GR-031     North Target  0.21  4.0   0.28  18.29         24.38  42.67
GR-031     North Target  0.54  7.5   0.67  16.8          53.3   70.1
GR-032     North Target  0.25  2.3   0.29  4.6           41.1   45.7  121.9
GR-032     North Target  0.62  17.3  0.91  18.3          53.3   71.6
GR-032     North Target  0.30  3.1   0.35  35.1          86.9   121.9
GR-033     North Target  0.45  12.1  0.65  3.0           54.9   57.9  170.7
GR-033     North Target  0.20  3.2   0.25  6.1           80.8   86.9
GR-034     North Target  0.37  8.2   0.51  16.8          64.0   80.8  153.9
GR-034     North Target  0.44  8.7   0.59  12.2          86.9   99.1
GR-034     North Target  0.25  1.6   0.28  4.6           112.8  117.3
GR-035     North Target  0.33  2.8   0.38  12.2          71.6   83.8   99.1
GR-036     North Target  NSA                                           61.0
GR-037     North Target  0.24  4.4   0.31  3.0           33.5   36.6   91.4
GR-038     North Target  NSA                                           76.2
GR-039     North Target  NSA                                           61.0
GR-040     North Target  0.38  4.5   0.46  3.0           56.4   59.4   99.1
GR-041     North Target  NSA                                           71.6
GR-042     North Target  0.21  3.8   0.27  3.0           129.5  132.6 167.6
GR-043     North Target  NSA                                          102.1
GR-044     North Target  0.28  0.4   0.29  3.0           27.4   30.5   91.4
GR-045     North Target  0.35  6.4   0.46  27.4          27.4   54.9   91.4
GR-045     North Target  0.47  9.3   0.63  7.6           61.0   68.6
GR-046     North Target  NSA                                          106.7
GR-047     North Target  1.09  6.1   1.19  4.6           29.0   33.5   91.4
GR-047     North Target  0.24  7     0.36  16.8          50.3   67.1
GR-047     North Target  0.65  6.2   0.75  13.7          77.7   91.4
GR-048     North Target  0.28  17.7  0.58  3.0           96.0   99.1  147.8
GR-049     North Target  0.66  13.2  0.88  6.1           74.7   80.8   91.4



AuEq = Au + Ag/60
Drillhole interval is not true thickness
//et

William Howald, the Company's President and CEO stated, "The 2015
drilling program extends the mineralization drilled in 2014 at the
North target along strike and at depth.  Management believes that Gold
Ridge property has significant potential for a bulk-tonnage, low-grade
gold and silver deposit.  The two established targets are located less
than 2 km west of the Lincoln Hill resource area, and the 2015 assay
results establish the Gold Ridge project as a valuable asset and a
prospective source of additional gold and silver for our Lincoln Hill
resource project. While additional drilling and work are required to
establish resources at the Gold Ridge deposit, these results are very
encouraging."

Rye Patch US maintains a strict quality control program at all of
its projects. All reverse circulation drill samples are submitted to
American Assay with prep-blanks, assay blanks, and gold and silver
standards.  Rye Patch US inserts approximately one quality control or
quality assurance sample for every ten samples submitted to the assay
laboratory.  The reverse circulation character samples are logged and
photographed on site. American Assay collects the drill samples and
transports them to their preparation and analytical facility located in
Reno, Nevada.  Gold analyses are conducted on 1-assay ton prepped
samples with gold determined using industry standard fire assay methods
with an ICP finish.  Gold values above 10 g/t gold (over limits) are
confirmed using fire assay with a gravimetric finish.  Silver is
analyzed using a two-acid digestion and an ICP finish. Silver values
are re-analyzed with a four-acid digestion and ICP finish on all
samples with gold values greater than a 0.2 g/t gold assay result.
Silver values over 100 g/t silver are re-analyzed using volumetric
dissolution.

Mr. William Howald, AIPG Certified Professional Geologist #11041,
Rye Patch Gold's CEO and President, is a Qualified Person as defined
under National Instrument 43-101. He has reviewed and approved the
contents of this news release.

About Rye Patch Gold Corp.

Rye Patch Gold Corp. is a Tier 1, well-funded junior mining
company led by a seasoned management team that has participated in
major discoveries totaling over 100-million ounces of gold.  The team
is engaged in the acquisition, exploration and development of quality
resource-based gold and silver projects along the emerging Oreana trend
and the prolific Cortez trend.  Benefitting from its strong financial
position, the Company's strategy is to balance development and
exploration risk, creating value by:

//st

Advancing the Lincoln Hill project toward production;
Pursuing a world class discovery - Garden Gate and Patty - contiguous to
and on strike with Barrick's Goldrush deposit; and
Seeking new project opportunities and accretive transactions.
//et
The Company's cash and cash flowing royalty allow for progress
without dilution to shareholders. For more information about the
Company, please visit our website at www.ryepatchgold.com.

On behalf of the Board of Directors

'William Howald'
William C. (Bill) Howald, CEO & President

This news release contains forward-looking statements, which
address future events and conditions, which are subject to various
risks and uncertainties. The Company's actual results, programs and
financial position could differ materially from those anticipated in
such forward-looking statements as a result of numerous factors, some
of which may be beyond the Company's control.  These factors include:
the availability of funds; the financial position of Rye Patch; the
timing and content of work programs; the results of exploration
activities and development of mineral properties; the interpretation of
drilling results and other geological data; the reliability of
calculation of mineral resources (and, in respect of the Coeur
Rochester mine 3.4% NSR, the reliability of calculation of Coeur's
mineral resources and reserves); the reliability of calculation of
precious metal recoveries; the receipt and security of mineral property
titles; project cost overruns or unanticipated costs and expenses;
fluctuations in metal prices; currency fluctuations; and general market
and industry conditions.

Forward-looking statements are based on the expectations and
opinions of the Company's management on the date the statements are
made.  The assumptions used in the preparation of such statements,
although considered reasonable at the time of preparation, may prove to
be imprecise and, as such, undue reliance should not be placed on
forward-looking statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for RPM-V
Date: 2016/01/05
Closing Price: 0.15

TEL:  (604) 638-1588  Rye Patch Gold Corp
FAX:  (604) 638-1589
E-mail:   info@ryepatchgold.com
Internet: http://www.ryepatchgold.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1600500014TS11600500876-06230220160106

[200/News Release]RPMVRYE PATCH GOLD CORPJAN 06 2016  06:23 AMHits at 
Gold Ridge --->@NEWS RELEASE
RYE PATCH GOLD CORP ("RPM-V;RPMGF-0")
- Hits at Gold Ridge

Rye Patch Gold Corp (the "Company" or "Rye Patch") announces
completion of drilling and assay results for its 100% owned Gold Ridge
project located along the Oreana trend in Pershing County, Nevada.

The drill program focused along a 2.2 kilometre, north-south
oriented structural zone associated with a fold and thrust system.  The
style of mineralization appears similar to and along strike with the
Florida Canyon mine located 16 kilometres to the north.  The folded
sediments host gold and silver mineralization along the axial plane of
the anticline and within low-angle structural zones (thrust faults).

The drill program tested the limbs and axial zone of the anticline
with 18 of the 24 drillholes intersecting significant mineralization.
A total of 2,420 metres (7,940 feet) was completed in this drill
campaign. The mineralization is open to the north and south with a
follow-up drill program planned as part of the larger Plan of
Operations permit that is in progress.

Highlights:

//st

GR-027 tested the west side in the southern portion of the anticline and
cut 1.16 g/t AuEq. over 42.7m including 3.28 g/t AuEq over 7.6m;
GR-032 tested the west limb in the northern portion of the anticline and
intercepted 0.91 g/t AuEq over 18.3m with the drillhole ending in
mineralization;
75% of the drillholes encountered significant gold and silver
mineralization;
Two target areas are showing good potential and continuity along the
zone; and
Structural style, alteration, and precious metal content look similar to
the nearby Florida Canyon mine.
//et

Two target areas are showing good potential and continuity along
the zone.  The northern target has a strike length of 800 metres and is
characterized by outcrops of jasperoid breccia with fragments of quartz
vein and jasperoid in an iron rich matrix. The amount of quartz-vein
fragments has a relationship with higher gold and silver grades than
breccia with jasperoid fragments only.  Sedimentary rocks consisting of
limestone and black mudstone are inter-bedded and folded in to a large
anticline overlying a major thrust fault.  The west limb is over
steepened with the hinge zone exposed at the surface and providing the
structural preparation to host gold and silver.  At North target,
mapping shows a repetition of the mineralized zone.  Drillholes GR-045,
GR-046 and GR-047 targeted a jasperoid zone beneath the outcropping
mineralization. Multiple mineralized intervals were intercepted in two
drillholes and indicates upside potential for multiple, stacked zones
of gold and silver.

The South target area is approximately 1.5 kilometres south of the
North area and has a surface exposure of 500 metres, where four
drillholes intersected significant gold and silver mineralization.
Drillhole GR-027 cut 42.7 metres grading 1.16 g/t AuEq starting at
shallow depths.  Limited drilling has been completed on the South
target area; however, the zone is open to the south and north along the
axial plane of the anticline.

Geologically, the mineralized intervals encountered are within the
oxide zone.  However, no metallurgical test work has been completed
yet.

Table 1 summarizes the result of the Gold Ridge fall 2015 drill
program.

//st
Table 1: Gold Ridge Project - 2015 Drilling Results (cut off 0.2 g/t Au)

Drillhole  Remarks       Au    Ag    AuEq  Drill hole    From   To     TD
g/t   g/t   g/t   interval      (m)    (m)    (m)
(m)
GR-026     South Target  0.45  3.6   0.51  12.2          12.2   24.4   61.0
GR-027     South Target  0.92  14.6  1.16  42.7          9.1    51.8   61.0
Including                2.58  42.1  3.28  7.6           15.2   22.9
GR-028     South Target  0.38  8.8   0.53  42.7          25.9   68.6  106.7
GR-029     South Target  0.52  4.2   0.59  15.2          12.2   27.4   76.2
GR-030     North Target  0.29  1.7   0.32  3.0           21.3   24.4  128.0
GR-030     North Target  0.33  4.3   0.40  7.6           41.1   48.8
GR-031     North Target  0.21  3.4   0.27  10.7          9.1    19.8   91.4
GR-031     North Target  0.21  4.0   0.28  18.29         24.38  42.67
GR-031     North Target  0.54  7.5   0.67  16.8          53.3   70.1
GR-032     North Target  0.25  2.3   0.29  4.6           41.1   45.7  121.9
GR-032     North Target  0.62  17.3  0.91  18.3          53.3   71.6
GR-032     North Target  0.30  3.1   0.35  35.1          86.9   121.9
GR-033     North Target  0.45  12.1  0.65  3.0           54.9   57.9  170.7
GR-033     North Target  0.20  3.2   0.25  6.1           80.8   86.9
GR-034     North Target  0.37  8.2   0.51  16.8          64.0   80.8  153.9
GR-034     North Target  0.44  8.7   0.59  12.2          86.9   99.1
GR-034     North Target  0.25  1.6   0.28  4.6           112.8  117.3
GR-035     North Target  0.33  2.8   0.38  12.2          71.6   83.8   99.1
GR-036     North Target  NSA                                           61.0
GR-037     North Target  0.24  4.4   0.31  3.0           33.5   36.6   91.4
GR-038     North Target  NSA                                           76.2
GR-039     North Target  NSA                                           61.0
GR-040     North Target  0.38  4.5   0.46  3.0           56.4   59.4   99.1
GR-041     North Target  NSA                                           71.6
GR-042     North Target  0.21  3.8   0.27  3.0           129.5  132.6 167.6
GR-043     North Target  NSA                                          102.1
GR-044     North Target  0.28  0.4   0.29  3.0           27.4   30.5   91.4
GR-045     North Target  0.35  6.4   0.46  27.4          27.4   54.9   91.4
GR-045     North Target  0.47  9.3   0.63  7.6           61.0   68.6
GR-046     North Target  NSA                                          106.7
GR-047     North Target  1.09  6.1   1.19  4.6           29.0   33.5   91.4
GR-047     North Target  0.24  7     0.36  16.8          50.3   67.1
GR-047     North Target  0.65  6.2   0.75  13.7          77.7   91.4
GR-048     North Target  0.28  17.7  0.58  3.0           96.0   99.1  147.8
GR-049     North Target  0.66  13.2  0.88  6.1           74.7   80.8   91.4



AuEq = Au + Ag/60
Drillhole interval is not true thickness
//et

William Howald, the Company's President and CEO stated, "The 2015
drilling program extends the mineralization drilled in 2014 at the
North target along strike and at depth.  Management believes that Gold
Ridge property has significant potential for a bulk-tonnage, low-grade
gold and silver deposit.  The two established targets are located less
than 2 km west of the Lincoln Hill resource area, and the 2015 assay
results establish the Gold Ridge project as a valuable asset and a
prospective source of additional gold and silver for our Lincoln Hill
resource project. While additional drilling and work are required to
establish resources at the Gold Ridge deposit, these results are very
encouraging."

Rye Patch US maintains a strict quality control program at all of
its projects. All reverse circulation drill samples are submitted to
American Assay with prep-blanks, assay blanks, and gold and silver
standards.  Rye Patch US inserts approximately one quality control or
quality assurance sample for every ten samples submitted to the assay
laboratory.  The reverse circulation character samples are logged and
photographed on site. American Assay collects the drill samples and
transports them to their preparation and analytical facility located in
Reno, Nevada.  Gold analyses are conducted on 1-assay ton prepped
samples with gold determined using industry standard fire assay methods
with an ICP finish.  Gold values above 10 g/t gold (over limits) are
confirmed using fire assay with a gravimetric finish.  Silver is
analyzed using a two-acid digestion and an ICP finish. Silver values
are re-analyzed with a four-acid digestion and ICP finish on all
samples with gold values greater than a 0.2 g/t gold assay result.
Silver values over 100 g/t silver are re-analyzed using volumetric
dissolution.

Mr. William Howald, AIPG Certified Professional Geologist #11041,
Rye Patch Gold's CEO and President, is a Qualified Person as defined
under National Instrument 43-101. He has reviewed and approved the
contents of this news release.

About Rye Patch Gold Corp.

Rye Patch Gold Corp. is a Tier 1, well-funded junior mining
company led by a seasoned management team that has participated in
major discoveries totaling over 100-million ounces of gold.  The team
is engaged in the acquisition, exploration and development of quality
resource-based gold and silver projects along the emerging Oreana trend
and the prolific Cortez trend.  Benefitting from its strong financial
position, the Company's strategy is to balance development and
exploration risk, creating value by:

//st

Advancing the Lincoln Hill project toward production;
Pursuing a world class discovery - Garden Gate and Patty - contiguous to
and on strike with Barrick's Goldrush deposit; and
Seeking new project opportunities and accretive transactions.
//et
The Company's cash and cash flowing royalty allow for progress
without dilution to shareholders. For more information about the
Company, please visit our website at www.ryepatchgold.com.

On behalf of the Board of Directors

'William Howald'
William C. (Bill) Howald, CEO & President

This news release contains forward-looking statements, which
address future events and conditions, which are subject to various
risks and uncertainties. The Company's actual results, programs and
financial position could differ materially from those anticipated in
such forward-looking statements as a result of numerous factors, some
of which may be beyond the Company's control.  These factors include:
the availability of funds; the financial position of Rye Patch; the
timing and content of work programs; the results of exploration
activities and development of mineral properties; the interpretation of
drilling results and other geological data; the reliability of
calculation of mineral resources (and, in respect of the Coeur
Rochester mine 3.4% NSR, the reliability of calculation of Coeur's
mineral resources and reserves); the reliability of calculation of
precious metal recoveries; the receipt and security of mineral property
titles; project cost overruns or unanticipated costs and expenses;
fluctuations in metal prices; currency fluctuations; and general market
and industry conditions.

Forward-looking statements are based on the expectations and
opinions of the Company's management on the date the statements are
made.  The assumptions used in the preparation of such statements,
although considered reasonable at the time of preparation, may prove to
be imprecise and, as such, undue reliance should not be placed on
forward-looking statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for RPM-V
Date: 2016/01/05
Closing Price: 0.15

TEL:  (604) 638-1588  Rye Patch Gold Corp
FAX:  (604) 638-1589
E-mail:   info@ryepatchgold.com
Internet: http://www.ryepatchgold.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1600500014TS11600500876-06230220160106