Source	MARKET NEWS
Date	01/14/2016
Time	07:13:59 AM

Company	 Northern Superior Resources Inc.
Title	Inferred Mineral Resource Estimates At Its Crote





    CDNX Symbol: SUP











Press Release





Inferred Mineral Resource Estimates At Its Croteau Est GoldProperty, West 
central Quebec. --->@NEWS RELEASE
NORTHERN SUPERIOR RESOURCES INC ("SUP-V;NSUPF-0")
- Inferred Mineral Resource Estimates At Its Croteau Est Gold
- Property, West-central Quebec.

Northern Superior Resources Inc.

Highlights:

//st
Inferred Mineral Resource estimate for the central section (approximately
550m strike by 150m width) of the Croteau Bouchard Shear Zone ("CBSZ")
reported using a gold cut-off of 1.0 g/t Au totaling 11.6 million tonnes
grading 1.7ppm Au, yielding 640,000 ounces of gold;

The Inferred Mineral Resource estimate is based on 64 core drill holes
(20,643 m);

An exploration potential/target, ranging from 3.2 to 3.8 million tonnes,
for a total of 122,000 to 270,000 ounces of gold, was identified by
mineralization defined by single drillhole intersections (see cautionary
language noted in the discussion below); and

Mineralization occurs at surface, and remains open along strike in both
directions (length defined thus far 1.1km) and at depth (only one hole to
575m vertical depth).

//et

Northern Superior Resources Inc. ("Northern Superior" or the
"Company") reports that the Company has received a National Instrument
43-101 - Standards of Disclosure for Mineral Projects ("NI 43-101")
Technical Report dated September 28, 2015, prepared by Optiro Pty
Limited (the "Optiro Report"), which includes Inferred Mineral Resource
estimates (see Table 1) for the central part of the CBSZ. The CBSZ is
located within Northern Superior's 100% owned Croteau Est gold
property, west-central Quebec.

//st
Table 1. Croteau Est Sep 2015 Mineral Resource appropriate for public
reporting at 1.0 ppm gold cut-off.

Category                  Tonnes (Mt) Gold grade (Au g/t) Gold ounces (Koz)
Inferred Mineral Resource        11.6                 1.7               640
//et

Due to the inherent sample support issues associated with including
channel sample assay data into resource models, previously reported
high grade assay values from several trench exposures across the
central CBSZ were excluded from the Optiro Report and model (see press
releases: October 12, 2011; November 12, 2013; November 3, 2014).

Dr. T.F. Morris, President and CEO of Northern Superior commented:
"Northern Superior management believes that the Inferred Mineral
Resource estimates presented by the Optiro Report represent a great
start to understanding the gold potential of the CBSZ specifically, and
the Croteau Est property as a whole. On the CBSZ alone, a tremendous
opportunity exists to expand the number of gold ounces within the CBSZ
based on the premise that additional exploration may:



1. upgrade some of the exploration potential/target of the CBSZ;

2. convert part of the Inferred Mineral Resource to Indicated Mineral
Resource category by infill drilling of core drill holes, from 50m x 50m to
25m x 25m;

3. add additional gold ounces by inclusion of the high grade gold values
previously reported from channel samples cut in several trenches at surface
within the central part of the CBSZ in future modelling;

4. identify potential high grade rods or shoots within the CBSZ (see press
release: November 3, 2014) with tighter collar spacing; and

5. identify additional gold ounces along strike (east and west) of the
central CBSZ and at depth, as the system is open in those directions."



Management at Northern Superior has always maintained that the CBSZ
is a small component of a much larger gold mineralized system on the
property, based not only on management's observations but from those
recommendations made from several qualified consultants who have worked
on the project. Northern Superior hopes to find a partner that will
assist the Company to realize the potential at the CBSZ."

Optiro Report Recommendations Include:

//st

Infill drilling of the central section of the CBSZ deposit to 25 x 25m
drill hole spacing to potentially upgrade the classification of this area
to Indicated Mineral Resource category; and

Exploration drilling to test along strike extensions of the central CBSZ
deposit, in particular on the eastern end of the deposit, where there are
three drill holes that have mineralized intervals consistent with the
projection of the CBSZ. These intersections may suggest either an isolated
zone of mineralization, or continuation of mineralization of an unknown
extent along the CBSZ.

//et

Inferred Mineral Resource Classification:

//st

The Inferred Mineral Resource estimates have been generated from drill hole
sample assay results and the interpretation of an integrated 3D geological
model that defines the relationships of various geological elements within
the CBSZ. The interpreted mineralization wireframes (using a nominal 0.25
ppm Au cut-off grade) have been used to constrain gold grade estimates.
Block grade estimation parameters have been defined on the basis of
geology, drillhole spacing, and through geostatistical analysis of the
data. Block grade estimation is by ordinary kriging (OK) into a panel size
of 12.5 mE by 2.5 mN on 2.5 mRL, which is considered appropriate for the
distribution of sample data and the deposit type.

The Inferred Mineral Resource estimates have been classified by their
proximity to the sample locations and confidence in the block model grade
estimate, and have been reported in accordance with the guidelines of the
JORC Code (JORC, 2012). The JORC Code was used because the company's former
partner on the project was an ASX and TSX listed company with an Australian
head office. The company's QP (defined below) is confident there are no
material differences between JORC Code guidelines regarding inferred
mineral resources and those set forth in Standards on Mineral Resources and
Reserves of the Canadian Institute of Mining, Metallurgy and Petroleum
(CIM, 2010).

A more detailed description on the modelling and statistical parameters
used to determine the Inferred Mineral Resource estimates are provided
within the Optiro Report.

//et

Exploration Potential/Target:

The Optiro Report also identified additional mineralized material
on the CBSZ which lacked sufficient confidence to be classified as an
Inferred Mineral Resource but that the uncertainty with this material
is such that with further work, this could change and hence, represents
an exploration potential/target. Specifically, the Optiro Report
indicates an exploration potential range of 3.2 to 3.8 million tonnes,
for a total of 122,000 to 270,000 ounces of gold. To evaluate the
exploration potential, the unclassified mineralization above 1.0 g/t
cut-off, was tabulated as being above/below 325 m below surface and by
lode. Any mineralization associated with lode 1 (the main lode) was
incorporated into the exploration potential. The lower range for the
minor lode was estimated as follows: (i) below 325 m below surface,
lodes greater than 2.0 g/t gold were included as exploration potential;
and (ii) above 325 m below surface, lodes greater than 1.5g/t golf were
included as exploration potential. The maximum range assumed that with
further work, up to 100% of the unclassified mineralization may be
upgraded. The Optiro Report further noted that more than 90% of this
material is at depths greater than 325 m below surface and that a
significant amount of work will be required to improve the confidence
for this material. As such, caution must be exercised as the potential
quantity and grade is conceptual in nature, there has been insufficient
exploration to define a mineral resource and that it is uncertain if
further exploration will result in the target being delineated as a
mineral resource.

About Northern Superior

Northern Superior is a junior exploration company exploring for
gold in the Superior Province of the Canadian Shield. The Company
currently has 2 gold properties (Croteau Est, Lac Surprise) and 1
diamond exploration property (Ville Marie) in Quebec and 1 gold, silver
copper property in Ontario (Ti-pi-haa-kaa-ning). All these properties
are 100% owned and operated by Northern Superior. All properties have
core drill- ready targets defined on each. The Company also has one
early stage mineral property in Quebec, Wapistan. A summary for each of
these properties is available on Northern Superior's website
(www.nsuperior.com). Northern Superior has identified an additional 22
mineral properties in west-central Quebec from it's in-house terabyte
of geoscientific data.

The disclosure in this press release is based on excerpts taken
from the Optiro Report, which was principally authored and certified by
Mark Drabble, Principal Consultant at Optiro Pty Limited (B.App.Sci
Geology, MAIG, MAusIMM). Mr. Drabble meets the requirements of an
"independent" Qualified Person under NI 43-101. The Optiro Report will
be filed on SEDAR (www.sedar.com) immediately following dissemination
of this news release and will also be posted on Northern Superior's
website (www.nsuperior.com). The Company's Qualified Person ("QP") for
the Croteau Est property is Ron Avery (P.Geo.). As the QP, Mr. Avery
has approved information disclosed in this press release.

Northern Superior is a reporting issuer in British Columbia,
Alberta, Ontario and Quebec, and trades on the TSX Venture Exchange
under the symbol SUP.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Cautionary Note Regarding Mineral Reserves and Mineral Resources:
The terms "Mineral Resource", "Indicated Mineral Resource", "Inferred
Mineral Resource" used in this release are Canadian mining terms as
defined in accordance with National Instruction 43-101 - Standards of
Disclosure for Mineral Projects under the guidelines set out in the CIM
Standards. Mineral Resources which are not Mineral Reserves do not have
demonstrated economic viability.

Cautionary Note Regarding Forward-Looking Statements: This Press
Release contains forward-looking statements that involve risks and
uncertainties, which may cause actual results to differ materially from
the statements made. When used in this document, the words "may",
"would", "could", "will", "intend", "plan", "anticipate", "believe",
"estimate", "expect" and similar expressions are intended to identify
forward-looking statements. Such statements reflect our current views
with respect to future events and are subject to such risks and
uncertainties. Many factors could cause our actual results to differ
materially from the statements made, including those factors discussed
in filings made by us with the Canadian securities regulatory
authorities. Should one or more of these risks and uncertainties, such
actual results of current exploration programs, the general risks
associated with the mining industry, the price of gold and other
metals, currency and interest rate fluctuations, increased competition
and general economic and market factors, occur or should assumptions
underlying the forward looking statements prove incorrect, actual
results may vary materially from those described herein as intended,
planned, anticipated, or expected. We do not intend and do not assume
any obligation to update these forward-looking statements, except as
required by law. Shareholders are cautioned not to put undue reliance
on such forward-looking statements.

Thomas F. Morris (President and CEO)
1351C Kelly Lake Road, Unit 7,

































TSX Venture closing price for SUP-V
Date: 2016/01/07
Closing Price: 0.02

TEL: (705) 525-0992
FAX: (705) 525-7701
Internet: www.nsuperior.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1601300017TS11601301011-07131920160114