Source	MARKET NEWS
Date	01/15/2016
Time	05:03:52 AM

Company	 Cadan Resources Corporation
Title	First Gold 
Production and Commissioning Update





    CDNX Symbol: CXD











Press Release





CADAN RESOURCES CORP ("CXD-V;CADAF-0")
- First Gold Production and Commissioning Update

Cadan Resources Corporation ("Cadan" or the "Company") is pleased
to provide an update on its commissioning progress and initial
production, including the results of its first gold pour since the
plant closure in September 2014.

Production Highlights (Commissioning Phase)

-Gold and silver production to-date of 6.2kg Au and 20kg Ag

-Total throughput to date of 5,189 tonnes

-Average grade to date of 1.87g/t Au & 28.7g/t Ag

-Average gold recovery to date of 91%

-Throughput during December 2015 of 3,540 tonnes, averaging 114
tonnes per day

-Average gold recoveries in December of 90%

-Average grade during December of 1.83g/t Au and 30.02g/t Ag

-Throughput January 1 to date is 1,649 tonnes, averaging 127
tonnes per day

-Average grade year-to-date of 1.97g/t Au and 29.7g/t Ag

-Average gold recovery year to-date of 95.6%

-Current throughput 145tpd

Cadan's gold production since commencing commissioning on the 7th
of November has totalled 6.2kg of gold (Au), and 20kg of silver (Ag)
equivalent to 199oz Au and 643oz Ag, at an average grade 1.87g/t Au and
28.7g/t Ag.

Commissioning is ongoing and has taken longer than anticipated,
primarily due to the plant construction contractor not meeting agreed
refurbishment specifications, timing and key performance milestones. As
a result of those delays, in late December 2015 Cadan replaced the
contractor and with Cadan's own plant management team including
appointing its own Mill Manager and maintenance contractor MagDrills to
manage all mill maintenance. Cadan has observed significant
improvements in the performance of the plant since the changes have
been made.

The issues with the prior construction contractor has resulted in
the planned ramp up of production to the plant design capacity of 200
tonnes per day (tpd) being delayed by approximately 8 weeks.
Nonetheless production rates are continuing to increase at a steady
rate and plant performance over the last 3 weeks has demonstrated much
greater consistency.

As at the current date, the plant is operating at 150tpd which is
approximately 50% above its highest ever production levels. That has
been achieved on a significantly smaller budget (almost 20% less) when
compared to plant budget for the prior launch and operation of the
plant. Total capital expenditures to-date to completely rebuild the
company and its main project T'Boli is approximately US$3.4 million
(C$4.6 million).

T'Boli gold pour - Weight 1.5kg, Grade 99.79% purity

Processing continues on the low and marginal grade stockpiles with
the results above initial expectations. There have been considerably
more tonnes identified than initial estimates, due to higher metal
content mineralized material being found in areas previously identified
as uneconomic.

-------------------------------------------------------

The Company further announces that it is seeking to enter into
shares-for-debt settlement agreements whereby Cadan is proposing to
issue up to 20,000,000 units to current creditors of the Company to
settle aged account payables. Each unit consists of one common share of
the corporation and one share purchase warrant. Each share purchase
warrant entitles the holder to acquire one common share of the Company
at a price of $0.10 for up to 12 months. The units will be offered at a
price of five cents per unit. The shares-for-debt settlements will be
subject to the approval of the TSX Venture Exchange ("TSX-V") and the
unites will be subject to a 4-month hold period.

The shares-for-debt transaction is one of a series of ongoing
steps that the Company has been carrying out since March 2014. Those
steps include a reduction of net debt by share settlement as well as
careful control over operating costs and general and administrative
expenses. In addition, the Company continues to actively seek funds to
further the progress on the T'Boli Project. The recently announced
Facility agreement for up to $6.4 mill (see press release of January
11, 2016) is intended to provide Cadan with the necessary funding to
carry the project through the commissioning stage, and to achieve
targeted expansion of production rates to 400tpd.

The Company also confirms that as per its press release on
December 23, 2015 it has received approval from the TSX-V and completed
the issuance of shares for debt of 1,088,250 shares to former directors
and officers of the Company.

Statement Regarding T'Boli Production: The Company advises that
the decision to restart production at the T'Boli mine was not based on
the results of a pre-feasibility or feasibility study of mineral
reserves prepared in accordance with NI 43-101 demonstrating economic
and technical viability. There are no known mineral reserves, as that
term is used in NI 43-101, on any of its mineral properties and as a
result the economic viability of the properties has not been
demonstrated. A feasibility study or pre-feasibility study provides
more in-depth economic analysis of resources, more detailed metallurgy
and a number of specialized studies in areas such as mining and
recovery methods, market analysis, and environmental and community
impacts. Readers are cautioned that there is increased uncertainty and
higher risk of economic and technical failure associated with
production decisions that are not supported by a current feasibility or
pre-feasibility study.

On Behalf of the Board,
Peter Main
Interim President and CEO
info@CadanResources.com

For further information visit our website at
www.CadanResources.com; email us at info@CadanResources.com

Phone: 778-370-1372 Fax: 604-608-5442

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
______________________________________
_______________________________________________
TSX Venture closing price for CXD-V
Date: 2016/01/06
Closing Price: 0.05
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1601300056TS11601302501-21510020160114