Source	MARKET NEWS
Date	01/25/2016
Time	07:46:56 AM

Company	 Unigold Inc.
Title	Intersects 15.7 
Metres Averaging 7.45 G/t Au Wit





    CDNX Symbol: UGD











Press Release





UNIGOLD INC ("UGD-V;UGDIF-0")
- Intersects 15.7 Metres Averaging 7.45 G/t Au With 1.1% Cu

Unigold Inc. ("Unigold" or the "Company") is pleased to announce
results from ongoing exploration at the Company's 100% owned Neita
Concession in the Dominican Republic.

Exploration drilling testing potential high grade feeder zones at
the Candelones Extension deposit commenced at "Target A" (Ref. Figure
1.0); evaluating a zone of massive sulphides intersected in late 2013
in hole LPMET-01 (6.93 g/t Au; 0.6% Cu / 22.0m).

LP15-93 was designed to test 40 - 50 metres to the southwest of
LPMET-01 and 40 - 50 metres above hole LP17 (6.05 g/t Au; 0.8% Cu /
6.0m.

LP15-93 intersected a broad zone of stratabound mineralization
that returned:

//st
230.1 to 334.0 metres       103.9 metres(1)    2.09 g/t Au    0.3% Cu;
//et

including a massive sulphide lens averaging:

//st
298.6 to 314.3.0 metres       15.7 metres(2)    7.45 g/t Au    1.1% Cu;
//et

(1) Interval is drilled length not true width. Hole orientation is
perpendicular to mineralization, therefore the drilled length should
approximate true width.

(2) Interval is drilled length not true width. There is
insufficient data at this time to estimate true width.

Joseph Del Campo, Interim President and CEO of Unigold notes: "We
are very excited with the results from the first hole of our winter
exploration program. The discovery of a discordant lens of high grade
massive sulphide within the broader, lower grade, stratabound
mineralization previously drilled on 100 metre centers, demonstrates
the potential we are attempting to capture with this targeted
exploration program. This model, of higher grade feeder zones within a
broader zone of lower grade mineralization, is consistent with other
gold / copper deposits within the Tireo Formation of the Dominican
Republic and we believe there is an excellent opportunity to increase
the mineral resources at the Candelones Extension."

Early exploration at the Candelones Extension deposit was focused
on defining a large tonnage, low grade mineral resource amenable to
open pit mining. Mineralization was stratabound, occurring within 25 to
100 metres of the contact between overlying andesite volcanic rocks
with underlying dacite volcanic rocks. The low grade mineralization
occurred almost entirely within the dacites. All the historical
drilling was oriented perpendicular to the andesite - dacite contact
and spaced on 100 metre centers along this contact zone.

This drilling supported the initial mineral resource estimate of
November 12, 2013 (UGD PR# 2013-22) totaling:

39,493,000 tonnes averaging 1.59 g/t Au (2,014,000 ounces
Au)(3)

LP15-93 intersected a broad zone of gold and copper mineralization
(2.09 g/t Au; 0.3% Cu over 103.9 metres) commencing at the andesite -
dacite contact. The results are consistent with grades reported from
other holes in the same area (LP15, LP17 and LP27 - UGD PR# 2012-11)
and exceed the average gold grade of the initial mineral resource
estimate.

In 2014, the mineral resource estimate was updated, focusing on
higher grade gold and copper mineralization at the Candelones Extension
deposit that could be exploited by means of underground mining. As with
the initial mineral resource estimate, mineralization was assumed to be
stratagraphically controlled, parallel to the andesite - dacite
contact. On February 24, 2015 (UGD PR# 2015-02); the Company announced
an updated Inferred Mineral Resource for the Candelones Extension
deposit of:

5,274,000 tonnes averaging 5.27 g/t Au (894,000 ozs Au); 0.35 %
Cu (41,175,000 lbs Cu)(3)

(3) Mineral resources were estimated by Mr. W. Lewis, P.Geo. and
Mr. A. San Martin, MAusIMM(CP) of Micon International Ltd. ("Micon"), a
Toronto based consulting company, independent of Unigold. Both Mr.
Lewis and Mr. San Martin meet the requirements of a "qualified person"
as established by the Canadian Institute of Mining, Metallurgy and
Petroleum (CIM) Definition Standards for Mineral Resources and Mineral
Reserves (May 2014) ("the CIM Standards"). The 2014 estimate is based
on a long term gold price of US$ 1,200 per ounce, a long term copper
price of US$ 3.00 per pound and an economic cut-off grade of 3.50 g/t
Au and assumed exploitation of the Candelones Extension deposit by
means of underground mining.

The massive sulphide mineralization, also intersected in holes
LPMET-01 (44 metres to the northeast) and the upper portion of the
mineralization intersected in hole LP17 (50 metres below LP15-93),
suggest the massive sulphides are not parallel to the andesite - dacite
contact. The three holes suggest the massive sulphide mineralization is
relatively flat, 40 to 45 degrees relative to the andesite - dacite
contact. The historical drilling, largely perpendicular to the andesite
dacite contact, is not optimally oriented to test this mineralization,
especially with widely spaced drill holes.

The Company believes that the stratabound mineralization may be
the result of discordant feeder systems that introduced the stratabound
mineralization along the fragmental dacite volcanic rocks at the
andesite -dacite contact. The Company plans to continue systematically
exploring higher grade areas of the Candelones Extension deposit.

Figure 1.0 - Candelones Extension Deposit - Target A - Plan View:
http://media3.marketwire.com/docs/1040685_fig1.pdf

Figure 2.0 - Candelones Extension Deposit - Target A - Cross
Section: http://media3.marketwire.com/docs/1040685_fig2.pdf

Premier Mining Destination - Dominican Republic

The Dominican Republic is host to world-class gold and base metal
mines and deposits. The government supports development and exploration
in the mining sector. In addition, the country has well established
Mining Laws and Environmental Laws. Unigold's wholly owned flagship
property, Neita is compliant with all mineral and environmental
requirements and work is conducted to internationally accepted
environmental and social standards. The Neita concession exploration
license was renewed in 2012 and is in good standing.

Unigold has sufficient funding to meet the goals and objectives
established for the current exploration program.

QA/QC

Diamond drilling at the Candelones Project utilizes both HQ and NQ
diameter tooling. Holes are established using HQ diameter tooling
before reducing to NQ tooling to complete the hole. The core is
received at the on-site logging facility where it is, photographed,
logged for geotechnical and geological data and subjected to other
physical tests including magnetic susceptibility and specific gravity
analysis. Samples are identified, recorded, split by wet diamond saw,
and half the core is sent for assay with the remaining half stored on
site. A minimum sample length of 0.3 metres and a maximum sample length
of 1.5 metres are employed with most samples averaging 1.0 metres in
length except where geological contacts dictate. Certified standards
and blanks are randomly inserted into the sample stream and constitute
approximately 5-10% of the sample stream. Samples are shipped to a
sample preparation facility in the Dominican Republic operated by
Bureau Veritas. Assaying is performed at Bureau Veritas Commodities
Canada Ltd.'s laboratory in Vancouver, B.C. Canada. All samples are
analyzed for gold using a 50 gram lead collection fire assay fusion
with an atomic adsorption finish. In addition, most samples are also
assayed using a 36 element multi-acid ICP-ES analysis method.

Wes Hanson P.Geo., Chief Operating Officer of Unigold, has
reviewed and approved the contents of this press release.

About Unigold Inc. - Discovering Gold in the Caribbean

Unigold is a Canadian based mineral exploration company traded on
the TSX Venture Exchange under the symbol UGD, focused primarily on
exploring and developing its gold assets in the Dominican Republic.

Forward-looking Statements

Certain statements contained in this document, including
statements regarding events and financial trends that may affect our
future operating results, financial position and cash flows, may
constitute forward-looking statements within the meaning of the federal
securities laws. These statements are based on our assumptions and
estimates and are subject to risk and uncertainties. You can identify
these forward-looking statements by the use of words like "strategy",
"expects", "plans", "believes", "will", "estimates", "intends",
"projects", "goals", "targets", and other words of similar meaning. You
can also identify them by the fact that they do not relate strictly to
historical or current facts. We wish to caution you that such
statements contained are just predictions or opinions and that actual
events or results may differ materially. The forward-looking statements
contained in this document are made as of the date hereof and we assume
no obligation to update the forward-looking statements, or to update
the reasons why actual results could differ materially from those
projected in the forward-looking statements. Where applicable, we claim
the protection of the safe harbour for forward-looking statements
provided by the (United States) Private Securities Litigation Reform
Act of 1995.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for UGD-V
Date: 2016/01/22
Closing Price: 0.15

TEL: 416.866.8157          Mr. Joseph Del Campo
jdelcampo@unigoldinc.com   Interim President & CEO
www.unigoldinc.com         Unigold Inc.
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1602400028TS11602401133-07435320160125