Source	Filing Services Canada
Date	01/25/2016
Time	08:15:15 AM

Company	 GOLDEN PREDATOR MINING CORP.
Title	Golden Predator Recovers 79.9 to 90.8% Gold from 3 Aces Preliminary Test 
Samples





    CDNX Symbol: GPY











Press Release




SOURCE: Filing Services Canada
Date: 01/25/2016
Time: 11:15:00

Company: GOLDEN PREDATOR MINING CORP
Title:Golden Predator Recovers 79.9 to 90.8% Gold from 3 Aces Preliminary Test 
Samples (GPY - TSXV) 
TSXV SYMBOL: GPY


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Golden Predator Mining Corp
TSXV SYMBOL: GPY
Monday, January 25, 2016 - 11:15 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/golden-predator-recovers-799-908-gold-3-aces-
preliminary-test-samples

Golden Predator Recovers 79.9 to 90.8% Gold from 3 Aces Preliminary Test Samples


Vancouver, BC, January  (FSCwire) - Golden Predator Mining Corp. (TSX.V: GPY) 
(the Company) is pleased to announce results from its preliminary process 
testing in advance of its announced bulk sampling program expected to begin in 
Q1-2016 at the 3 Aces project, Yukon. Gold recovery has been calculated at 
90.8% from a 108kg composite rock sample processed through a conventional 
gravity recovery facility. A second sample consisting of 61.5kg of material 
composited from rejects from previous Rotary Air Blast (RAB) drilling (1) 
returned a calculated gold recovery of 79.9%. The calculated head grades of 
these samples, based on the sampling methodology described below, are 82.03 g/t 
Au and 40.49 g/t respectively.



We are encouraged by the very high recoveries indicated in these preliminary 
processing tests, said Janet Lee-Sheriff, CEO of Golden Predator. The numbers 
are consistent with expectations, and coincide with results from previous 
metallurgical work (2) completed on quartz vein material obtained from the same 
3 Aces location. These tests have enabled us to source an economical processing 
plant to be used for the upcoming bulk sampling program. We look forward to 
refining our understanding of the mineralization, its distribution and its 
potential for recovery from the high grade veins present at 3 Aces.



Preliminary processing was conducted on two composite samples; a 108kg grab 
sample composite of vein material collected from the bulk sample zone at 3 Aces 
during the RAB drill program and a 61.5kg composite of RAB drilling rejects 
prepared by ALS Minerals (ALS) Whitehorse sample prep facility. Both samples 
were shipped to Mt. Baker Mining and Metals (MBMM), LLC in Bellingham 
Washington, USA for individual processing through a 1 ton per hour (20 tpd) 
demonstration plant consisting of a 6 x 10 jaw crusher, a 16 x 12 hammer mill 
and a single 4 x 8 shaker table. The shaker table produces 2 gravity 
concentrates and tailings.





The following table shows the weight and gold content for each concentrate as 
well as for the tails.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-recovers-799-908-gold-3-aces-
preliminary-test-samples






* Panned gold concentrates were treated with hot nitric acid (HNO3) following 
magnetic separation of trace amounts of magnetite, removing approximately 17% 
of associated gangue minerals by weight.

** Tailings weights are calculated using the original sample weight



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-recovers-799-908-gold-3-aces-
preliminary-test-samples






* Panned gold concentrates were treated with hot nitric acid (HNO3) following 
magnetic separation of trace amounts of magnetite, removing approximately 17% 
of associated gangue minerals by weight.

** Tailings weights are calculated using the original sample weight



Further testing of the tails included screening to size with each resulting 
size fraction being assayed for gold. The results of this testing is shown 
below. These results indicate that the initial crushing and grinding process 
may sufficiently grind the feed without the need for further classification or 
re-grinding.



To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/golden-predator-recovers-799-908-gold-3-aces-
preliminary-test-samples






* Calculated Weight 



** Weight is the combined weight of the +8 fraction combined with the -8+20 
fraction; resulting in a +20 mesh composite sample; fractions were combined to 
provide enough material for assay



*** Gold value estimated from ICP21 overlimit, as not enough sample material 
remained to run Au-GRA21



Sampling Methodology, Quality Control and Analysis



The composite of quartz vein material was collected by Mike Burke, Chief 
Geologist for Golden Predator. These samples were stored in a secured facility 
until preparation and weighing prior to shipping to the MBMM facility. Reject 
material from previous RAB drilling was stored at the ALS facility in 
Whitehorse until being shipped directly to the MBMM facility.



All samples were securely stored at the MBMM facility until the arrival of 
Company personnel who supervised the processing. Concentrates and 
tailings-splits produced from the sample processing were analyzed by ALS at 
their Reno, Nevada facility. Gold was using ALS Au-ICP21 method, and any 
overlimit samples (>10 g/t Au) were fire assayed using ALS AU-GRA21 method. 
Prior to ALS analysis, Company Chairman, William Sheriff, facilitated the 
processing of an additional panned gold concentrate, whereby precision weights 
were attained using a Mettler balance, after magnetic separation and treatment 
with nitric acid, at the University of Texas, Dallas, Geoscience Laboratory. 
The sample head grades were calculated by adding back the recovered gold 
(grams) to the total contained gold (grams) in all sample fractions as 
determined from ALS assays, divided by the total sample composite weight 
(tonnes).



The technical content of this news release has been reviewed and approved by 
Mike Burke, P. Geo, Chief Geologist and a Qualified Person as defined by 
National Instrument 43-101. 



Golden Predator Mining Corp.



Golden Predator Mining Corp. holds the Brewery Creek Project, a past producing 
heap leach gold mine with a preliminary economic assessment delivered in Q4 
2014. The Company also holds the 3 Aces Gold Project in the Yukon, which it 
continues to delineate and test, and the Castle West Project in Nevada.



(1) Golden Predator Mining Corp., News Release dated September 14, 2015.



(2) Golden PredatorMining Corp., News Release dated December 2, 2014







For additional information:



Janet Lee-Sheriff 

Chief Executive Officer 

(214) 304-9552

info@goldenpredator.com (mailto:info@goldenpredator.com)

www.goldenpredator.com (http://www.goldenpredator.com)



Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in policies of the TSX Venture Exchange) accepts responsibility for 
the adequacy or accuracy of this release. No stock exchange, securities 
commission or other regulatory authority has approved or disapproved the 
information contained herein. This press release contains projections and 
forward-looking information that involve various risks and uncertainties 
regarding future events. Such forward-looking information can include without 
limitation statements based on current expectations involving a number of risks 
and uncertainties and are not guarantees of future performance. There are 
numerous risks and uncertainties that could cause actual results and the 
Companys plans and objectives to differ materially from those expressed in the 
forward-looking information. Actual results and future events could differ 
materially from those anticipated in such information. These and all subsequent 
written and oral forward-looking information are based on estimates and 
opinions of management on the dates they are made and are expressly qualified 
in their entirety by this notice. Except as required by law, the Company 
assumes no obligation to update forward-looking information should 
circumstances or management's estimates or opinions change.




To view this press release as a PDF file, click onto the following link:
http://fscwire.com/sites/default/files/news_release_pdf/Goldenpredator01252016.p
df
Source: Golden Predator Mining Corp (TSX Venture:GPY) 
http://www.goldenpredator.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2016 Filing Services Canada Inc.