Source	Marketwire
Date	01/26/2016
Time	05:46:43 AM

Company	 RIVERSIDE RESOURCES INC.
Title	Riverside Resources Inc.: Exploration Work Defines Gold Zone and Drilling 
Targets at the Tajitos Gold Project, Sonora, Mexico





    CDNX Symbol: RRI











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Riverside Resources Inc.

TSX VENTURE SYMBOL: RRI
OTC PINK SYMBOL: RVSDF
FRANKFURT SYMBOL: R99

January 26, 2016

Riverside Resources Inc.: Exploration Work Defines Gold Zone and Drilling 
Targets at the Tajitos Gold Project, Sonora, Mexico


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Jan. 26, 2016) - Riverside 
Resources Inc. ("Riverside" or the "Company") (TSX VENTURE:RRI)(OTC 
PINK:RVSDF)(FRANKFURT:R99) is pleased to announce that exploration work 
continues with partner Centerra Gold Inc. ("Centerra") at the Company's Tajitos 
Gold Project (the "Project") in Sonora, Mexico. The initial exploration program 
funded by Centerra Gold over the past two months included extensive continuous 
rock chip channel sampling and stream sediment sampling. Drill targets are 
being defined with further work now underway and up to 4,500 metres in drilling 
expected to follow.

Results so far are favourable and provide indications of potential large width, 
near surface, gold mineralization reminiscent of some of the mined gold bodies 
of Sonora. Six rock chip channel lines totaling nearly 3 kilometres (2,991 
metres) of continuous sampling were completed at Tajitos. A total of 997, three 
metre long continuous chip-channel rock samples were collected. Assays returned 
Au values ranging from less than 0.005 g/t to 12 g/t gold including sixty seven 
three-metre long samples containing more than 0.2 g/t gold. Several intervals 
of gold mineralization occur in faults and shear zones with quartz-sericite 
pyrite (QSP) alteration and minor quartz veining, with an extensive chlorite to 
propyllitic halo. The QSP zones with anomalous gold are up to 70 metres wide on 
surface and contain elevated values of lead, tellurium, arsenic, and antimony. 
Mineralization occurs on the footwall and hangingwall of the low angle faults 
with wide alteration zones. Trenching is now underway to sample covered areas 
along the major fault and shear trend.

The channel sample lines generally run perpendicular to the strike of the 
several kilometre long shear zone. The sampling on northeast trending traverses 
evaluated approximately 4,000 metres of sheared and altered rock along 6 sample 
lines in an area 2 km wide. Strongly silicified rhyolitic volcanic rocks with 
well-developed sericite and oxidized pyrite were encountered in all 6 sample 
lines. The mineralized relationship at Tajitos is very similar to 
mineralization style known at Fresnillo's Noche Buena Mine located 35 
kilometres to the NW along the major shear zone trend.

The initial stream sediment sampling program was completed on the Tejo 
concession with Riverside collecting 46 stream sediment samples over an area 
approximately 4 km in diameter. Sample results range from less than 0.005 to 
0.528 g/t Au. Nineteen samples had values greater than 0.02 ppm and identify an 
area 2.8 km long by 1.3 km wide along an approximate east-west trend in the 
southern portion of the Tejo concession. Elevated values of arsenic, lead, 
antimony, and cobalt are associated with the gold bearing samples similar to 
the mineralization at Tajitos in outcrop. Additional stream sediment sampling 
is underway to find the limit of the gold anomaly to the north.

Riverside's President and CEO, John-Mark Staude, stated: "We are delighted to 
have Centerra funding 100% of the program and quickly progressing with 
additional field work and preparations ahead of anticipated trenching and 
drilling."

An induced polarization (IP) geophysical survey was completed over 2 target 
areas in Tajitos and moderate resistivity and chargeability anomalies were 
detected and possibly identify a major feeder fault zones with stronger 
alteration and partially oxidized and disseminated pyrite as seen in 
outcropping mineralization.

Two areas in the Tejo claim were evaluated with IP lines testing features seen 
in the airborne magnetic data. The Tejo zone is a gravel covered valley with 
very few bedrock exposures and the IP was designed to identify faults and 
alteration features similar to those seen in Tajitos. An area of higher 
resisitivity with elevated chargeability occurs coincident with magnetic highs. 
The anomalous zone is at least 1 km by 600 metres. The magnetic high which 
corresponds with the IP zone trends southeast and is approximately 5 km long by 
2 km wide. Additional IP survey lines are planned to further define the 
anomalous zone.

A drill program at Tajitos and Tejo is planned to begin in the first quarter of 
2016 as part of the ongoing exploration program funded by Centerra Gold. An 
initial 1,000 to 1,500 metres of diamond core drilling is planned on two target 
areas at Tajitos to test coincident geologic, geochemical, and geophysical 
targets. An additional 3,000 metres of RC drilling is planned for the Tejo area 
to identify bedrock below the gravel cover and partially test the coincident 
magnetic high and IP anomaly.

About the Tajitos Project:

The approx. 60km2 Tajitos Gold Project is located in the heart of the 
Sonora-Mojave Megashear Gold Belt. The Project was acquired by Riverside from a 
private owner and is owned by Riverside 100% with no underlying royalties. 
Previous work programs completed by Riverside confirmed high grade gold values 
in quartz veins and anomalous values of gold in fault zones with only minor 
quartz veining. Riverside results from rock chip geochemical sampling on the 
vein systems at Tajitos range from less than 0.005 to 34.74 g/t gold and from 
less than 0.1 to 383 g/t silver over widths ranging from 0.5 to 3.0 metres. 
Sampling outside the veins in silicified and sericite altered volcanic and 
intrusive rocks have returned gold values from less than 0.005 to 1.02 g/t.

Qualified Person & QA/QC:

The scientific and technical data contained in this news release pertaining to 
the Tajitos Gold Project was reviewed by Greg Myers, PhD, P.Geo, - VP, 
Exploration, a non-independent qualified person to Riverside Resources, who is 
responsible for ensuring that the geologic information provided in this news 
release is accurate and who acts as a "qualified person" under National 
Instrument 43-101 Standards of Disclosure for Mineral Projects.

Reported samples were taken to Hermosillo, Mexico where Bureau Veritas 
Laboratory Group's (BV) mineral division crushed and pulverized each sample. 
Gold fire assays with AA finish were analysed in BV Hermosillo laboratory. The 
rejects remained with BV in Hemosillo while the pulps were transported to BV 
ISO 9001-2008 certified laboratory in Vancouver, BC, Canada for multi-element 
ICP analysis. A QA/QC program was implemented as part of the sampling 
procedures for the exploration program. Standard and blank samples were 
randomly inserted into the sample stream prior to being sent to the laboratory.

ON BEHALF OF RIVERSIDE RESOURCES INC.,

Dr. John-Mark Staude, President & CEO

Certain statements in this press release may be considered forward-looking 
information. These statements can be identified by the use of forward looking 
terminology (e.g., "expect"," estimates", "intends", "anticipates", "believes", 
"plans"). Such information involves known and unknown risks -- including the 
availability of funds, the results of financing and exploration activities, the 
interpretation of exploration results and other geological data, or 
unanticipated costs and expenses and other risks identified by Riverside in its 
public securities filings that may cause actual events to differ materially 
from current expectations. Readers are cautioned not to place undue reliance on 
these forward-looking statements, which speak only as of the date of this press 
release.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Riverside Resources Inc.
John-Mark Staude
President, CEO
(778) 327-6671
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

or

Riverside Resources Inc.
Joness Lang
VP, Corporate Development
(778) 686-6836
Fax: (778) 327-6675
info@rivres.com
www.rivres.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=555643374