Source	MARKET NEWS
Date	01/12/2017
Time	06:40:22 AM

Company	 Tudor Gold Corp.
Title	American Creek 
Reports On Jv Partner Tudor Gold'





    CDNX Symbol: TUD











Press Release





AMERICAN CREEK RESOURCES LTD ("AMK-V;ACKRF-0")
TUDOR GOLD CORP.  ("TUD-V")
- American Creek Reports On Jv Partner Tudor Gold's 539 G/t Ag
- With 2.82 G/t Au And 1.97% Zn Electrum Project Bulk Sample

American Creek Resources Ltd. ("American Creek") is pleased to
report that Tudor Gold Corp. ("Tudor") has released the final results
of the 2016 exploration program conducted at the Electrum Project JV
located in northwest BC's "Golden Triangle" near Stewart.

Background

The Electrum project is a 60:40 joint venture between Tudor (as
operator) and American Creek. The Electrum property is located directly
between the past producing Silbak Premier mine some 25 Km south and
Pretium Resources' Brucejack deposit some 20 Km to the north (currently
under development with production targeted for 2017). Within that same
area are several other past producing mines as well as new projects
undergoing exploration. One small area of the Electrum property itself
includes the site of the historic East Gold mine which was mined by
hand between 1939 and 1965, and which produced 3,816 oz of gold and
2,442 oz of silver from 45 tons of hand selected ore (BC Ministry of
Mines Assessment Report 30206); mining operations ceased with the
unfortunate and untimely death of the mine operator. More recently, the
Scottie Gold mine operated from 1981 to 1985 approximately five
kilometers from the Electrum property. The current owners of the
Scottie Gold mine, Rotation Minerals Ltd., note on their website that
the mine "milled vein material averaging 16.20 g/t gold, producing
2,967,748 grams of gold (95,426 ounces gold) from 183,147 tonnes of
mineralization" (these historic production values have not been
independently verified).

Tudor was attracted to the Electrum property by the presence of
a complex system of mineralized fault structures within which are
networks of gold and silver bearing quartz veins. The gold and silver
typically occurs within these veins as electrum, a naturally occurring
amalgam of both metals.

The complexity of both the fault structures and the vein
networks make it very difficult to specifically target the veins of
gold and silver bearing materials using conventional surface-based
exploration techniques such as diamond drilling or magnetotelluric
surveys. With that in mind, Tudor set out to develop an exploration
program which includes sub-surface exploration techniques and which
targets mineralization rather than just vein structures. In this way,
Tudor will gain a better and more useful understanding of the overall
geology of the property.

The success of the East Gold mine demonstrates that the
mineralized fault material is accessible using conventional underground
mining systems and practices. The cost of either rehabilitating the
East Gold mine or opening new adits is, however, prohibitive at this
stage of the project's development. Tudor is instead focused on a
scalable bulk sampling program which would, if warranted, conclude with
the development of an open-cut mine of sufficient size to generate both
a return for shareholders and financing for further exploration on the
property. As with other properties in this area of the "Golden
Triangle", an open-cut mine could be carried out in association with
related conventional underground mining.

Tudor's exploration programs and long-term planning take into
account two of the key economic advantages of the Electrum property; it
is within 4 kilometers of a power-line, and the property is adjacent to
an established haul road leading to the bulk terminal and deep-water
port at Stewart.

2016 Exploration Program

The exploration program achieved the following three goals set
for the 2016 field season:

//st

Diamond drilling aimed at furthering the exploration work previously
carried out by American Creek,

Trench sampling of a newly discovered mineralized surface exposure in what
is now referred to as the "New Blast Zone", and

Collection and analysis of a 4 tonne bulk sample from the New Blast Zone.

//et

In addition to the work aimed at achieving these goals, work
carried out during the 2016 field season included the construction of
temporary (removable) bridges and the stabilization and improvement of
road access to ensure safe and efficient access to the property.

2016 Diamond Drilling

Nineteen drill holes totaling 1,406 meters were completed. A
total of 1492 core samples were collected and assayed. The 2016
drilling program was carried out to extend and expand on the drilling
programs carried out by American Creek in previous years. The results
of the 2015 American Creek drilling program included these findings
previously released by American Creek:

//st
Drill Hole   From (m)  To (m)  Interval (m)  Gold (g/t)  Silver (g/t)
EL15-02           9.0    10.0           1.0        1.04          78.0
EL15-03          16.5    17.5           1.0        6.09         242.0
EL15-04          32.0    33.0           1.0        6.76          38.0
EL15-05          28.0    29.0           1.0        1.31         189.0
35.0    36.0           1.0        6.93          62.0
EL15-07          13.0    14.0           1.0       14.65          22.0
14.0    15.0           1.0        6.59         461.0
35.0    36.0           1.0        3.47          58.0
EL15-08           1.0     2.0           1.0        1.05          89.0

//et

One of the key goals of both the American Creek and Tudor
drilling programs was to confirm that mineralized exposures visible on
the surface carried on at depth below the surface. The results of these
drilling programs do suggest that, as expected, mineralization carries
on at depth.

Of particular interest, holes TG16-13-UTM, TG16-14-UTM, and
TG16-15-UTM reveal sub-surface mineralization in the area generally
below the newly identified "New Blast Zone". Because of the complexity
of the fault structures in this area, however, Tudor is currently
unable to state with the certainty required by NI 43-101 that the
sub-surface mineralization confirms the presence of an unbroken,
continuous zone of mineralization linking these drill holes with the
surface mineralization.

Trench Sampling

As noted in the Tudor news release issued September 12, 2016, a
trenching program was carried out on the New Blast Zone. The program
targeted a vein system which is infilled with a fine-grained blackish,
blue-grey mineralization. The structure includes wide sharp edged
quartz fragments in a foliated sulphide-quartz-carbonate matrix; the
sulphides are pyrite, pyrrhotite, with thin galena/silver seams.

Twelve representative specimens were collected across the vein
structure. Assays of those specimens yielded averages of 3,461.92 grams
(111.30 oz) silver per tonne and 2.24 grams gold per tonne. Complete
results of the trench sampling may be found in the noted news release
on the Tudor website at www.tudor-gold.com.

Four Tonne Bulk Sample

Following the success of the trench sampling program, a 4 tonne
bulk sample was collected from the New Blast Zone. The sample was
collected utilizing localized blasting resulting in an exposed face of
approximately 120 square meters, and a total rubble pile of
approximately 600 cubic meters, from which was selected approximately 4
tonnes of representative material.

The collected bulk material was then crushed to a size of "3
inch minus" using a crusher at a quarry in Mission, British Columbia.
The crushed material was then provided to ALS Global's metallurgical
laboratory ('ALS') in Kamloops, BC for metallurgical processing and
testing. The processing included the use of rod and ball mill grinding
followed by both floatation and gravity separation. The resultant
material was then analyzed in four separate test runs over four
consecutive days. The overall results of the analysis are set out in
the following table:

//st
Au (g/t)           Ag (g/t)      PB (%)      Zn (%)      Sulphur (%)
2.82                    539        1.96        1.97             13.8

//et

As with the trenching program, Tudor is very encouraged by
these results. A complete description of the processing and testing
employed by ALS will be added to the Tudor website at
www.tudor-gold.com.

2017 Exploration Program

Tudor is satisfied that the results of the 4 tonne bulk sample
program, together with all previous exploration work on the property,
justifies scaling up the exploration program on the Electrum property.
Tudor is satisfied that all of these results justify long-term planning
based on an assumption that currently known mineralization on the
property has the potential to support a modest sized open-cut mine that
can be scaled up as further exploration dictates.

Subject to obtaining all necessary permits and financing, the
current plan for the 2017 field season is to carry out the largest
possible bulk sample program along with an as yet to be determined
amount of diamond drilling.

The anticipated bulk sample program will utilize commercially
available mining equipment commonly used in open-pit mining. Blasting
will be carried out with the use of track-mounted drills, and on-site
crushing will be carried out with the use of track-mounted crushers. It
is anticipated that crushed, mineralized material will be hauled to
Stewart and from there it will be transported to an appropriate smelter
for final processing.

Walter Storm, Tudor President and CEO, stated: "We are very
pleased with the results of the work on the Electrum this summer. Not
only have we confirmed and increased the known mineralized gold and
silver zones, we have also begun to develop a much better understanding
of the geology of the property and we are satisfied that we have a
proper basis for expanding our exploration program."

Darren Blaney, American Creek CEO stated: "We are very pleased
with what Walter and the Tudor team have accomplished with this initial
program. The bulk sample results are very encouraging and indicate the
future potential of the property. We are very much looking forward to
2017."

The Qualified Person for the Electrum property and the
technical data in this new release is James McCrea, P. Geo. for the
purposes of National Instrument 43-101.

American Creek also has other projects in BC's prolific "Golden
Triangle" including the Treaty Creek Project which is a joint venture
between Tudor, American Creek and Teuton Resources Corp. and the 100%
owned Dunwell property package which encompasses the past producing
Dunwell gold/silver mine.

Information relating to the Corporation is available on its
website at www.americancreek.com.

Cautionary Statements regarding Forward-Looking Information:
Certain statements contained in this press release constitute
forward-looking information. These statements relate to future events
or future performance. The use of any of the words "could", "intend",
"expect", "believe", "will", "projected", "estimated" and similar
expressions and statements relating to matters that are not historical
facts are intended to identify forward-looking information and are
based on the Company's current belief or assumptions as to the outcome
and timing of such future events. Actual future results may differ
materially.

All statements including, without limitation, statements relating
to the potential mineralization and geological merits of the Electrum
property and other future plans, objectives or expectations of the
Company are forward looking statements that involve various risks and
uncertain ties. There can be no assurance that such statements will
prove to be accurate and actual results and future events could differ
materially from those anticipated in such statements. Important factors
that could cause actual results to differ materially from the Company's
plans or expectations include risks relating to the actual results of
current exploration activities, fluctuating gold prices, possibility of
equipment breakdowns and delays, exploration cost overruns,
availability of capital and financing, general economic, market or
business conditions, regulatory changes, timeliness of government or
regulatory approvals and other risks detailed herein and from time to
time in the filings made by the Company with securities regulators. The
Company expressly disclaims any intention or obligation to update or
revise any forward-looking statements whether as a result of new
information, future events or otherwise except as otherwise required by
applicable securities legislation.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.































TSX Venture closing price for TUD-V
Date: 2017/01/11
Closing Price: 0.67

TEL:  403 752-4040    Kelvin Burton
E-mail: info@americancreek.com
Internet: www.americancreek.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1701100017TS11701100925-06381820170112