Source	Marketwire
Date	01/17/2017
Time	09:55:17 AM

Company	 WESTHAVEN VENTURES INC.
Title	Westhaven Expands Zone of Gold-Silver Mineralization at Shovelnose; Drills 
161m of 0.23 g/t Gold, including 5m of 1.69 g/t Au





    CDNX Symbol: WHN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Westhaven Ventures Inc.

TSX VENTURE SYMBOL: WHN

January 17, 2017

Westhaven Expands Zone of Gold-Silver Mineralization at Shovelnose; Drills 161m 
of 0.23 g/t Gold, including 5m of 1.69 g/t Au


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Jan. 17, 2017) - Westhaven Ventures 
Inc. (TSX VENTURE:WHN) is pleased to report drill results from its 19,012 
hectare Shovelnose gold property, located within the prospective Spences Bridge 
Gold Belt (SBGB), approximately 30 km south of Merritt, British Columbia. This 
drill program consisted of 4 holes totaling 725 metres of diamond drilling.

The objective of this second drill program was to determine the geometry of 
gold mineralization evident in the southern portion of the Alpine Zone, by 
drilling an east-west oriented fence line of holes to follow up on hole 16-02 
drilled earlier this year which intersected 16.7g/t gold (Au) over 0.5 metres ( 
news release dated July 27th, 2016). It was determined that the southern 
portion of the Alpine Zone consists of a +135-metre thick southeast dipping 
gold bearing silicified rhyolite tuff extending downward from bedrock surface. 
The orientation of quartz veining within this unit suggests that a deeper 
feeder source dips to the west and extends over 800 metres northward along 
strike. The style of mineralization is similar to that found at the Tower Zone, 
situated approximately 400 metres west.

Management intends to test for a potentially higher-grade feeder zone at depth 
by conducting a deep- penetrating IP survey and follow-up drilling in 2017.

Highlights of the program include:

/T/

----------------------------------------------------------------------------
Drill Hole        From (m)      To (m)   Length (m)     Au (g/t)    Ag (g/t)
----------------------------------------------------------------------------
SN16-06                 30         164          134         0.17         1.2
----------------------------------------------------------------------------
incl:                   48          50            2         1.48         3.8
----------------------------------------------------------------------------
also incl:              49          50            1         2.63         6.9
----------------------------------------------------------------------------
also incl:           124.2       124.4          0.2         8.27        76.6
----------------------------------------------------------------------------
also incl:             127         128            1         2.60        25.2
----------------------------------------------------------------------------
SN16-07                 21       182.1          161         0.23         1.4
----------------------------------------------------------------------------
incl:                   57          62            5         0.81           3
----------------------------------------------------------------------------
also incl:              59          61            2         1.45         3.8
----------------------------------------------------------------------------
also incl:             177         182            5         1.69          11
----------------------------------------------------------------------------
also incl:             178         180            2         3.58          24
----------------------------------------------------------------------------
SN16-08                 59         100           41         0.25         1.2
----------------------------------------------------------------------------
incl:                   64          65            1         3.33           8
----------------------------------------------------------------------------
SN16-09                 29         210          181         0.11         0.8
----------------------------------------------------------------------------
incl:                   81          83            2         1.16         0.9
----------------------------------------------------------------------------

/T/

"With each successive drill program at Shovelnose we continue to find better 
gold grades locally within greater thicknesses of gold mineralized sections. In 
2016, we drilled 9 holes for a total of 1,902 metres. This resulted in 
intercepts of 161 metres grading 0.23 g/t Au and 119.6m of 0.27 g/t Au with 
higher grade intervals including 16.7 g/t Au over 0.5 metres and 4.95 g/t Au 
over 0.6 metres. We have outlined a large mineralized system that remains open 
in all directions including potential for higher grade mineralization. 
Shovelnose's advantaged location near infrastructure and its proximity to the 
Coquihalla Highway significantly enhances its potential. We are keen to expand 
mineralization at the Alpine Zone and drill other untested, high priority 
targets in this large and favourable gold system. Westhaven is currently fully 
financed and preparing for a drill program in the near term as we have 
high-priority drill-ready targets," stated Shaun Pollard, Director and CFO.

Shovelnose Gold Property Overview

To date Westhaven has completed 40 drill holes (2 were abandoned in overburden) 
for a cumulative total of 6,371 metres, in four separate target areas. There is 
evidence of a significant mineralized alteration system within the property 
where float samples grading 119 g/t Au and 273 g/t Ag, veins in trenches 
grading 66 g/t Au, as well as wide low grade alteration zones typical of 
epithermal gold deposits have been discovered. Please refer to the Shovelnose 
Project page on our website for further information. 
http://westhavenventures.com/projects/shovelnose-gold/details/

The Spences Bridge Gold Belt (SBGB)

Westhaven owns a 100%-interest in over 29,000 hectares within the prospective 
SBGB, which is situated within a geological and structural setting similar to 
other significant epithermal gold-silver systems. It is close to existing 
transportation arteries allowing for cost-effective exploration. The SBGB is a 
110-kilometre northwest-trending belt of intermediate to felsic volcanic rocks 
dominated by the Cretaceous Spences Bridge Group. Westhaven has been working on 
the SBGB since 2011 and believes these relatively underexplored volcanic rocks 
are highly prospective for epithermal style gold and silver mineralization.

On behalf of the Board of Directors

WESTHAVEN VENTURES INC.

Gareth Thomas, Director

About Westhaven Ventures Inc.

Westhaven Ventures Inc. is a Canadian based exploration company focused on the 
acquisition and exploration of prospective resource properties. Westhaven is 
focused on advancing its Shovelnose and Prospect Valley gold projects in 
British Columbia. Westhaven trades on the TSX Venture Exchange under the ticker 
symbol WHN. For further information, please call 604-681-5558 or visit 
Westhaven's website at www.westhavenventures.com.

Qualified Person Statement

L. John Peters, P.Geo., who is a Qualified Person within the context of 
National Instrument 43-101 has read and takes responsibility for this release.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Westhaven Ventures Inc.
604-681-5558
www.westhavenventures.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=586119295