Source	CANADA NEWSWIRE
Date	01/20/2017
Time	04:33:23 AM

Company	 Algold Resources Ltd.
Title	Algold Reports More High-Grade Results and Discovery of a New Parallel
Structure at Tijirit's Eleonore





    CDNX Symbol: ALG











Press Release




" BC-AlGold-ResultsEleonor   01-20 1679
News release via CNW Telbec, Montreal 514-878-2520 -ME-

Attention Business Editors:
^Algold Reports More High-Grade Results and Discovery of a New Parallel
Structure at Tijirit's Eleonore@

MONTREAL, Jan. 20, 2017 /CNW Telbec/ - ALGOLD RESOURCES LTD. (TSXV: ALG)
(the "Corporation") today announced the final assay results from its Phase II
- 10,000-meter drilling campaign, as well as the results of a regional rock
chip sampling program carried out on the Tijirit property ("Tijirit") in
Mauritania. Results have not only continued to demonstrate the high-grade
nature of the Eleonore zones, but have also revealed a new mirror-image
structure 500 meters west and parallel to Eleonore, further expanding the
overall footprint of the mineralized area. (Figure 1)
Highlights
<<

--  Hole T16RC137 (Eleonore North) - 3 m (at) 4.69 g/t Au, extending the
mineralization 100 meters below the surface (Figure 2).

--  Hole T16DD013 (Eleonore North) - 4.65 m (at) 3.24 g/t Au (Figure 2), on a
parallel structure situated about 50 meters west of the intersect 5.0 m
(at) 6.6 g/t Au in hole T16RC045.

--  Hole T16DD012 (Eleonore Central) - 5.53 m (at) 1.14 g/t Au - in a parallel
structure about 100 meters east of the high-grade 6 m (at) 9.31 g/t Au
intersection in hole T16RC032. The core section analyzed displayed
visible gold in a quartz vein, which was left in the half-cut core
section at Algold Tijirit's camp for further reference. The low-grade
nature of the intersection, while visible gold was observed, is typical
of the type of deposit with nugget effect, such as Eleonore. (Ref. Photo
1) (Figure 3)

--  A grab sample from a newly uncovered zone (West Zone) returned 9.29 g/t
Au from the bottom of a pit situated 1.5 kilometers northeast of RC
holes 12TRC048 and 12TRC049, which returned 3.0 m (at) 1.9 g/t Au and 2.0 m
(at) 2.71 g/t Au, respectively.

--  A grab sample from the south of Eleonore South returned 43.9 g/t Au,
while a grab sample from an area to the north of the Nour vein returned
an outstanding 102.5 g/t Au. These samples suggest that the Eleonore
structure remains open along strike.
>>
The Phase II 10,000-meter drilling program was completed on December 8,
2016 and included 8,583 meters of reverse-circulation ("RC") and 1,147 meters
of diamond drilling ("DDH") drilling, for a total 20,411 meters.
As of January 16, 2017, Algold was in receipt of all assays from the two
phases, representing 20,411 meters of drilling on the Tijirit property. The
Corporation sent 5,790 samples for analysis as part of Phase II and a total of
11,780 samples from both phases of the 2016 exploration program.
The Eleonore North zone has now been defined by drilling over 1,000
meters along strike to a vertical depth of up to 150 meters below the surface.
The Eleonore Central zone has been defined over 670 meters and up to a
vertical depth of 180 meters, while the Eleonore South zone has been defined
over 1,200 meters and to a vertical depth of 200 meters. All three zones are
open along strike and at depth over a three-kilometer strike (Figure 1). This
is in addition to the Nour discovery announced on November 1, 2016.
These results, combined with the 10,000 meters drilled from Phase I and
the 35,000-meter drilling program carried out by previous operators, will
serve as the basis for the resource estimate to be published in the coming
weeks.


Table 1: New Assay Result Highlights - Phase II Reverse-Circulation Drilling 
Program
--------------------------------------------------------------------------------
----

Hole ID                        Prospect                               
East           North              From                    To            
Vertical             Average        Width(x)(x)(x)                              
Comments
-------                        
--------                                                                        
                                                                                
                         --------

UTM                            UTM                        (m)             
(m)            Depth(x) (m)        Grade(x)(x) (g/t Au)                (m)
---                            ---                        ---             
---             ---------        ----------------                ---

T16DD013                              Eleonore North                        
482325          2250550               48.1                   
52.75                  39.0            3.24        4.65     Including 2.4 m 
(at) 6.0 g/
t Au
--------                                    --------------                  
------         -------              ----                  -----                 
----           ----        ----  -------------------------

T16RC137                              Eleonore North                        
482463          2250556                108                   
113.0                  87.0            1.16         5.0
--------                              --------------                        
------          -------                ---                   
-----                  ----            ----         ---

125                          128.0                    100.0             
4.69                3.0    40 m depth extension
---                          -----                    -----             
----                ---    --------------------

T16DD012                             Eleonore Central                       
482278          2249849               53.0                   
58.53                  40.0            1.14        5.53     Wide mineralized 
zone
with VG (Photo 1)
--------                                  ----------------                  
------         -------              ----                  -----                 
----           ----        ----  ----------------------

T16RD080                              Eleonore South                        
481797          2248915             196.25                  
199.35                 158.0            2.57         3.1     Extends 
mineralization
100 m below last
intercept
--------                                    --------------                  
------         -------            ------                 ------                
-----           ----         ---  -----------------------

T16RC138                              Eleonore West                         
481147          2248641                 43                    
46.0                  34.5            1.87         3.0     New zone 400 m west 
of
previously defined
mineralization
--------                                     -------------                  
------         -------               ---                   ----                 
----           ----         ---  -----------------------
(x) Vertical depth of intersection below RL collar.

(x)(x) Weighted average grade, composite based on a minimum grade of 0.3 g/t Au 
with an internal dilution of 0.005 g/t Au over 2 m and an edge grade of 0.25
g/t permitted.

(x)(x)(x) Down-hole length (believed to be close to true width)

No capping of higher values has been applied.

Note: Complete assay results are available on Algold's website (www.algold.com).

Exploration - New Parallel Structure
Geological mapping and rock chip sampling carried out during the drill
program in the fourth quarter 2016 identified a potential three-kilometer-long
anomalous structure, not yet drill-tested, located approximately 600 meters
west of the currently defined Eleonore mineralization. Results from a grab
sample returned 9.29 g/t Au from this new discovery (Figure 1). This structure
had not been previously identified, being covered by a northeast trending
sandbar. This area will be further drilled and delineated in Q1 of 2017 with
results potentially leading to a significant increase in the total Eleonore
resource.
In addition, another visible gold bearing quartz vein has been located
200 meters southwest of previous drilling at Eleonore South. This vein, also
in an area of abundant transported sand cover, was identified in Q4 of 2016,
but not drill tested. The sample is currently being analyzed by the screen
fire assay method, the original fire assay returned 43.9 g/t Au. It highlights
the significant potential for further high-grade discoveries along strike from
those currently defined. (Figure 1).
A 102.5 g/t Au sample was returned from another new area approximately
eight kilometers north of the Nour vein in the north of the Tijirit
exploration permit. The location of this rock chip sample result once again
highlights the potential of Algold's permitted land in Mauritania.



Sample
ID                     Zone           Easting        Northing          g/t 
Au        Lith1                Description
UTM             UTM
---                                      ---             ---

A08449 Eleonore South                   481409           2248282          
43.9     QzST        Quartz boulders with sulphide
up to 40 cm

A11943 Eleonore West                    481547           2250132          
9.29      Qz         Smoky quartz with oxides of
Fe(FeOx)+ Box works

A11950 New Vein North                   488144           2265926         
102.5      Qz         Quartz vein with CuO + FeO
(cavity and fractures) + VG
------           --------------         ------          -------        
-----           --- ---------------------------

Detailed geological descriptions of all mineralized zones can be found on
Algold's website (www.algold.com) and on SEDAR (www.sedar.com) in the report
entitled "Algold 43-101 Technical Report: Tijirit Maiden Mineral Resources
Estimates for the Tijirit Gold Project in Mauritania".
Quality Assurance / Quality Control (QA/QC)Analytical work for drill core
and chips, geochemical samples and rock chip samples is being carried out at
the independent ALS Laboratories Ltd. in Loughrea, Co. Galway, Ireland, an ISO
17025 (2005) Certified Laboratory. Samples are stored at the Corporation's
field camps and put into sealed bags until delivered by a geologist to the ALS
preparation laboratory in Nouakchott, Mauritania, where samples are prepared
for shipping. Until the end of 2015, samples were analyzed at ALS facility in
Bamako, Mali. Since early 2016, samples are analyzed at ALS in Ireland.
Samples are logged in the tracking system, weighed, dried and finely crushed
to better than 70%, passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A
split of up to 1,000 g is taken and pulverized to better than 85%, passing a
75-micron (Tyler 200 mesh) screen, and a 50-gram split is analyzed by fire
assay with an AA finish. Blanks, duplicates and certified reference material
(standards) are being used to monitor laboratory performance during the
analysis.
This press release has been reviewed for accuracy and compliance under
National Instrument 43-101 by André Ciesielski, DSc., PGeo., Algold Resources
Ltd Lead Consulting Geologist and Qualified Person, and Alastair Gallaugher,
C.Geo. (Chartered Geologist and Fellow of the Geological Society of London),
BSc. Geology, Algold's Exploration Manager in Mauritania, Qualified Persons as
defined by NI 43-101 Standards of Disclosure for Mineral Projects. André
Ciesielski has further approved the scientific and technical disclosure in the
news release.
ABOUT ALGOLDAlgold Resources Ltd is focused on the exploration and
development of gold deposits in West Africa. The board of directors and
management team are seasoned resource industry professionals with extensive
experience in the exploration and development of world-class gold projects in
Africa.
Algold is the operator of all of its exploration licenses in Mauritania.
Algold owns 100% of Tijirit, which represents an area of more than 1,000 km2,
situated approximately 25 kilometers southeast of the Tasiast gold mine as
well as the Akjout properties, which were acquired from Gryphon Minerals
(Australia) through a transaction completed earlier in 2016. Exploration is
being carried out on the Eleonore, Sophie I, Sophie II-III and Lily zones. The
Kneivissat property is 90% owned by Algold and the Legouessi property is being
managed through a 51% earn-in interest agreement with Caracal Gold LLC. Algold
can earn up to a 90% interest in the Legouessi exploration permit (reference
Algold's press release dated October 10, 2013 for more details), however,
Caracal has the right to participate in the joint venture at either 51% or 75%
by funding its share of expenditures.
CAUTIONARY LANGUAGE REGARDING FORWARD-LOOKING INFORMATION
This press release contains and refers to forward-looking information
based on current expectations. All other statements other than statements of
historical fact included in this release are forward-looking statements (or
forward-looking information). The Corporation's plans involve various
estimates and assumptions and its business is subject to various risks and
uncertainties. For more details on these estimates, assumptions, risks and
uncertainties, see the Corporation's most recent Annual Information Form 
andmost recent Management Discussion and Analysis on file with the Canadian
provincial securities regulatory authorities on SEDAR at www.sedar.com. These
forward-looking statements are made as of the date hereof and there can be no
assurance that such statements will prove to be accurate. Forward-looking
statements are subject to significant risks and uncertainties, and actual
results and future events could differ materially from those anticipated in
such statements. Accordingly, readers should not place undue reliance on
forward-looking statements that are included herein, except in accordance with
applicable securities laws.

SOURCE Algold Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/January2017/20/c2714.html

-0-                           01/20/2017
/For further information: Algold Resources Ltd., 1320, boul. Graham,
bureau 132, Mont-Royal, Quebec, H3P 3C8, www.algold.com; Francois Auclair
M.Sc., PGeo, President & Chief Executive Officer, f.auclair(at)algold.com, +1
(514) 889 5089; Alex Ball, Executive VP, Finance and Corporate Development,
a.ball(at)algold,com, +1 (647) 919 2227/
/Web Site: www.algold.com /
(ALG.)

CO:  Algold Resources Ltd.
ST:  Quebec, Mauritania
IN:  MNG
SU:  SVY

-30-