Source	MARKET NEWS
Date	01/24/2017
Time	05:23:02 AM

Company	 Troymet Exploration Corp.
Title	Reviews Redhill Plans





    CDNX Symbol: TYE











Press Release





Reviews Redhill Plans --->@NEWS RELEASE
TROYMET EXPLORATION CORP ("TYE-V")
- Reviews Redhill Plans

Troymet Exploration Corp. ("Troymet" or the Company") is pleased
to review its plans for advancing the Redhill project in British
Columbia. Troymet's 2016 diamond drilling program on the Alpha prospect
intersected two zones of significant copper, volcanogenic massive
sulphide ("VMS") mineralization in hole RH16-04, drilled in Horizon 2:

* Upper Zone: 0.72% copper and 6.5 g/t silver over 6.5 metres,
starting at a depth of 5.1 metres

* Lower Zone: 0.64% copper and 1.5% zinc over 2.0 metres from
206.3-208.3 metres downhole

Lower Zone

Figure 1 shows the limited extent of drilling in the Lower Zone
mineralization. Figure 2, a vertical longitudinal section, shows the
distribution of the various mineralized drill intercepts in the Lower
Zone. The geometry of the mineralization indicates the better
mineralization lies below the levels drill tested to date. High-grade
copper mineralization was intersected in the deepest holes (RH16-04 and
RH-06-25) and this mineralization is open along strike and at depth. As
well, the mineralized zone has not been drill tested to the northwest
or southeast. A transient EM conductor is associated with the
mineralization. With the exception of one shallow test (hole 85-2) this
conductor is untested/undrilled to the southeast, and remains a
significant target. The mineralization is crudely bedded and
dips/plunges steeply west. The topography also drops off to the west
into a prominent valley with the result that the mineralization is
expected to remain or come close to surface. Troymet has identified a
characteristic blue quartz eye pyroclastic porphyry that is associated
with the VMS mineralization. The recognition of this important unit
will guide future exploration.

Upper Zone

Hole RH16-04 collared in the Upper Zone which grades 0.72% copper
and 6.5 g/t silver over 6.5 metres, starting at a depth of 5.1 metres
(Figure 3). The mineralization extends upwards an additional 3.8 metres
to the base of the casing; however, because of poor recovery in this
interval, a reportable mineralized interval cannot be calculated.
Secondary copper mineralization is present in the wall of the drill
platform (Figure 4). The total downhole width of the mineralized zone
is estimated to be in excess of 11.5 metres. This significant new
discovery of VMS mineralization carries strong copper mineralization
over a significant interval with samples up to 1.5% copper over 0.5
metres (Table 1).

The Upper Zone copper mineralization occurs on or just within the
lower boundary of Horizon 3 (Figure 1). Horizon 3 is unexplored. The
mineralization is open along strike and to depth and there are no
nearby drill holes. As previously reported (News Release of July 25,
2016) breccia boulders, several of which contain massive sulphide
blocks, have been found within Horizon 3 in a locale that is
approximately 200 metres northwest of where hole RH16-04 was collared.
The newly discovered Upper Zone together with the breccia boulders
indicate significant discovery potential in Horizon 3.

Historically, three stacked prospective volcanic sequences are
recognized (Horizons 1, 2 and 3), dipping steeply to the west. Stacked
mineralized horizons are a common feature in VMS mining camps
world-wide. Within a camp, deposits may occur laterally at a discrete
time - stratigraphic interval or vertically stacked through hundreds of
metres of volcanic stratigraphy. The distribution of TEM conductors in
the Alpha prospect indicates there are additional prospective sequences
that have not yet been mapped/recognized.

2017 Plans

Troymet's exploration has resolved the form and configuration of
the VMS mineralization in the Lower Zone, and identified high potential
drill targets. As well, the Company discovered a new copper VMS zone
(Upper Zone) in a prospective volcanic sequence that has not been
explored. The Upper Zone is shallow and amenable to inexpensive follow
up exploration. Troymet plans to strip, map, trench and sample the
Upper Zone mineralization prior to further drilling. As well, Troymet
plans borehole electromagnetic surveys ("EM") of holes drilled in 2016
to identify off-hole conductors and conductors too deep to have been
detected by surface EM and shallow penetrating airborne EM surveys.

Troymet plans to test the Beta target, when drilling resumes. As
previously reported (News Release of October 25, 2016), the Company has
identified a new, large chargeability anomaly associated with the 40
mho Beta target which is located on a 550 metre long EM conductor. The
Beta target Is located 200 metres south of borehole S83-4 (2.54%
copper, 2.78% zinc, 77.0 g/t Ag, and 0.37 g/t Au over 7.75 metres).

The gold-in-soil anomaly is aligned along the northeast edge of a
resistivity high, in a magnetic low, in a diorite intrusive. Troymet
plans overburden trenching of the better anomalies prior to drilling.

Table 1. Copper intercepts in the Upper Zone

//st
Hole    From (m) To (m) Width (m) Cu (ppm) Ag (ppm)               Notes
RH16-04      1.3    2.1       0.8      850     2.58 Incomplete recovery
RH16-04      2.1    3.1         1      862     5.54 Incomplete recovery
RH16-04      3.1    4.1         1      363    10.55 Incomplete recovery
RH16-04      4.1    5.1         1     1995     8.38 Incomplete recovery
RH16-04      5.1    5.6       0.5    15000    14.65
RH16-04      5.6    6.1       0.5     3390     3.97
RH16-04      6.1    6.6       0.5     5750     5.05
RH16-04      6.6    7.1       0.5     8900     6.29
RH16-04      7.1    7.6       0.5     4860     4.70
RH16-04      7.6    8.1       0.5    10000    10.35
RH16-04      8.1    8.6       0.5     5470     4.28
RH16-04      8.6    9.1       0.5     9060     9.44
RH16-04      9.1    9.6       0.5    10900     7.16
RH16-04      9.6   10.1       0.5     7230     6.97
RH16-04     10.1   10.6       0.5     4330     4.16
RH16-04     10.6   11.1       0.5     6610     5.61
RH16-04     11.1   11.6       0.5     2480     2.63
//et

Widths presented in Table 1 are downhole core lengths; true widths
cannot be reliably estimated at this time. Core samples were analysed
at ALS Global, Vancouver.

Qualified Persons

All technical data, as disclosed in this press release, has been
verified by Kieran Downes, Ph.D., P.Geo., a Qualified Person as defined
by National Instrument 43-101.

About Troymet Exploration Corp.

Troymet Exploration Corp. is a junior exploration company with a
solid treasury and with projects in British Columbia (Redhill and
Golden Eagle), Manitoba (McClarty Lake) and Utah (Wildcat). Troymet
operates the Wildcat, Redhill and Golden Eagle projects. Hudbay
Minerals Inc. is the operator of the McClarty Lake joint venture and
must contribute $1,151,052 in joint venture expenditures before Troymet
is required to fund its participating interest. Troymet retains a 2%
net smelter returns royalty (NSR) on the Key property, British
Columbia, which was sold to New Gold Inc. in 2013.

TROYMET EXPLORATION CORP.
Kieran Downes, Ph.D., P.Geo.,President, CEO & Director

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release.

This news release contains certain forward-looking information.
All statements included herein, other than statements of historical
fact, are forward-looking information and such information involves
various risks and uncertainties. In particular, this news release
contains forward-looking information in respect of: the Redhill
Project, including the possible exploration and development of the
Redhill Project; the exploration potential and analogous deposit
potential of the Redhill Project; future data analysis, sampling plans
and exploration plans on the Redhill Project, including potential
stripping, mapping, trenching and sampling, potential EM surveys, and
the resumption of exploration on identified targets; the timing for
exploration and drilling on the Redhill Project; exploration targets
and the potential of such exploration targets; and the ability and the
timeframe within which the Redhill Project can be advanced. There can
be no assurance that such information will prove to be accurate, and
actual results and future events could differ materially from those
anticipated in such information. This forward-looking information
reflects Troymet's current beliefs and is based on information
currently available to Troymet and on assumptions Troymet believes are
reasonable. These assumptions include, but are not limited to: the
current share price of Troymet's common shares and the ability to raise
future equity financing, if needed, at prices acceptable to Troymet;
Troymet's current and initial understanding and analysis of the Redhill
Project; the ability of Troymet to discover viable exploration targets
and the results of exploration on the Redhill Project; the cost of
exploration, including stripping, mapping, trenching, sampling, EM
surveys and drilling, on the Redhill Project; Troymet's general and
administrative costs remaining constant; and the market acceptance of
Troymet's business strategy.

Forward-looking information is subject to known and unknown risks,
uncertainties and other factors which may cause the actual results,
level of activity, performance or achievements of Troymet to be
materially different from those expressed or implied by such
forward-looking information. Such risks and other factors may include,
but are not limited to: the early stage development of Troymet and its
projects, and in particular, the Redhill Project; general business,
economic, competitive, political and social uncertainties; capital
market conditions and market prices for securities, junior market
securities and mining exploration company securities; commodity prices;
the actual results of current exploration and development or
operational activities; competition; changes in project parameters as
plans continue to be refined; accidents and other risks inherent in the
mining industry; lack of insurance; delay or failure to receive board
or regulatory approvals; changes in legislation, including
environmental legislation, affecting Troymet; timing and availability
of external financing on acceptable terms; conclusions of economic
evaluations; and lack of qualified, skilled labour or loss of key
individuals. A description of other assumptions used to develop such
forward-looking information and a description of other risk factors
that may cause actual results to differ materially from forward-looking
information can be found in Troymet's disclosure documents on the SEDAR
website at www.sedar.com. Troymet does not undertake to update any
forward-looking information except in accordance with applicable
securities laws.

TSX Venture closing price for TYE-V
Date: 2017/01/20
Closing Price: 0.02

TEL:  250-729-0453  Troymet Exploration Corp.
EMAIL:  info@troymet.com
INTERNET:  www.troymet.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1702300004TS11702300591-05220420170124