Source	Marketwire
Date	01/24/2017
Time	05:01:43 AM

Company	 TROYMET EXPLORATION CORP.
Title	Troymet Reviews Redhill Plans





    CDNX Symbol: TYE











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Troymet Exploration Corp.

TSX VENTURE SYMBOL: TYE

January 24, 2017

Troymet Reviews Redhill Plans


NANAIMO, BRITISH COLUMBIA--(Marketwired - Jan. 24, 2017) - Troymet Exploration 
Corp. (TSX VENTURE:TYE) ("Troymet" or the Company") is pleased to review its 
plans for advancing the Redhill project in British Columbia. Troymet's 2016 
diamond drilling program on the Alpha prospect intersected two zones of 
significant copper, volcanogenic massive sulphide ("VMS") mineralization in 
hole RH16-04, drilled in Horizon 2:

- Upper Zone: 0.72% copper and 6.5 g/t silver over 6.5 metres, starting at a 
depth of 5.1 metres
- Lower Zone: 0.64% copper and 1.5% zinc over 2.0 metres from 206.3-208.3 
metres downhole

Lower Zone

Figure 1 shows the limited extent of drilling in the Lower Zone mineralization. 
Figure 2, a vertical longitudinal section, shows the distribution of the 
various mineralized drill intercepts in the Lower Zone. The geometry of the 
mineralization indicates the better mineralization lies below the levels drill 
tested to date. High-grade copper mineralization was intersected in the deepest 
holes (RH16-04 and RH-06-25) and this mineralization is open along strike and 
at depth. As well, the mineralized zone has not been drill tested to the 
northwest or southeast. A transient EM conductor is associated with the 
mineralization. With the exception of one shallow test (hole 85-2) this 
conductor is untested/undrilled to the southeast, and remains a significant 
target. The mineralization is crudely bedded and dips/plunges steeply west. The 
topography also drops off to the west into a prominent valley with the result 
that the mineralization is expected to remain or come close to surface. Troymet 
has identified a characteristic blue quartz eye pyroclastic porphyry that is 
associated with the VMS mineralization. The recognition of this important unit 
will guide future exploration.

Upper Zone

Hole RH16-04 collared in the Upper Zone which grades 0.72% copper and 6.5 g/t 
silver over 6.5 metres, starting at a depth of 5.1 metres (Figure 3). The 
mineralization extends upwards an additional 3.8 metres to the base of the 
casing; however, because of poor recovery in this interval, a reportable 
mineralized interval cannot be calculated. Secondary copper mineralization is 
present in the wall of the drill platform (Figure 4). The total downhole width 
of the mineralized zone is estimated to be in excess of 11.5 metres. This 
significant new discovery of VMS mineralization carries strong copper 
mineralization over a significant interval with samples up to 1.5% copper over 
0.5 metres (Table 1).

The Upper Zone copper mineralization occurs on or just within the lower 
boundary of Horizon 3 (Figure 1). Horizon 3 is unexplored. The mineralization 
is open along strike and to depth and there are no nearby drill holes. As 
previously reported (News Release of July 25, 2016) breccia boulders, several 
of which contain massive sulphide blocks, have been found within Horizon 3 in a 
locale that is approximately 200 metres northwest of where hole RH16-04 was 
collared. The newly discovered Upper Zone together with the breccia boulders 
indicate significant discovery potential in Horizon 3.

Historically, three stacked prospective volcanic sequences are recognized 
(Horizons 1, 2 and 3), dipping steeply to the west. Stacked mineralized 
horizons are a common feature in VMS mining camps world-wide. Within a camp, 
deposits may occur laterally at a discrete time - stratigraphic interval or 
vertically stacked through hundreds of metres of volcanic stratigraphy. The 
distribution of TEM conductors in the Alpha prospect indicates there are 
additional prospective sequences that have not yet been mapped/recognized.

2017 Plans

Troymet's exploration has resolved the form and configuration of the VMS 
mineralization in the Lower Zone, and identified high potential drill targets. 
As well, the Company discovered a new copper VMS zone (Upper Zone) in a 
prospective volcanic sequence that has not been explored. The Upper Zone is 
shallow and amenable to inexpensive follow up exploration. Troymet plans to 
strip, map, trench and sample the Upper Zone mineralization prior to further 
drilling. As well, Troymet plans borehole electromagnetic surveys ("EM") of 
holes drilled in 2016 to identify off-hole conductors and conductors too deep 
to have been detected by surface EM and shallow penetrating airborne EM surveys.

Troymet plans to test the Beta target, when drilling resumes. As previously 
reported (News Release of October 25, 2016), the Company has identified a new, 
large chargeability anomaly associated with the 40 mho Beta target which is 
located on a 550 metre long EM conductor. The Beta target Is located 200 metres 
south of borehole S83-4 (2.54% copper, 2.78% zinc, 77.0 g/t Ag, and 0.37 g/t Au 
over 7.75 metres).

The gold-in-soil anomaly is aligned along the northeast edge of a resistivity 
high, in a magnetic low, in a diorite intrusive. Troymet plans overburden 
trenching of the better anomalies prior to drilling.

Table 1. Copper intercepts in the Upper Zone

/T/

----------------------------------------------------------------------------
Hole        From (m)   To (m) Width (m)  Cu (ppm)  Ag (ppm)            Notes
----------------------------------------------------------------------------
Incomplete
RH16-04          1.3      2.1       0.8       850      2.58         recovery
----------------------------------------------------------------------------
Incomplete
RH16-04          2.1      3.1         1       862      5.54         recovery
----------------------------------------------------------------------------
Incomplete
RH16-04          3.1      4.1         1       363     10.55         recovery
----------------------------------------------------------------------------
Incomplete
RH16-04          4.1      5.1         1      1995      8.38         recovery
----------------------------------------------------------------------------
RH16-04          5.1      5.6       0.5     15000     14.65
----------------------------------------------------------------------------
RH16-04          5.6      6.1       0.5      3390      3.97
----------------------------------------------------------------------------
RH16-04          6.1      6.6       0.5      5750      5.05
----------------------------------------------------------------------------
RH16-04          6.6      7.1       0.5      8900      6.29
----------------------------------------------------------------------------
RH16-04          7.1      7.6       0.5      4860      4.70
----------------------------------------------------------------------------
RH16-04          7.6      8.1       0.5     10000     10.35
----------------------------------------------------------------------------
RH16-04          8.1      8.6       0.5      5470      4.28
----------------------------------------------------------------------------
RH16-04          8.6      9.1       0.5      9060      9.44
----------------------------------------------------------------------------
RH16-04          9.1      9.6       0.5     10900      7.16
----------------------------------------------------------------------------
RH16-04          9.6     10.1       0.5      7230      6.97
----------------------------------------------------------------------------
RH16-04         10.1     10.6       0.5      4330      4.16
----------------------------------------------------------------------------
RH16-04         10.6     11.1       0.5      6610      5.61
----------------------------------------------------------------------------
RH16-04         11.1     11.6       0.5      2480      2.63
----------------------------------------------------------------------------

/T/

Widths presented in Table 1 are downhole core lengths; true widths cannot be 
reliably estimated at this time. Core samples were analysed at ALS Global, 
Vancouver.

Qualified Persons

All technical data, as disclosed in this press release, has been verified by 
Kieran Downes, Ph.D., P.Geo., a Qualified Person as defined by National 
Instrument 43-101.

About Troymet Exploration Corp.

Troymet Exploration Corp. is a junior exploration company with a solid treasury 
and with projects in British Columbia (Redhill and Golden Eagle), Manitoba 
(McClarty Lake) and Utah (Wildcat). Troymet operates the Wildcat, Redhill and 
Golden Eagle projects. Hudbay Minerals Inc. is the operator of the McClarty 
Lake joint venture and must contribute $1,151,052 in joint venture expenditures 
before Troymet is required to fund its participating interest. Troymet retains 
a 2% net smelter returns royalty (NSR) on the Key property, British Columbia, 
which was sold to New Gold Inc. in 2013.

TROYMET EXPLORATION CORP.

Kieran Downes, Ph.D., P.Geo., President, CEO & Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

This news release contains certain forward-looking information. All statements 
included herein, other than statements of historical fact, are forward-looking 
information and such information involves various risks and uncertainties. In 
particular, this news release contains forward-looking information in respect 
of: the Redhill Project, including the possible exploration and development of 
the Redhill Project; the exploration potential and analogous deposit potential 
of the Redhill Project; future data analysis, sampling plans and exploration 
plans on the Redhill Project, including potential stripping, mapping, trenching 
and sampling, potential EM surveys, and the resumption of exploration on 
identified targets; the timing for exploration and drilling on the Redhill 
Project; exploration targets and the potential of such exploration targets; and 
the ability and the timeframe within which the Redhill Project can be advanced. 
There can be no assurance that such information will prove to be accurate, and 
actual results and future events could differ materially from those anticipated 
in such information. This forward-looking information reflects Troymet's 
current beliefs and is based on information currently available to Troymet and 
on assumptions Troymet believes are reasonable. These assumptions include, but 
are not limited to: the current share price of Troymet's common shares and the 
ability to raise future equity financing, if needed, at prices acceptable to 
Troymet; Troymet's current and initial understanding and analysis of the 
Redhill Project; the ability of Troymet to discover viable exploration targets 
and the results of exploration on the Redhill Project; the cost of exploration, 
including stripping, mapping, trenching, sampling, EM surveys and drilling, on 
the Redhill Project; Troymet's general and administrative costs remaining 
constant; and the market acceptance of Troymet's business strategy.

Forward-looking information is subject to known and unknown risks, 
uncertainties and other factors which may cause the actual results, level of 
activity, performance or achievements of Troymet to be materially different 
from those expressed or implied by such forward-looking information. Such risks 
and other factors may include, but are not limited to: the early stage 
development of Troymet and its projects, and in particular, the Redhill 
Project; general business, economic, competitive, political and social 
uncertainties; capital market conditions and market prices for securities, 
junior market securities and mining exploration company securities; commodity 
prices; the actual results of current exploration and development or 
operational activities; competition; changes in project parameters as plans 
continue to be refined; accidents and other risks inherent in the mining 
industry; lack of insurance; delay or failure to receive board or regulatory 
approvals; changes in legislation, including environmental legislation, 
affecting Troymet; timing and availability of external financing on acceptable 
terms; conclusions of economic evaluations; and lack of qualified, skilled 
labour or loss of key individuals. A description of other assumptions used to 
develop such forward-looking information and a description of other risk 
factors that may cause actual results to differ materially from forward-looking 
information can be found in Troymet's disclosure documents on the SEDAR website 
at www.sedar.com. Troymet does not undertake to update any forward-looking 
information except in accordance with applicable securities laws.

- 30 -

CONTACT INFO:

Troymet Exploration Corp.
Investor Relations
250-729-0453
info@troymet.com
www.troymet.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=586460445