Source	MARKET NEWS
Date	01/10/2018
Time	06:56:01 AM

Company	 Golden Predator Mining Corp.
Title	Continues to Expand Gold Zones at 3 Aces Project





    CDNX Symbol: GPY











Press Release





Continues to Expand Gold Zones at 3 Aces Project --->@NEWS RELEASE
GOLDEN PREDATOR MINING CORP.  ("GPY-V")
- Continues to Expand Gold Zones at 3 Aces Project

Golden Predator Mining Corp. (the "Company" or "Golden Predator")
reports the results of 42 Reverse Circulation (RC) drill holes
completed in 2017 at the 3 Aces Project in southeastern Yukon. Initial
drilling is reported from the Diamonds Zone along with the Hearts/Clubs
Corridor. All areas encountered encouraging results and will see
continued drilling in 2018. The final 43 RC holes completed in 2017
will be reported separately.

Significant results include:

* Hole 3A17-287 intersected 2.29 m of 35.72 g/t gold from a depth
of 5.33 m, including 0.76 m of 105.5 g/t gold (Lower Hearts);

* Hole 3A17-250 intersected 0.76 m of 10.15 g/t gold from a depth
of 35.05 m (Queen of Clubs Vein); and,

* Hole 3A17-251 intersected 1.53 m of 5.86 g/t gold from a depth
47.24 m, and3.05 m of 4.17 g/t gold from a depth of 153.92 m, including
0.76 m of 11.75 g/t gold (Diamonds Zone).

3 Aces Drill Results Overview

Gold mineralization ranging from anomalous to high grade was
encountered in 30 of the 42 holes drilled across the Central Core,
including the Hearts, Clubs and the Diamonds Zones. High-grade quartz
veins continue to be encountered along with an increasing abundance of
disseminated and stockwork occurrences. These two types of
mineralization are integral to the Company's conceptual geological
model.

The Hearts-Club Corridor is presently defined as a 1.6 km
structural zone with upper and lower northwest trending shear zones
extending from the Ace of Hearts to the Ten of Clubs. The Hearts-Clubs
Corridor drill program in 2017 was designed to test and establish
continuity along shear zones hosting gold-in-quartz veins. A second
lower parallel shear zone, within the Hearts-Clubs Corridor was also
established and confirmed with visible gold along a 450 m segment.
These moderately dipping shear zones host quartz veins with gold and
arsenopyrite. Additional drilling will test the projected extension of
the Corridor of mineralization for an additional 1.2 km along trend to
the northwest in 2018.

Despite the difficult drilling conditions caused by the intense
fracturing and shearing encountered in several areas, drilling has
continued to confirm high-grade gold mineralization and near surface
bulk tonnage type mineralization from the Diamonds Zone, the Clubs Zone
and the lower Hearts Zone. Core drilling will be implemented across the
3 Aces Project in 2018 to better address the structural conditions
inherent to the Hearts-Clubs Corridor while allowing the Company to
expand its focus on deeper drill targets.

To view 3 Aces Project location and drilling maps please visit:


http://www.goldenpredator.com/_resources/news/NR-801-Combined-Maps.pdf

"We are pleased to see mineralization continuing in all zones
tested across the Central Core Area and encouraged by the structural
intensity of the shear zone which displays continuity along the western
and northern portions of the Clubs-Hearts Corridor," said Janet
Lee-Sheriff, Chief Executive Officer. 'structurally complex and
intensely fractured rock are excellent hosts for gold mineralization
and we look forward to drilling the Corridor with diamond core in
2018."

Diamonds: Initial Drill Program

Initial drilling of the Diamonds Area, located 1.8 km north and
over 400 m higher in elevation, from the Central Spades area, included
8 reconnaissance holes designed to test favorable stratigraphy and
structure as indicated by surface mapping. Spread out over more than
700 m, 6 of 8 holes were completed to target depths ranging from 240 m
to 350 m. Hole 3A17-251 encountered anomalous gold clustered throughout
the hole with the best interval of 3.05 m of 4.17 g/t gold including
0.76 m of 11.75 g/t gold. Hole 3A17-262 intersected 5.33 m of 1.03 g/t
gold along with several anomalous zones lower in the hole. 5 of the 6
holes (246, 251, 254, 262, 265) drilled to target depth intersected
multiple intervals of )1.0 g/t gold as well as more extensive zones of
anomalous gold. In addition to intersecting gold mineralization,
important structural and stratigraphic information was gathered from
the first drill program at the Diamonds Zone.

Hearts-Clubs Corridor: Lower Hearts

Drilling included 10 RC holes with mineralization encountered in 8
holes. All holes were stopped short of target depth due to intense
fracturing and challenging RC drilling conditions encountered in the
Heart/Clubs Corridor. Late season ice combined with extreme topography
resulted in all holes being collared from existing roads with average
depth of the sampled holes of 56.6 m. Drilling was situated along 400 m
of strike and represents the westerly most drilling to date on the
project.

Hole 3A17-287 returned several intervals greater than 1.0 g/t gold
highlighted by 1.53 m of 53.0 g/t gold from a depth of 5.33 m which
includes 0.76 m of 105.5 g/t gold. Hole 3A17-291 intersected 8.38 m of
0.41 g/t bottoming at 14.48 m in mineralization, hole 3A17-293
intersected 16.0 m of 0.41 g/t from a depth of 14.48 m, and hole
3A17-294 intersected 9.14 m of 0.57 g/t gold from a depth of 6.86 m.
Initial drilling of the lower structural zone at the Hearts zone
confirmed gold mineralization along the lower shear zone. Two holes
were lost in the first 10 m with no sample returned.

Heart/Clubs Corridor: Clubs Zone
Fifteen RC drill holes were completed in an area 200 m by 300 m
with 8 of these not reaching target depths due to intense fracturing,
shearing and related gouge zones along the mineralized horizon in the
Hearts/Clubs Corridor. 13 of the 15 sampled holes encountered anomalous
gold.

Hole 3A17-267 intersected 6.09 m of 0.49 g/t gold from a depth of
21.34 m and a second lower zone of 10.67 m of 0.75 g/t gold highlighted
by a 0.76 m interval of 7.49 g/t gold. Hole 3A17-269 intersected
sporadic mineralization throughout the hole with 16.76 m of 0.34 g/t
gold from 19.05 m and 2 separate 0.76 m intervals of 7.65 g/t and 4.73
g/t gold from 115.06 m and 143.26 m respectively. Similarly hole
3A17-282 intersected 9.91 m of 0.89 g/t gold at a depth of 31.24 m and
hole 3A17-284 intersected 9.14 m of 1.06 g/t gold at a depth of 22.86
m.

Queen of Clubs Vein

The Queen of Clubs Vein is located 400 m northeast of the
Hearts/Clubs Corridor with 6 holes drilled in 2017. Drill hole 3A17-250
has more than doubled the known strike of the Queen of Clubs vein by 34
m, to at least 65 m, having intersected 0.76 m of 10.15 g/t gold at a
depth of 35.05 m. No further significant results were reported, and
further analysis suggests that the target is open at depth but either
pinches out or has been offset laterally along strike.

3 Aces Project, Yukon

The 3 Aces Project is an orogenic gold project consisting of 1,734
claims covering 357 km (35,700 ha) in southeast Yukon. The Company has
focused exploration on the 13.5 km2 Central Core Area, a broad
gold-in-soil anomaly, where numerous orogenic gold-bearing quartz veins
have been discovered. Exploration over the past 18 months has
systematically advanced the project by establishing: (1) high gold
grades can be reliably sampled, (2) gold mineralization is in
predictable stratigraphic locations, and (3) gold grades have robust
continuity within the recognized controlling features. Results have led
to a geological model that predicts extensive lateral and vertical
continuity of the 3 Aces mineral system. The Company is now developing
a strategy to establish this continuity between the Central Core Area
and the Sprogge property 6 to 8 kilometers to the south.

The Project is located along the all-season Nahanni Range Road
that was recently announced as being a part of the $360 million
Federally and Yukon funded, Yukon Resource Gateway Project. Golden
Predator operates under an Exploration Agreement with the Ross River
Dena Council and the Liard First Nation, and a Class 4 Mining Land Use
Permit issued by the Yukon Government.

Geology

The 3 Aces Property is in the Selwyn Basin; a lenticular belt of
sedimentary rocks that extends across the Yukon. The property is
underlain by interbedded clastic and carbonate sedimentary rocks of the
Hyland Group, the basal unit of the Selwyn Basin. Polyphase fold and
fault systems overprint the stratigraphy, structurally preparing the
rocks with pathways for the mineralizing fluids. Gold with minor pyrite
and arsenopyrite are in late, brittle faults formed within an
extensional zone between two regional dextral faults.

Mineralized hydrothermal fluids migrated through these faults
during late phases of brittle faulting. Gold on the property is
associated with extensive argillic, iron carbonate, and limonitic
alteration zones that broadly overprint the stratigraphy and early
structural fabrics.

The current exploration strategy on the 3 Aces Property is based
on the metallogenic models developed for orogenic gold deposits. The
primary characteristics of the 3 Aces Property that make the orogenic
gold model an appropriate analogy for the property are: (1) mid- to
upper-crustal level crack-seal style quartz veins, (2) high competency
contrast between lithologies, (3) crustal-scale regional faults that
provide pathways for deeply sourced fluids, and (4) a prolonged
polyphase deformation history.

Sampling Methodology, Quality Control and Assurance

All analyses for the drill samples from the program were performed
by ALS with sample preparation in BC, Kamloops, BC and assaying in
North Vancouver, BC. Drill samples were analyzed using a 50 g fire
assay with atomic absorption finish (Au-AA26). If the procedure
returned a value of 2.0 g/t gold or greater it is re-run using a 2kg
screen metallic gold method (Au-SCR24). Refer to the Company's news
release dated July 10th, 2017 for a complete discussion of sampling
methods, quality control and assurance.

The technical content of this news release has been reviewed and
approved by Mark Shutty, CPG, a Qualified Person as defined by National
Instrument 43-101 and an employee of the Company.

Golden Predator Mining Corp.

Golden Predator Mining Corp. is a well-financed gold exploration
company focused on its high-grade orogenic gold-in-quartz 3 Aces
Project in Canada's Yukon. The Company also holds 100% of the advanced
Brewery Creek Project in Yukon, Canada. With proven management and an
experienced technical team, the Company is well positioned for growth.

For additional information:

Janet Lee-Sheriff

Chief Executive Officer

(604)260-0289

info@goldenpredator.com

www.goldenpredator.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release. No
stock exchange, securities commission or other regulatory authority has
approved or disapproved the information contained herein. This press
release contains forward-looking information that involve various risks
and uncertainties regarding future events. Such forward-looking
information can include without limitation statements based on current
expectations that the private placement will complete as described
herein, that the Project will advance through permitting and
feasibility. Actual results and future events could differ materially
from those anticipated in such information. These and all subsequent
written and oral forward-looking information are based on estimates and
opinions of management on the dates they are made and are expressly
qualified in their entirety by this notice. Except as required by law,
the Company assumes no obligation to update forward-looking information
should circumstances or management's estimates or opinions change.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1800900037TS11800900941-06530820180110