Source	CANADA NEWSWIRE
Date	01/24/2018
Time	05:03:27 AM

Company	 Atlantic Gold Corporation
Title	Atlantic Gold reports additional results from the Phase 3 Resource
Expansion drill program at Fifteen Mile Stream





    CDNX Symbol: AGB











Press Release




" BC-Atlantic-Gold-results   01-24 2346
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Atlantic Gold reports additional results from the Phase 3 Resource
Expansion drill program at Fifteen Mile Stream@

HIGHLIGHTS INCLUDE:Egerton Maclean: 20m (at) 21.9g/t Au from 35m (incl 1m (at)
419g/t Au) Plenty: 3m (at) 52.9g/t Au from 18m (incl 1m (at) 156g/t Au), 2m (at)
10.25g/t Au from 27m and 16m (at) 1.05g/t Au from 9m
INFILLING, AND IDENTIFYING EXTENSIONS TO KNOWN MINERALIZATION AT FIFTEEN
MILE STREAM
VANCOUVER, Jan. 24, 2018 /CNW/ - Atlantic Gold Corporation (TSX-V: AGB)
("Atlantic" or the "Company") is pleased to report further assay results
received from the Phase 3 Resource Expansion drilling program at the Fifteen
Mile Stream gold deposit.
Fifteen Mile Stream is located approximately 57km northeast of the
central processing facility at Touquoy and is readily accessible by highway.
Fifteen Mile Stream's current measured and indicated mineral resources stand
at 10.59 million tonnes at 1.33 g/t Au for 452,000 oz. at 0.35g/t cut-off
grade. Inferred mineral resources amount to 6.64 million tonnes at 1.12 g/t Au
for 240,000 oz. at 0.35g/t cut-off grade (see Company announcement July 21,
2017)1.
As per previous news releases the objectives of the Phase 3 Resource
Expansion drilling program are to identify additional gold resources
immediately peripheral to those resources previously defined at Fifteen Mile
Stream and Cochrane Hill. At Cochrane Hill and at Fifteen Mile Stream -
particularly at the Hudson and Plenty zones, upgrade previously defined
inferred resources to measured and indicated categories, and seek additional
new resources within the 350m gap between the Plenty and Egerton MacLean zones
at Fifteen Mile Stream.
(1)The Mineral Resource
estimate for Fifteen Mile
Stream is quoted at a cut-
off grade of 0.35g/t. It has
an effective date of July 20,
2017 and was prepared as part
of a technical report in
accordance with NI 43-101 by
Mr. Neil Schofield, a
principal of FSSI (Australia)
Pty Ltd, released on
September 1, 2017 on SEDAR.

2018 drilling has recently re-commenced with three drilling rigs
presently operating at the Plenty deposit. Twenty holes for 2217m have so far
been completed. Up until the end of 2017 a total of 185 holes for 21,000m had
been drilled at Fifteen Mile Stream. Holes are generally drilled on 25m x 20m
centres, although for the first-pass drilling along the 350m gap between
Plenty and Egerton MacLean holes have been drilled on 50m-spaced sections.
Assay results have now been received from a further 36 holes, with about
two-thirds of all assays expected from this program having now been received.
Assays reported here from Egerton MacLean and Hudson, the eastern and western
deposits respectively along the Fifteen Mile Stream anticline, are from widely
distributed holes testing the peripheries of these deposits as presently
known. Best result is the shallow high grade intersection (20m (at) 21.9g/t
including 1m (at) 419g/t) towards the western end of Egerton MacLean which, at a
vertical depth of only 30m, infills an information gap between surface and
mineralization intersected in deeper holes beneath.
At Plenty, infill and step-out drilling westwards on 25m-spaced sections
is underway to enable definition of measured and indicated resources, as
upgrade from existing inferred resources. Drilling continues to outline a
steep, northerly dipping, tabular zone of gold mineralization over more than
300m strike length, defined both by wide intersections of moderate grades (eg.
16m (at) 1.05g/t) and more isolated, narrow high grade intervals (eg. 1m (at)
202g/t). At this time mineralization appears to be more vein-hosted than that
along the hinge of the Fifteen Mile Stream anticline at Hudson and Egerton
MacLean just to the north.
First-pass drilling further east from Plenty on 50m-spaced sections in
the hitherto un-drilled gap between Plenty and Egerton MacLean continues to
encounter encouraging shallow mineralization though more assay data are
awaited to confirm resource potential.
The accompanying cross sections and drilling progress plan can be viewed
here: http://files.newswire.ca/1485/atla0123.pdf
Assay results are tabulated below:
<<


Error occurred while generating ASCII Content for table

>>

NSA: No significant assays;
that is, no intervals >(equal sign)
3.0g/t x m.


^ fire assays of 50g charge
from 1kg pulverized sub-
sample split from -2mm
crushed parent of half
sawn 1m NQ core. All
others are fire assays of
50g charge from 1kg
pulverized sub-sample
split from -2mm crushed
parent of whole 1m NQ.

True width of the mineralization varies according to the dip of the host
stratigraphy and declination of the relevant drill hole. For intersections
quoted above true width averages approximately 90% of the down-hole width.
Nature of the mineralization:
Mineralization at Egerton MacLean and Hudson occurs within argillites,
greywackes and bedding-parallel quartz veins across the hinge zone and limbs
of the E-W trending Fifteen Mile Stream (FMS) Anticline. The northern limb of
the anticline dips moderately north, with the southern limb overturned
(generally steeply north dipping). All holes are therefore declined to the
south. Highest grades so far encountered occur within the hinge zone of the
anticline. Mineralization at Plenty is tabular in overall disposition and is
thought to be hosted in a deeper, up-faulted southern limb of the Fifteen Mile
Stream anticline. Free gold is commonly observed, and in association with
pyrrhotite and arsenopyrite.
Technical Disclosure
At Fifteen Mile Stream all assays by default are 50g charge fire assays
of 1kg pulverized sub-sample split from -2mm crushed parent of whole 1m NQ
core, with 1-in-10 duplicate assays of the same pulp, and 1-in-10 assays of a
second 1kg pulverized sub-sample split from the same crushed parent. Where
otherwise noted (^) assays are 50g charge fire assays of 1kg pulverized
sub-sample split from -2mm crushed parent of sawn half 1m NQ core, with
1-in-10 duplicate assays of the same pulp. Standards and blind blanks are
routinely inserted. Sample preparation and assaying is conducted at the
Sudbury and Vancouver laboratories of ALS Canada Ltd, an entity having no
other relationship with the Company. Core recovery is estimated for each metre
and averages >97%, excluding occasional voids, usually <2m, representing
historic underground workings. Wing samples to voids may be less than 1m to
re-establish routine sampling on 1m intervals. Drill core in the hangingwall
of the northern limb of the anticline where adjacent historic holes very
clearly indicate this upper stratigraphy to be barren may not be sampled and
assayed. Standards, blind blanks and duplicate assay results are acceptable.
Results and updates from this drilling program will be reported
progressively.
Wally Bucknell, Director of Exploration to the Company and a Qualified
Person as defined by National Instrument 43-101 ("NI 43-101") has reviewed and
approved the contents of this news release.
Further updates will be provided in due course and as new results come to
hand.
On behalf of the Board of Directors,
Steven DeanChairman and Chief Executive Officer
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
About Atlantic:
Atlantic is a well-financed, growth-oriented gold development group with
a long term strategy to build a mid-tier gold production company focused on
manageable, executable projects in mining-friendly jurisdictions. Atlantic
owns Canada's newest open pit gold mine Moose River Consolidated in Nova
Scotia with first gold pour and initial production announced October 2017.
Phase 1 Life of Mine production guidance for 2018 is between 82,000-90,000 oz.
gold at All-In-Sustaining-Costs (AISC) between $CAD675/oz.-$735/oz.
(US$540-588/oz.(x)) as stated in the Company's news release (January 19, 2018).
Additional satellite deposits containing 850,000 oz's measured & indicated
within pit shells and 309,000 oz's inferred as referenced in a NI 43-101
Technical Report with an effective date of July 20, 2017, form the basis of a
Phase 2 expansion currently under study and has potential to add significantly
to Life of Mine production. Atlantic is committed to the highest standards of
environmental and social responsibility and continually invests in people and
technology to manage risks, maximize outcomes and returns to all stakeholders.
Forward-Looking Statements:
This release contains certain "forward looking statements" and certain
"forward-looking information" as defined under applicable Canadian and U.S.
securities laws. Forward-looking statements and information can generally be
identified by the use of forward-looking terminology such as "may", "will",
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans"
or similar terminology. Forward-looking statements and information are not
historical facts, are made as of the date of this press release, and include,
but are not limited to, statements regarding discussions of future plans,
guidance, projections, objectives, estimates and forecasts and statements as
to management's expectations with respect to, among other things, the
activities contemplated in this news release and the timing and receipt of
requisite regulatory, and shareholder approvals in respect thereof.
Forward-looking statements in this news release include, without limitation,
statements related to proposed exploration and development programs, grade and
tonnage of material and resource estimates. These forward looking statements
involve numerous risks and uncertainties and actual results may vary.
Important factors that may cause actual results to vary include without
limitation, the timing and receipt of certain approvals, changes in commodity
and power prices, changes in interest and currency exchange rates, risks
inherent in exploration estimates and results, timing and success, inaccurate
geological and metallurgical assumptions (including with respect to the size,
grade and recoverability of mineral reserves and resources), changes in
development or mining plans due to changes in logistical, technical or other
factors, unanticipated operational difficulties (including failure of plant,
equipment or processes to operate in accordance with specifications, cost
escalation, unavailability of materials, equipment and third party
contractors, delays in the receipt of government approvals, industrial
disturbances or other job action, and unanticipated events related to health,
safety and environmental matters), political risk, social unrest, and changes
in general economic conditions or conditions in the financial markets. In
making the forward-looking statements in this press release, the Company has
applied several material assumptions, including without limitation, the
assumptions that: (1) market fundamentals will result in sustained gold demand
and prices; (2) the receipt of any necessary approvals and consents in
connection with the development of any properties; (3) the availability of
financing on suitable terms for the development, construction and continued
operation of any mineral properties; and (4) sustained commodity prices such
that any properties put into operation remain economically viable. Information
concerning mineral reserve and mineral resource estimates also may be
considered forward-looking statements, as such information constitutes a
prediction of what mineralization might be found to be present if and when a
project is actually developed. Certain of the risks and assumptions are
described in more detail in the Company's audited financial statements and
MD&A for the year ended December 31, 2016 and for the quarter ended September
30, 2017 on the SEDAR website at www.sedar.com. The actual results or
performance by the Company could differ materially from those expressed in, or
implied by, any forward-looking statements relating to those matters.
Accordingly, no assurances can be given that any of the events anticipated by
the forward-looking statements will transpire or occur, or if any of them do
so, what impact they will have on the results of operations or financial
condition of the Company. Except as required by law, the Company is under no
obligation, and expressly disclaim any obligation, to update, alter or
otherwise revise any forward-looking statement, whether written or oral, that
may be made from time to time, whether as a result of new information, future
events or otherwise, except as may be required under applicable securities
laws.
SOURCE Atlantic Gold Corporation



View original content with multimedia:
http://www.newswire.ca/en/releases/archive/January2018/24/c1857.html

-0-                           01/24/2018
/For further information: Maryse Bélanger (COO), +1 604 689-5564; Sean
Thompson (Manager Investor Relations), Toll Free: 1 877 689-5599/
(AGB.)

CO:  Atlantic Gold Corporation
ST:  British Columbia
IN:  MIN MNG
SU:

-30-