Source	Marketwire
Date	01/19/2018
Time	05:00:51 AM

Company	 WHITE GOLD CORP.
Title	White Gold Intersects Gold Mineralization Supporting Continuity of the Arc 
Deposit, Encounters Gold on Newly Defined Target and on Schedule to Provide 
Updated Mineral Resource Estimate in Q1 2018





    CDNX Symbol: WGO











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

January 19, 2018

White Gold Intersects Gold Mineralization Supporting Continuity of the Arc 
Deposit, Encounters Gold on Newly Defined Target and on Schedule to Provide 
Updated Mineral Resource Estimate in Q1 2018


TORONTO, ONTARIO--(Marketwired - Jan. 19, 2018) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce final reverse circulation 
("RC") drill results for the White Gold Property, Yukon from its 2017 
exploration program. This final batch includes 2 holes from the historical 
Golden Saddle deposit (the "Golden Saddle deposit" or "Golden Saddle 
resource")(4), 6 holes from the historical Arc deposit (the "Arc deposit")(4) 
as well as 5 holes from newly defined exploration targets. These new targets 
were primarily defined through a recently completed airborne geophysical survey 
that included magnetic and electromagnetic (DIGHEM) data. All drill assays from 
the White Gold Property have now been released and the Company is in the 
process of compiling the relevant databases for independent review and 
calculation of an updated National Instrument 43-101 mineral resource estimate. 
The Company expects to have a resource estimate ready for release in Q1 2018. 
Detailed maps related to the drilling and additional information can be found 
at http://whitegoldcorp.ca/investors/exploration-highlights/.

Highlights include:

/T/

--  Gold encountered on all Arc Zone drill holes; adding continuity to
mineralization including infill of recently announced 250m strike length
extension.

--  Arc hole WHTARC17RC-005 returned 7.62m of 3.95 g/t Au from 62.48m depth;
including 1.52m of 17.8 g/t Au from 62.48m depth, representing a 60m
down-dip step-out of historic hole WD-073(4) and infilling a 150m gap in
the central portion of the historic resource area.

--  Strong potential for subparallel zones of mineralization below historic
Arc resource area identified.

--  All holes on the Ulli's target maiden drill program encountered gold,
including WHTULR17RC-002 which intercepted 9.7 g/t Au over 1.52m from
97.54m depth, ending in mineralization, and hole WHTULR17RC-001 which
intercepted 2.58 g/t Au over 3.048m from 7.62m depth and 6.27 g/t Au
over 1.52m from 67.06m depth.

--  Continuity added to the near surface expression of the Golden Saddle
Main Zone and Golden Saddle Footwall extended 40m up dip.

/T/

"Since acquiring the White Gold Property in June 2017, we have successfully 
completed an aggressive exploration program on the property, comprised of 4 
diamond drill holes, 31 reverse circulation holes, 1,224 line-km of airborne 
DIGHEM surveys, 17.2 line-km of IP-Resistivity surveys, 2,913 soil samples, 195 
GT probe samples and detailed geologic mapping," commented Shawn Ryan, the 
Company's Chief Technical Advisor. "This season's work supports the potential 
to expand both the Golden Saddle and Arc resources and also highlights the 
opportunity for new discoveries on the White Gold Property. We look forward to 
the completion of an updated NI 43-101 resource estimate in Q1 2018, and to an 
extensive program during the 2018 field season."

Arc Exploration Update

The Arc occurs adjacent to the Golden Saddle deposit approximately 400m to the 
south. Historic drilling on the Arc was limited and wide spaced, but defined an 
east - west trending and north dipping zone of mineralization at least 850m 
long extending 400m down-dip with an inferred historic resource of 170,470 
ounces contained within 4.37 Mt at a grade of 1.21 g/t Au(4), with strong 
potential for subparallel zones of mineralization that have been identified 
below the historic resource area. Drill holes WHTARC17RC-001 to 005 were 
drilled within the historic resource area to in-fill historic drilling and 
confirm historic drill results for QA/QC purposes. WHTARC17RC-006 was drilled 
approximately 200m west of the historic resource area, encountering multiple 
zones of mineralization and indicating continuity between the historic resource 
area and previously released Arc holes WHTARR17RC-002 and 003 which extended 
strike length by 250m to the west(1).

Gold zones were encountered in all 6 drill holes, returning assays from trace 
to 17.8 g/t Au, with results consistent with historic assays. Highlights 
include hole WHTARC17RC-005 which returned 7.62m of 3.95 g/t Au from 62.48m 
depth, including 1.52m of 17.8 g/t Au from 62.48m depth. The intercept was a 
60m down-dip step-out of historic hole WD-073(2) and infilled a 150m gap in the 
central portion of the historic resource area. Results also supported the 
potential for subparallel zones of mineralization below the historic resource 
area. (A qualified person has not done sufficient work to classify the 
historical estimates as current mineral resources or mineral reserves and the 
Company is not treating the historical estimate as current mineral resources.) 
Significant results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Arc - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTARC17RC-001                    41.148      44.196       3.048        2.22
----------------------------------------------------------------------------
And                               65.532      97.536      32.004        0.51
----------------------------------------------------------------------------
Including                         65.532      73.152        7.62        1.46
----------------------------------------------------------------------------
WHTARC17RC-002                    82.296      86.868       4.572        1.49
----------------------------------------------------------------------------
Including                          83.82      85.344       1.524        3.09
----------------------------------------------------------------------------
WHTARC17RC-003                    67.056      88.392      21.336        0.53
----------------------------------------------------------------------------
Including                         77.724      88.392      10.668        0.81
----------------------------------------------------------------------------
WHTARC17RC-004                     15.24      19.812       4.572        2.00
----------------------------------------------------------------------------
And                               47.244      70.104       22.86        0.61
----------------------------------------------------------------------------
Including                          53.34      57.912       4.572        1.79
----------------------------------------------------------------------------
WHTARC17RC-005                    35.052      44.196       9.144        1.00
----------------------------------------------------------------------------
And                               62.484      70.104        7.62        3.95
----------------------------------------------------------------------------
Including                         62.484      64.008       1.524        17.8
----------------------------------------------------------------------------
And                                91.44     109.728      18.288        0.67
----------------------------------------------------------------------------
Including                          91.44       99.06        7.62        1.38
----------------------------------------------------------------------------
WHTARC17RC-006                    27.432      48.768      21.336        0.56
----------------------------------------------------------------------------
And                                 76.2       83.82        7.62        0.57
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

(1) Reported in the Company's news release dated Nov. 20, 2017 and available on 
SEDAR

(2) Reported in Underworld Resources news release dated Sept. 28, 2009 and 
available on SEDAR

Ulli's Target Exploration Update

The Ulli's target is located on trend approximately 2.2km SW of the Golden 
Saddle and consists of an extensive gold in soil anomaly approximately 860m 
long and 220m wide with values ranging from trace up to 1,117 ppb Au. Trenching 
completed on the target by Kinross Gold Corp. ("Kinross") in 2012 returned 
0.681 g/t Au over 55m from WGUR12TR01, and its extension WGUR12TR03; including 
1.38 g/t Au over 20m(2). These results are comparable to the trenching 
completed by Underworld Resources Inc. in 2007 on the Golden Saddle deposit 
which returned a 38m wide zone of mineralization averaging 1.12g/t Au, 
including 4.7g/t Au over 5m and a minimum grade of 0.1g/t Au over 0.3m(2). 
Mineralization within the trenches are associated with fractured and brecciated 
quartzite, quartz veining, and fine-grained sulfide mineralization and the 
target has not been previously drill tested. The 2017 drill campaign consisted 
of 3 reconnaissance RC holes that encountered numerous intervals of anomalous 
mineralization with individual assays varying from trace to 9.7 g/t Au over 
1.52m (starting at 97.54m) from hole WHTULR17RC-002, ending in mineralization. 
These results were very encouraging and warrant follow-up in 2018. Significant 
results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Ulli's - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTULR17RC-001                      7.62      10.668       3.048        2.58
----------------------------------------------------------------------------
And                               67.056       68.58       1.524        6.27
----------------------------------------------------------------------------
WHTULR17RC-002(i)                 97.536       99.06       1.524         9.7
----------------------------------------------------------------------------
WHTULR17RC-003                    79.248      82.296       3.048        2.19
----------------------------------------------------------------------------

/T/

(i)Hole ended in mineralization

True thickness is estimated to be between 65 - 95% of the reported intercepts.

Golden Saddle Exploration Update

Results for the 2 remaining 2017 RC holes from Golden Saddle include Hole 
WHTGS17RC-007 ("Hole 7") which is located on the same site as previously 
reported hole WHTGS17RC-006(1) and returned two zones of mineralization. The 
upper intercept corresponds to the GS Main Zone and returned 12.19m of 0.68 g/t 
Au from 10.67m depth. The lower intercept corresponds to the GS Footwall Zone 
and returned 13.72m of 1.33 g/t Au from 86.87m depth. Hole WHTGS17RC-008 was 
collared 50m to the NE of Hole 007 and returned 6.10m of 1.58 g/t Au from 6.10m 
depth. Both holes infilled and added continuity to the near surface expression 
of the GS Main Zone and extended the continuity of the GS Footwall Zone an 
additional 40m up dip. Significant results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-007                     10.668       22.86      12.192        0.68
----------------------------------------------------------------------------
And                               86.868     100.584      13.716        1.33
----------------------------------------------------------------------------
WHTGS17RC-008                      6.096      12.192       6.096        1.58
----------------------------------------------------------------------------
And                              120.396     135.636       15.24        0.47
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

(3) Reported in the Company's news release dated Oct. 30, 2017 and available on 
SEDAR

Golden Saddle East Target Exploration Update

The newly identified GS East target is located 600m to the NE and on strike 
with the Golden Saddle deposit. The target was generated through 3D modeling of 
IP-Resistivity sections and airborne DIGHEM data over the Golden Saddle area. 
At Golden Saddle, gold mineralization is associated with distinct resistivity 
and chargeability features that are interpreted to be related to the broader 
alteration halo of the system. The GS East target has a similar geophysical 
signature and is associated with anomalous gold in soils at surface. The target 
area was identified during the 2017 field season and was not tested by historic 
drill campaigns on the property. 2 RC drill holes were attempted late in the 
2017 season, however, weather and ground conditions led to both holes being 
terminated prior to target depth without intersecting mineralization. The 
target will be properly drill tested and evaluated in 2018.

(4) Information Regarding Historical Resources/Deposits
All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource 
Statement). Both Underworld's and Kinross' resource estimates are considered 
historical estimates and the Company is not treating them as current mineral 
resources. Although the Company believes these sources to be generally 
reliable, such information is subject to interpretation and cannot be verified 
with complete certainty due to limits on the availability and reliability of 
raw data, the voluntary nature of the data gathering process and other inherent 
limitations and uncertainties. In addition to the Golden Saddle and Arc 
deposits, there are numerous other targets known on the property that warrant 
follow-up work (for more information see Yukon Assessment Report #'s 095338, 
096206, & 096207).
The information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
Company as available on Sedar, and the Company considers such information to be 
relevant solely on the basis that it may indicate the presence of 
mineralization in the region. There are numerous uncertainties inherent in the 
historical estimates, which are subject to all of the assumptions, parameters 
and methods used to prepare such historical estimates and reference is made to 
the full text of the Technical Report with respect thereto. The historic 
estimates of mineral resources were estimated in conformity with generally 
accepted CIM "Estimation of Mineral Resource and Mineral Reserve Best 
Practices" Guidelines. Mineral resources are not mineral reserves and do not 
have demonstrated economic viability. There are no other recent estimates or 
data are available to the Company as at the date of this news release and a 
detailed exploration program is required to be conducted by the Company in 
order to verify or treat the historical estimate as a current mineral resource. 
A qualified person has not done sufficient work to classify the historical 
estimates as current mineral resources or mineral reserves and the Company is 
not treating the historical estimate as current mineral resources.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.

The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made.
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis. Although the 
forward-looking statements contained in this news release are based upon what 
management of the Company believes, or believed at the time, to be reasonable 
assumptions, the Company cannot assure shareholders that actual results will be 
consistent with such forward-looking statements, as there may be other factors 
that cause results not to be as anticipated, estimated or intended.
Accordingly, readers should not place undue reliance on forward-looking 
statements and information. There can be no assurance that forward-looking 
information, or the material factors or assumptions used to develop such 
forward-looking information, will prove to be accurate. The Company does not 
undertake any obligations to release publicly any revisions for updating any 
voluntary forward-looking statements, except as required by applicable 
securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

White Gold Corp.
David D'Onofrio
Chief Executive Officer
(416) 643-3880
ddonofrio@whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=602054479


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: White Gold Corp.

TSX VENTURE SYMBOL: WGO

January 19, 2018

White Gold Intersects Gold Mineralization Supporting Continuity of the Arc 
Deposit, Encounters Gold on Newly Defined Target and on Schedule to Provide 
Updated Mineral Resource Estimate in Q1 2018


TORONTO, ONTARIO--(Marketwired - Jan. 19, 2018) - White Gold Corp. (TSX 
VENTURE:WGO) (the "Company") is pleased to announce final reverse circulation 
("RC") drill results for the White Gold Property, Yukon from its 2017 
exploration program. This final batch includes 2 holes from the historical 
Golden Saddle deposit (the "Golden Saddle deposit" or "Golden Saddle 
resource")(4), 6 holes from the historical Arc deposit (the "Arc deposit")(4) 
as well as 5 holes from newly defined exploration targets. These new targets 
were primarily defined through a recently completed airborne geophysical survey 
that included magnetic and electromagnetic (DIGHEM) data. All drill assays from 
the White Gold Property have now been released and the Company is in the 
process of compiling the relevant databases for independent review and 
calculation of an updated National Instrument 43-101 mineral resource estimate. 
The Company expects to have a resource estimate ready for release in Q1 2018. 
Detailed maps related to the drilling and additional information can be found 
at http://whitegoldcorp.ca/investors/exploration-highlights/.

Highlights include:

/T/

--  Gold encountered on all Arc Zone drill holes; adding continuity to
mineralization including infill of recently announced 250m strike length
extension.

--  Arc hole WHTARC17RC-005 returned 7.62m of 3.95 g/t Au from 62.48m depth;
including 1.52m of 17.8 g/t Au from 62.48m depth, representing a 60m
down-dip step-out of historic hole WD-073(4) and infilling a 150m gap in
the central portion of the historic resource area.

--  Strong potential for subparallel zones of mineralization below historic
Arc resource area identified.

--  All holes on the Ulli's target maiden drill program encountered gold,
including WHTULR17RC-002 which intercepted 9.7 g/t Au over 1.52m from
97.54m depth, ending in mineralization, and hole WHTULR17RC-001 which
intercepted 2.58 g/t Au over 3.048m from 7.62m depth and 6.27 g/t Au
over 1.52m from 67.06m depth.

--  Continuity added to the near surface expression of the Golden Saddle
Main Zone and Golden Saddle Footwall extended 40m up dip.

/T/

"Since acquiring the White Gold Property in June 2017, we have successfully 
completed an aggressive exploration program on the property, comprised of 4 
diamond drill holes, 31 reverse circulation holes, 1,224 line-km of airborne 
DIGHEM surveys, 17.2 line-km of IP-Resistivity surveys, 2,913 soil samples, 195 
GT probe samples and detailed geologic mapping," commented Shawn Ryan, the 
Company's Chief Technical Advisor. "This season's work supports the potential 
to expand both the Golden Saddle and Arc resources and also highlights the 
opportunity for new discoveries on the White Gold Property. We look forward to 
the completion of an updated NI 43-101 resource estimate in Q1 2018, and to an 
extensive program during the 2018 field season."

Arc Exploration Update

The Arc occurs adjacent to the Golden Saddle deposit approximately 400m to the 
south. Historic drilling on the Arc was limited and wide spaced, but defined an 
east - west trending and north dipping zone of mineralization at least 850m 
long extending 400m down-dip with an inferred historic resource of 170,470 
ounces contained within 4.37 Mt at a grade of 1.21 g/t Au(4), with strong 
potential for subparallel zones of mineralization that have been identified 
below the historic resource area. Drill holes WHTARC17RC-001 to 005 were drilled within the historic resource area to 
in-fill historic drilling and confirm historic drill results for QA/QC 
purposes. WHTARC17RC-006 was drilled approximately 200m west of the historic 
resource area, encountering multiple zones of mineralization and indicating 
continuity between the historic resource area and previously released Arc holes 
WHTARR17RC-002 and 003 which extended strike length by 250m to the west(1).

Gold zones were encountered in all 6 drill holes, returning assays from trace 
to 17.8 g/t Au, with results consistent with historic assays. Highlights 
include hole WHTARC17RC-005 which returned 7.62m of 3.95 g/t Au from 62.48m 
depth, including 1.52m of 17.8 g/t Au from 62.48m depth. The intercept was a 
60m down-dip step-out of historic hole WD-073(2) and infilled a 150m gap in the 
central portion of the historic resource area. Results also supported the 
potential for subparallel zones of mineralization below the historic resource 
area. (A qualified person has not done sufficient work to classify the 
historical estimates as current mineral resources or mineral reserves and the 
Company is not treating the historical estimate as current mineral resources.) 
Significant results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Arc - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTARC17RC-001                    41.148      44.196       3.048        2.22
----------------------------------------------------------------------------
And                               65.532      97.536      32.004        0.51
----------------------------------------------------------------------------
Including                         65.532      73.152        7.62        1.46
----------------------------------------------------------------------------
WHTARC17RC-002                    82.296      86.868       4.572        1.49
----------------------------------------------------------------------------
Including                          83.82      85.344       1.524        3.09
----------------------------------------------------------------------------
WHTARC17RC-003                    67.056      88.392      21.336        0.53
----------------------------------------------------------------------------
Including                         77.724      88.392      10.668        0.81
----------------------------------------------------------------------------
WHTARC17RC-004                     15.24      19.812       4.572        2.00
----------------------------------------------------------------------------
And                               47.244      70.104       22.86        0.61
----------------------------------------------------------------------------
Including                          53.34      57.912       4.572        1.79
----------------------------------------------------------------------------
WHTARC17RC-005                    35.052      44.196       9.144        1.00
----------------------------------------------------------------------------
And                               62.484      70.104        7.62        3.95
----------------------------------------------------------------------------
Including                         62.484      64.008       1.524        17.8
----------------------------------------------------------------------------
And                                91.44     109.728      18.288        0.67
----------------------------------------------------------------------------
Including                          91.44       99.06        7.62        1.38
----------------------------------------------------------------------------
WHTARC17RC-006                    27.432      48.768      21.336        0.56
----------------------------------------------------------------------------
And                                 76.2       83.82        7.62        0.57
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

(1) Reported in the Company's news release dated Nov. 20, 2017 and available on 
SEDAR

(2) Reported in Underworld Resources news release dated Sept. 28, 2009 and 
available on SEDAR

Ulli's Target Exploration Update

The Ulli's target is located on trend approximately 2.2km SW of the Golden 
Saddle and consists of an extensive gold in soil anomaly approximately 860m 
long and 220m wide with values ranging from trace up to 1,117 ppb Au. Trenching 
completed on the target by Kinross Gold Corp. ("Kinross") in 2012 returned 
0.681 g/t Au over 55m from WGUR12TR01, and its extension WGUR12TR03; including 
1.38 g/t Au over 20m(2). These results are comparable to the trenching 
completed by Underworld Resources Inc. in 2007 on the Golden Saddle deposit 
which returned a 38m wide zone of mineralization averaging 1.12g/t Au, 
including 4.7g/t Au over 5m and a minimum grade of 0.1g/t Au over 0.3m(2). 
Mineralization within the trenches are associated with fractured and brecciated 
quartzite, quartz veining, and fine-grained sulfide mineralization and the 
target has not been previously drill tested. The 2017 drill campaign consisted 
of 3 reconnaissance RC holes that encountered numerous intervals of anomalous 
mineralization with individual assays varying from trace to 9.7 g/t Au over 
1.52m (starting at 97.54m) from hole WHTULR17RC-002, ending in mineralization. 
These results were very encouraging and warrant follow-up in 2018. Significant 
results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Ulli's - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTULR17RC-001                      7.62      10.668       3.048        2.58
----------------------------------------------------------------------------
And                               67.056       68.58       1.524        6.27
----------------------------------------------------------------------------
WHTULR17RC-002(i)                 97.536       99.06       1.524         9.7
----------------------------------------------------------------------------
WHTULR17RC-003                    79.248      82.296       3.048        2.19
----------------------------------------------------------------------------

/T/

(i)Hole ended in mineralization

True thickness is estimated to be between 65 - 95% of the reported intercepts.

Golden Saddle Exploration Update

Results for the 2 remaining 2017 RC holes from Golden Saddle include Hole 
WHTGS17RC-007 ("Hole 7") which is located on the same site as previously 
reported hole WHTGS17RC-006(1) and returned two zones of mineralization. The 
upper intercept corresponds to the GS Main Zone and returned 12.19m of 0.68 g/t 
Au from 10.67m depth. The lower intercept corresponds to the GS Footwall Zone 
and returned 13.72m of 1.33 g/t Au from 86.87m depth. Hole WHTGS17RC-008 was 
collared 50m to the NE of Hole 007 and returned 6.10m of 1.58 g/t Au from 6.10m 
depth. Both holes infilled and added continuity to the near surface expression 
of the GS Main Zone and extended the continuity of the GS Footwall Zone an 
additional 40m up dip. Significant results are detailed in the table below.

/T/


----------------------------------------------------------------------------
Golden Saddle - 2017 RC Drill Holes
----------------------------------------------------------------------------
Interval
Hole ID                         From (m)      To (m)         (m)    Au (g/t)
----------------------------------------------------------------------------
WHTGS17RC-007                     10.668       22.86      12.192        0.68
----------------------------------------------------------------------------
And                               86.868     100.584      13.716        1.33
----------------------------------------------------------------------------
WHTGS17RC-008                      6.096      12.192       6.096        1.58
----------------------------------------------------------------------------
And                              120.396     135.636       15.24        0.47
----------------------------------------------------------------------------

/T/

True thickness is estimated to be between 65 - 95% of the reported intercepts.

(3) Reported in the Company's news release dated Oct. 30, 2017 and available on 
SEDAR

Golden Saddle East Target Exploration Update

The newly identified GS East target is located 600m to the NE and on strike 
with the Golden Saddle deposit. The target was generated through 3D modeling of 
IP-Resistivity sections and airborne DIGHEM data over the Golden Saddle area. 
At Golden Saddle, gold mineralization is associated with distinct resistivity 
and chargeability features that are interpreted to be related to the broader 
alteration halo of the system. The GS East target has a similar geophysical 
signature and is associated with anomalous gold in soils at surface. The target 
area was identified during the 2017 field season and was not tested by historic 
drill campaigns on the property. 2 RC drill holes were attempted late in the 
2017 season, however, weather and ground conditions led to both holes being 
terminated prior to target depth without intersecting mineralization. The 
target will be properly drill tested and evaluated in 2018.

(4) Information Regarding Historical Resources/Deposits
All historical scientific and technical information relating to the White Gold 
Properties is based on and derived from the 43-101 report titled "White Gold 
Property Dawson Range Yukon, Canada" dated March 3, 2010, prepared by Lars 
Weiershauser, P.Geo, Marek Nowak, P.Eng and Wayne Barnett, Pr.Sci.Nat. of SRK 
Consulting (Canada) Inc.) (the "Technical Report") available on Sedar and other 
information available to the Company as referenced herein. The property was 
historically explored by Underworld Resources from 2007 - 2009 and included the 
discovery of the Golden Saddle and Arc deposits. In 2010, Underworld reported a 
resource estimate of 1,004,570 ounces contained in 9.80 Mt at a grade of 3.19 
g/t Au in an Indicated category, with an additional 407,410 ounces contained in 
5.02 Mt at a grade of 2.5 g/t Au in an Inferred category for the Golden Saddle 
deposit. At the Arc deposit, the initial resource included 170,470 ounces 
contained within 4.37 Mt at a grade of 1.21 g/t Au in the inferred category 
(reported in Underworld Resources New Release UW2010-NR#2 dated January 19, 
2010 and the Technical Report. Kinross purchased Underworld shortly after the 
initial resource was released in 2010 and explored the property from 2010 - 
2012. In 2013, Kinross released the results of a resource estimate for the 
Golden Saddle deposit and reported a resource of 840,000 ounces within 9.79 Mt 
at a grade of 2.67 g/t Au in an Indicated category, with an additional 125,000 
ounces within 2.17 Mt at a grade of 1.8 g/t Au in an Inferred category 
(reported in Kinross Gold Corp.'s 2016 Mineral Reserves and Resource 
Statement). Both Underworld's and Kinross' resource estimates are considered 
historical estimates and the Company is not treating them as current mineral 
resources. Although the Company believes these sources to be generally 
reliable, such information is subject to interpretation and cannot be verified 
with complete certainty due to limits on the availability and reliability of 
raw data, the voluntary nature of the data gathering process and other inherent 
limitations and uncertainties. In addition to the Golden Saddle and Arc 
deposits, there are numerous other targets known on the property that warrant 
follow-up work (for more information see Yukon Assessment Report #'s 095338, 
096206, & 096207).
The information contained herein is subject to all of the assumptions, 
qualifications and procedures set out in the Technical Report and reference 
should be made to the full details of the Technical Report which may be 
obtained from the Company by contacting dschmidt@whitegoldcorp.ca. Disclosure 
of the historical estimates in this news release is derived from the Technical 
Report and other information as set forth above previous press releases of the 
Company as available on Sedar, and the Company considers such information to be 
relevant solely on the basis that it may indicate the presence of 
mineralization in the region. There are numerous uncertainties inherent in the 
historical estimates, which are subject to all of the assumptions, parameters 
and methods used to prepare such historical estimates and reference is made to 
the full text of the Technical Report with respect thereto. The historic 
estimates of mineral resources were estimated in conformity with generally 
accepted CIM "Estimation of Mineral Resource and Mineral Reserve Best 
Practices" Guidelines. Mineral resources are not mineral reserves and do not 
have demonstrated economic viability. There are no other recent estimates or 
data are available to the Company as at the date of this news release and a 
detailed exploration program is required to be conducted by the Company in 
order to verify or treat the historical estimate as a current mineral resource. 
A qualified person has not done sufficient work to classify the historical 
estimates as current mineral resources or mineral reserves and the Company is 
not treating the historical estimate as current mineral resources.

The Company encourages individuals interested in the Company to visit its 
website (www.whitegoldcorp.ca) to further understand the size and scope of the 
Company's projects in the White Gold District.

The analytical work for the 2017 program has been performed by Bureau Veritas 
Commodities Canada Ltd., an internationally recognized analytical services 
provider, at its Vancouver, British Columbia laboratory. Sample preparation was 
carried out at its Whitehorse, Yukon facility. All soil samples were using 
procedure SS80 (dry at 60 C and sieve 100g at -80 mesh) and analyzed by method 
AQ201 (aqua regia digestion and ICP-MS analysis). All rock, GT Probe, RAB, RC, 
and diamond core samples were prepared using procedure PRP70-250 (crush, split 
and pulverize 250 g to 200 mesh) and analyzed by method FA430 (30g fire assay 
with AAS finish) and AQ200 (0.5g, aqua regia digestion and ICP-MS analysis). 
Samples containing greater than 10g/t Au were reanalyzed using method FA530 
(30g Fire Assay with gravimetric finish). Metallic-screen analysis may also be 
utilized if coarse gold mineralization is encounter (FS600).

Qualified Person

Jodie Gibson, PGeo, VP, Exploration of the Company is a "qualified person" as 
defined under National Instrument 43-101 - Standards of Disclosure for Mineral 
Projects ("NI 43-101"), and has reviewed and approved the content of this news 
release. Potential quantity and grade is conceptual in nature. There has been 
insufficient exploration to define a mineral resource on any of the Company's 
properties to date, and it is uncertain if further exploration will result in 
any such target being delineated as a mineral resource.

The reported work was completed using industry standard procedures, including a 
quality assurance/quality control (QA/QC) program consisting of the insertion 
of certified standards, blanks, and field duplicates into the sample stream. 
The qualified person detected no significant QA/QC issues during review of the 
data.

About White Gold Corp.

The Company owns a portfolio of 19,438 quartz claims across 30 properties 
covering over 390,000 hectares representing approximately 40% of the Yukon's 
White Gold district. Preliminary exploration work has produced several 
prospective targets. The claim packages are bordered by sizable gold 
discoveries including the Coffee project owned by Goldcorp Inc., Western Copper 
and Gold Corporation's Casino project, and the Golden Saddle and Arc deposits 
acquired by the Company in June 2017 from Kinross Gold Corp. The Company has 
outlined an aggressive exploration plan to further explore its properties. For 
more information visit www.whitegoldcorp.ca.

Cautionary Note Regarding Forward Looking Information

This news release contains "forward-looking information" and "forward-looking 
statements" (collectively, "forward-looking statements") within the meaning of 
the applicable Canadian securities legislation. All statements, other than 
statements of historical fact, are forward-looking statements and are based on 
expectations, estimates and projections as at the date of this news release. 
Any statement that involves discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions, future 
events or performance (often but not always using phrases such as "expects", or 
"does not expect", "is expected", "anticipates" or "does not anticipate", 
"plans", "budget", "scheduled", "forecasts", "estimates", "believes" or 
"intends" or variations of such words and phrases or stating that certain 
actions, events or results "may" or "could", "would", "might" or "will" be 
taken to occur or be achieved) are not statements of historical fact and may be 
forward-looking statements. In this news release, forward-looking statements 
relate, among other things, to: the anticipated benefits to the Company and its 
shareholders respecting the Company's objectives, goals and exploration 
activities conducted and proposed to be conducted at the White Gold properties; 
future growth potential of the Company, including whether any mineral resource 
will be established in accordance with NI 43-101 at any of the Company's 
properties; exploration results; and future exploration plans.

These forward-looking statements are based on reasonable assumptions and 
estimates of management of the Company at the time such statements were made.
Actual future results may differ materially as forward-looking statements 
involve known and unknown risks, uncertainties and other factors which may 
cause the actual results, performance or achievements of the Company to 
materially differ from any future results, performance or achievements 
expressed or implied by such forward-looking statements. Such factors, among 
other things, include: the expected benefits to the Company relating to the 
exploration conducted and proposed to be conducted at the White Gold 
properties; failure to identify mineral resources; the preliminary nature of 
metallurgical test results; uncertainties relating to the availability and 
costs of financing needed in the future, including to fund any exploration 
programs on the White Gold properties and the Company's other properties; 
business integration risks; fluctuations in general macroeconomic conditions; 
fluctuations in securities markets; fluctuations in spot and forward prices of 
gold, silver, base metals or certain other commodities; fluctuations in 
currency markets (such as the Canadian dollar to United States dollar exchange 
rate); change in national and local government, legislation, taxation, 
controls, regulations and political or economic developments; risks and hazards 
associated with the business of mineral exploration, development and mining 
(including environmental hazards, industrial accidents, unusual or unexpected 
formations pressures, cave-ins and flooding); inability to obtain adequate 
insurance to cover risks and hazards; the presence of laws and regulations that 
may impose restrictions on mining; employee relations; relationships with and 
claims by local communities and indigenous populations; availability of 
increasing costs associated with mining inputs and labour; the speculative 
nature of mineral exploration and development (including the risks of obtaining 
necessary licenses, permits and approvals from government authorities); the 
unlikelihood that properties that are explored are ultimately developed into 
producing mines; geological factors; actual results of current and future 
exploration; changes in project parameters as plans continue to be evaluated; 
soil sampling results being preliminary in nature and are not conclusive 
evidence of the likelihood of a mineral deposit; title to properties; and those 
factors described under the heading "Risks and Uncertainties" in the Company's 
most recently filed management's discussion and analysis. Although the 
forward-looking statements contained in this news release are based upon what 
management of the Company believes, or believed at the time, to be reasonable 
assumptions, the Company cannot assure shareholders that actual results will be 
consistent with such forward-looking statements, as there may be other factors 
that cause results not to be as anticipated, estimated or intended.
Accordingly, readers should not place undue reliance on forward-looking 
statements and information. There can be no assurance that forward-looking 
information, or the material factors or assumptions used to develop such 
forward-looking information, will prove to be accurate. The Company does not 
undertake any obligations to release publicly any revisions for updating any 
voluntary forward-looking statements, except as required by applicable 
securities law.

Neither the TSX Venture Exchange (the "Exchange") nor its Regulation Services 
Provider (as that term is defined in the policies of the Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

White Gold Corp.
David D'Onofrio
Chief Executive Officer
(416) 643-3880
ddonofrio@whitegoldcorp.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=602054479