Source	MARKET NEWS
Date	01/16/2018
Time	05:51:56 AM

Company	 Durango Resources Inc.
Title	Designs 
Drill Program for Decouverte Property in





    CDNX Symbol: DGO











Press Release





DURANGO RESOURCES INC ("DGO-V;ATOXF-0")
- Designs Drill Program for Decouverte Property in Quebec

Durango Resources Inc. (the "Company" or "Durango") is
pleased to announce results from an independent technical review for
the Decouverte gold property (the "Property") in James Bay, Quebec.

The Company recently retained Danae Voormeij, PGeo. (see news
release November 20, 2017) to analyze and interpret all relevant data
on the Property, to determine the gold potential, and to design a drill
program accordingly. A presentation of this information can be found on
Durango's website at:
http://durangoresourcesinc.com/wp-content/uploads/2018/01/D%C3%A9couverte_I
nvestor-Presentation_15Jan2018.pdf.

Program Highlights:




- Six target areas are defined on the Property, each ranging from
100m to 400m along strike

- Mineralization in the Main Zone is focused within a 1km by 0.3km
northwest trend

- The Company's claims cover a deformed fold nose in the
Frotet-Evan Greenstone Belt

- There is evidence of a well-preserved gold system, hosted in
finely-bedded and iron-rich metasediments in contact with metavolcanic
rocks

- Rusty and sulphuric polymict conglomerates have been mapped in
the Main Zone along 1km strike

- The Property is easily accessed, being only 10km from the
all-season Route Nord

- A high voltage powerline, part of Quebec's Plan Nord, runs
directly through the Property

- The technical review supports a diamond drilling program of
3,800m across 36 holes

- Drill holes are relatively shallow, ranging from 40 to 180m,
averaging 102 m in length




"James Bay is considered a highly-prospective new gold camp by the
majors, with such quality deposits as Goldcorp's multi-million-ounce
Eleonore, Eastmain's Clearwater, and La Grande Sud, all situated along
the same north-northwest trend as Decouverte," said Marcy Kiesman, CEO
of Durango. "We are intrigued by the compelling geology at Decouverte
and are extremely pleased with the progress that Ms. Voormeij has
accomplished thus far. Our next step will be to raise the necessary
funds to commence drilling on the Property."

Danae Voormeij, a consultant with Mynah Exploration Inc., has more
than 15 years' experience in gold exploration and a proven track record
of discovery; she led AIM-listed Hummingbird Resources to the
grassroots discovery of 2.4 million ounces of gold at Tuzon, a Birimian
greenstone-hosted gold deposit in Liberia. She placed in the top 20 out
of 1,342 participants in the 2015 Integra Gold Challenge with her
innovative proposal on target selection and has published a book on
gold exploration for Edumine.

Ms. Voormeij reports that large deposits tend to occur
stratigraphically near the unconformity at the base of conglomeratic
sequences such as the ones mapped in the Main Zone of Decouverte. The
conglomerates of the Main Zone are rusty and smell strongly of sulphur,
indicating that the mineralization is very near to surface. Drill holes
targeting the Main zone range from 50 to 180m, averaging 121m in
length.

Geophysical evidence for mineralized trends on the Property are
electromagnetic (EM) conductors with coincident magnetic, resistivity
and gravity anomalies (see November 20, 2017 news release and
presentation on the website), which suggest sulphide mineralization,
such as pyrrhotite, associated with gold mineralization.

Soil geochemistry outlines gold mineralized trends with anomalous
gold in soil values ranging from 50 to 177 ppb. Gold pathfinder
elements at Decouverte include gold (Au), copper (Cu), arsenic (As),
antimony (Sb) and Zinc (Zn).

Based on surface data collected to date, there are six target
areas for the proposed 3,800m drilling program: Main Zone, Shear Zone
1, Skip Vein, BIF Vein, Swift Vein and Shear Zone 2. The mineralized
trends within these zones range from 100 to 400m in strike length. Gold
mineralization in the Main Zone is focused within a 1.0km by 0.3km
northwest shear trend of the Decouverte Fault Zone.

The Frotet-Evans Break (the "Break") runs for 100km east-west
along the greenstone belt and takes a drastic bend to the northeast
within the Property claims. Ms. Voormeij believes the Break is the main
structural control for gold mineralization at Decouverte, particularly
along the Decouverte Fault Zone, a secondary structure, which
intersects it. The Break was a dextral strike slip and then became a
thrust fault, which is why gold mineralization is well preserved in the
hanging wall, on the north side of the Break (see Figure 1)
http://durangoresourcesinc.com/fig1_durango-Decouverte-geol-map_07jan2018/.


(img
src='https://www.thenewswire.com/data/tnw/clients/img/47073f12c47b737552ac9
3fb13486462_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/47073f12c47b737552ac93fb13
486462.png
Click Image To View Full Size

The Property is easily accessible, and the terrain is relatively
flat and largely covered by a thin veneer of glacial till. Targets in
the Main Zone are beneath a rusty and sulphuric polymict, undeformed
conglomerate that has been mapped along a strike length of 1km. Host
rocks for gold mineralization are finely bedded and iron-rich
metasediments within the wacke at the contact with metavolcanic rocks.

Ms. Voormeij reviewed all technical data collected on the Property
to date and proposes a drilling program to test six (6) areas of
inferred mineralized trends, which range from 100m to potentially 400m
along strike. The proposed program, a first for the Property, will
drill-test the inferred trends below surface, both down dip and along
strike. Drill hole lengths range from 40 to 180m, averaging 102m.
Drilling in the Main Zone (see Figure 2)
http://durangoresourcesinc.com/fig-2_durango-Decouverte-main-zone-proposed-
drilling_jan2018/ is targeting a northwest trending, southeast dipping,
mineralized trend that is hosted in a highly structurally deformed fold
nose.

(img
src='https://www.thenewswire.com/data/tnw/clients/img/def72c8c23d0109d01ea0
4124f5d6a17_.png' /) @
https://www.thenewswire.com/data/tnw/clients/img/def72c8c23d0109d01ea04124f
5d6a17.png
Click Image To View Full Size

Drill holes and drill fences are planned along 50 by 50m metric
grids towards future potential resource drilling. Drilling along fences
will provide information to draft geological cross-sections and
increase the understanding of gold mineralization controls at
Decouverte.

Figure 1. Geological map of Decouverte gold project, James Bay,
Quebec

Figure 2. Proposed drilling of Decouverte Main Zone

About Decouverte

Decouverte is a grassroots gold project targeting
greenstone-hosted orogenic gold mineralization. The Property is in the
Frotet-Evans Greenstone Belt with Troilus gold-copper mine 60 km to the
northeast and Goldcorp's Eleonore gold mine 240 km to the north along
the same northwest trend.

The Property is 57 square kilometres (5,700 ha) and covers a
section of the main Frotet-Evans shear-zone where it bends; trending
from east-west to northeast. The dominant structural feature within the
Property is a large synclinal fold nose composed of Archean
metasedimentary and metavolcanic rocks that has been deformed by
northwest and northeast-trending faults and intruded by syn-orogenic
granodiorite bodies. Rusty and sulphuric polymict, undeformed
conglomerates have been mapped within the Property, in the hanging wall
of the Main Zone.

The Property has never been drilled. Since 2011, Durango has
collected and assayed 343 soils, 65 boulders, 30 basal till and 208
rock chip samples. Outcrop mapping of limited exposed bedrock was
completed in 2012 and 2015. Fugro conducted an airborne DIGHEM
magnetic/EM geophysical survey of the Property and in 2015 deep ground
geophysical surveys were completed by INRS (Institut National de la
Recherche Scientifique), who in 2017 delivered a report listing nine
exploration target areas based on the interpretation of the geophysical
data (see news release dated December 6, 2017).

Qualified Person

The technical information contained in this news release was
prepared by Danae Voormeij, MSc, PGeo. Ms. Voormeij is a "qualified
person" under CIM's National Instrument 43-101 Standards of Disclosure
for Mineral Projects.

About Durango

Durango is a natural resources company engaged in the acquisition
and exploration of mineral properties. The Company has a 100% interest
in the Mayner's Fortune limestone property and the Golden Triangle
properties in northwest British Columbia, the Decouverte and Trove &
Windfall gold properties in Quebec, lithium properties near the
Whabouchi Mine, the Buckshot graphite property near the Miller Mine in
Quebec, the Dianna Lake silver project in northern Saskatchewan and the
Whitney Northwest gold property near Timmins, Ontario.

For further information on Durango, please refer to the documents
posted on its SEDAR profile at www.sedar.com or contact:

Marcy Kiesman, CEO
Telephone: 604.339.2243
Email: durangoresourcesinc@gmail.com
Website: www.durangoresourcesinc.com

Forward-Looking Statements

This news release may contain or refer to forward-looking
information based on current expectations, including commencement and
completion of future exploration on the Property, drilling, financing,
and the impact on the Company of these events. Forward-looking
information is subject to significant risks and uncertainties,
including market conditions, raising additional capital for exploration
expenditures, as actual results may differ materially from forecasted
results. Forward-looking information is provided as of the date hereof
and we assume no responsibility to update or revise them to reflect new
events or circumstances. For a detailed list of risks and uncertainties
relating to Durango, please refer to its prospectus filed on its SEDAR
profile at www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1801500021TS11801500725-05512820180116