Source	MARKET NEWS
Date	01/16/2018
Time	02:16:07 PM

Company	 San Marco Resources Inc.
Title	Continues to Discover High Grade Mineralization





    CDNX Symbol: SMN











Press Release





Continues to Discover High Grade Mineralization at Chunibas; Samples6.41% 
Copper and 27.3 g/t Silver --->@NEWS RELEASE
SAN MARCO RESOURCES INC ("SMN-V;SMREF-0")
- Continues to Discover High Grade Mineralization at
- Chunibas; Samples 6.41% Copper and 27.3 g/t Silver

San Marco Resources Inc. ("San Marco" or "the Company") announces
further assay results from continuing fieldwork at Chunibas. As
disclosed in the Company's news release dated January 10th, 2018, newly
discovered copper and silver mineralization at the Company's 100% owned
Chunibas property has been located over an area of approximately 1.2
kilometres of strike and at least 100 metres of width. That zone has
now been extended to 1.7 kilometres of strike and up to 150 metres of
width, and open in all directions.

Recent surface work included 38 rock chip samples, of which 26%
assayed greater than 1% copper and 50% greater than 0.2 % copper.
Highlights of the recent 38 assay results are:

Sample number     Cu (%)                Ag (g/t)

366587                0.75                      4.8

366588                1.28                      13.7
366589                2.62                      26.3

366590                1.29                      5.83

366591                 1.82                     29.8

366592                1.52                      10.9

366596                 3.95                     32.8

366597                 6.41                     27.3

366601                 2.13                     7.2

366606                 1.59                     10.8

366608                 0.58                     3.6

366610                 1.06                     5.1

366612                 0.87                     1.9

An initial petrographic study has identified bornite, chalcocite,
covellite and idaite as the primary copper minerals which appear
associated with hydrothermal alteration. Microscopic textural features
indicate that chalcocite, covellite and idaite are replacing bornite.
The nature of the replacement could be a late hydrothermal event or
supergene. The dominant alteration assemblage is represented by Iron -
epidote -) chlorite ) quartz ) calcite.

The andesitic host rocks of presumed Larimide age have undergone
hydrothermal alteration, represented by patches, cavity filling and
microbrecciation.

Additional and pending exploration on the Chunibas property
includes:

*  Continuous rock chip channel sampling over outcrops is
underway.
*  Follow-up more detailed petrographic studies to be initiated.
*  A trenching program between individual outcrops is being
evaluated. Success of this program will depend on the depth of cover
between outcrops.
*  Induced Polarization (I.P.), as well as ground magnetic surveys
are being considered to help define the boundaries of the system.

For related images, please visit the Chunibas Project on the
Company's website.

About San Marco

San Marco Resources Inc. is a Canadian mineral exploration company
with a portfolio of promising projects in mining-friendly Mexico,
including the Chunibas, Mariana and 1068 Projects in Sonora State.

San Marco actively pursues strategic project generation program
focused on high-caliber, low acquisition cost opportunities in
northwestern Mexico. The Company has a committed management team with
extensive experience in Mexico and a proven track record of building
shareholder value. San Marco currently has 64,716,276 issued and
outstanding shares.

On behalf of the Board of Directors:

Robert Willis, P. Eng.
President & CEO

Nancy Curry
info@sanmarcocorp.com

National Instrument 43-101 Disclosure

This news release has been approved by San Marco's CEO, Robert D.
Willis, P. Eng. a "Qualified Person" as defined in National Instrument
43-101, Standards of Disclosure for Mineral Projects of the Canadian
Securities Administrators. He has verified the data disclosed,
including sampling, analytical and test data, underlying such technical
information by reviewing the assay reports provided to San Marco by its
independent testing laboratory.

The Company has implemented quality assurance ("QA") and quality
control ("QC") programs to ensure sampling and analysis of all
exploration work is conducted in accordance with the best possible
practices. All sampling programs are carried out in a careful and
diligent manner using scientifically established sampling practices
designed and tested to ensure that the results are representative and
reliable. Quality control programs appropriate to the type of sample
and the mineralization are implemented, including such measures as
external blanks, standards and duplicate samples. The security of
samples from sample acquisition to analysis is a vital component of the
sampling process. Procedures include the use of secure core logging,
sampling, storage and preparation facilities as appropriate and the
prompt, secure and direct shipping of samples to the laboratories.
Appropriate sample security procedures are employed given the
geographic and topographic conditions and the logistics created by the
site location.

Forward Looking Information

Information set forth in this document may include forward-looking
statements. While these statements reflect management's current plans,
projections and intents, by their nature, forward-looking statements
are subject to numerous risks and uncertainties, some of which are
beyond the control of San Marco. Readers are cautioned that the
assumptions used in the preparation of such information, although
considered reasonable at the time of preparation, may prove to be
imprecise and, as such, undue reliance should not be placed on these
forward-looking statements. San Marco's actual results, programs,
activities and financial position could differ materially from those
expressed in or implied by these forward-looking statements.

Neither the TSX Venture Exchange nor the Investment Industry
Regulatory Organization of Canada accepts responsibility for the
adequacy or accuracy of this release.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1801500058TS11801502018-14153620180116