Source	MARKET NEWS
Date	01/17/2018
Time	05:37:02 AM

Company	 ATAC Resources Ltd.
Title	Summarizes 
Barrick's Successful 2017 Exploration





    CDNX Symbol: ATC











Press Release





ATAC RESOURCES LTD ("ATC-V")
- Summarizes Barrick's Successful 2017 Exploration Program On
- The Orion Project

ATAC Resources Ltd. ("ATAC") is pleased to announce a summary of
the comprehensive 2017 exploration program on the Orion Project,
located within the Rackla Gold Property, Yukon. The Orion Project
comprises the central portion of ATAC's Rackla Gold Property and is
subject to a $55 million earn-in agreement with Barrick Gold
Corporation ("Barrick") (see ATAC news release dated April 10, 2017).

As part of the earn-in requirements, Barrick must spend $10
million on exploration at the Orion Project by December 31, 2019.
Expenditures by Barrick in 2017 were ~$4 million.

The primary objective of Barrick's first exploration program was
to systematically establish a surface and sub-surface geologic and
structural framework for identifying favourable rocks. The following
work was completed on the Orion Project in 2017 to support this
objective:

//st

* Detailed mapping, prospecting and trenching;
* Extensive rock, soil and stream sediment sampling;
* Diamond and rotary air blast "RAB" drilling; and,
* Ground based gravity survey and Lidar terrain mapping.

//et

"Barrick's systematic and geoscience driven 2017 exploration
program at the Orion Project was very successful in quickly
establishing a better geological understanding of the large land
package of Orion," states Ed Cope, ATAC's Technical Advisor. "The
presence of robust Carlin-type alteration identified in diamond drill
holes well away from any surface geochemical anomalies demonstrates
that favourable environments for the development of gold mineralization
are more extensive than previously understood. 2018 will be an exciting
year as Barrick focuses on targeting gold mineralization."

Mapping and Prospecting

A substantial component of the 2017 exploration program was the
initiation of both regional-scale and target delineation geological
mapping. The mapping teams, made up of Barrick and ATAC geologists,
systematically mapped approximately 300 km of the eastern section of
the Orion Project area between June and September 2017. The mapping
resulted in a detailed classification of the Paleozoic stratigraphy and
a refined understanding of the complex structural environment. The
resulting data will be used to target favourable host rocks during
future drill campaigns. An updated Orion Project map can be found on
ATAC's website.

Diamond Drilling

Four stratigraphic diamond drill holes totalling 2,503 m were
positioned specifically outside known mineralization and pathfinder
soil geochemical anomalies in order to obtain an unaltered view of the
Orion area stratigraphy. Drill data including lithology, structure,
alteration and mineralogy was used in combination with major and trace
element geochemistry to characterise the stratigraphic setting of the
geologic units. Although drilling occurred outside of the known
mineralization and pathfinder footprint, favourable Carlin-type
observations included:

//st

* anomalous gold and elevated pathfinder elements (As, Sb, Hg and Tl) in
holes three and four highlighting the prospective nature of both of the
Anubis and Northern faults along their westward mapped extensions; and,
* several debris flow packages and turbidite sequences identified in
holes
two, three and four confirming important slope facies environments exist
throughout the Paleozoic sequence at Orion.

//et

RAB Drilling

Thirty-two holes totalling 1,532 m were completed on the Orion
Project in 2017. The RAB drilling tested the stratigraphy, alteration
and the mineralizing potential of bedrock within overburden covered
areas. The Pyramid target area was a particular focus of the RAB
drilling as little was known about the geological environment as it is
located in an area of low relief and significant surface cover.

Rock, Soil and Stream Sediment Sampling

An extensive rock, soil and stream sediment sampling program was
undertaken in 2017. This sampling program expanded coverage over known
Paleozoic stratigraphy that had not previously been assessed. As part
of the program, representative samples were collected for the purposes
of geochemical classification of lithology and the identification of
alteration suites. This data will be compiled into the existing
database to assist in the overall understanding of the geologic setting
and gold potential of the district.

Gravity Survey and Lidar

A ~50 km ground-based gravity survey was conducted between the
Anubis and Pyramid target areas. The gravity survey was performed to
assist in the identification of structures and characterization of
rocks within covered terrain. A fixed-wing based Lidar survey was also
conducted to provide better ground control and to improve the
identification of geologic contacts and structures below treeline.
Preliminary interpretation of results from the gravity survey indicate
good consistency with the regionally mapped geologic units while posing
some alternative structural geometries of buried units within the
Anubis Fault corridor.

Anubis Cluster and Previous Exploration by ATAC

Prior to Barrick's involvement on the Orion Project, ATAC
discovered Carlin-type gold mineralization at the Anubis Zone in 2012
through follow-up of an 18 km arsenic-in-soil anomaly. Between 2012 and
2016 ATAC completed ~5,000 m of diamond drilling within the Anubis
Cluster and highlights include 8.51 m of 19.85 g/t gold from the Anubis
Zone and 61.29 m of 2.75 g/t gold from the Orion Zone. Nine other
prospecting discoveries within the Anubis Cluster (Ana, Corona,
Columba, Dale, Dorado, Draco, Hydra, Lyra and Zodiac) have received
only cursory follow-up since their discovery in 2012.

The technical information in this news release has been approved
by Julia Lane, P.Geo., Vice President of Exploration for ATAC and a
qualified person for the purposes of National Instrument 43-101.

About ATAC

ATAC is a Yukon-based exploration company focused on developing
Canada's only known Carlin-type gold district at the Rackla Gold
Property. Recent work on the ~1,700 km2 property has resulted in a
positive Preliminary Economic Assessment for the Tiger Gold Deposit,
drilling of multiple high-grade Carlin-type gold zones and the
identification of numerous early-stage gold exploration targets. ATAC
and Barrick Gold Corporation recently partnered to explore the Rackla
Gold Property's Orion Project, with Barrick having the option to earn
up to 70% of Orion by spending $55 million in exploration. ATAC is
well-financed with approximately $13 million in its treasury and
recently completed an approximately $10 million exploration program at
the Osiris and Rau Projects (which are not subject to Barrick's earn-in
right), while concurrently working with Barrick to advance the 780 km2
Orion Project.

On behalf of Management and the Board of Directors
of ATAC Resources Ltd.
Graham Downs, President and CEO

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.

TEL:  604-687-2522 x260  Vanessa Pickering
Manager, Corporate Communications
ATAC Resources Ltd.
EMAIL:  info@atacresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1801600011TS11801600528-05353120180117