Source	Marketwire
Date	01/17/2018
Time	07:43:15 AM

Company	 AMEX EXPLORATION INC.
Title	Amex Reports High Grade Results of Up to 47.2 g/t Au Over 1.0 Meter from 
Core Section with Free Coarse Gold in Hole PE-2017-03 at Perron





    CDNX Symbol: AMX











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

January 17, 2018

Amex Reports High Grade Results of Up to 47.2 g/t Au Over 1.0 Meter from Core 
Section with Free Coarse Gold in Hole PE-2017-03 at Perron


MONTREAL, QUEBEC--(Marketwired - Jan. 17, 2018) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex" or the "Corporation") is pleased to report that it has 
just received initial analytical results from the core samples where multiple 
free coarse gold were identified in hole PE2017-03 (see PR2018-01-04). The 
section of the hole where free coarse gold was observed is from a depth of 
311.9 meters to 316.56 meters. In fact, two core sections with free coarse gold 
were sent to the laboratory, the first one from a depth of 311.9 to 312.47 
returned a value of 16.7 g/t Au over 0.57 meters and the second one from a 
depth of 315.56 to 316.56 returned a value of 47.2 g/t Au over 1.00 meter, 
leaving an overall intersection with an average grade of 12.22 g/t Au over 
4.66(i)meters. ((i)Interval intersected along the hole, undetermined true 
thickness)

This high grade gold zone is hosted within a highly sericitized and sheared 
rhyolite unit of about 5-10m that corresponds very well with a similar altered 
rhyolite unit intersected in hole PE-2013-04 where free coarse gold within some 
quartz veining was also noted and values of up to 12.93 g/t Au over 0.30 meters 
were intersected. This specific zone was the main follow-up target of hole 
PE-2017-03 and was collared at about 75 meters to the East and 50 meters to the 
North of hole PE-2013-04. It is important to note that this gold zone is of 
orogenic type and is not directly related or of the same type as that the 
so-called discovery gold-rich VMS polymetallic mineralization intersected in 
hole PE-2013-03 which is located some 800 meters to the West (see PR2017-11-13).

"I am very pleased with the initial results from our first few holes of the 
Perron drilling program," said Jacques Trottier PhD, Executive Chairman of 
Amex. "Hole PE2017-03 is intersecting what seems to be a whole new gold bearing 
zone at Perron and is quite separate from our VMS target which is about 1 
kilometre away. A property as large as Perron, which covers an important 
segment of an entire greenstone belt in that region of Quebec, has the 
potential to host multiple gold discoveries."

Amex has also received analytical results from hole PE-2017-01A (located in the 
same area) to hole PE-2017-05 (which is the deepening of hole PE-2013-04). In 
addition Amex has re-sampled intervals which were lacking data from the 
mineralized zone of hole PE-2013-04. The company is currently compiling and 
integrating these results and will announce them as soon as they are available.

UPDATE ON CURRENT DRILLING

Before the Holiday break, five drill holes were completed (holes PE-2017-01A to 
PE-2017-05) totalling 1,341 meters. On January 5th drilling resumed and on 
January 15th, hole PE-2017-06 totalling 408 meters was completed. Nine 
additional holes on nine different targets totalling about 2,727 meters are 
still planned to be drilled on the Perron property before the end of March 2018.

Nabil Tarbouche, Geologist of Explo-Logik, a Qualified Person as defined by 
Canadian NI 43-101, Revised and approved the geological information of the 
current drilling reported in this news release. The drilling campaign and the 
quality control program has been planned and supervised by Nabil Tarbouche and 
Amex's management. The QAQC include insertion of blank, standard or duplicate 
every 10 samples on average. The gold value is estimated by Fire Assay 
(AU-ICP-21) by ALS Mineral, Val d'Or. 823 samples were submitted to ALS Mineral 
for gold, base metals and major and trace elements. Core Logging and sampling 
was realized by Lisa Cote, Trainee Geologist of Explo-Logik under supervision 
of Nabil Tarbouche.

About Amex

Amex Exploration Inc. is a junior mining exploration company, the primary 
objective of which is to develop and bring into production viable gold and base 
metals deposits in mining-friendly jurisdictions. Amex has multiple highly 
prospective projects: the 100% owned Perron gold project located 110 kilometres 
north of Rouyn Noranda, Quebec, consisting of 116 adjacent claims covering 4518 
hectares; the 100% owned Eastmain River gold properties consisting of 135 
claims covering 7,102 hectares and the 100% owned Lebel-sur-Quevillon project 
in Quebec, comprising 263 claims covering 14,743 hectares. In addition, Amex 
has an option agreement to acquire a 100% interest in the Gowan Property 
located near the Kidd Creek Mine.

Forward-looking statements:

Except for statements of historical facts, all statements in this news release 
regarding, without limitation, future plans and objectives are forward-looking 
statements which involve risks and uncertainties. There can be no assurance 
that such statements will prove to be accurate. Actual results and future 
events could differ materially from those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Amex Exploration
Victor Cantore
President and Chief Executive Officer
514-866-8209

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=602011844