Source	MARKET NEWS
Date	01/18/2018
Time	06:34:10 AM

Company	 Fjordland Exploration Inc.
Title	Commander and Fjordland Announce Results from Dr





    CDNX Symbol: FEX











Press Release





Commander and Fjordland Announce Results from Drilling at SouthVoisey's Bay 
Nickel Project, Labrador --->@NEWS RELEASE
COMMANDER RESOURCES LTD ("CMD-V;CMDRF-0")
FJORDLAND EXPLORATION INC. ("FEX-V")
- Commander and Fjordland Announce Results from Drilling at South
- Voisey's Bay Nickel Project, Labrador

Commander Resources Ltd. ("Commander") and project partner
Fjordland Exploration Inc. ("Fjordland") provide results from the
recent drilling at their South Voisey's Bay nickel-copper-cobalt
project (the "SVB Property") located 80 kilometres south of Vale's
Voisey's Bay nickel mine located in Labrador, Canada. The exploration
program was completed in October 2017 and comprised 1,469 metres of
drilling in eight holes and accompanying borehole geophysics for five
of the holes.

Best results were from holes 17-2 which returned 0.8 metres
grading 0.63% nickel, 0.30% copper and 0.1% cobalt and hole 17-6 which
returned 3.9 metres grading 0.37% nickel, 0.27% copper and 0.1 %
cobalt.  The intersections are semi-massive to massive sulphide
comprised of pyrrhotite, pentlandite and chalcopyrite.  Both
intersections occur within or at the base of the Worm Gabbro within a
sequence of troctolite.  They are overlain by several metres of blebby
and net textured sulphides.   Holes 17-3, 5 and 7 returned low nickel
values. Three holes, 17-1, 17-4 and 17-8, located 1.8 km south of hole
17-6 tested a prominent low angle conductor within paragneiss adjacent
to an arm of the Worm Gabbro and all three holes encountered zones of
high sulphide with low nickel values hosted by structures and sometimes
accompanied by mixed gabbro breccia.  Borehole Electro-Magnetic (BHEM)
data, collected by Crone Geophysics in November, defined several
extremely high conductivity targets between holes 17-1, 17-4, and 17-8.
In addition, BHEM data from holes 17-6 and 17-7 delineate a strong
conductor associated with the intersected sulphides, and an even
stronger non-decaying off-hole conductor.

Drill results are summarized below in Table 1 and hole locations
in Table 2 at the end of this release.  Sections and plans will be
posted to the Company website.  Reported core lengths are estimated to
be true width for hole 17-6, while hole 17-2 is of unknown orientation.


Table 1: Results

//st

Hole     From(m)   To (m)   length (m)   Ni (%)   Co (%)   Cu (%)

FL17-2   52.4      53.2     0.8          0.63     0.11     0.30

FL17-6   45.3      49.2     3.9          0.37     0.10     0.27

//et

Discussion

The large 29,400 Ha SVB Property is in central Labrador 80
kilometres south of Vale's Voisey's Bay Nickel mine and covers parts of
the Pants Lake Gabbro Complex. The Pants Lake Complex contains host
rocks with alteration and nickel mineralization styles consistent with
high nickel prospectivity. This drill program tested a single
exploration target centred of a portion of the Worm Gabbro, a 200 metre
thick possible feeder dyke to larger magma bodies or chambers located
both north and south of the area.  Drilling was centred on modeled
conductors derived from re-processed historical UTEM-3 surveys
conducted in 2002 and 2014. Targeting incorporated recent geological
concepts being successfully applied at the Voisey's Bay Mine wherein
structure plays an important ore control role and where massive
sulphide accumulations may also occur in wall rock structures.

Dawn Evans-Lamswood, project manager and former head of
brownfields exploration at the Voisey's Bay Mine states, "Drill holes
within the wall rock paragneiss (in particular hole 17-4) intersected a
feeder environment that can be described as a "nursery" for sulphide
production, an essential ingredient for the production of high grade
sulphides. Key ingredients include ultramafic cumulates, digested
paragneiss, magmatic contamination and structural controls to focus
wall rock digestion, sulphide production and distribution. The
observations suggest the system is not rootless, that it has a sulphide
source rock and favorable structural constraints and establishes the
SVB property as hosting a Voisey's Bay-styled nickel environment."

Ongoing work includes property wide re-processing of additional
historical EM data including UTEM-3 surveys and Crone pulse EM surveys.
Initial focus is on the large South Gabbro body where limited
historical drilling has retuned elevated nickel within basal olivine
gabbro units and in wall rock veins.

Expenditures by Fjordland have resulted in the increase of their
property interest to 35%.  Under the terms of the Commander/Fjordland
option agreement, announced on June 5, 2017, Fjordland may earn up to a
100% interest in the property by paying Commander combined cash
payments of $290,000, completing $8.0 million in exploration
expenditures and issuing to Commander an aggregate of 4.5 million
shares of Fjordland.  Upon Fjordland acquiring a 100% interest in the
project, Commander will retain a 2% NSR with Fjordland having the right
to buy down 50% of the Royalty for a payment of $5,000,000 as a cash
payment, or a cash payment equal $2,500,000 plus the issuance of shares
having a fair market value of 50% of the buy down amount.  Commander
will receive a $10,000,000 advance royalty payment at the commencement
of commercial production. Fjordland is 30% held by an affiliate of High
Power Exploration Inc. who have separately entered into a funding
agreement with Fjordland to provide up to $7.4 million in expenditures
and $290,000 in property payments, following which Fjordland has agreed
to assign a 65% project interest in SVB to HPX (see FEX news release
dated August 28, 2017).   HPX is a privately owned, metals-focused
exploration company deploying proprietary in-house geophysical
technologies to rapidly evaluate mineral prospects. The HPX technology
cluster comprises systems for targeting, modelling, survey
optimization, acquisition, processing and interpretation.  HPX has a
highly experienced board and management team led by Co-Chair and Chief
Executive Officer Robert Friedland.

QA/QC

Drill core was NTQ with recoveries typically above 90 per cent.
After drilling, the core is logged for geology, structure and
geotechnical characteristics, marked up for sampling, and photographed
on site. The cores for analyses are marked for sampling based on
geological intervals with individual samples 1.0 m or less in length.
They are cut in half lengthwise, with a rock saw on site. One half-core
are stored on site for future reference. The other with half-core are
bagged in individual plastic bags along with ID tag and sealed.  The
individual plastic sample bags are then placed into rice bags labelled
with sample ID's for all enclosed samples (typically 3 to 5 samples per
rice bag); and then the rice bag is sealed with packing tape. The rice
bags are sent by commercial carrier to Eastern Analytical Ltd,
Springdale NL. for assaying. A QA/QC program, including insertion of
standards, blanks and duplicates with regular samples under, the
supervision of Gary Thompson, P.Geo. was undertaken.

Upon arrival at Eastern Analytical rice bags and sample bags are
inspected for tampering or damage during transportation. The samples
are dried and then crushed to 80% -10mesh, and a 250g split is then
pulverized to 95% 150mesh. A 200mg subsample is dissolved in four acids
and analyzed by ICP-OES for 34 elements. Samples with significant Ni,
Cu or Co are re-analyzed by atomic absorption following a three acid
digestion. Eastern Analytical is an ISO17025 certified laboratory. On
site supervision and core logging was by Dawn Evans-Lamswood, P, Geo.

Table 2- Drill Collars

//st

Hole     Easting   Northing   Elev (m)   LENGTH(m)   Az    Dip

FL17-1   567500    6147644    427.8      212.3       220   -65

FL17-2   567430    6148949    436        153         210   -55

FL17-3   567302    6148761    408.4      150.55      180   -50

FL17-4   567676    6147783    421        271.1       170   -50

FL17-5   566202    6148848    418.4      157.2       180   -60

FL17-6   566660    6149010    450        150.85      180   -50

FL17-7   566600    6149060    451        225.95      180   -50

FL17-8   567598    6147584    408.4      151.55      220   -65

//et

Robert Cameron, P. Geo. is a qualified person within the context
of National Instrument 43-101, and has read and takes responsibility
for the technical aspects of this release.

About Commander Resources:

Commander Resources is a Canadian focused exploration company that
has leveraged its success in exploration through partnerships and sale
of properties, while retaining equity and royalty interests. Commander
has a portfolio of base and precious metal projects across Canada and
significant equity positions in Maritime Resources Corp. (MAE-TSX.V)
and Aston Bay Holdings (BAY-TSX.V). Commander also retains royalties
from properties that have been partnered, optioned or sold.

On behalf of the Board of Directors Robert Cameron, P. Geo.
President and CEO

For further information, please call: Robert Cameron, President
and CEO Toll Free: 1-800-667-7866 info@commanderresources.com

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This news release may include forward-looking statements that are
subject to risks and uncertainties. All statements within, other than
statements of historical fact, are to be considered forward looking.
Although the Company believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions, such
statements are not guarantees of future performance and actual results
or developments may differ materially from those in forward-looking
statements.  Factors that could cause actual results to differ
materially from those in forward-looking statements include market
prices, exploitation and exploration successes, continued availability
of capital and financing, and general economic, market or business
conditions.  There can be no assurances that such statements will prove
accurate and, therefore, readers are advised to rely on their own
evaluation of such uncertainties.  We do not assume any obligation to
update any forward-looking statements except as required under the
applicable laws.

TEL: 604-685-5254    COMMANDER RESOURCES LTD
FAX: 604-685-2814
E-mail: c.divito@commanderresources.com
Website: http://www.commanderresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1801700031TS11801700840-06314220180118