Source	MARKET NEWS
Date	01/23/2018
Time	05:55:38 AM

Company	 Great Thunder Gold Corp.
Title	Drilling Results from Chubb Lithium Project





    CDNX Symbol: GTG











Press Release





Drilling Results from Chubb Lithium Project --->@NEWS RELEASE
GREAT THUNDER GOLD CORP ("GTG-V;MLBVF-0")
- Drilling Results from Chubb Lithium Project

Great Thunder Gold Corp. is pleased to announce that it has
received assay results from its drilling program at its 100%-owned
Chubb Lithium Project located approximately 32 kilometres north of Val
d'Or, Quebec.

Highlights from Hole C-17-01 include 1.33% of lithium oxide
(Li(sub)2(/sub)O) over 5.3 metres and 1.15% Li(sub)2(/sub)O over 2.1
metres. Hole C-17-02 yielded 0.9% Li(sub)2(/sub)O over 3.6 metres.
Following are the complete results.

//st
Hole     UTM     UTM    From     To     Length   Li2O    Be      Cs
Rb      Ta     Weighted
No.     East   North    (m)     (m)     (m)     (%)    (ppm)   (ppm)
(ppm)   (ppm)   average

Li2O%

C-17-01   280    5       55.00   56.00   1.00     1.46   340     72.5
1180    32      1.33%
607    354
Li2O /
622
5.3 m

56.00   57.00   1.00     1.04   183     139
2920    19.55

57.00   58.00   1.00     2.40   220     93.6
1380    32.3

58.00   59.00   1.00     1.35   138.5   150
3870    8.42

59.00   60.30   1.30     0.63   210     179.5
3180    14.3

64.00   65.00   1.00     1.06   190.5   84.5
1275    17.75   1.15%

Li2O /

2.1 m

65.00   66.10   1.10     1.23   138.5   107.5
1700    20

C-17-02   280    5       11.60   12.60   1.00     0.02   210     83.8
720     59.9
615    354
726

12.60   13.60   1.00     0.02   260     100.5
836     38

21.70   22.40   0.70     0.83   131.5   121.5
2030    27.1

32.80   33.80   1.00     0.71   145     107.5
1140    27.2    0.9%

Li2O /

3.6 m

33.80   34.80   1.00     0.69   153     135.5
2500    33.6

34.80   35.80   1.00     1.55   148.5   84
1810    20.8

35.80   36.40   0.60     0.47   142.5   102
1825    26.5

C-17-03   280    5       90.00   90.70   0.70     0.06   177     265
780     50.2
636    354
819

//et

Great Thunder's President, Kevin Whelan, said, "We are excited by
the assay results from our recent drilling program. Not only did we
confirm historical data, but we extended the depth of lithium-bearing
pegmatites."

The three holes, totaling 306 metres, were drilled from December 8
to December 13 to verify several induced polarization anomalies
previously located on the showings area. The holes were drilled with an
azimuth of 60 degrees and a dip at collar of -45 degrees, and were
spaced approximately 100 metres apart. All lengths reported are core
length and insufficient work has been done to establish the true width
of the pegmatites.

A total of 74 samples were collected and sent to the ALS Laboratory
in Val d'Or, Quebec. Several blanks were added as a measure of control
for contamination, no standards for Li(sub)2(/sub)O were used except
those included by the laboratory. Samples were assayed using protocol
ME-MS89L, which is a multi-elements package specially developed for
lithium in pegmatites analysis using sodium peroxide fusion and ICP-MS
methodology. ALS released the analytical results for lithium in ppm
lithium; for clarity the Company has reported the results as
Li(sub)2(/sub)O, using a conversion factor of 2.153.

About the Chubb Lithium Project

The Chubb Lithium Project is situated within the Preissac-Lacorne
plutonic complex of the Abitibi Greenstone Belt, the complex forming
one of the best prospective areas for lithium mineralization. The
plutonic complex generated the Quebec Lithium Project - located 60
kilometres north of Val d'Or, Quebec - for which Canada Lithium Corp.
reported proven and probable reserves of 17.1 million tonnes grading
0.94% Li(sub)2(/sub)O according to a feasibility study update by Canada
Lithium Corp. dated October 12, 2012.

The Chubb Lithium Project lies 32 kilometres north of Val d'Or and
consists of 35 contiguous recorded mineral claims with a total area of
1,509 hectares. The property's geology is dominated by quartz
monzodiorite and metasomatized quartz diorite (tonalite). A swarm of
spodumene-rich granitic pegmatite dykes intrude fractures and small
faults within the plutonic rocks. The pegmatite dykes are 1 to 6 metres
thick, oriented 345 - 350 and vary in length from 25 to 250 metres.
They are crudely zoned, some having quartz cores and border zones of
aplite. The granitic pegmatites are composed of quartz, albite and/or
cleavelandite, K-feldspar, muscovite, with 5 to 25% spodumene. There
are three important granitic pegmatite dykes containing spodumene
mineralization (Dyke #1, #2 and Main Dyke).

Exploration of the Chubb Lithium Project persists since the early
1950s and has consisted mainly of mapping, trenching, geophysical
surveys and diamond drilling. The best historical drilling
intersections were obtained in 1994 by Abitibi Lithium Corp., producing
intervals of 3.72 m @1.78 wt. % Li(sub)2(/sub)O, 2.75 m @1.00 wt. %
Li(sub)2(/sub)O and 2.38 m @1.25 wt. % Li(sub)2(/sub)O. In 2010,
Mineral Hill Industries Ltd. carried out magnetic and IP geophysical
surveys, mapping, channel sampling and grab sampling in the area
surrounding the three principal spodumene-bearing dykes. The main dyke
- which is 300 m long - was shown to have Li(sub)2(/sub)O concentration
of 1.00 wt. % (n=41).

About Great Thunder Gold Corp.

Great Thunder Gold Corp. is a mineral exploration and development
company based in Vancouver, British Columbia, Canada. Our Company
mandate is to acquire high quality exploration assets with a specific
focus on gold and lithium. We intend to build NI 43-101 compliant
resource determinations for each of our gold and lithium projects in
order to demonstrate their long-term economic viability. In the case of
our lithium projects, we are determined to define the mineralogical and
metallurgical characteristics for efficient recovery of this coveted
metal, to further the Company's plan to become an integral part of the
rechargeable battery storage technology supply chain. Great Thunder is
managed by an experienced team of mining professionals with extensive
operating and financial experience.

The technical contents of this release were approved by Donald
Theberge, P.Eng., MBA, an independent Qualified Person as defined by
National Instrument 43-101.

ON BEHALF OF THE BOARD
Kevin C. Whelan, President
Direct line: (250) 474-6640

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TEL: 604-682-3701    GREAT THUNDER GOLD CORP
FAX: 250-590-1167
E-mail: info@greatthundergold.com
Website: http://www.greatthundergold.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1802200016TS11802200676-05522520180123