Source	Marketwire
Date	01/25/2018
Time	05:55:27 AM

Company	 AMEX EXPLORATION INC.
Title	Amex Intersects 7.89 g/t Au Over 7.5 Meters in Hole PE-2017-03 and 2.63 
g/t Over 10.5 Meters in Hole PE-2017-01A at Perron





    CDNX Symbol: AMX











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

January 25, 2018

Amex Intersects 7.89 g/t Au Over 7.5 Meters in Hole PE-2017-03 and 2.63 g/t 
Over 10.5 Meters in Hole PE-2017-01A at Perron


MONTREAL, QUEBEC--(Marketwired - Jan. 25, 2018) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex" or the "Corporation") is very pleased to report the 
complete results from hole PE-2017-03 that was partly reported in Amex last 
press release dated January 16th 2017 where a high grade gold intercept was 
reported to contain multiple free coarse gold grains with a value of 12.22 g/t 
Au over 4.66 meters, including 16,7 g/t Au over 0.57 meter and 47.2 g/t Au over 
1.00 meter.

This high grade zone is in fact part of a broader mineralized zone 
characterized by a large envelope of highly sericitized and silicified host 
rhyolite unit that has returned an average value of 7.89 g/t Au over 7.5 meters 
(from depth of 310.5 to 318.0 meter). A second well mineralized wide zone was 
also intersected in the same hole PE-2017-03 at about a hundred meters deeper 
averaging 0.81 g/t Au over 76.5 meters (from 406.5 to 483.0 meter) including 
multiple higher grade zones of 5.10 g/t Au over 1.5 meters (from 406.5 to 408.0 
m), and 3.91 g/t Au over 4.5 meters (from 447.0 to 451.5 m) including 9.67 g/t 
Au over 1.5 meter (from 448.5 to 450.0 m) (see Table 1).

/T/

----------------------------------------------------------------------------
Hole                      From         To        Length (m)      Au (g/t)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
PE-2017-01A               201.0       240.0         39.0           1.40
----------------------------------------------------------------------------
PE-2017-01A incl          214.5       225.0         10.5           2.63
----------------------------------------------------------------------------
PE-2017-01A incl          214.5       216.0          1.5           6.66
----------------------------------------------------------------------------
PE-2017-01A incl          222.0       232.5         10.5           2.07
----------------------------------------------------------------------------
PE-2017-01A incl          222.0       228.0          6.0           3.18
----------------------------------------------------------------------------
PE-2017-01A incl          222.0       225.0          3.0           5.62
----------------------------------------------------------------------------
PE-2017-01A incl (i)      223.5       225.0          1.5          9.55(i)
----------------------------------------------------------------------------
PE-2017-01A incl          238.5       240.0          1.5           5.12
----------------------------------------------------------------------------

----------------------------------------------------------------------------
PE2017-03                 310.5       318.0          7.5           7.89
----------------------------------------------------------------------------
PE2017-03 incl            311.9      316.56         4.66           12.22
----------------------------------------------------------------------------
PE2017-03 incl (i)        311.9      312.47         0.57         16.70(i)
----------------------------------------------------------------------------
PE2017-03 incl (i)       315.56      316.56          1.0         47.20(i)
----------------------------------------------------------------------------
PE2017-03                 406.5       483.0         76.5           0.81
----------------------------------------------------------------------------
PE2017-03 incl            406.5       423.0         16.5           1.20
----------------------------------------------------------------------------
PE2017-03 incl            406.5       408.0          1.5           5.10
----------------------------------------------------------------------------
PE2017-03 incl            447.0       451.5          4.5           3.91
----------------------------------------------------------------------------
PE2017-03 incl            448.5       450.0          1.5           9.67
----------------------------------------------------------------------------
PE2017-03                 498.0       510.0         12.0           0.56
----------------------------------------------------------------------------
PE2017-03 incl            502.5       510.0          7.5           0.73
----------------------------------------------------------------------------
PE2017-03 incl            502.5       505.5          3.0           1.01
----------------------------------------------------------------------------
Table 1: Geochemical analysis was executed by ALS Mineral in Val D'Or.
(i) Coarse grain of gold.
Note that those are Intervals intersected along the hole, the true thickness
are undetermined.

/T/

In addition, Amex also received complete results of hole PE-2017-01A that 
returned values of 2.63 g/t Au over 10.5 meters (from 214.5 to 225.0 m) 
including higher grade sub intervals of 6.66 g/t Au over 1.5 meter (from 214.5 
to 216.0 m) and 9.55 g/t Au over 1.5 meter (from 223.5 to 225.0m). This 
intersect is part of a wider zone of 39.0 meters grading an average of 1.40 g/t 
Au (see table 1) that is also hosted by highly altered rhyolite similar to the 
host rock unit of the mineralized zones of hole PE-2017-03.

These two holes were planned with the objective of testing the lateral 
extension of the mineralized gold intersect of hole PE-2013-04 drilled in a 
previous campaign in 2013 that returned values of up to 12.93 g/t Au over 0.3 
meter. Amex has also received results from its re-sampling of some sections 
that were not previously available to complete the average content of the 
mineralized zone of hole PE-2013-04 (see Table 2). Accordingly, hole 
PE-2017-01A was collared at about 75 meters to the West of hole PE-2013-04 
while hole PE-2017-03 was collared at some 75 meters to the North-East of hole 
PE-2013-04.

/T/

----------------------------------------------------------------------------
Hole                      From         To        Length (m)      Au (g/t)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
PE-2013-04                200.7       219.4         18.7           0.53
----------------------------------------------------------------------------
PE-2013-04 incl           206.3       214.7          8.4           1.04
----------------------------------------------------------------------------
PE-2013-04 incl           207.7       211.2          3.5           1.71
----------------------------------------------------------------------------
PE-2013-04 incl (i)       210.9       211.2          0.3         12.93(i)
----------------------------------------------------------------------------
Table 2: Geochemical analysis was executed by ALS Mineral in Val D'Or.
(i) Coarse grain of gold.
Interval intersected along the hole, undetermined true thickness.
Hole PE-2013-04 was re-sampled in 2017, with historic results.

/T/

Jacques Trottier, PhD, Executive Chairman of Amex said, "Even though we are 
just beginning to test this new gold target, the results from these two holes 
combined with the historical results, showing similar mineralization and host 
rock, leads to the hypothesis that mineralization in these three holes could be 
part of the same wide gold bearing structure. This would constitute a new gold 
zone located in the Eastern part of the Perron property that can be now be 
followed over a strike length of at least 150 meters and to a minimum vertical 
depth of 400 meters. Our next step is to test this theory with much closer 
spaced follow-up drill holes and to also test its lateral and depth extensions 
in a next drill campaign. I am very pleased with these first impressive results 
in this new promising area and looking forward to seeing the results of the 
other targets that are still to be drilled, especially in the area of the 
"discovery hole" PE-2013-03 located some 800 meters to the west of this new 
gold bearing area. Drilling is underway on these targets and we will be back 
with more results as we receive them."

Nabil Tarbouche, Geologist of Explo-Logik, a Qualified Person as defined by 
Canadian NI 43-101, revised and approved the geological information of the 
current drilling reported in this news release. The drilling campaign and the 
quality control program has been planned and supervised by Nabil Tarbouche and 
Amex's management. The QAQC include insertion of blank, standard or duplicate 
every 10 samples on average. The gold value is estimated by Fire Assay 
(AU-ICP-21) by ALS Mineral, Val d'Or. 1,222 samples were submitted to ALS 
Mineral for gold, base metals and major and trace elements up to now. Core 
Logging and sampling was realized by Lisa Cote, Trainee Geologist of 
Explo-Logik under supervision of Nabil Tarbouche.

About Amex

Amex Exploration Inc. is a junior mining exploration company, the primary 
objective of which is to develop and bring into production viable gold and base 
metals deposits in mining-friendly jurisdictions. Amex has multiple highly 
prospective projects: the 100% owned Perron gold project located 110 kilometres 
north of Rouyn Noranda, Quebec, consisting of 116 adjacent claims covering 4518 
hectares; the 100% owned Eastmain River gold properties consisting of 135 
claims covering 7,102 hectares and the 100% owned Lebel-sur-Quevillon project 
in Quebec, comprising 263 claims covering 14,743 hectares. In addition, Amex 
has an option agreement to acquire a 100% interest in the Gowan Property 
located near the Kidd Creek Mine.

Forward-looking statements:

Except for statements of historical facts, all statements in this news release 
regarding, without limitation, future plans and objectives are forward-looking 
statements which involve risks and uncertainties. There can be no assurance 
that such statements will prove to be accurate. Actual results and future 
events could differ materially from those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Amex Exploration
Victor Cantore
President and Chief Executive Officer
514-866-8209

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=602133795