Source	MARKET NEWS
Date	01/26/2018
Time	06:12:34 AM

Company	 Sandspring Resources Ltd.
Title	Toroparu Gold Project Update





    CDNX Symbol: SSP











Press Release




[200/News Release]SSPVSANDSPRING RESOURCES LTDJAN 26 2018  06:10 AM
Toroparu Gold Project Update --->@NEWS RELEASE
SANDSPRING RESOURCES LTD ("SSP-V;SSPXF-0")
- Toroparu Gold Project Update

Sandspring Resources Ltd. ("Sandspring" or the "Company") is
pleased to announce results from phase one of its 2017 - 2018
exploration program (the "Program") at its 7.1-million-ounce resource
(Measured & Indicated) Toroparu Gold Deposit ("Toroparu") 1 in Guyana,
South America. The Program was announced in the Company's press release
of September 18, 2017.

Phase One targeted mineralization in weathered saprolite and
shallow fresh rocks in the Sona Hill and Wynamu Prospect Areas (Fig.
1). Highlights include:

*  12.07 g/t over 5.05m* in Sona Hill Drill (SOD120) (step-out),
1.35 g/t over 9m and 1.96 g/t over 8m in SOD113 (step-out), 1.78g/t
over 16.79m in SOD128 (infill), and 5.58 g/t over 3.96m in SOD128
(infill) from 3,119m of exploratory, step-out, and infill drilling at
Sona Hill.

*  1.68 g/t over 16.5m* in Wynamu Drill hole 22 (WYD022)
(exploration), 1.72 g/t over 6.15m in WYD 035 (exploration), 1.04 g/t
over 17.2m in WYD040 (exploration), and 1.54 g/t over 5.2m, 1.25 g/t
over 3.9m, & 1.92 g/t over 10.23m in WYD043 (exploration) from 2,813.5m
of exploratory drilling at Wynamu Hill.

*All results reported as true widths

To view Fig 1. Location Map, please visit the following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/e9debd9d-55d1-4e82-9632-
0c243c0d8495

The Sona Hill maiden resource estimate (Feb 2017) increased total
resources for the Toroparu project to 7.1 Moz. Measured & Indicated
(M&I) and 3.3 Moz. Inferred (Inf) ounces of gold. Significantly, the
weathered saprolite gold resource estimate increased by 158% to 218,600
M&I and 330,400 Inferred ounces of gold with the addition of with
50,200 Indicated and 70,400 Inferred ounces from Sona Hill. 1

An analysis by SRK Consulting (US) Inc. conducted in 2017
indicated that a potentially positive economic trade-off exists for an
expanded startup saprolite leach operation at Toroparu assuming
sufficient saprolite reserves can be defined from the resources defined
at Toroparu and Sona Hill.

The drilling portion of the Program was designed to target
conversion of these resources to reserves and explore for additional
mineralization in saprolite and shallow fresh rocks adjacent and within
the Sona Hill Resource and Wynamu Prospect Areas.

Phase Two of the Program commenced on January 9th and is expected
to be completed by March 31st 2018. Phase Two includes 6,350m of infill
drilling at Sona Hill targeting conversion of the 241,000 ounces of
Inferred gold resource, 1,850m of additional step-out and infill
drilling at Wynamu Hill, and 1,600m of exploration drilling at Ameeba
Hill.

Otomung saprolite geochemistry and Kurupung Hydroelectric Project

The Program's geochemical surveys planned for the Otomung
Concession are complete. Two areas with anomalous gold values have been
identified as potential drilling targets. Additional exploratory work,
including trenching across these areas is underway to confirm the
presence of mineralization prior to a drilling decision being made.

Sandspring has continued to do work under its Memorandum of
Understanding with the Government of Guyana for the development of the
Kurupung River Hydroelectric Project, a run-of-river hydroelectric
project located at Kumerau Falls, approximately 50km southwest of
Toroparu. Sandspring completed a site visit with hydropower experts
from Hydroscience Consulting and Knight Piesold Consulting in November
2017 and expects to have a pre-feasibility report for the project in
1Q2018. The Company is evaluating the optimal size of the project as
the site can support various levels of power production.

Rich Munson, CEO states: "Our exploration program has expanded our
Indicated and Inferred resources and continues to report excellent
results. These results are supportive of our interpretations of the
potential resources available at Sona Hill and Wynamu. The continuing
drilling program will be an important planning tool for the feasibility
study for Toroparu with additional results due from exploration and
infill drill holes as they are reported. Sona Hill and Wynamu are seen
as feeders for the Toroparu processing plant in the early years of
operation, buoying the economics of the project through its early
life."

"We are also excited about the results of the ongoing work on the
Hydroelectric Project. The advancement of the Hydroelectric Project,
which will have a very significant impact on our operating costs, and
the potential enhancement of a start-up plan for Toroparu from the
additional saprolite ore underpin the development plans for the 7.1
million ounce (M&I) project," continued Mr. Munson.

2017 Program - Sona Hill Drilling

The Company has received assay results from 22 core holes (3,119m)
drilled within the Sona Hill Prospect during November and December
2017. Highlights of the boreholes (SOD110 to SOD131) are presented in
the list below.

//st

Highlights from the Sona Hill Drill Program - borehold SOD110 to SOD131

Sona Hill - Highlighted Gold Intercepts

HoleID  From   To (m)  True  Weighted HoleID   From     To     True Weighted
(m)            Width Av. Au            (m)      (m)    Width  Av. Au
(m)   Grade                             (m)    Grade
(g/t)                                    (g/t)

SOD113  193.5  202.5    9    1.35     SOD127   154.5    159     4.5   3.70

Incl    194.75 195.74   0.99 5.43     Incl     156      157.1   1.1   13.40

SOD113  222    230      8    1.96     SOD127   168      172.5   4.5   1.27

Incl    226.68 230      3.32 3.85     Incl     169.5    171     1.5   2.29

SOD114  193.06 195.45   2.4  2.87     SOD128   0        20.5    16.79 1.78

SOD114  236.84 239.26   2.4  6.41     Incl     14.5     16      1.23  6.20

SOD120  247.5  252.55   5.05 12.07    SOD128   39.5     44.28   3.92  5.58

Incl    249.1  250.34   1.24 48.40    Incl     39.5     41.44   1.59  13.10

SOD124  145.5  148.5    3    1.22     SOD129   4        20.5    14.95 3.11

SOD125  183.88 187.89   4.01 2.55     Incl     5.5      8.5     4.08  6.38

Incl    187.04 187.89   0.85 5.51     SOD130   16       23.28   5.96  1.07

SOD127  93     96.51    3.51 2.10     SOD130   47.5     52.62   4.19  3.02

SOD127  109.24 115.5    6.26 3.55     Incl     47.5     50.72   2.64  4.29

Incl    110.79 111.64   0.85 18.60    SOD130   57       59.64   2.16  2.43
SOD127  126.86 131.39   4.53 1.42     SOD130   65.81    69.72   3.2   1.25

Incl    128.97 130.15   1.18 2.71     SOD130   121.95   135     10.69 1.68

Incl     126.12   127.7   1.29  6.60

* Results presented are true thickness of the mineralized zone

//et

Hard rock mineralization was first discovered at Sona Hill in 2012
during follow-up exploration of ten gold geochemical anomalies
clustered around Toroparu. Drill programs at Sona Hill have focused on
the opportunity to add higher grade resources in proximity to the
existing Toroparu deposit reserves (see Sandspring press releases dated
February 3, 2016, August 17, 2016, November 3, 2016, February 13, 2017
and February 23, 2017) by exploring the mineralization located within
the hanging wall of a north-south oriented west dipping low angle shear
structure.

To view Fig. 2: Sona Hill Cross Section, please visit the
following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/e39ac986-0a2d-4f16-b0c7-
909493f0c250

The Sona Hill mineralized system remains open at depth to the
west. A complete list of gold mineralized drill intercepts from
boreholes SOD110 to SOD131 is provided as Exhibit 1 to this Press
release.

2017 Program - Wynamu Hill Drilling

The Company has received assay results from 29 core holes (2,813m)
drilled within the Wynamu Hill Prospect during November and December
2017. Highlights of the boreholes (WYD015 to WYD043) drilled to an
average length of 97m from surface are presented in the list below.

//st

Highlights from the Wynamu Hill Drill Program - borehole WYD015 to WYD043

Wynamu Hill - Highlighted Gold Intercepts

HoleID  From   To (m)  True  Weighted HoleID   From     To     True Weighted
(m)            Width Av. Au            (m)      (m)    Width  Av. Au
(m)   Grade                             (m)    Grade
(g/t)                                    (g/t)



WYD019  54.50  57.50   3.00  1.18     WYD034   36.50   41.00   4.50    2.30

WYD020  101.7  102.85  1.15  1.38     incl     36.50   38.00   1.50    6.17

WYD020  114.93 120.5   5.57  1.57     WYD035   65.00   71.15   6.15    1.72

WYD022  29     45.5    16.50 1.68     incl     68.78   70.40   1.62    4.46

incl    33.5   39.5    6.00  2.77     WYD040   61.06   65.00   3.94    1.08

WYD022  58.38  66.5    8.12  2.47     incl     63.84   65.00   1.16    2.45

incl    59     60.5    1.50  7.46     WYD040   68.84   86.00   17.16   1.04

WYD023  117.50 122.00  4.50  1.38     incl     68.84   71.00   2.16    2.53

WYD024  45.50  48.93   3.43  3.29     incl     74.00   75.50   1.50    3.35

WYD024  54.50  56.87   2.37  1.41     WYD043   14.50   20.50   5.20    1.54

WYD027  0.00   3.50    3.50  1.42     WYD043   54.00   58.50   3.90    1.25

WYD033  30.50  33.50   3.00  1.16     WYD043   67.50   79.31   10.23   1.92

WYD033  71.00  83.84   12.84 1.03     incl     67.50   70.50   2.60    5.65

WYD034  3.50   6.50    3.00  1.36

* Results presented are true thickness of the mineralized zone.

//et

Wynamu Hill, located 9 km north of the Main Toroparu deposit, was
first identified as an anomalous gold feature during regional
geochemical surveys conducted in 2012. Our 2013 geochemistry campaign
confirmed the gold anomaly, which forms a NNE-oriented, 1km long by
500m wide feature of continuous 100+ ppb values, including a dozen high
values of )500 ppb. Initial air-core test holes drilled in 2014
confirmed the presence of gold in saprolite and the upper layers of
bedrock. This was also tested with 14 diamond drill holes in 2016.

The gold mineralization interpretation consists of several
parallel gold mineralized lenses with an ENE orientation and dipping 55
to the north. The main lens is situated in the saprolite with a
vertical thickness of 60m. The gold mineralization lies within a zone
of hydrothermal alteration (carbonate-sericite-pyrite-quartz
assemblage) inside which the gold occurrence is related to a more
abundant pyrite content and a minor to moderate presence of
quartz-carbonate veins, veinlets, fractures, locally even brecciation.
Most often, one or a set of low gold grade to barren tonalite dikes are
found within or in the vicinity of the mineralization. The host rock is
a sequence from intermediate hypabyssal intrusive (diorite,
micro-diorite) to a volcano- volcaniclastic whose orientation is NNE,
60dipping to the west.

To view Fig. 3: Wynamu Hill -LEAPFROG 3D View, please visit the
following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/826209dd-b18c-4719-affd-
dead253fc195

A complete list of gold drill intercepts for boreholes WYD015
through WYD043can be found in Exhibit 1 to this press release.

Sandspring is evaluating further exploration work at Wynamu Hill,
Otomung and other exploration targets within the regional
litho-structural and hydrothermal alteration interpretation surrounding
Toroparu deposit.

Quality Assurance / Quality Control

The drill program and sampling protocol is managed by Sandspring
under the supervision of Pascal Van Osta, P.Geo. The diamond drill
holes are drilled at HQ and NQ sizes and core recovery to date has
averaged 94%. Half core is cut by rock saw and is generally sampled
using 1.5 m meter intervals.

Analytical testing and reporting of quantitative assays for the
Sona Hill results reported in this press release was performed
independently by Bureau Veritas Mineral Laboratories Vancouver, Canada.
Bureau Veritas Commodities Canada Ltd. is an ISO9001: 2008 accredited
metallurgical testing laboratory. Gold analyses reported in this
release was performed by standard fire assay (FA450) using a 50-gram
charge with atomic absorption finish and a gravimetric finish for
assays greater than 10 grams per tonne. Samples from the geochemical
survey were submitted for analysis of ICP 37 elements (including gold)
AQ252 30 gram (Aqua Regia digestion - Ultratrace ICP-MS analyses). A
system of blanks, standards and duplicates were added by the Company to
the sample streams to verify accuracy and precision of assay results,
supplementing a variety of internal QA/QC tests performed by Bureau
Veritas Mineral Laboratories. The half core samples were securely
transported by Sandspring personnel from the project site to the Bureau
Veritas sample preparation facility in Georgetown, Guyana.

Analytical testing and reporting of quantitative assays for the
Wynamu Hill results reported in this press release was performed
independently by MS Analytical, Langley, British Columbia, Canada. MS
Analytical, Langley, British Columbia is an IAS accredited
metallurgical testing laboratory. Gold analyses reported in this
release was performed by standard fire assay (FAS-121) using a 50-gram
charge with atomic absorption finish and a gravimetric finish for
assays greater than 10 grams per tonne. Samples from the geochemical
survey were submitted for analysis of ICP 51 elements (including gold)
IMS-131 20 gram (Aqua Regia digestion - Ultratrace ICP-MS analyses). A
system of blanks, standards and duplicates were added by the Company to
the sample streams to verify accuracy and precision of assay results,
supplementing a variety of internal QA/QC tests performed by MS
Analytical Laboratories. The half core samples were securely
transported by Sandspring personnel from the project site to the MS
Analytical sample preparation facility in Georgetown, Guyana.

Qualified Persons Review

The technical information in this document has been reviewed and
approved by Pascal van Osta, P.Geo., Senior Exploration Consultant for
Sandspring Resources Ltd., who has experience with the style of
mineralization under consideration and is a Qualified Person under
National Instrument 43-101.

Settlement of Debt

The Company announces that further to the news release of December
20, 2017, the Company has settled $432,852 of outstanding indebtedness
through the issuance of a total of 1,236,718 units at a price of $ 0.35
per unit. Each unit will consist of one common share and one share
purchase warrant entitling the holder to acquire one additional common
share at a price of $0.50 for a period of five years. The securities
issued are subject to a hold period expiring May 24, 2018.
On behalf of the Board of Directors of Sandspring Resources

"Richard A. Munson"

Director and Chief Executive Officer

About Sandspring Resources Ltd.

Sandspring Resources Ltd. is a Canadian junior mining company
currently moving toward a definitive feasibility study for the
multi-million ounce Toroparu Project in Guyana, South America. A
prefeasibility study completed in May 2013 (NI 43-101 Technical Report,
Prefeasibility Study, Toroparu Gold Project, Upper Puruni River Area,
Guyana, dated May 24, 2013 completed by SRK Consulting (U.S.), Inc.,
available on SEDAR at www.sedar.com) outlined the design of an open-pit
mine producing more than 200,000 ounces of gold annually over an
initial 16-year mine life. Sandspring and Silver Wheaton have entered
into a gold and silver purchase agreement for the Toroparu Project.
Additional information is available at www.sandspringresources.com or
by email at info@sandspringresources.com.

Contact Sandspring Resources

Richard A Munson
Chief Executive Officer
Tel: 303-991-5683 or via email at info@sandspringresources.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-looking Statements
This news release contains certain forward-looking information and
statements within the meaning of applicable securities laws. The use of
any of the words "potential", "suggesting", "indicating", "will",
"plans" and similar expressions are intended to identify
forward-looking information and/or statements. Forward-looking
statements and/or information are based on a number of material
factors, expectations and/or assumptions that Sandspring has used to
develop such statements and/or information, but which may prove to be
incorrect. Although Sandspring believes that the expectations reflected
in such forward-looking statements and/or information are reasonable,
undue reliance should not be placed on forward-looking statements since
Sandspring can give no assurance that such expectations will prove to
be correct. Such information and/or statements, including the
assumptions made in respect thereof, involve known and unknown risks,
uncertainties and other factors that may cause actual results and/or
events to differ materially from those anticipated in such
forward-looking information and/or statements including, without
limitation: the speculative nature of mineral exploration and
development; risks associated with the uncertainty of exploration
results and estimates; results from drilling and exploration activities
and Sandspring's ability to identify additional gold mineralization;
Sandspring's ability to successfully advance the Toroparu Gold Project
toward feasibility; Sandspring's future plans; the availability of
financing and/or cash flow to fund current and future plans and
expenditures; the impact of increasing competition; fluctuating
commodity prices; the general stability of applicable economic and
political environments; the general continuance of current industry
conditions; uncertainty regarding the market price for gold, silver and
copper; uncertainty of conducting operations under a foreign regime;
uncertainty of obtaining all applicable regulatory approvals and
related timing matters; Sandspring's dependence on management
personnel; and/or certain other risks detailed from time-to-time in
Sandspring's public disclosure documents. Furthermore, the
forward-looking statements contained in this news release are made as
at the date of this news release and the Company does not undertake any
obligations to publicly update and/or revise any of the included
forward-looking statements, whether as a result of additional
information, future events and/or otherwise, except as may be required
by applicable securities laws.

1   2013 SRK Consulting (U.S.) Inc., Toroparu mineral resource
statement estimates 44.5 Mt of Measured Resource at a grade of 0.98 g/t
Au containing 1.398 Moz of gold, Indicated Resource of 195.7 Mt at 0.87
g/t containing 5.497 Moz gold. 2017 SRK Consulting (U.S.) Inc., Sona
Hill mineral resource statement estimates 5.563 Mt of Indicated
Resource at a grade of 1.09 g/t Au containing 195 koz of gold, for a
total M&I resource for Toroparu and Sona Hill of 7.089 Moz of gold.

//st

Exhibit 1. Weighted Average Mineral Intercepts

HoleID                From (m)   To (m)   True Width      Weighted
(m)             Average Grade
Gold (g/t)

SOD112                23.5       26.7     3.2             0.46

SOD113                139.5      145.5    6               0.38

SOD113                193.5      202.5    9               1.35

Incl                  194.75     195.74   0.99            5.43

SOD113                222        230      8               1.96

Incl                  226.68     230      3.32            3.85

SOD114                193.06     195.45   2.4             2.87

SOD114                217.5      223.5    6               0.75

SOD114                236.84     239.26   2.4             6.41

SOD114                255        261.3    6.3             0.52

SOD114                270        280.5    10.5            0.74

SOD120                29.04      33       3.96            0.85

SOD120                37.59      45.13    7.54            0.86

SOD120                247.5      252.55   5.05            12.07

Incl                  249.1      250.34   1.24            48.40

SOD124                136.5      141      4.5             0.69

SOD124                145.5      148.5    3               1.22

SOD125                183.88     187.89   4.01            2.55

Incl                  187.04     187.89   0.85            5.51

SOD125                193.5      196.5    3               0.92

SOD127                93         96.51    3.51            2.10

SOD127                109.24     115.5    6.26            3.55

Incl                  110.79     111.64   0.85            18.60

SOD127                126.86     131.39   4.53            1.42

Incl                  128.97     130.15   1.18            2.71

SOD127                154.5      159      4.5             3.70

Incl                  156        157.1    1.1             13.40

SOD127                168        172.5    4.5             1.27

Incl                  169.5      171      1.5             2.29

SOD127                189        192      3               0.79

SOD127                202.5      205.5    3               0.66

SOD128                0          20.5     16.79           1.78

Incl                  14.5       16       1.23            6.20

SOD128                39.5       44.28    3.92            5.58

Incl                  39.5       41.44    1.59            13.10

SOD128                50.64      52.5     1.52            1.52

SOD128                88.5       98.42    8.13            0.50

SOD129                4          20.5     14.95           3.11

Incl                  5.5        8.5      4.08            6.38

SOD130                0          7        5.73            0.61

SOD130                16         23.28    5.96            1.07

SOD130                29.5       34       3.69            0.51

SOD130                47.5       52.62    4.19            3.02

Incl                  47.5       50.72    2.64            4.29

SOD130                57         59.64    2.16            2.43

SOD130                65.81      69.72    3.2             1.25

SOD130                121.95     135      10.69           1.68

Incl                  126.12     127.7    1.29            6.60

WYD015                53         80       27.00           0.44

incl                  75.50      80.00    4.50            1.11

WYD016                31.90      49.40    17.50           0.95

incl                  44.00      49.40    5.40            2.42

WYD017                0.00       16.90    16.90           0.84

incl                  0.00       3.40     3.40            1.73

WYD019                54.50      57.50    3.00            1.18

WYD020                53         62       9.00            0.42

WYD020                72.5       80       7.50            0.81

WYD020                101.7      102.85   1.15            1.38

WYD020                114.93     120.5    5.57            1.57

WYD020                150.5      158      7.50            0.75

incl                  155        155.53   0.53            3.96

WYD022                29         45.5     16.50           1.68

incl                  33.5       39.5     6.00            2.77

WYD022                58.38      66.5     8.12            2.47

incl                  59         60.5     1.50            7.46

WYD023                27.50      33.50    6.00            0.48

WYD023                117.50     122.00   4.50            1.38

WYD024                45.50      48.93    3.43            3.29

WYD024                54.50      56.87    2.37            1.41

WYD025                36.50      44.00    7.50            0.58

WYD027                0.00       3.50     3.50            1.42

WYD030                26.00      29.00    3.00            0.85

WYD032                78.50      98.00    19.50           0.50

WYD033                30.50      33.50    3.00            1.16

WYD033                71.00      83.84    12.84           1.03

WYD034                0.00       12.50    12.50           0.67

incl                  3.50       6.50     3.00            1.36

WYD034                36.50      41.00    4.50            2.30

incl                  36.50      38.00    1.50            6.17

WYD035                65.00      71.15    6.15            1.72

incl                  68.78      70.40    1.62            4.46

WYD038                81.50      86.00    4.50            0.65

incl                  84.50      86.00    1.50            1.13

WYD040                0.00       5.00     5.00            0.60

WYD040                18.50      29.00    10.50           0.51

WYD040                61.06      65.00    3.94            1.08

incl                  63.84      65.00    1.16            2.45

WYD040                68.84      86.00    17.16           1.04

incl                  68.84      71.00    2.16            2.53

incl                  74.00      75.50    1.50            3.35

WYD043                14.50      20.50    5.20            1.54

WYD043                26.50      34.00    6.50            0.72

WYD043                43.50      52.50    7.79            0.55

WYD043                54.00      58.50    3.90            1.25

WYD043                67.50      79.31    10.23           1.92

incl                  67.50      70.50    2.60            5.65

//et

TEL: 604-609-6125    SANDSPRING RESOURCES LTD
FAX: 604-609-6145
E-mail: jvastardis@fiorecorporation.com
Website: http://www.sandspringresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1802500013TS11802500438-06102120180126


[200/News Release]SSPVSANDSPRING RESOURCES LTDJAN 26 2018  06:10 
AMToroparu Gold Project Update --->@NEWS RELEASE
SANDSPRING RESOURCES LTD ("SSP-V;SSPXF-0")
- Toroparu Gold Project Update

Sandspring Resources Ltd. ("Sandspring" or the "Company") is
pleased to announce results from phase one of its 2017 - 2018
exploration program (the "Program") at its 7.1-million-ounce resource
(Measured & Indicated) Toroparu Gold Deposit ("Toroparu") 1 in Guyana,
South America. The Program was announced in the Company's press release
of September 18, 2017.

Phase One targeted mineralization in weathered saprolite and
shallow fresh rocks in the Sona Hill and Wynamu Prospect Areas (Fig.
1). Highlights include:

*  12.07 g/t over 5.05m* in Sona Hill Drill (SOD120) (step-out),
1.35 g/t over 9m and 1.96 g/t over 8m in SOD113 (step-out), 1.78g/t
over 16.79m in SOD128 (infill), and 5.58 g/t over 3.96m in SOD128
(infill) from 3,119m of exploratory, step-out, and infill drilling at
Sona Hill.

*  1.68 g/t over 16.5m* in Wynamu Drill hole 22 (WYD022)
(exploration), 1.72 g/t over 6.15m in WYD 035 (exploration), 1.04 g/t
over 17.2m in WYD040 (exploration), and 1.54 g/t over 5.2m, 1.25 g/t
over 3.9m, & 1.92 g/t over 10.23m in WYD043 (exploration) from 2,813.5m
of exploratory drilling at Wynamu Hill.

*All results reported as true widths

To view Fig 1. Location Map, please visit the following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/e9debd9d-55d1-4e82-9632-
0c243c0d8495

The Sona Hill maiden resource estimate (Feb 2017) increased total
resources for the Toroparu project to 7.1 Moz. Measured & Indicated
(M&I) and 3.3 Moz. Inferred (Inf) ounces of gold. Significantly, the
weathered saprolite gold resource estimate increased by 158% to 218,600
M&I and 330,400 Inferred ounces of gold with the addition of with
50,200 Indicated and 70,400 Inferred ounces from Sona Hill. 1

An analysis by SRK Consulting (US) Inc. conducted in 2017
indicated that a potentially positive economic trade-off exists for an
expanded startup saprolite leach operation at Toroparu assuming
sufficient saprolite reserves can be defined from the resources defined
at Toroparu and Sona Hill.

The drilling portion of the Program was designed to target
conversion of these resources to reserves and explore for additional
mineralization in saprolite and shallow fresh rocks adjacent and within
the Sona Hill Resource and Wynamu Prospect Areas.

Phase Two of the Program commenced on January 9th and is expected
to be completed by March 31st 2018. Phase Two includes 6,350m of infill
drilling at Sona Hill targeting conversion of the 241,000 ounces of
Inferred gold resource, 1,850m of additional step-out and infill
drilling at Wynamu Hill, and 1,600m of exploration drilling at Ameeba
Hill.

Otomung saprolite geochemistry and Kurupung Hydroelectric Project

The Program's geochemical surveys planned for the Otomung
Concession are complete. Two areas with anomalous gold values have been
identified as potential drilling targets. Additional exploratory work,
including trenching across these areas is underway to confirm the
presence of mineralization prior to a drilling decision being made.

Sandspring has continued to do work under its Memorandum of
Understanding with the Government of Guyana for the development of the
Kurupung River Hydroelectric Project, a run-of-river hydroelectric
project located at Kumerau Falls, approximately 50km southwest of
Toroparu. Sandspring completed a site visit with hydropower experts
from Hydroscience Consulting and Knight Piesold Consulting in November
2017 and expects to have a pre-feasibility report for the project in
1Q2018. The Company is evaluating the optimal size of the project as
the site can support various levels of power production.

Rich Munson, CEO states: "Our exploration program has expanded our
Indicated and Inferred resources and continues to report excellent
results. These results are supportive of our interpretations of the
potential resources available at Sona Hill and Wynamu. The continuing
drilling program will be an important planning tool for the feasibility
study for Toroparu with additional results due from exploration and
infill drill holes as they are reported. Sona Hill and Wynamu are seen
as feeders for the Toroparu processing plant in the early years of
operation, buoying the economics of the project through its early
life."

"We are also excited about the results of the ongoing work on the
Hydroelectric Project. The advancement of the Hydroelectric Project,
which will have a very significant impact on our operating costs, and
the potential enhancement of a start-up plan for Toroparu from the
additional saprolite ore underpin the development plans for the 7.1
million ounce (M&I) project," continued Mr. Munson.

2017 Program - Sona Hill Drilling

The Company has received assay results from 22 core holes (3,119m)
drilled within the Sona Hill Prospect during November and December
2017. Highlights of the boreholes (SOD110 to SOD131) are presented in
the list below.

//st

Highlights from the Sona Hill Drill Program - borehold SOD110 to SOD131

Sona Hill - Highlighted Gold Intercepts

HoleID  From   To (m)  True  Weighted HoleID   From     To     True Weighted
(m)            Width Av. Au            (m)      (m)    Width  Av. Au
(m)   Grade                             (m)    Grade
(g/t)                                    (g/t)

SOD113  193.5  202.5    9    1.35     SOD127   154.5    159     4.5   3.70

Incl    194.75 195.74   0.99 5.43     Incl     156      157.1   1.1   13.40

SOD113  222    230      8    1.96     SOD127   168      172.5   4.5   1.27

Incl    226.68 230      3.32 3.85     Incl     169.5    171     1.5   2.29

SOD114  193.06 195.45   2.4  2.87     SOD128   0        20.5    16.79 1.78

SOD114  236.84 239.26   2.4  6.41     Incl     14.5     16      1.23  6.20

SOD120  247.5  252.55   5.05 12.07    SOD128   39.5     44.28   3.92  5.58

Incl    249.1  250.34   1.24 48.40    Incl     39.5     41.44   1.59  13.10

SOD124  145.5  148.5    3    1.22     SOD129   4        20.5    14.95 3.11

SOD125  183.88 187.89   4.01 2.55     Incl     5.5      8.5     4.08  6.38

Incl    187.04 187.89   0.85 5.51     SOD130   16       23.28   5.96  1.07

SOD127  93     96.51    3.51 2.10     SOD130   47.5     52.62   4.19  3.02

SOD127  109.24 115.5    6.26 3.55     Incl     47.5     50.72   2.64  4.29

Incl    110.79 111.64   0.85 18.60    SOD130   57       59.64   2.16  2.43
SOD127  126.86 131.39   4.53 1.42     SOD130   65.81    69.72   3.2   1.25

Incl    128.97 130.15   1.18 2.71     SOD130   121.95   135     10.69 1.68

Incl     126.12   127.7   1.29  6.60

* Results presented are true thickness of the mineralized zone

//et

Hard rock mineralization was first discovered at Sona Hill in 2012
during follow-up exploration of ten gold geochemical anomalies
clustered around Toroparu. Drill programs at Sona Hill have focused on
the opportunity to add higher grade resources in proximity to the
existing Toroparu deposit reserves (see Sandspring press releases dated
February 3, 2016, August 17, 2016, November 3, 2016, February 13, 2017
and February 23, 2017) by exploring the mineralization located within
the hanging wall of a north-south oriented west dipping low angle shear
structure.

To view Fig. 2: Sona Hill Cross Section, please visit the
following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/e39ac986-0a2d-4f16-b0c7-
909493f0c250

The Sona Hill mineralized system remains open at depth to the
west. A complete list of gold mineralized drill intercepts from
boreholes SOD110 to SOD131 is provided as Exhibit 1 to this Press
release.

2017 Program - Wynamu Hill Drilling

The Company has received assay results from 29 core holes (2,813m)
drilled within the Wynamu Hill Prospect during November and December
2017. Highlights of the boreholes (WYD015 to WYD043) drilled to an
average length of 97m from surface are presented in the list below.

//st

Highlights from the Wynamu Hill Drill Program - borehole WYD015 to WYD043

Wynamu Hill - Highlighted Gold Intercepts

HoleID  From   To (m)  True  Weighted HoleID   From     To     True Weighted
(m)            Width Av. Au            (m)      (m)    Width  Av. Au
(m)   Grade                             (m)    Grade
(g/t)                                    (g/t)



WYD019  54.50  57.50   3.00  1.18     WYD034   36.50   41.00   4.50    2.30

WYD020  101.7  102.85  1.15  1.38     incl     36.50   38.00   1.50    6.17

WYD020  114.93 120.5   5.57  1.57     WYD035   65.00   71.15   6.15    1.72

WYD022  29     45.5    16.50 1.68     incl     68.78   70.40   1.62    4.46

incl    33.5   39.5    6.00  2.77     WYD040   61.06   65.00   3.94    1.08

WYD022  58.38  66.5    8.12  2.47     incl     63.84   65.00   1.16    2.45

incl    59     60.5    1.50  7.46     WYD040   68.84   86.00   17.16   1.04

WYD023  117.50 122.00  4.50  1.38     incl     68.84   71.00   2.16    2.53

WYD024  45.50  48.93   3.43  3.29     incl     74.00   75.50   1.50    3.35

WYD024  54.50  56.87   2.37  1.41     WYD043   14.50   20.50   5.20    1.54

WYD027  0.00   3.50    3.50  1.42     WYD043   54.00   58.50   3.90    1.25

WYD033  30.50  33.50   3.00  1.16     WYD043   67.50   79.31   10.23   1.92

WYD033  71.00  83.84   12.84 1.03     incl     67.50   70.50   2.60    5.65

WYD034  3.50   6.50    3.00  1.36

* Results presented are true thickness of the mineralized zone.

//et

Wynamu Hill, located 9 km north of the Main Toroparu deposit, was
first identified as an anomalous gold feature during regional
geochemical surveys conducted in 2012. Our 2013 geochemistry campaign
confirmed the gold anomaly, which forms a NNE-oriented, 1km long by
500m wide feature of continuous 100+ ppb values, including a dozen high
values of )500 ppb. Initial air-core test holes drilled in 2014
confirmed the presence of gold in saprolite and the upper layers of
bedrock. This was also tested with 14 diamond drill holes in 2016.

The gold mineralization interpretation consists of several
parallel gold mineralized lenses with an ENE orientation and dipping 55
to the north. The main lens is situated in the saprolite with a
vertical thickness of 60m. The gold mineralization lies within a zone
of hydrothermal alteration (carbonate-sericite-pyrite-quartz
assemblage) inside which the gold occurrence is related to a more
abundant pyrite content and a minor to moderate presence of
quartz-carbonate veins, veinlets, fractures, locally even brecciation.
Most often, one or a set of low gold grade to barren tonalite dikes are
found within or in the vicinity of the mineralization. The host rock is
a sequence from intermediate hypabyssal intrusive (diorite,
micro-diorite) to a volcano- volcaniclastic whose orientation is NNE,
60dipping to the west.

To view Fig. 3: Wynamu Hill -LEAPFROG 3D View, please visit the
following link:
http://www.globenewswire.com/NewsRoom/AttachmentNg/826209dd-b18c-4719-affd-
dead253fc195

A complete list of gold drill intercepts for boreholes WYD015
through WYD043can be found in Exhibit 1 to this press release.

Sandspring is evaluating further exploration work at Wynamu Hill,
Otomung and other exploration targets within the regional
litho-structural and hydrothermal alteration interpretation surrounding
Toroparu deposit.

Quality Assurance / Quality Control

The drill program and sampling protocol is managed by Sandspring
under the supervision of Pascal Van Osta, P.Geo. The diamond drill
holes are drilled at HQ and NQ sizes and core recovery to date has
averaged 94%. Half core is cut by rock saw and is generally sampled
using 1.5 m meter intervals.

Analytical testing and reporting of quantitative assays for the
Sona Hill results reported in this press release was performed
independently by Bureau Veritas Mineral Laboratories Vancouver, Canada.
Bureau Veritas Commodities Canada Ltd. is an ISO9001: 2008 accredited
metallurgical testing laboratory. Gold analyses reported in this
release was performed by standard fire assay (FA450) using a 50-gram
charge with atomic absorption finish and a gravimetric finish for
assays greater than 10 grams per tonne. Samples from the geochemical
survey were submitted for analysis of ICP 37 elements (including gold)
AQ252 30 gram (Aqua Regia digestion - Ultratrace ICP-MS analyses). A
system of blanks, standards and duplicates were added by the Company to
the sample streams to verify accuracy and precision of assay results,
supplementing a variety of internal QA/QC tests performed by Bureau
Veritas Mineral Laboratories. The half core samples were securely
transported by Sandspring personnel from the project site to the Bureau
Veritas sample preparation facility in Georgetown, Guyana.

Analytical testing and reporting of quantitative assays for the
Wynamu Hill results reported in this press release was performed
independently by MS Analytical, Langley, British Columbia, Canada. MS
Analytical, Langley, British Columbia is an IAS accredited
metallurgical testing laboratory. Gold analyses reported in this
release was performed by standard fire assay (FAS-121) using a 50-gram
charge with atomic absorption finish and a gravimetric finish for
assays greater than 10 grams per tonne. Samples from the geochemical
survey were submitted for analysis of ICP 51 elements (including gold)
IMS-131 20 gram (Aqua Regia digestion - Ultratrace ICP-MS analyses). A
system of blanks, standards and duplicates were added by the Company to
the sample streams to verify accuracy and precision of assay results,
supplementing a variety of internal QA/QC tests performed by MS
Analytical Laboratories. The half core samples were securely
transported by Sandspring personnel from the project site to the MS
Analytical sample preparation facility in Georgetown, Guyana.

Qualified Persons Review

The technical information in this document has been reviewed and
approved by Pascal van Osta, P.Geo., Senior Exploration Consultant for
Sandspring Resources Ltd., who has experience with the style of
mineralization under consideration and is a Qualified Person under
National Instrument 43-101.

Settlement of Debt

The Company announces that further to the news release of December
20, 2017, the Company has settled $432,852 of outstanding indebtedness
through the issuance of a total of 1,236,718 units at a price of $ 0.35
per unit. Each unit will consist of one common share and one share
purchase warrant entitling the holder to acquire one additional common
share at a price of $0.50 for a period of five years. The securities
issued are subject to a hold period expiring May 24, 2018.
On behalf of the Board of Directors of Sandspring Resources

"Richard A. Munson"

Director and Chief Executive Officer

About Sandspring Resources Ltd.

Sandspring Resources Ltd. is a Canadian junior mining company
currently moving toward a definitive feasibility study for the
multi-million ounce Toroparu Project in Guyana, South America. A
prefeasibility study completed in May 2013 (NI 43-101 Technical Report,
Prefeasibility Study, Toroparu Gold Project, Upper Puruni River Area,
Guyana, dated May 24, 2013 completed by SRK Consulting (U.S.), Inc.,
available on SEDAR at www.sedar.com) outlined the design of an open-pit
mine producing more than 200,000 ounces of gold annually over an
initial 16-year mine life. Sandspring and Silver Wheaton have entered
into a gold and silver purchase agreement for the Toroparu Project.
Additional information is available at www.sandspringresources.com or
by email at info@sandspringresources.com.

Contact Sandspring Resources

Richard A Munson
Chief Executive Officer
Tel: 303-991-5683 or via email at info@sandspringresources.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-looking Statements
This news release contains certain forward-looking information and
statements within the meaning of applicable securities laws. The use of
any of the words "potential", "suggesting", "indicating", "will",
"plans" and similar expressions are intended to identify
forward-looking information and/or statements. Forward-looking
statements and/or information are based on a number of material
factors, expectations and/or assumptions that Sandspring has used to
develop such statements and/or information, but which may prove to be
incorrect. Although Sandspring believes that the expectations reflected
in such forward-looking statements and/or information are reasonable,
undue reliance should not be placed on forward-looking statements since
Sandspring can give no assurance that such expectations will prove to
be correct. Such information and/or statements, including the
assumptions made in respect thereof, involve known and unknown risks,
uncertainties and other factors that may cause actual results and/or
events to differ materially from those anticipated in such
forward-looking information and/or statements including, without
limitation: the speculative nature of mineral exploration and
development; risks associated with the uncertainty of exploration
results and estimates; results from drilling and exploration activities
and Sandspring's ability to identify additional gold mineralization;
Sandspring's ability to successfully advance the Toroparu Gold Project
toward feasibility; Sandspring's future plans; the availability of
financing and/or cash flow to fund current and future plans and
expenditures; the impact of increasing competition; fluctuating
commodity prices; the general stability of applicable economic and
political environments; the general continuance of current industry
conditions; uncertainty regarding the market price for gold, silver and
copper; uncertainty of conducting operations under a foreign regime;
uncertainty of obtaining all applicable regulatory approvals and
related timing matters; Sandspring's dependence on management
personnel; and/or certain other risks detailed from time-to-time in
Sandspring's public disclosure documents. Furthermore, the
forward-looking statements contained in this news release are made as
at the date of this news release and the Company does not undertake any
obligations to publicly update and/or revise any of the included
forward-looking statements, whether as a result of additional
information, future events and/or otherwise, except as may be required
by applicable securities laws.

1   2013 SRK Consulting (U.S.) Inc., Toroparu mineral resource
statement estimates 44.5 Mt of Measured Resource at a grade of 0.98 g/t
Au containing 1.398 Moz of gold, Indicated Resource of 195.7 Mt at 0.87
g/t containing 5.497 Moz gold. 2017 SRK Consulting (U.S.) Inc., Sona
Hill mineral resource statement estimates 5.563 Mt of Indicated
Resource at a grade of 1.09 g/t Au containing 195 koz of gold, for a
total M&I resource for Toroparu and Sona Hill of 7.089 Moz of gold.

//st

Exhibit 1. Weighted Average Mineral Intercepts

HoleID                From (m)   To (m)   True Width      Weighted
(m)             Average Grade
Gold (g/t)

SOD112                23.5       26.7     3.2             0.46

SOD113                139.5      145.5    6               0.38

SOD113                193.5      202.5    9               1.35

Incl                  194.75     195.74   0.99            5.43

SOD113                222        230      8               1.96

Incl                  226.68     230      3.32            3.85

SOD114                193.06     195.45   2.4             2.87

SOD114                217.5      223.5    6               0.75

SOD114                236.84     239.26   2.4             6.41

SOD114                255        261.3    6.3             0.52

SOD114                270        280.5    10.5            0.74

SOD120                29.04      33       3.96            0.85

SOD120                37.59      45.13    7.54            0.86

SOD120                247.5      252.55   5.05            12.07

Incl                  249.1      250.34   1.24            48.40

SOD124                136.5      141      4.5             0.69

SOD124                145.5      148.5    3               1.22

SOD125                183.88     187.89   4.01            2.55

Incl                  187.04     187.89   0.85            5.51

SOD125                193.5      196.5    3               0.92

SOD127                93         96.51    3.51            2.10

SOD127                109.24     115.5    6.26            3.55

Incl                  110.79     111.64   0.85            18.60

SOD127                126.86     131.39   4.53            1.42

Incl                  128.97     130.15   1.18            2.71

SOD127                154.5      159      4.5             3.70

Incl                  156        157.1    1.1             13.40

SOD127                168        172.5    4.5             1.27

Incl                  169.5      171      1.5             2.29

SOD127                189        192      3               0.79

SOD127                202.5      205.5    3               0.66

SOD128                0          20.5     16.79           1.78

Incl                  14.5       16       1.23            6.20

SOD128                39.5       44.28    3.92            5.58

Incl                  39.5       41.44    1.59            13.10

SOD128                50.64      52.5     1.52            1.52

SOD128                88.5       98.42    8.13            0.50

SOD129                4          20.5     14.95           3.11

Incl                  5.5        8.5      4.08            6.38

SOD130                0          7        5.73            0.61

SOD130                16         23.28    5.96            1.07

SOD130                29.5       34       3.69            0.51

SOD130                47.5       52.62    4.19            3.02

Incl                  47.5       50.72    2.64            4.29

SOD130                57         59.64    2.16            2.43

SOD130                65.81      69.72    3.2             1.25

SOD130                121.95     135      10.69           1.68

Incl                  126.12     127.7    1.29            6.60

WYD015                53         80       27.00           0.44

incl                  75.50      80.00    4.50            1.11

WYD016                31.90      49.40    17.50           0.95

incl                  44.00      49.40    5.40            2.42

WYD017                0.00       16.90    16.90           0.84

incl                  0.00       3.40     3.40            1.73

WYD019                54.50      57.50    3.00            1.18

WYD020                53         62       9.00            0.42

WYD020                72.5       80       7.50            0.81

WYD020                101.7      102.85   1.15            1.38

WYD020                114.93     120.5    5.57            1.57

WYD020                150.5      158      7.50            0.75

incl                  155        155.53   0.53            3.96

WYD022                29         45.5     16.50           1.68

incl                  33.5       39.5     6.00            2.77

WYD022                58.38      66.5     8.12            2.47

incl                  59         60.5     1.50            7.46

WYD023                27.50      33.50    6.00            0.48

WYD023                117.50     122.00   4.50            1.38

WYD024                45.50      48.93    3.43            3.29

WYD024                54.50      56.87    2.37            1.41

WYD025                36.50      44.00    7.50            0.58

WYD027                0.00       3.50     3.50            1.42

WYD030                26.00      29.00    3.00            0.85

WYD032                78.50      98.00    19.50           0.50

WYD033                30.50      33.50    3.00            1.16

WYD033                71.00      83.84    12.84           1.03

WYD034                0.00       12.50    12.50           0.67

incl                  3.50       6.50     3.00            1.36

WYD034                36.50      41.00    4.50            2.30

incl                  36.50      38.00    1.50            6.17

WYD035                65.00      71.15    6.15            1.72

incl                  68.78      70.40    1.62            4.46

WYD038                81.50      86.00    4.50            0.65

incl                  84.50      86.00    1.50            1.13

WYD040                0.00       5.00     5.00            0.60

WYD040                18.50      29.00    10.50           0.51

WYD040                61.06      65.00    3.94            1.08

incl                  63.84      65.00    1.16            2.45

WYD040                68.84      86.00    17.16           1.04

incl                  68.84      71.00    2.16            2.53

incl                  74.00      75.50    1.50            3.35

WYD043                14.50      20.50    5.20            1.54

WYD043                26.50      34.00    6.50            0.72

WYD043                43.50      52.50    7.79            0.55

WYD043                54.00      58.50    3.90            1.25

WYD043                67.50      79.31    10.23           1.92

incl                  67.50      70.50    2.60            5.65

//et

TEL: 604-609-6125    SANDSPRING RESOURCES LTD
FAX: 604-609-6145
E-mail: jvastardis@fiorecorporation.com
Website: http://www.sandspringresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1802500013TS11802500438-06102120180126