Source	MARKET NEWS
Date	03/01/2018
Time	06:06:49 AM

Company	 Infinite Lithium Corp.
Title	Current 
Drilling Program Results Support Histori





    CDNX Symbol: ILI











Press Release





INFINITE LITHIUM CORP ("ILI-V;ARXRF-0")
- Current Drilling Program Results Support Historic Drilling:
- Infinite Lithium Intersects 7.23 Metres of 2.47% LI2O,
- Including 2 Metres of 4.48% LI2O

INFINITE LITHIUM CORP. ("Infinite" or the "Company") is pleased to
announce initial results from the first 5 drill holes of the ongoing
Phase 1 drilling program which began in December 2017. This program,
now on hole twelve, is aimed at confirming and expanding on the
historical drilling (1955) at the Jackpot Property. Results from the
Phase 1 drilling program will be used to guide future drilling and to
complete a National Instrument 43-101 ("NI-43-101") Technical Report
and Mineral Resource Estimation.

Five (5) drill holes, totalling 681 metres, are now available for
reporting as follows:

//st

Drill Hole   From (m)   To (m)   Intercept (m)   Li2O (wt%)

J-17-01      31.45      39.00    7.55            1.00

incl.        33.00      34.00    1.00            1.63

incl.        31.45      34.00    2.55            1.33

incl.        35.00      37.00    2.00            1.28

J-18-01      73.00      76.00    3.00            1.22

incl.        74.00      76.00    2.00            1.55

J-18-01      78.00      81.57    3.57            0.86

incl.        80.00      81.57    1.57            1.77

J-18-01      84.00      88.35    4.35            1.18

incl.        85.00      88.35    3.35            1.38

J-18-02      82.00      90.00    8.00            0.78

incl.        84.00      86.00    2.00            1.16

J-18-02      91.00      95.00    4.00            1.04

incl.        93.00      95.00    2.00            1.24

J-18-02      100.00     103.00   3.00            1.15

J-18-03      10.40      12.40    2.00            2.32

J-18-04      2.20       9.43     7.23            2.47

incl.        6.00       8.00     2.00            4.48

J-18-04      166.00     167.00   1.00            1.01

//et

These five drill holes are approximate twins of historic drill
holes as follows: J-17-01: twin of historic hole 425; J-18-01: twin of
historic hole 426; J-18-02: twin of historic hole 427; J-18-03: twin of
historic hole 428; J-18-04: twin of historic hole 429.

Mike England President and CEO of Infinite Lithium commented,
"These early drilling results support the historic drill core
intercepts reported in 1955-56 from the Property. I am very pleased
with these initial results which, in some cases, show even better grade
over larger widths than the historic drilling results. All five drill
holes intersected greater than 1% Li(sub)2(/sub)O which is an important
consideration when one contemplates the economic extraction of lithium
from a hard rock deposit."

A total of twelve (12) drill holes, totalling approximately 1,700
metres, have been completed to date and results will be released as
assays become available. Locations of the Phase 1 drill holes are
designed to support historic drilling results, assist in modelling the
orientation of the pegmatites, and provide a more robust understanding
of the property's potential. Drilling to date confirms the presence of
the two pegmatite dykes, one near or at surface and relatively
flat-lying, and the second striking approximately east-northeast and
dripping shallowly to the northwest.

Mr. England continued, "Our drilling to date, although relatively
shallow, has confirmed the presence of the two lithium-bearing
pegmatite dykes as was reported from the historic work. In addition to
confirming historic drill core assay results we will be completing
additional drilling in the current program with the intention of
expanding the historic mineral resources, which was based only on one
of the two dykes. There are also numerous other pegmatite dykes on the
Property which will provide targets in the future surface exploration
and diamond drilling programs. We are off to a great start and I look
forward to reporting the balance of the drilling results from this
ongoing program. Our goal is to build sufficient enough tonnage to
issue an NI 43-101 compliant mineral resource estimation as soon as
possible."

The historic Jackpot lithium pegmatites were described by E.G. Pye
(1965), in a government report published by the Ontario Department of
Mines (Georgia Lake Area). In 1955, the LCT pegmatite dykes were tested
by a total of 32 drill holes by the Ontario Lithium Company Limited and
its associated company Conwest Exploration Company Limited. This
historic drilling confirmed the presence of at least two
spodumene-bearing pegmatite bodies; one at and near the surface (No. 1)
and the second (No. 2) lying beneath the No. 1 pegmatite. The No.1
pegmatite was found to be a flat-lying body variably exposed at surface
and with thicknesses ranging from 6 to 9 metres.  Interpretation to
date confirms that the lower No. 2 pegmatite strikes at approximately
N65E and dips 15-25NW as reported by Pye (1965).  Both the upper No. 1
and lower No. 2 pegmatites are open towards the east and west and down
dip.

Reported historical mineral resources at Jackpot were calculated
on the basis of the No. 2 pegmatite and reported as 2 million tonnes @
1.09% Li(sub)2(/sub)O (estimated in 1956 by the Ontario Lithium Company
Limited*). The No. 2 pegmatite was intersected by drilling at 30 to 100
metre intervals over a strike length of 215 metres, and at 30 to 60
metre intervals over a distance of approximately 365 metres across
strike. The No. 2 pegmatite is approximately 4 to 20 metres thick,
averaging 11 metres. It should be noted that no evidence exists to
suggest that assaying was ever carried out for any elements other than
lithium.

*The estimates presented above are treated as historic information
and have not been verified or relied upon for economic evaluation by
the Company. These Historical Mineral Resources do not refer to any
category of sections 1.2 and 1.3 of the National Instrument 43-101 such
as mineral resources or mineral reserves as stated in the 2010 CIM
Definition Standards on Mineral Resources and Mineral Reserves. A
Qualified Person has not yet done sufficient enough work to classify
the historical resource estimate as current mineral resources or
mineral reserves and should not be relied upon. The Company is not
treating the historical estimate as current mineral resources or
mineral reserves.

The technical contents of this news release were approved by Dr.
Scott Jobin-Bevans, P.Geo., a Qualified Person as defined by the
National Instrument 43-101. The properties have not been the subject of
a National Instrument 43-101 report.

Infinite Lithium is a junior mining exploration company focused on
seeking and acquiring world class lithium projects globally. Infinite
Lithium continues to evaluate suitable prospects that fit the mandate
of the Company.

ON BEHALF OF THE BOARD

"Michael England"

Michael England, President, Director

FOR FURTHER INFORMATION, PLEASE CONTACT:

Telephone: 1-604-683-3995

Toll Free: 1-888-945-4770

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

FORWARD LOOKING STATEMENTS: This news release contains
forward-looking statements, which relate to future events or future
performance and reflect management's current expectations and
assumptions.  Such forward-looking statements reflect management's
current beliefs and are based on assumptions made by and information
currently available to the Company. Investors are cautioned that these
forward looking statements are neither promises nor guarantees, and are
subject to risks and uncertainties that may cause future results to
differ materially from those expected. These forward-looking statements
are made as of the date hereof and, except as required under applicable
securities legislation, the Company does not assume any obligation to
update or revise them to reflect new events or circumstances. All of
the forward-looking statements made in this press release are qualified
by these cautionary statements and by those made in our filings with
SEDAR in Canada (available at www.sedar.com).

TEL: 604-683-3995    INFINITE LITHIUM CORP
FAX: 604-683-3988
E-mail: info@alixresources.com
Website: http://www.alixresources.com
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1805900032TS11805901123-06060720180301