Source	CANADA NEWSWIRE
Date	01/18/2019
Time	05:03:28 AM

Company	 Blue Moon Zinc Corp.
Title	Blue Moon Cuts 30.3% Zinc, 1.7% Copper Plus Precious Metals Over 30 Feet
at Blue Moon Deposit (true width ~55%)





    CDNX Symbol: MOON











Press Release




" BC-MOON-Disovers-Metals   01-18 1438
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Blue Moon Cuts 30.3% Zinc, 1.7% Copper Plus Precious Metals Over 30 Feet
at Blue Moon Deposit (true width ~55%)@

VANCOUVER, Jan. 18, 2019 /CNW/ - Blue Moon Zinc Corp. (TSX.V: MOON; OTC:
BMOOF) ("Blue Moon" or the "Company") is pleased to announce the discovery of
high-grade zinc-copper-rich massive sulphides with precious metal values at
its 100%-owned Blue Moon VMS deposit in Mariposa County, California.
Given the significance of the results, the first drilling at Blue Moon in
nearly 30 years, a Phase 2 follow-up drill program is planned to commence
shortly in an attempt to expand the highest-grade zone ever encountered at the
deposit.
Highlights:
<<

--  Drill hole BMZ-78 cut 30 feet (9.35 metres) of massive sulphide
mineralization grading 30.3% zinc, 1.7% copper, 1.67 g/t gold and 71 g/t
silver for a zinc equivalent of 36.8% within a broader interval of 120.7
feet (36.5 m) that returned 9.45% zinc, 0.58% copper, 1.1 g/t gold and
42.9 g/t silver for a zinc equivalent of 12.61%;
--  BMZ-78 was drilled into a previously untested area (200 feet x 500 feet)
within the West and Main Zones at a vertical depth of approximately
1,200 feet (374 metres);
--  Blue Moon's 2018 drill program demonstrates that the massive sulphide
lenses are now traceable for approximately 3,000 feet (900 metres) along
plunge and remain open to surface and depth.
<>>
The Blue Moon NI 43-101 Inferred mineral resource announced on November
20, 2018 had a zinc equivalent ("ZnEq") of 8.07% at a ZnEq cut-off grade of
4.0%.
Patrick McGrath, Blue Moon CEO, commented: "Drill hole BMZ-78 is a major
breakthrough at this zinc-rich VMS deposit, supporting the continuity of the
system while also demonstrating the presence of a very high-grade zinc core
with impressive copper and precious metal content. Gold values of 4.98 g/t and
5.00 g/t, respectively, over five feet and silver values of 130 g/t over three
feet are present within the massive sulphides."
"Our crews are eagerly preparing for the next round of drilling to
further build on the grade and the footprint of this deposit," McGrath
continued. "Meanwhile, we look forward to carrying out studies in 2019 to
verify the clean metallurgical profile of the Blue Moon mineralization as
reported through historical work documented in our NI-43-101 filed on SEDAR on
November 20, 2018."
Significant Assay Results


From                          To                            Length
(2)                       Zinc                       
Gold                        Silver        Lead       Copper

Zinc
Equivalent
Hole




(4)                       (feet)                       
(feet)                          (feet)                          
(%)                       (g/t)                       (g/t)         (%)         
(%)
(%)
(1)

---                                                                             
                                                                                
                                                                                
     ---

BMZ78                         1425.0                        
1545.7                               120.7                        
9.45                         1.10                         42.93        
0.15         0.58                   12.61

---

inc                          1436.0                        
1441.0                                 5.0                        
1.90                         4.98                         32.60        
0.47         0.11                    8.08

---

inc                          1459.0                        
1464.0                                 5.0                        
2.60                         5.01                         18.50        
0.01         0.33                    8.77

---

inc                          1468.5                        
1453.3                                15.2                        
5.98                         2.30                         15.44        
0.03         0.38                    9.40

---

inc                          1508.0                        
1538.0                                30.0                       
30.30                         1.67                         71.07        
0.05         1.70                   36.80

---

inc                          1508.0                        
1511.0                                 3.0                       
46.50                         3.14                        130.00        
0.13         2.20                   56.51

---



BMZ75                         1022.0                        
1038.0                                16.0                         
1.2                         0.08                           0.7           
0         0.04                     1.4

---

inc                          1027.0                        
1029.0                                 2.0                         
2.9                         0.05                           1.5           
0         0.08                     3.2

---


(1) Zinc Equivalent calculation below.



(2) True widths of the reported mineralized intervals are estimated to be 55% 
of the drilled width.



(3) These are uncut assays.


(4) The dip angle of hole BMZ-78 was -60 degrees and the average azimuth was 
approximately 257. The dip angle of hole BMZ-75 was -40 degrees and the average 
azimuth was approximately 260.

A long section is attached to this news release. The drill program
consisted of approximately 4,000 feet of HQ core drilling in 4 holes. BMZ-78
confirms the presence of thick and steeply plunging massive sulphide
mineralization with in the Main Zone. Step-out hole BMZ-75 demonstrates that
mineralization extends an additional 200 feet up plunge and north of
historical workings showing the massive sulphide lenses are now traceable for
approximately 3,000 feet along plunge and remain open to surface and depth.
Hole BMZ-76 was drilled to a depth of 950 feet and was terminated due to a
material deviation of the hole after exiting a fault and would not have
reached the intended target zone. Hole BMZ-77 was drilled to a depth of 180
feet and was terminated due to poor drilling conditions and was re-drilled
from the same platform and renamed BMZ-78.
Quality Assurance/Quality Control
Drilling completed on the project in 2018 was supervised on-site by Peter
A. Herrera, P. Geo, who collected and tracked samples and implemented a full
QA/QC program using blanks, standards and duplicates to monitor analytical
accuracy and precision. Drill core was logged and sampled in a secure core
processing and storage facility located at the Blue Moon site in Mariposa
County, California. Core samples from the program were cut in half using a
diamond bladed rock saw, sealed onsite, and were delivered directly by Mr.
Herrera to Bureau Veritas's (BV) lab facility in Sparks, Nevada, for analysis.
BV's quality system complies with global certifications for Quality
ISO9001:2008. Pulps from the higher-grade samples as well as the duplicate
samples were analyzed by ALS laboratories in Reno. Core samples were analyzed
using a combination of BV's MA300 process for low level concentrations (ICP-ES
4 acid digestion) and the MA404 process for higher level concentrations of
lead (ICP-ES 4 acid digestion). Gold assaying was completed with FA430, a
30-gram fire assay with ICP-AAS finish. Base metal over-limits were finalized
with titration GC816 (zinc), GC820 (copper), and a silica wash was used
between high-grade samples to ensure no sample carry-over. No material
differences were found in any of the quality control samples nor were there
any material differences between the results received from BV and those
received from ALS. No QA/QC concerns were observed with the results shown in
this report.
Zinc Equivalent Calculation (ZnEq)
The ZnEq formula and the underlying parameters used in its formulation
are set out below:
Metal                            Price (US$)                           Recovery 
(%) Factor


Zinc
1.30/lb                                             95    24.70

---                                                                             
                         ---

Silver
17.00/oz                                            65    11.05

---                                                                             
                         ---

Copper
3.00/lb                                             93    55.80

---                                                                             
                         ---

Gold
1,250.00/oz                                           70   875.00

---                                                                             
                         ---

Lead
1.00/lb                                             95    19.00

---                                                                             
                         ---

The metal prices and the recoveries selected represent reasonable estimates of 
long-
term metal prices and potential recoveries of metal in concentrate as detailed 
in the
NI 43-101 filed on SEDAR on November 20, 2018. The equation to calculate ZnEq 
is as
follows:


ZnEq (equal sign) (Zn%(x)24.70 + Cu%(x)55.80 + Pb%(x)19.00 + Ag(oz/t)(x)11.05 + 
Au(oz/t)(x)875.00) /
24.70.

About Blue Moon
Blue Moon (TSX.V: MOON; OTC: BMOOF) is currently advancing its
100%-controlled Blue Moon zinc deposit which also contains copper, gold and
silver. The deposit is open at depth and along strike. The Blue Moon 43-101
Mineral Resource includes 7.8 million inferred tons at 8.07% zinc equivalent,
which includes 771 million pounds of 4.95% zinc, 71 million pounds of 0.46%
copper, 300,000 ounces of gold at 0.04 oz/t, and 10 million ounces of silver
at 1.33 oz/t. The 43-101 was filed on www.sedar.com on November 20, 2018. More
information is available on the company's web site (www.bluemoonmining.com).
The Company plans to advance the Blue Moon Project through to feasibility,
permitting and ultimately production.
Qualified Persons
Peter A. Herrera, P. Geo, is a qualified person as defined by NI-43-101,
and has reviewed the scientific and technical information that forms the basis
for this news release.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release. Resource
estimates included in this news release are forward-looking statements.
Although the Company believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions set forth in
the relevant technical report and otherwise, such statements are not
guarantees of future performance and actual results or developments may differ
materially from those in the forward-looking statements. Factors that could
cause actual results to differ materially from those in forward-looking
statements include market prices for zinc, the results of future exploration,
uncertainties related to the ability to obtain necessary permits, licenses and
titles, changes in government policies regarding mining, continued
availability of capital and financing, and general economic, market or
business conditions. Investors are cautioned that any such statements are not
guarantees of future performance and actual results or developments may differ
materially from those projected in the forward-looking statements. Readers are
cautioned not to place undue reliance on this forward-looking information,
which is given as of the date it is expressed in this press release, and the
Company undertakes no obligation to update publicly or revise any
forward-looking information, whether as a result of new information, future
events or otherwise, except as required by applicable securities laws.
The securities referenced in this news release have not and will not be
registered under the U.S. Securities Act of 1933 and may not be offered or
sold in the United States absent registration or an applicable exemption from
registration requirements.
SOURCE Blue Moon Zinc Corp.



View original content:
http://www.newswire.ca/en/releases/archive/January2019/18/c1881.html

-0-                           01/18/2019
/For further information: Patrick McGrath, CEO, 1-832-499-6009,
pmcgrath(at)bluemoonmining.com/
(BMOOF MOON.)

CO:  Blue Moon Zinc Corp.
ST:  British Columbia
IN:  MNG MIN PRM
SU:

-30-