Source	Business Wire
Date	02/11/2019
Time	08:02:42 AM

Company	 BLACK DRAGON GOLD CORP.
Title	[EXTERNAL] Black Dragon Gold Corp.: Positive Preliminary Economic 
Assessment f...





    CDNX Symbol: BDG











Press Release




Feb. 11, 2019 16:02 UTC

Black Dragon Gold Corp.: Positive Preliminary Economic Assessment for  Salave 
Underground 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Black Dragon Gold Corp. 

TSX VENTURE SYMBOL: BDG 

VANCOUVER, British Columbia--(BUSINESS WIRE)-- Black Dragon Gold Corp. 
(ASX/TSX-V: BDG) ("Black Dragon" or the  "Company") is pleased to announce the 
positive results of  the Preliminary Economic Assessment ("PEA") completed on 
its 100% owned  Salave Gold Project ("Salave" or "Project") located in Asturias 
in  northern Spain. The PEA is based on the recently completed Mineral  
Resource Estimate completed by CSA Global (See October 25, 2018 News  Release). 
All figures are in United States Dollars unless otherwise  stated. 

This press release features multimedia. View the full release here:  
https://www.businesswire.com/news/home/20190211005527/en/ 

The PEA demonstrates robust economics for an underground mining  operation with 
a 14-year mine life. 

Paul Cronin, Managing Director and CEO commented, 

"The completion of the PEA is a major milestone on the path to  development of 
the Salave Project and the metrics support our belief  that Salave can 
potentially generate strong returns for shareholders. It  forms the first step 
in our permitting process, presenting a new  optimised process on a zero- 
discharge basis that minimises the visual  and surface impact of the project. 

The robust results of this PEA underline the potential economic  viability of 
the current Salave resource to be mined over an initial 14  year mine life, and 
our successful drilling campaign last year indicates  strong potential for 
growth in mine life at Salave. 

This study supports that Salave can produce over 1.1Moz (560 kt of  concentrate 
averaging over 59 g/t Au), providing a number of marketing  options for export 
and refining, minimising the need for additional  plant and equipment, and 
hence reducing the Project’s footprint. The  relatively low upfront capex also 
opens alternative financing  opportunities which will ensure that both 
shareholders and the local  community benefit from the success of this 
Project." 

KEY PEA OUTCOMES

Pre-Tax NPV at 5% discount rate: US$ 296.2 million. 
After-Tax NPV: US$ 230.0 million 
Pre-Tax Internal Rate of Return ("IRR"): 28% 

After-Tax Internal Rate of Return ("IRR"): 25% 

After-Tax Payback: 3.8 years 
Pre-Production Capital Cost, including contingency: US$ 95.3 million 
Life of Mine ("LOM") Sustaining Capital Cost: US$19.3 million 
Estimated Average LOM Total Cash Cost: $729/ounce (oz) Au 
Estimated Average LOM All-In Sustaining Costs ("AISC"): $752/oz Au 

CAUTIONARY STATEMENT

The PEA is a preliminary technical and economic study of the potential  
viability of the Salave Gold Project. It is preliminary in nature and  includes 
Inferred Mineral Resources that are considered too  speculative geologically to 
have economic considerations applied to  them that would enable them to be 
categorized as Mineral Reserves.  There can be no assurance, and there is no 
certainty, that the  preliminary economic assessment contained therein will be 
realised.  Further exploration and evaluation work and appropriate studies are  
required before Black Dragon will be in a position to estimate any Ore  
Reserves or to provide any assurance of an economic development case. 
The production target and forecast financial information referred to  in this 
PEA are comprised of Measured and Indicated Mineral Resources  (73%) and 
Inferred Mineral Resources (27%). The proportion of Inferred  Mineral Resources 
is not determinative of the project viability and  does not feature as a 
significant proportion early in the mine plan. 
Metallurgical recoveries have been based on test work data and costs  have been 
estimated by independent consultants generally from budget  quotations, 
factored estimates or cost data from similar  operations/projects. Cost 
estimate accuracy for the PEA is in the  order of +/-35%. 
The PEA is based on the material assumptions outlined herein and in  the 
report. These include assumptions about the availability of  funding. While BDG 
considers all of the material assumptions to be  based on reasonable grounds, 
there is no certainty that they will  prove to be correct or that the range of 
outcomes indicated by the PEA  will be achieved. To achieve the range of 
outcomes indicated in the  PEA, among other things, funding of in the order of 
US$100 million  will likely be required. Investors should note that there is 
no  certainty that Black Dragon will be able to raise that amount of  funding 
when needed. 
It is also likely that such funding may only be available on terms  that may be 
dilutive to or otherwise affect the value of BDG’s  existing shares. It is also 
possible that BDG could pursue other  ‘value realisation’ strategies such as a 
sale, partial sale or joint  venture of the project. If it does, this could 
materially reduce BDG’s  proportionate ownership of the project. Given the 
uncertainties  involved, investors should not make any investment decisions 
based  solely on the results of the PEA. 

NEXT STEPS

Submission of the Project Description for the Environmental and Social  Impact 
Assessment ("ESIA") in February 2019; 
Additional geophysics over the entire Investigation Permit at Salave –  April 
2019; 
Issuance of the ESIA Terms of Reference in June 2019; 
Soil Geochemistry testing on potential drill targets – June 2019; 
Pre-Feasibility Study – October 2019. 

PEA KEY ASSUMPTIONS AND INPUTS

Assumed gold price: US$1,250/oz 
Exchange Rate of $1.15 / € 
Life of Mine: 14-years 
Main Underground Mining Method: Vertical Retreat & Sub-Level Stoping 
Average Diluted Head Grade: 3.87 g/t Au 
Total Underground Dilution: 43% 
LOM Plant Throughput 9.19 Mt 
Access Ramp Gradient of 15% at a 5.0m x 5.5m profile 
Mineralised Zone Development at a 4.0m x 4.5m profile 
Average Mining and Processing throughput: 2,000 tonnes per day ("tpd") 
Flotation Plant Recoveries: 97% 
Average Annual Production (LOM): 79,200 oz Au in concentrate at an  average 
grade of 59.7 g/t Au 
LOM recovered gold in concentrate production: 1,108,420 oz; 
Refining and Processing Charges: US$368/t concentrate or US$188/oz Au 

Table 1 - PEA Summary Parameters

Input 	  	Unit 	  	  	
Physical Parameters		  		  	
Total Mineralised Material Tonnes Mined (LOM) 		Mt		
9.19 	
Average Annual Throughput (LOM) 		ktpa		
656.3 	
Head Grade 		Au g/t		3.87 	
Gold Recovery to Concentrate 		% 		97% 	
Mine Life 		years		14 	
Gold Grade of Concentrate 		Au g/t		59.71 	
Total Concentrate Produced 		kt		560.5 	
Total Ounces in Concentrate 		koz		1,108.4 	
Average Annual Production (LOM) 		koz		79.2 	
  		  		  	
Cost Parameters 		  		  	
Mining Costs 		US$/t		40.68 	
Processing Costs 		US$/t		14.00 	
General & Administrative 		US$/t		2.71 	
Total Costs 		US$/t		57.39 	
  		  		  	
Pre-Production Capital Costs		  		  	
Mine Development & Infrastructure 		US$m		
29.7 	
Mining Equipment 		US$m		11.2 	
Tailings 		US$m		1.3 	
Process Plant 		US$m		28.3 	
Owners Costs & EPCM 		US$m		12.5 	
Contingency (15%) 		US$m		12.4 	
Total Pre-Production Capital 		US$m		95.3 	
  		  		  	
Sustaining Capital 		US$m		19.3 	
  		  		  	
LOM Cash Costs 		US$/oz		729.15 	
LOM AISC 		US$/oz		752.80 	

MINERAL RESOURCE ESTIMATE

An updated NI 43-101 Mineral Resource Estimate, effective 22 October  2018 is 
included in this PEA and has been filed on SEDAR and the ASX  market 
announcements platform (See October 25, 2018 News Release). 

	  	Tonnes	  			Au	
Category		Mt		g/t	  	koz	
Measured 		1.03 		5.59 		185 	
Indicated 		7.18 		4.43 		
1,023 	
Measured & Indicated 		8.21 		4.58 		
1,208 	
Inferred 		3.12 		3.47 		348 	

Notes:1. Rounding may cause apparent discrepancies2.  Resource Estimate 
conducted by CSA Global of Perth Australia ("CSA")  with an effective date of 
October 22, 2018. Classification of the MRE  was completed based on the 
guidelines presented by Canadian Institute  for Mining (CIM, May 2014), adopted 
for Technical Reports which adhere  to the regulations defined in Canadian NI 
43-101. The Mineral Resource  Estimate was also prepared in accordance with the 
Australasian Code for  Reporting of Exploration Results, Mineral Resources and 
Ore Reserves,  2012 edition ("2012 JORC Code").3. The Mineral Resource  
Estimate was first announced on 25 October 2018. Black Dragon confirms  that it 
is not aware of any new information or data that materially  affects the 
information in the previous announcement and that all  material assumptions and 
technical parameters underpinning the Mineral  Resource Estimate continue to 
apply and have not materially changed.4.  A cut-off grade of 2 g/t Au has been 
applied when reporting the Mineral  Resource Estimate.5. Mineral Resources that 
are not Mineral  Reserves do not have demonstrated economic viability but do 
have  reasonable prospects for eventual economic extraction.6. The  quantity 
and grade of reported Inferred Resources in this estimation are  conceptual in 
nature and there has been insufficient exploration to  define these Inferred 
Resources as an Indicated or Measured Resource. It  is uncertain if further 
exploration will result in upgrading them to an  Indicated or Measured Resource 
category, although it is reasonably  expected that the majority of the Inferred 
Resources could be upgraded  to Indicated Mineral Resources with further 
exploration.7. The  Mineral Resource Estimate underpinning the production 
targets in this  announcement was prepared by a Competent Person under the 2012 
JORC Code.8.  The title of the report is "Salave Gold Project Mineral Resource 
Update  for Black Dragon Gold Corp.", with an effective date of October 22,  
2018, and it was authored by Ian Stockton, B.Sc (Geol)., MAusIMM, FAIG,  Dmitry 
Pertel, MSc (Geol), MAIF, GAA, and Galen White, B.Sc, FAusIMM,  FGS. 

POTENTIALLY EXTRACTABLE PORTION OF  MINERALISATION FOR MINE PLANNING

The mine plan supported by the PEA demonstrates that approximately 81.1%  of 
the total 2018 updated Mineral Resource tonnage is amenable to  underground 
extraction. For purposes of mine planning, the potentially  extractable portion 
of the Mineral Resources are comprised of 9.19  million tonnes at a diluted 
grade of 3.87 g/t Au, containing just over  1.1 million ounces of gold. The 
mineralised material modelled to be  mined in the PEA contains Mineral 
Resources classified in the Inferred  category (28%) that are too speculative 
geologically to have economic  considerations applied that would enable them to 
be categorized as  Mineral Reserves. These Inferred Resources will require 
further  exploration and definition to meet the criteria to be classified as  
Indicated or Measured Mineral Resources before being considered for  conversion 
to Mineral Reserves at the next level of detailed economic  study. 

MINE PLAN

Given environmental and community considerations, the PEA has only  evaluated 
underground mining operations. The primary mining method  selected for detailed 
analysis in this study was the vertical retreat  mining ("VRM"). Sub-level 
stoping was considered as a secondary method  applicable to specific vertical 
thin geometries (<15m length). Rock and  paste fill will be used as backfill to 
maximize mining recovery. 

The mine design was based on basic economic assumptions to create  mineable 
stope outlines. A value of 2 g/t was assumed as mine cut-off  grade. Mining 
dilution and mineralised material loss factors were also  applied to each 
mining shape to reflect the selected mining method. 

The mine production rate targets a 0.70 Mtpa of RoM. A conceptual mine  layout 
was designed including stopes and development as illustrated in  Figure 1, with 
60m levels and 3 x 20m sub-levels. The total mineralised  material from stopes, 
drives and sill pillar recovery (50%) will total  9.2Mt at 3.87 g/t Au. 

A long term mine schedule was created integrating stopes and development  as 
shown in Figures 2 and 3. Mineralised zones were sequenced to  prioritise 
higher grades at lower operating costs. 

MINERAL PROCESSING

In order to minimise potential social and environmental issues,  processing of 
Salave mineralised material has been limited to crushing,  grinding and 
flotation, with concentrates exported via local ports. Mine  feed will be 
crushed on surface at a rate of 0.7 Mtpa, and then be  processed via 
conventional SAG and ball milling followed by sulphide  flotation and 
thickening. 

The run-of-mine will feed a primary jaw crusher with a capacity of 400  t/h 
with a physical availability of 70% with design factor of 20%. 

From an intermediate stockpile, the coarse material will feed the mill  circuit 
which consists of a conventional SAG and ball mill configuration  working in 
close circuit with the cyclones. 

The flotation circuit consists of a number of cells of 300-400 m3  capacity 
(9-10 cells of 40 m3 each) with two conditioning  tanks for pH stabilisation 
and reagents. 

The final stage consists of tailings thickening to minimise the fresh  water 
consumption and to re-cycle process water. A ‘paste’ thickener  will achieve a 
product of 70-75% of solids. 

Based on flotation test work conducted to date, it is assumed that 97%  of the 
gold head grade will be recovered in the flotation concentrate  that will be 
thickened, filtered and bagged for shipping to customers. 

INFRASTRUCTURE AND TAILINGS

Power to the project is available from Tapia, which is linked to the  Asturias 
main distribution grid, and an existing network of power lines  enter the 
property that are connected to the Spanish national  transmission grid. Water 
for both domestic and plant usage can be  sourced from wells, the Porcia River 
(2.5km east of the property) or the  reticulated water supply that is currently 
in place near the plant  location. 

A Tailings Management Facility ("TMF") will be constructed at surface  for 
temporary storage of plant tailings. The paste and backfill of the  mine will 
minimise the amount of tailings storage at surface, and  various options for 
complete tailings disposal are being evaluated. The  TMF design will involve 
water recovery in the processing plant and  transportation to geo-membrane 
lined facility eliminating any risk for  potential surface and ground water 
contamination. 

Surface facilities to support the Salave Project will include an  
administration and engineering building, security, warehouse, fuel and  
explosive storage, fire protection, maintenance shops with a site design  to 
accommodate for 50 full time staff. 

CAPITAL COSTS AND SENSITIVITIES

Input (US$M) 	  	Pre-Production 	  	
Sustaining	  	LOM	
Development 		29.7 		15.7 		
45.3 	
Equipment & Infrastructure 		11.2 		
3.6 		14.8 	
Tailings 		1.3 		0.0 		1.3 	
Process Plant 		28.3 		0.0 		
28.3 	
Owner Costs & EPCM 		12.5 		0.0 		
12.5 	
Contingency (15%) 		12.4 		0.0 		
12.4 	
Total Capex 		95.3		19.3		
114.6	

																		
																		
Sensitivity Analysis 
																			
	
  									
After-Tax NPV (US$M) 	
  							% relative to the 
Base Case 	
Parameter		-20% 	  			Base 
Case 	  			+20% 		-20% 	
  			Base Case 	  	+20% 	
Gold price 		95.8 				
230.0 				361.0 		-58% 
				0% 		57% 	
Processing costs 		244.5 				
230.0 				163.4 		
6% 				0% 		-29% 	
Mining costs 		296.1 				
230.0 				192.3 		
29% 				0% 		-16% 	
Capex 		245.3 				
230.0 				214.6 		
7% 				0% 		-7% 	
																		
Gold Price Sensitivities 	
Macro Parameters 				Unit	
  			-20%	  					
Base Case	  			+20%	
Gold Price 				
US$/oz 				
1,000 						
1,250 				1,500 	
																		
Pre-Tax	
NPV5% 				US$M 				
122.2 						
296.2 				469.2 	
IRR 				% 				
16% 						
28% 				40% 	
																		
Post-Tax	NPV5% 				
US$M 				
95.8 						
230.0 				361.0 	
IRR 				% 				
14% 						
25% 				36% 	
Payback 				Years 				
6.3 						
3.8 				2.6 	

PROJECT FUNDING

The Board of BDG believes there is a reasonable basis to assume the  necessary 
funding for the Salave Gold Project will be obtained for the  following 
reasons: 

The Company has been able to raise funding for its exploration over  the past 
years in order to progress its project. In the last two years  BDG has raised 
over $14.5 million via equity placements. These raises  indicate a clear base 
of support from new and existing shareholders  and third-party investors. The 
Company considers it will be able to  raise funding for the next stage of the 
Project, which will advance  the Project to the completion of a detailed 
Feasibility Study. 
The positive outcomes delivered by the PEA give confidence to the  Board in the 
ability of the Company to fund the development capital  through conventional 
debt and equity financing. A mix of debt and  equity is the most likely funding 
model so 100% of the capital  expenditure will not need to be borrowed. The 
Board has a strong  financing track record in funding start up mining 
operations, and in  their view, it is reasonably expected that when the project 
parameters  in this PEA are met, that funding will be able to be arranged.  
Notwithstanding this, the normal risks for the raising of capital will  apply 
to the Company, such as the state of equity capital and debt  markets, the 
results of the Feasibility Study and the price of gold. 
The Company believes that its funding opportunities will be improved  at the 
completion of the Feasibility Study as a result of: 
(i) confidence in the possibility to increase the Mineral Resource  Estimate 
that would serve to improve the mine life of the Project; 
(ii) confirmation of earlier metallurgical test work to support,  optimise and 
potentially improve concentrate grades; and 
(iii) finalisation of further engineering studies to improve the  accuracy of 
the assessed capital and operating costs 
(iv) offtake contracts for concentrates to improve revenue and  treatment 
charge assumptions 
The funding models being considered will depend on the outcomes of the  
Feasibility Study, but as set out above will likely be conventional  debt and 
equity financing, but may include convertible notes, gold  streaming, 
prepayment of royalties and other options for projects of a  similar nature. 
The raising of equity by the Company may be dilutive to existing  shareholders, 
but that will depend on the price at which the then  funding is completed. 
Where the market capitalisation of the Company  is low as against the amount of 
equity that is required to be raised  at the time, there is a high likelihood 
that shareholders will be  substantially diluted. This is to be balanced 
against the reasonable  expectation of the Company that as the Project becomes 
more advanced,  the value of the Company is more likely to increase, resulting 
in the  actual dilution to existing shareholders being less. The reality is  
that in this case, although the percentage holding of each shareholder  will be 
reduced, the value of that holding will be assessed against a  Company that is 
anticipated to have a higher market capitalisation at  the time of the raising. 

PEA KEY RECOMMENDATIONS

CRS Ingenieria ("CRS"), in Madrid were the principal authors of the PEA  and 
have made the following recommendations for further evaluation that  may 
improve the economics of the project: 

The mineralisation style indicates that both vertical retreat mining  (VRM) and 
room and pillar (RP) are applicable to Salave. For this  study, a combination 
of VRM and SLS was selected, configured with  60m-height panels, however, CRS 
recommends assessing the benefits of  RP for individual panels. 
The production rate of Salave used for the PEA was 0.70 Mtpa. While  this 
production capacity is optimal under current assumptions of  mining method and 
cut-off grade, CRS suggests the evaluation of  alternative cut-off strategies 
that may lead to review the production  rate. 
Evaluate mining methods by panel and create integrated layouts. 
Develop detailed geotechnical studies to estimate stope and room  dimensions 
and modifying factors such as dilution and mineralised  material loss. 
Develop a volume balance of waste and paste over the LoM sequence. 
Further investigate low grade materials by additional drilling to  verify 
geological continuity. 
Sill pillars may be recovered if specific technical and economic  studies 
demonstrate that economic extraction could reasonably be  justified under 
realistic conditions. CRS recommends the completion of  detailed geotechnical 
studies to confirm the viability of sill pillar  recovery. 
Complete an economic study considering obtain free gold through  panning before 
shipment the product. 
Develop a detailed market study to identify potential clients for the  Salave 
gold concentrates. 

QUALIFIED PERSONS AND COMPETENT PERSONS STATEMENT 

The information in this announcement that relates to the PEA for the  Salave 
Gold Project is based on and fairly represents information and  supporting 
documentation prepared by CRS Ingenieria and CSA Global.  Paulo Laymen (P.Eng., 
M.AusIMM., B.Eng., M.Eng.) of CRS Ingenieria  supervised the preparation of the 
PEA, is independent of the Company and  a qualified person as defined by 
National Instrument 43-101 and has  reviewed and approved the technical 
disclosure reported herein. Dmitry  Pertel (P.Geo., MSc (Geol), MAIF, GAA) and 
Belinda van Lente (P.Geo.) of  CSA Global were responsible for the Mineral 
Resource Estimate and are  independent of the Company and qualified persons as 
defined by National  Instrument 43-101 and have reviewed and approved the 
technical  disclosure reported herein. 

The NI 43-101 Technical Report will be fined on SEDAR within 45 days of  this 
release. 

BLACK DRAGON GOLD CORP.1000 Cathedral Place925 West Georgia  StreetVancouver, 
BC V6C 3L2, Canada,T- +44 20 79934077 F-  +44 20 
71128814info@blackdragongold.comwww.blackdragongold.com 

ABOUT BLACK DRAGON GOLD

Black Dragon Gold "BDG" is the 100% owner of one of the largest  undeveloped 
gold projects in Europe, the Salave project. Salave is  situated in the North 
of Spain in the province of Asturias. The Salave  project has an updated 
combined Measured and Indicated Mineral Resource  of 8.21 million tonnes 
grading 4.58 g/t Au, containing 1.21 million  ounces of gold, plus Inferred 
resources totalling 3.12 million tonnes  grading 3.47 g/t Au, containing 
348,000 ounces of gold. 

A full technical report summarizing the Mineral Resource estimate  completed by 
CSA Global is available on the company’s web site and  posted on SEDAR. In 
addition to the current Mineral Resource, historical  exploration work suggests 
there is the potential for additional  mineralisation within Black Dragon’s 
landholdings. 

FORWARD LOOKING STATEMENTS

This news release contains forward-looking statements that are based on  the 
Corporation's current expectations and estimates. Forward-looking  statements 
are frequently characterized by words such as "plan",  "expect", "project", 
"intend", "believe", "anticipate", "estimate",  "suggest", "indicate" and other 
similar words or statements that certain  events or conditions "may" or "will" 
occur. Such forward-looking  statements involve known and unknown risks, 
uncertainties and other  factors that could cause actual events or results to 
differ materially  from estimated or anticipated events or results implied or 
expressed in  such forward-looking statements. Such factors include, among 
others: the  actual results of current planned exploration activities; changes 
in  project parameters as plans to continue to be refined; possible  variations 
in recovered material grade or recovery rates; accidents,  labor disputes and 
other risks of the mining industry; delays or any  inability in obtaining 
governmental approvals or financing; and  fluctuations in metal prices. There 
may be other factors that cause  actions, events or results not to be as 
anticipated, estimated or  intended. Any forward-looking statement speaks only 
as of the date on  which it is made and, except as may be required by 
applicable securities  laws, the Corporation disclaims any intent or obligation 
to update any  forward-looking statement, whether as a result of new 
information,  future events or results or otherwise. Forward-looking statements 
are  not guarantees of future performance and accordingly undue reliance  
should not be put on such statements due to the inherent uncertainty  therein. 

Neither the TSX Venture Exchange, nor its Regulation Services Providers  (as 
that term is defined in the policies of the TSX Venture Exchange)  accepts 
responsibility for the adequacy or accuracy of this news release. 

All figures are rounded to reflect the relative accuracy of the news  release. 

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20190211005527/en/

Contacts

Paul CroninCEO & Managing DirectorP: +44 20  79934077E: 
paul.cronin@blackdragongold.com 

Source: Black Dragon Gold Corp.


Feb. 11, 2019 16:02 UTC

Black Dragon Gold Corp.: Positive Preliminary Economic Assessment for  Salave 
Underground 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Black Dragon Gold Corp. 

TSX VENTURE SYMBOL: BDG 

VANCOUVER, British Columbia--(BUSINESS WIRE)-- Black Dragon Gold Corp. 
(ASX/TSX-V: BDG) ("Black Dragon" or the  "Company") is pleased to announce the 
positive results of  the Preliminary Economic Assessment ("PEA") completed on 
its 100% owned  Salave Gold Project ("Salave" or "Project") located in Asturias 
in  northern Spain. The PEA is based on the recently completed Mineral  
Resource Estimate completed by CSA Global (See October 25, 2018 News  Release). 
All figures are in United States Dollars unless otherwise  stated. 

This press release features multimedia. View the full release here:  
https://www.businesswire.com/news/home/20190211005527/en/ 

The PEA demonstrates robust economics for an underground mining  operation with 
a 14-year mine life. 

Paul Cronin, Managing Director and CEO commented, 

"The completion of the PEA is a major milestone on the path to  development of 
the Salave Project and the metrics support our belief  that Salave can 
potentially generate strong returns for shareholders. It  forms the first step 
in our permitting process, presenting a new  optimised process on a zero- 
discharge basis that minimises the visual  and surface impact of the project. 

The robust results of this PEA underline the potential economic  viability of 
the current Salave resource to be mined over an initial 14  year mine life, and 
our successful drilling campaign last year indicates  strong potential for 
growth in mine life at Salave. 

This study supports that Salave can produce over 1.1Moz (560 kt of  concentrate 
averaging over 59 g/t Au), providing a number of marketing  options for export 
and refining, minimising the need for additional  plant and equipment, and 
hence reducing the Project’s footprint. The  relatively low upfront capex also 
opens alternative financing  opportunities which will ensure that both 
shareholders and the local  community benefit from the success of this 
Project." 

KEY PEA OUTCOMES

Pre-Tax NPV at 5% discount rate: US$ 296.2 million. 
After-Tax NPV: US$ 230.0 million 
Pre-Tax Internal Rate of Return ("IRR"): 28% 

After-Tax Internal Rate of Return ("IRR"): 25% 

After-Tax Payback: 3.8 years 
Pre-Production Capital Cost, including contingency: US$ 95.3 million 
Life of Mine ("LOM") Sustaining Capital Cost: US$19.3 million 
Estimated Average LOM Total Cash Cost: $729/ounce (oz) Au 
Estimated Average LOM All-In Sustaining Costs ("AISC"): $752/oz Au 

CAUTIONARY STATEMENT

The PEA is a preliminary technical and economic study of the potential  
viability of the Salave Gold Project. It is preliminary in nature and  includes 
Inferred Mineral Resources that are considered too  speculative geologically to 
have economic considerations applied to  them that would enable them to be 
categorized as Mineral Reserves.  There can be no assurance, and there is no 
certainty, that the  preliminary economic assessment contained therein will be 
realised.  Further exploration and evaluation work and appropriate studies are  
required before Black Dragon will be in a position to estimate any Ore  
Reserves or to provide any assurance of an economic development case. 
The production target and forecast financial information referred to  in this 
PEA are comprised of Measured and Indicated Mineral Resources  (73%) and 
Inferred Mineral Resources (27%). The proportion of Inferred  Mineral Resources 
is not determinative of the project viability and  does not feature as a 
significant proportion early in the mine plan. 
Metallurgical recoveries have been based on test work data and costs  have been 
estimated by independent consultants generally from budget  quotations, 
factored estimates or cost data from similar  operations/projects. Cost 
estimate accuracy for the PEA is in the  order of +/-35%. 
The PEA is based on the material assumptions outlined herein and in  the 
report. These include assumptions about the availability of  funding. While BDG 
considers all of the material assumptions to be  based on reasonable grounds, 
there is no certainty that they will  prove to be correct or that the range of 
outcomes indicated by the PEA  will be achieved. To achieve the range of 
outcomes indicated in the  PEA, among other things, funding of in the order of 
US$100 million  will likely be required. Investors should note that there is 
no  certainty that Black Dragon will be able to raise that amount of  funding 
when needed. 
It is also likely that such funding may only be available on terms  that may be 
dilutive to or otherwise affect the value of BDG’s  existing shares. It is also 
possible that BDG could pursue other  ‘value realisation’ strategies such as a 
sale, partial sale or joint  venture of the project. If it does, this could 
materially reduce BDG’s  proportionate ownership of the project. Given the 
uncertainties  involved, investors should not make any investment decisions 
based  solely on the results of the PEA. 

NEXT STEPS

Submission of the Project Description for the Environmental and Social  Impact 
Assessment ("ESIA") in February 2019; 
Additional geophysics over the entire Investigation Permit at Salave –  April 
2019; 
Issuance of the ESIA Terms of Reference in June 2019; 
Soil Geochemistry testing on potential drill targets – June 2019; 
Pre-Feasibility Study – October 2019. 

PEA KEY ASSUMPTIONS AND INPUTS

Assumed gold price: US$1,250/oz 
Exchange Rate of $1.15 / € 
Life of Mine: 14-years 
Main Underground Mining Method: Vertical Retreat & Sub-Level Stoping 
Average Diluted Head Grade: 3.87 g/t Au 
Total Underground Dilution: 43% 
LOM Plant Throughput 9.19 Mt 
Access Ramp Gradient of 15% at a 5.0m x 5.5m profile 
Mineralised Zone Development at a 4.0m x 4.5m profile 
Average Mining and Processing throughput: 2,000 tonnes per day ("tpd") 
Flotation Plant Recoveries: 97% 
Average Annual Production (LOM): 79,200 oz Au in concentrate at an  average 
grade of 59.7 g/t Au 
LOM recovered gold in concentrate production: 1,108,420 oz; 
Refining and Processing Charges: US$368/t concentrate or US$188/oz Au 

Table 1 - PEA Summary Parameters

Input 	  	Unit 	  	  	
Physical Parameters		  		  	
Total Mineralised Material Tonnes Mined (LOM) 		Mt		9.19 	
Average Annual Throughput (LOM) 		ktpa		656.3 	
Head Grade 		Au g/t		3.87 	
Gold Recovery to Concentrate 		% 		97% 	
Mine Life 		years		14 	
Gold Grade of Concentrate 		Au g/t		59.71 	
Total Concentrate Produced 		kt		560.5 	
Total Ounces in Concentrate 		koz		1,108.4 	
Average Annual Production (LOM) 		koz		79.2 	
  		  		  	
Cost Parameters 		  		  	
Mining Costs 		US$/t		40.68 	
Processing Costs 		US$/t		14.00 	
General & Administrative 		US$/t		2.71 	
Total Costs 		US$/t		57.39 	
  		  		  	
Pre-Production Capital Costs		  		  	
Mine Development & Infrastructure 		US$m		29.7 	
Mining Equipment 		US$m		11.2 	
Tailings 		US$m		1.3 	
Process Plant 		US$m		28.3 	
Owners Costs & EPCM 		US$m		12.5 	
Contingency (15%) 		US$m		12.4 	
Total Pre-Production Capital 		US$m		95.3 	
  		  		  	
Sustaining Capital 		US$m		19.3 	
  		  		  	
LOM Cash Costs 		US$/oz		729.15 	
LOM AISC 		US$/oz		752.80 	

MINERAL RESOURCE ESTIMATE

An updated NI 43-101 Mineral Resource Estimate, effective 22 October  2018 is 
included in this PEA and has been filed on SEDAR and the ASX  market 
announcements platform (See October 25, 2018 News Release). 

	  	Tonnes	  																																																																																																																																																																																																																																																																	Au			
Category		Mt		g/t	  	koz	
Measured 		1.03 		5.59 		185 	
Indicated 		7.18 		4.43 		1,023 	
Measured & Indicated 		8.21 		4.58 		1,208 	
Inferred 		3.12 		3.47 		348 	

Notes:1. Rounding may cause apparent discrepancies2.  Resource Estimate 
conducted by CSA Global of Perth Australia ("CSA")  with an effective date of 
October 22, 2018. Classification of the MRE  was completed based on the 
guidelines presented by Canadian Institute  for Mining (CIM, May 2014), adopted 
for Technical Reports which adhere  to the regulations defined in Canadian NI 
43-101. The Mineral Resource  Estimate was also prepared in accordance with the 
Australasian Code for  Reporting of Exploration Results, Mineral Resources and 
Ore Reserves,  2012 edition ("2012 JORC Code").3. The Mineral Resource  
Estimate was first announced on 25 October 2018. Black Dragon confirms  that it 
is not aware of any new information or data that materially  affects the 
information in the previous announcement and that all  material assumptions and 
technical parameters underpinning the Mineral  Resource Estimate continue to 
apply and have not materially changed.4.  A cut-off grade of 2 g/t Au has been 
applied when reporting the Mineral  Resource Estimate.5. Mineral Resources that 
are not Mineral  Reserves do not have demonstrated economic viability but do 
have  reasonable prospects for eventual economic extraction.6. The  quantity 
and grade of reported Inferred Resources in this estimation are  conceptual in 
nature and there has been insufficient exploration to  define these Inferred 
Resources as an Indicated or Measured Resource. It  is uncertain if further 
exploration will result in upgrading them to an  Indicated or Measured Resource 
category, although it is reasonably  expected that the majority of the Inferred 
Resources could be upgraded  to Indicated Mineral Resources with further 
exploration.7. The  Mineral Resource Estimate underpinning the production 
targets in this  announcement was prepared by a Competent Person under the 2012 
JORC Code.8.  The title of the report is "Salave Gold Project Mineral Resource 
Update  for Black Dragon Gold Corp.", with an effective date of October 22,  
2018, and it was authored by Ian Stockton, B.Sc (Geol)., MAusIMM, FAIG,  Dmitry 
Pertel, MSc (Geol), MAIF, GAA, and Galen White, B.Sc, FAusIMM,  FGS. 

POTENTIALLY EXTRACTABLE PORTION OF  MINERALISATION FOR MINE PLANNING

The mine plan supported by the PEA demonstrates that approximately 81.1%  of 
the total 2018 updated Mineral Resource tonnage is amenable to  underground 
extraction. For purposes of mine planning, the potentially  extractable portion 
of the Mineral Resources are comprised of 9.19  million tonnes at a diluted 
grade of 3.87 g/t Au, containing just over  1.1 million ounces of gold. The 
mineralised material modelled to be  mined in the PEA contains Mineral 
Resources classified in the Inferred  category (28%) that are too speculative 
geologically to have economic  considerations applied that would enable them to 
be categorized as  Mineral Reserves. These Inferred Resources will require 
further  exploration and definition to meet the criteria to be classified as  
Indicated or Measured Mineral Resources before being considered for  conversion 
to Mineral Reserves at the next level of detailed economic  study. 

MINE PLAN

Given environmental and community considerations, the PEA has only  evaluated 
underground mining operations. The primary mining method  selected for detailed 
analysis in this study was the vertical retreat  mining ("VRM"). Sub-level 
stoping was considered as a secondary method  applicable to specific vertical 
thin geometries (<15m length). Rock and  paste fill will be used as backfill to 
maximize mining recovery. 

The mine design was based on basic economic assumptions to create  mineable 
stope outlines. A value of 2 g/t was assumed as mine cut-off  grade. Mining 
dilution and mineralised material loss factors were also  applied to each 
mining shape to reflect the selected mining method. 

The mine production rate targets a 0.70 Mtpa of RoM. A conceptual mine  layout 
was designed including stopes and development as illustrated in  Figure 1, with 
60m levels and 3 x 20m sub-levels. The total mineralised  material from stopes, 
drives and sill pillar recovery (50%) will total  9.2Mt at 3.87 g/t Au. 

A long term mine schedule was created integrating stopes and development  as 
shown in Figures 2 and 3. Mineralised zones were sequenced to  prioritise 
higher grades at lower operating costs. 

MINERAL PROCESSING

In order to minimise potential social and environmental issues,  processing of 
Salave mineralised material has been limited to crushing,  grinding and 
flotation, with concentrates exported via local ports. Mine  feed will be 
crushed on surface at a rate of 0.7 Mtpa, and then be  processed via 
conventional SAG and ball milling followed by sulphide  flotation and 
thickening. 

The run-of-mine will feed a primary jaw crusher with a capacity of 400  t/h 
with a physical availability of 70% with design factor of 20%. 

From an intermediate stockpile, the coarse material will feed the mill  circuit 
which consists of a conventional SAG and ball mill configuration  working in 
close circuit with the cyclones. 

The flotation circuit consists of a number of cells of 300-400 m3  capacity 
(9-10 cells of 40 m3 each) with two conditioning  tanks for pH stabilisation 
and reagents. 

The final stage consists of tailings thickening to minimise the fresh  water 
consumption and to re-cycle process water. A ‘paste’ thickener  will achieve a 
product of 70-75% of solids. 

Based on flotation test work conducted to date, it is assumed that 97%  of the 
gold head grade will be recovered in the flotation concentrate  that will be 
thickened, filtered and bagged for shipping to customers. 

INFRASTRUCTURE AND TAILINGS

Power to the project is available from Tapia, which is linked to the  Asturias 
main distribution grid, and an existing network of power lines  enter the 
property that are connected to the Spanish national  transmission grid. Water 
for both domestic and plant usage can be  sourced from wells, the Porcia River 
(2.5km east of the property) or the  reticulated water supply that is currently 
in place near the plant  location. 

A Tailings Management Facility ("TMF") will be constructed at surface  for 
temporary storage of plant tailings. The paste and backfill of the  mine will 
minimise the amount of tailings storage at surface, and  various options for 
complete tailings disposal are being evaluated. The  TMF design will involve 
water recovery in the processing plant and  transportation to geo-membrane 
lined facility eliminating any risk for  potential surface and ground water 
contamination. 

Surface facilities to support the Salave Project will include an  
administration and engineering building, security, warehouse, fuel and  
explosive storage, fire protection, maintenance shops with a site design  to 
accommodate for 50 full time staff. 

CAPITAL COSTS AND SENSITIVITIES

Input (US$M) 	  	Pre-Production 	  	Sustaining	  	LOM	
Development 		29.7 		15.7 		45.3 	
Equipment & Infrastructure 		11.2 		3.6 		14.8 	
Tailings 		1.3 		0.0 		1.3 	
Process Plant 		28.3 		0.0 		28.3 	
Owner Costs & EPCM 		12.5 		0.0 		12.5 	
Contingency (15%) 		12.4 		0.0 		12.4 	
Total Capex 		95.3		19.3		114.6	

																	
Sensitivity Analysis 
																			
	  																																																																																																																																																																																																																																																																	After-Tax NPV (US$M) 									  																																																																																																																																																																																																																																																																	% relative to the Base Case 							
Parameter		-20% 	  																																																																																																																																																																																																																																																																	Base Case 			  																																																																																																																																																																																																																																																																	+20% 				-20% 	  																																																																																																																																																																																																																																																																	Base Case 			  	+20% 	
Gold price 		95.8 																																																																																																																																																																																																																																																																		230.0 																																																																																																																																																																																																																																																																				361.0 				-58% 																																																																																																																																																																																																																																																																		0% 				57% 	
Processing costs 		244.5 																																																																																																																																																																																																																																																																		230.0 																																																																																																																																																																																																																																																																				163.4 				6% 																																																																																																																																																																																																																																																																		0% 				-29% 	
Mining costs 		296.1 																																																																																																																																																																																																																																																																		230.0 																																																																																																																																																																																																																																																																				192.3 				29% 																																																																																																																																																																																																																																																																		0% 				-16% 	
Capex 		245.3 																																																																																																																																																																																																																																																																		230.0 																																																																																																																																																																																																																																																																				214.6 				7% 																																																																																																																																																																																																																																																																		0% 				-7% 	
																																																																																																																																																																																																																																																																Gold Price Sensitivities 																			
Macro Parameters 																																																																																																																																																																																																																																																																		Unit			  																																																																																																																																																																																																																																																																	-20%			  																																																																																																																																																																																																																																																																	Base Case					  																																																																																																																																																																																																																																																																	+20%			
Gold Price 																																																																																																																																																																																																																																																																		US$/oz 																																																																																																																																																																																																																																																																				1,000 										1,250 																																																																																																																																																																																																																																																																						1,500 			
																																																																																																																																																																																																																																																																Pre-Tax																			
NPV5% 																																																																																																																																																																																																																																																																		US$M 																																																																																																																																																																																																																																																																				122.2 																																																																																																																																																																																																																																																																				296.2 																																																																																																																																																																																																																																																																						469.2 			
IRR 																																																																																																																																																																																																																																																																		% 																																																																																																																																																																																																																																																																				16% 																																																																																																																																																																																																																																																																				28% 																																																																																																																																																																																																																																																																						40% 			
																																																																																																																																																																																																																																																																Post-Tax																			
NPV5% 																																																																																																																																																																																																																																																																		US$M 																																																																																																																																																																																																																																																																				95.8 																																																																																																																																																																																																																																																																				230.0 																																																																																																																																																																																																																																																																						361.0 			
IRR 																																																																																																																																																																																																																																																																		% 																																																																																																																																																																																																																																																																				14% 																																																																																																																																																																																																																																																																				25% 																																																																																																																																																																																																																																																																						36% 			
Payback 																																																																																																																																																																																																																																																																		Years 																																																																																																																																																																																																																																																																				6.3 																																																																																																																																																																																																																																																																				3.8 																																																																																																																																																																																																																																																																						2.6 			

PROJECT FUNDING

The Board of BDG believes there is a reasonable basis to assume the  necessary 
funding for the Salave Gold Project will be obtained for the  following 
reasons: 

The Company has been able to raise funding for its exploration over  the past 
years in order to progress its project. In the last two years  BDG has raised 
over $14.5 million via equity placements. These raises  indicate a clear base 
of support from new and existing shareholders  and third-party investors. The 
Company considers it will be able to  raise funding for the next stage of the 
Project, which will advance  the Project to the completion of a detailed 
Feasibility Study. 
The positive outcomes delivered by the PEA give confidence to the  Board in the 
ability of the Company to fund the development capital  through conventional 
debt and equity financing. A mix of debt and  equity is the most likely funding 
model so 100% of the capital  expenditure will not need to be borrowed. The 
Board has a strong  financing track record in funding start up mining 
operations, and in  their view, it is reasonably expected that when the project 
parameters  in this PEA are met, that funding will be able to be arranged.  
Notwithstanding this, the normal risks for the raising of capital will  apply 
to the Company, such as the state of equity capital and debt  markets, the 
results of the Feasibility Study and the price of gold. 
The Company believes that its funding opportunities will be improved  at the 
completion of the Feasibility Study as a result of: 
(i) confidence in the possibility to increase the Mineral Resource  Estimate 
that would serve to improve the mine life of the Project; 
(ii) confirmation of earlier metallurgical test work to support,  optimise and 
potentially improve concentrate grades; and 
(iii) finalisation of further engineering studies to improve the  accuracy of 
the assessed capital and operating costs 
(iv) offtake contracts for concentrates to improve revenue and  treatment 
charge assumptions 
The funding models being considered will depend on the outcomes of the  
Feasibility Study, but as set out above will likely be conventional  debt and 
equity financing, but may include convertible notes, gold  streaming, 
prepayment of royalties and other options for projects of a  similar nature. 
The raising of equity by the Company may be dilutive to existing  shareholders, 
but that will depend on the price at which the then  funding is completed. 
Where the market capitalisation of the Company  is low as against the amount of 
equity that is required to be raised  at the time, there is a high likelihood 
that shareholders will be  substantially diluted. This is to be balanced 
against the reasonable  expectation of the Company that as the Project becomes 
more advanced,  the value of the Company is more likely to increase, resulting 
in the  actual dilution to existing shareholders being less. The reality is  
that in this case, although the percentage holding of each shareholder  will be 
reduced, the value of that holding will be assessed against a  Company that is 
anticipated to have a higher market capitalisation at  the time of the raising. 

PEA KEY RECOMMENDATIONS

CRS Ingenieria ("CRS"), in Madrid were the principal authors of the PEA  and 
have made the following recommendations for further evaluation that  may 
improve the economics of the project: 

The mineralisation style indicates that both vertical retreat mining  (VRM) and 
room and pillar (RP) are applicable to Salave. For this  study, a combination 
of VRM and SLS was selected, configured with  60m-height panels, however, CRS 
recommends assessing the benefits of  RP for individual panels. 
The production rate of Salave used for the PEA was 0.70 Mtpa. While  this 
production capacity is optimal under current assumptions of  mining method and 
cut-off grade, CRS suggests the evaluation of  alternative cut-off strategies 
that may lead to review the production  rate. 
Evaluate mining methods by panel and create integrated layouts. 
Develop detailed geotechnical studies to estimate stope and room  dimensions 
and modifying factors such as dilution and mineralised  material loss. 
Develop a volume balance of waste and paste over the LoM sequence. 
Further investigate low grade materials by additional drilling to  verify 
geological continuity. 
Sill pillars may be recovered if specific technical and economic  studies 
demonstrate that economic extraction could reasonably be  justified under 
realistic conditions. CRS recommends the completion of  detailed geotechnical 
studies to confirm the viability of sill pillar  recovery. 
Complete an economic study considering obtain free gold through  panning before 
shipment the product. 
Develop a detailed market study to identify potential clients for the  Salave 
gold concentrates. 

QUALIFIED PERSONS AND COMPETENT PERSONS STATEMENT 

The information in this announcement that relates to the PEA for the  Salave 
Gold Project is based on and fairly represents information and  supporting 
documentation prepared by CRS Ingenieria and CSA Global.  Paulo Laymen (P.Eng., 
M.AusIMM., B.Eng., M.Eng.) of CRS Ingenieria  supervised the preparation of the 
PEA, is independent of the Company and  a qualified person as defined by 
National Instrument 43-101 and has  reviewed and approved the technical 
disclosure reported herein. Dmitry  Pertel (P.Geo., MSc (Geol), MAIF, GAA) and 
Belinda van Lente (P.Geo.) of  CSA Global were responsible for the Mineral 
Resource Estimate and are  independent of the Company and qualified persons as 
defined by National  Instrument 43-101 and have reviewed and approved the 
technical  disclosure reported herein. 

The NI 43-101 Technical Report will be fined on SEDAR within 45 days of  this 
release. 

BLACK DRAGON GOLD CORP.1000 Cathedral Place925 West Georgia  StreetVancouver, 
BC V6C 3L2, Canada,T- +44 20 79934077 F-  +44 20 
71128814info@blackdragongold.comwww.blackdragongold.com 

ABOUT BLACK DRAGON GOLD

Black Dragon Gold "BDG" is the 100% owner of one of the largest  undeveloped 
gold projects in Europe, the Salave project. Salave is  situated in the North 
of Spain in the province of Asturias. The Salave  project has an updated 
combined Measured and Indicated Mineral Resource  of 8.21 million tonnes 
grading 4.58 g/t Au, containing 1.21 million  ounces of gold, plus Inferred 
resources totalling 3.12 million tonnes  grading 3.47 g/t Au, containing 
348,000 ounces of gold. 

A full technical report summarizing the Mineral Resource estimate  completed by 
CSA Global is available on the company’s web site and  posted on SEDAR. In 
addition to the current Mineral Resource, historical  exploration work suggests 
there is the potential for additional  mineralisation within Black Dragon’s 
landholdings. 

FORWARD LOOKING STATEMENTS

This news release contains forward-looking statements that are based on  the 
Corporation's current expectations and estimates. Forward-looking  statements 
are frequently characterized by words such as "plan",  "expect", "project", 
"intend", "believe", "anticipate", "estimate",  "suggest", "indicate" and other 
similar words or statements that certain  events or conditions "may" or "will" 
occur. Such forward-looking  statements involve known and unknown risks, 
uncertainties and other  factors that could cause actual events or results to 
differ materially  from estimated or anticipated events or results implied or 
expressed in  such forward-looking statements. Such factors include, among 
others: the  actual results of current planned exploration activities; changes 
in  project parameters as plans to continue to be refined; possible  variations 
in recovered material grade or recovery rates; accidents,  labor disputes and 
other risks of the mining industry; delays or any  inability in obtaining 
governmental approvals or financing; and  fluctuations in metal prices. There 
may be other factors that cause  actions, events or results not to be as 
anticipated, estimated or  intended. Any forward-looking statement speaks only 
as of the date on  which it is made and, except as may be required by 
applicable securities  laws, the Corporation disclaims any intent or obligation 
to update any  forward-looking statement, whether as a result of new 
information,  future events or results or otherwise. Forward-looking statements 
are  not guarantees of future performance and accordingly undue reliance  
should not be put on such statements due to the inherent uncertainty  therein. 

Neither the TSX Venture Exchange, nor its Regulation Services Providers  (as 
that term is defined in the policies of the TSX Venture Exchange)  accepts 
responsibility for the adequacy or accuracy of this news release. 

All figures are rounded to reflect the relative accuracy of the news  release. 

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20190211005527/en/

Contacts

Paul CroninCEO & Managing DirectorP: +44 20  79934077E: 
paul.cronin@blackdragongold.com 

Source: Black Dragon Gold Corp.
Powered by Business Wire